## Slide 1: Electron Cloud Effects at SuperKEKB
K. Ohmi (KEK)
ECLOUD’22, Sep. 26-28, 2022
d’Elba, Italy

## Slide 2: SuperKEKB
C=3016.3m, e+(4GeV)-e-(7GeV) circular collider
Half crossing angle, fc=41.5mrad, sz=6/5mm.
 | Phase 2 (May 2018) |  | Phase 3 2021-2022 |  | Design | 
 | LER | HER | LER | HER | LER | HER
bx*[mm] | 200 | 200 | 80 | 60 | 32 | 25
by*[mm] | 4 | 4 | 1 | 1 | 0.27 | 0.30
ex [nm] | 2.1 | 4.6 | 4.0 | 4.6 | 3.2 | 4.6
ey [pm] | 5 |  | 25 |  | 0.27 | 0.28
Ib [mA] | 340 | 285 | 1 | 0.8 | 1.44 | 1.04
xx |  |  | 0.0** | 0.0* | 0.0028 | 0.0012
xy | 0.019 | 0.013 | 0.0** | 0.03 | 0.088 | 0.081
Nbunch | 788 |  | 1576 |  | 2500 | 
L [cm-2s-1] | 1.3x1033 |  | 4.6x1034 |  | 8x1035 | 
PA Fc | 10 | 8 | 15.2 | 9.7 | 24.7 | 19.4

## Slide 3: Instability simulation at SuperKEKB design stage
Using code PEHTS
Simulation, reth=3.8x1011 m-3.
re=4.2x1011 at 4000-th turn
Design target for vacuum system: re<1011 m-3 in average of whole ring
Q=min(wesz/c,Qnl)
K=wesz/c=

## Slide 4: Wake force induced by electron cloud
Discuss later in detail.
Qnl=7

## Slide 5: KEKB: measurement and simulation of fast head-tail instability
Tail of train
Head of train
Betatron sideband
Simulation (PEHTS)
HEADTAIL gave similar results (E. Beneditto showed large cloud gave nice sideband signal)
Beam size blow up observed, and simultaneously synchro-beta sideband observed.
>νs
Measurement at KEKB
ρe,th=0.8x1012m-3
J. Flanagan et al., PRL94, 054801 (2005)

## Slide 6: Phase I commissioning
2017 Feb.-June
No collision. Test as two storage rings, e+(LER) and e-(HER).
I=1A(e+) and 0.8A(e-) were stored.
Electron cloud studies were performed.
  Beam size blow-up caused by electron cloud was seen, but was recovered by permanent solenoid magnets.

## Slide 7: Beam size blow-up in LER
June 1, 2016
4 train x150 bunches, Nbunch=600
Beam-size blowup observed in KEKB had been seen in early stage of SuperKEKB commissioning
Threshold I~300mA in Apr 19
Electron cloud has been monitored at AL chamber w and w/o TiN coating
Aluminum bellows, which were not coated by TiN, were suspected as an electron source.
Permanent magnets were installed at the aluminum bellows.(Y. Suetsugu et al.)
The blow up was suppressed.
Systematic studies were done in 1 June before PM and in 8 July after PM installation.
Threshold beam current
160, 200, 260,500 mA for 2, 3, 4, 6 bucket spacing
Before perm. mag installation
sy

## Slide 8: Simulation studies using beam study condition
Np=1.6x1010 Ith=160mA, 4ns spacing
Np=2.1x1010
Ith=200mA, 6ns spacing
Np=2.7x1010
Ith=260mA, 8ns spacing
Np=5.2x1010
Ith=500mA, 8ns spacing
Np=3.65x1010,
Ith=350mA, 6ns
Np=6.25x1010,
I=600mA, 8ns
Threshold of the electron density
ex=2nm, ey=15pm, sz =6mm, ns=0.019

## Slide 9: Electron density at the blow-up threshold
Simulated electron density at the threshold current
Measured threshold current and density
Simple formula Q=7
Local density at Al chamber
Al part (bellow) occupies only 5% of whole ring, but dominant for ecloud instability.
Discrepancy in ★ and 〇 is seen at narrow bunch spacing.
Electrons in antechamber part (95%) contributes the instability, especially large bunch spacing.
Overall density contributes at narrow bunch spacing.
r
Overall average density=0.05x
nbunch =600

## Slide 10: After installation of permanent solenoid at Al bellows
Simple formula Q=7
After : 2016/6/8
4/150/3
4/150/2
4/150/4
Ith=200 mA
Ith=330 mA
Ith>600 mA
Simulated electron density at the threshold current
r
Beam study nbunch =600
160mA to 200mA by 2 bucket
200mA to 330mA by 3
260mA to >600mA by 4
SuperKEKB nbunch=1500-2500 in physics run
sy
The density at Al bellows is not dominant for the instability.
Threshold is determined by the overall averaged density.
nbunch =600

## Slide 11: Summary of measurement and simulation
Before PM installation Assume simulation is correct
rth(by 2)=2x1012x0.05+r2(160mA), r2(160mA)=2.25x1011
rth(by3)=3x1012x0.05+r3(200mA), r3(200mA)=1.75x1011
rth(by4)=6x1012x0.05+r4(260mA), r4(260mA)=1.25x1011
rth(by6)=8x1012x0.05+r6(500mA), r6(500mA)=0.75x1011
After PM installation Assume linear increase for I
rth(by2)= r2(200mA) r2(200mA)=2.8x1011 3,4
rth(by3)= r3(330mA) r3(330mA)=2.9x1011 3,8
rth(by4)= r4(>600mA) r4(600mA)=2.9x1011 4.2
r6(600mA)=0.9x1011
Operation with 600 bunches

## Slide 12: Finding
rth given by simulation can explain measurement.
In the formula, ,
  Q=min(wesz/c,Qnl), Qnl is around ~6.
Q is lower for higher bunch current, I>0.5mA.
The formula works well as a first step evaluation.

## Slide 13: Electron buildup simulation in ante-chamber
Band matrix solver for electric field induced by electron cloud.
Beam force, combination of Basetti-Erskine formula (r<10sx) and potential solver (r>10sx).
Synchrotron light is assumed to illuminate innermost of the ante-slot.
Electron production, cos(q) distribution for normal direction.

## Slide 14: Beam force near ante-slot
inside slot x>45mm
inside slot x>45mm

## Slide 15: Electron distribution, potential and motion
Weak space charge limit. Production rate 0.8x105m-1/bunch, beam line density 2x1010 m-1.
No secondary no reflected electron
1 bunch before
2 bunch before
potential
Electron distribution
Phase space distribution of electrons

## Slide 16: Ecloud Simulation in antechamber
N0: Number of electron created at illuminated point (slot end), Nin: #electron go inside the beam area, Nout: go out to the slot area.
Np=6.26x1010 (1mA/bunch), 6ns spacing, lp=3.48x1010 m-1.
Weak space charge limit, production rate 5x105m-1/bunch
No secondary, no reflected electrons.
integrated during the bunch separation
Far downsream, straight section

## Slide 17: Ecloud Simulation in antechamber
N0: Number of electron created at illuminated point (slot end), Nin: #electron go inside the beam area, Nout: go out to the slot area.
Np=6.26x1010 (1mA/bunch), 6ns spacing, lp=3.48x1010 m-1.
Production rate, 0.016 e-/m/e+, 10x108m-1/bunch.
Secondary SEY=1.2, reflected electrons 0.7.
integrated during the bunch separation

## Slide 18: Finding in ecloud simulation in the antechamber
Beam force arrives only 5mm inside of slot.
Number of electrons coming from the slot is 7% of created electron at slot end for weak electron density. The number is reduced to 3-4% for average electron production.
The number change a little for the bunch current 0.5 or 1mA.

## Slide 19: Electron cloud Wake model (single bunch)
Assume a part of bunch shifts positive direction.
Electron cloud is kicked positive direction
Electron cloud oscillates with we.
  Positron bunch is kicked by the deviation of the electron cloud.
  Electron cloud is pinched, then the density increases.
Positron bunch (~10ps)
Electron cloud
<1ps
Uniform distribution for z.
lp: Positron line density in a bunch

## Slide 20: Example of wake force K.Ohmi, F. Zimmermann, E. Perevedentsev, PRE65, 016502 (2001)
For small x-y size of electron cloud,
Qnl=7

## Slide 21: Instability threshold for coasting beam model
Instability threshold in coasting model (A. Chao’s textbook Chap 5)
  Coherent growth due to the wake force
  Decoherence due to the longitudinal slippage
Wake is terminated by the bunch length, Q=Min(wesz/c,Qnl=7).
Number of electrons, which contributes to the instability, depends on wesz/c. The enhancement K is chosen K= wesz/c.
Stability condition

## Slide 22: Realistic model: Gaussian distribution for z
Conventional wake is a function of z-z’, where z is a variable of motion and z’ is the position with displacement in a bunch.
Longitudinal distribution is Gaussian, .
  Frequency of electron in bunch potential depends on z.
  Electrons are pinched, thus the transverse profile of electrons depends on z.
Wake force is a function of z and z’, Wy(z,z’).
The wake force are calculated by a simulation, in which momentum kick at z is calculated for giving a deviation in a part of bunch (z’).

## Slide 23: Wake force induced by electron cloud
Wy(z,z’) depends on z and z’.
2D plot for Wy(z,z’) Wy(z-z’;z’) (sz unit)
: diagonal component of Wy(z,z)
for z’>z.

## Slide 24: How to treat this wake force in Vlasov solver
Momentum kick induced by electron cloud
Expression by longitudinal phase space variables
Azimuthal mode expansion

## Slide 25: Reduce to the Eigenvalue problem
Momentum kick for azimuthal mode
Discretizing for J, the transformation is expressed by matrix.

## Slide 26: Eigen mode analysis for W(z,z’)
One turn Matrix with the size (2xnJx(2lmax+1))2 is constructed by multiplication of syncho-beta and the wake transformations.
W(z,z’)
W(z-z’;-3)
Decoherence of Wy may raise the threshold.
Preliminary

## Slide 27: Electron cloud Wake model (multi-bunch)
Positron bunch starts to create electron cloud.
A bunch shift positive in stationary formed electron cloud.
  Electron cloud start to move positive.
  The bunch is kicked positive.
Electrons in cloud
Positron bunch train
Electron cloud
~ns

## Slide 28: Coupled bunch instability
High R/Q and Low Q=1
Lower R/Q and higher Q=10
Growth of CBI is similar as drift electron.
wR=lprec2/r2wc

## Slide 29: Summary
Electron cloud instability had been seen in early stage of SuperKEKB commissioning (Phase I, 2016).
The instability was cured by installation of weak solenoids at aluminum bellow section.
The density of instability threshold is almost consistent with simulation and theory.
In recent measurement (June, 2022), any beam size blow up was not observed.
Specific luminosity did not depend on the number of bunches in physics and machine experiments. No electron effects in luminosity.
Electron leakage from antechamber slot was estimated as several, 3-7 %.
TMCI analysis for W(z,z’) is available.

## Slide 30: Thank you for your attention

## Slide 31: Simulated threshold electron density (before/after permanent magnet installation)
Nb=600, ex=2nm, ey=15pm, sz =6mm, ns=0.019
Np,th (1010) | we/2p (GHz) | wesz/c | reth (Q=10) (1011m-3) | reth (Q=6) (1011m-3) | reth (Simu) (1011m-3) | spacing | Ip,th (mA)
1.6 | 61 | 7.7 | 1.91 | 2.45 | 3.2 | 2 (4ns) | 160
2.1 | 71 | 8.9 | 1.65 | 2.45 | 3.4 | 3 (6ns) | 200
2.7 | 80 | 10.1 | 1.47 | 2.45 | 3.6 | 4 (8ns) | 260
5.2 | 111 | 14.0 | 1.47 | 2.45 | 4.0 | 6 (12ns) | 500
2.1 | 71 | 8.9 | 1.65 | 2.45 | 3.4 | 2 (4ns) | 200
3.65 | 91 | 11.5 | 1.47 | 2.45 | 3.8 | 3 (6ns) | 350
6.25 | 122 | 15.3 | 1.47 | 2.45 | 4.2 | 4 (8ns) | >600
6

## Slide 32: チェンバー内の電子数シミュレーション
放射光が当たっている場所（アンテチェンバースロット最奥部)から電子が放出される。数を1単位とする。
Np=3.13x1010 (0.5mA/bunch), 6ns spacing, lp=1.74x1010 m-1.
Weak space charge limit, production rate 5x105m-1/bunch
No secondary, no reflected electrons.

## Slide 33: チェンバー内の電子数シミュレーション
放射光が当たっている場所（アンテチェンバースロット最奥部)から電子が放出される。数を1単位とする。
Np=3.13x1010 (0.5mA/bunch), 6ns spacing, lp=1.74x1010 m-1.
Production rate, 0.016 e-/m/e+, 5x108m-1/bunch.
No secondary, no reflected electrons.

## Slide 34: チェンバー内の電子数シミュレーション
放射光が当たっている場所（アンテチェンバースロット最奥部)から電子が放出される。数を1単位とする。
Np=3.13x1010 (0.5mA/bunch), 6ns spacing, lp=1.74x1010 m-1.
Production rate, 0.016 e-/m/e+, 5x108m-1/bunch.
Secondary SEY=1.2, reflected electrons 0.7.

## Slide 35: チェンバー内の電子数シミュレーション
放射光が当たっている場所（アンテチェンバースロット最奥部)から電子が放出される。数を1単位とする。
Np=6.26x1010 (1mA/bunch), 6ns spacing, lp=3.48x1010 m-1.
Production rate, 0.016 e-/m/e+, 10x108m-1/bunch.
No secondary, no reflected electrons.