## Slide 1
Technical concepts and potential solutions for the vacuum challenges of the LF tower
S. Hanke, K. Battes, C. Day, X. Luo GWDVac‘22 Workshop Elba 30 Sept 2022 stefan.hanke@kit.edu

## Slide 2: Gas sources for ET-LF
Next steps: consideration of all gas sources
Find influences and sensitivities
Knowledge where effort is mostly needed
First source – from long beam pipe
Second source – from upper part of tower
Third source – from adjacent tower with much higher flow
All combined flows have to fulfill pressure and adsorption requirements

## Slide 3: Second gas source
Pumping requirements
Design of shielding
Reduction of outgassing
Frost formation and
recovery
Resulting local
pressures
Minimisation of
conductance

## Slide 4: Gas flow from upper tower towards the cryogenic mirror
Tower pressure 10-8 mbar or higher? (non-bakeable)
For pressure requirement around mirror minimisation of resulting gas flow through opening
Two approaches available:
  drastic conductance reduction
  tower pumping with cryopumps

## Slide 5: Conductance minimisation – orifice solution
Assumptions
  Suspension diameter: 12 mm
  Orifice thickness: 0.5 mm
  Clearance: 6 mm
  Clearance: 1 mm or 0.5 mm
with positioning apparatus (x/y table) following the actual position of the suspension cable in real-time
Opening/clearance needed
Suspension (fibre + cabling + glue)
Issue of flow through gap or probably due to friction if there is direct contact

## Slide 6: Conductance minimisation – tube solution
Opening/clearance needed
Suspension (fibre + cabling + glue)
Tube
Assumptions
  Suspension diameter: 12 mm
  Clearance: 6 mm
  Tube length: 300 mm, 500 mm, 800 mm or 1000 mm
K. Jousten, Handbuch Vakuumtechnik (2018)

## Slide 7: Conductance minimisation – cone solution
Assumptions
  Suspension diameter: 12 mm
  Clearance at bottom: 6 mm
  Tube length: 300 mm, 500 mm, 800 mm or 1000 mm
  Clearance at top: 1 mm or 0.5 mm
with x/y table moving the smaller opening with the position of the suspension cable
Suspension (fibre + cabling + glue)
Conical tube
Connected with x/y table
at top very small clearance
Clearance
much larger since not movable

## Slide 8: Calculated gas flows from tower to mirror
 | Radius suspension | Radius opening | Radius opening 2 | Clearance | Orifice/tube length | Transmission surface | Transmission probability | Conductance | Gas flow to mirror
 | ri | ro | ro2 | dr | l | A | P | C | Q
 | (mm) |  |  |  |  | (m²) |  | (m³/s) | (Pa m³/s)
orifice | 6 | 12 |  | 6 | 0.5 | 3.39E-04 | 0.95 | 1.41E-01 | 1.41E-06
 | 6 | 7 |  | 1 | 0.5 | 4.08E-05 | 0.80 | 1.43E-02 | 1.43E-07
 | 6 | 6.5 |  | 0.5 | 0.5 | 1.96E-05 | 0.70 | 6.03E-03 | 6.03E-08
tube | 6 | 12 |  | 6 | 300 | 3.39E-04 | 0.055 | 8.19E-03 | 8.19E-08
 | 6 | 12 |  | 6 | 500 | 3.39E-04 | 0.035 | 5.21E-03 | 5.21E-08
 | 6 | 12 |  | 6 | 800 | 3.39E-04 | 0.025 | 3.72E-03 | 3.72E-08
 | 6 | 12 |  | 6 | 1000 | 3.39E-04 | 0.020 | 2.97E-03 | 2.97E-08
cone | 6 | 7 | 12 | 1 | 300 | 4.08E-05 | 0.067 | 1.21E-03 | 1.21E-08
 | 6 | 6.5 | 12 | 0.5 | 300 | 1.96E-05 | 0.070 | 6.01E-04 | 6.01E-09
 | 6 | 6.5 | 12 | 0.5 | 500 | 1.96E-05 | 0.043 | 3.70E-04 | 3.70E-09
 | 6 | 6.5 | 12 | 0.5 | 800 | 1.96E-05 | 0.028 | 2.37E-04 | 2.37E-09
 | 6 | 6.5 | 12 | 0.5 | 1000 | 1.96E-05 | 0.022 | 1.91E-04 | 1.91E-09

## Slide 9: Results
Best geometric solution of tower isolation: combination of long conical tube (1 m) with actively moving orifice of very small clearance (0.5 mm)  Gas flow from tower influence still is 1.9.10-9 Pa.m3/s
Extra pressure reduction by factor 10 in tower required (by additional means to reduce outgassing and/or increase pumping speed, most probably cryopumping)
Next gas source to be implemented

## Slide 10: Third gas source
Pumping requirements &
design of cryopumps
Design of shielding
Frost formation and
recovery
Resulting local
pressures

## Slide 11: Details of third gas source
Source is adjacent warm tower/optics
Separated by only 50 m from cryogenic mirror
Releasing high gas flow with 10-7 Pa m3/s for H2 and 10-6 Pa m3/s for water
Much higher flow as from other two sources
Cryopump needed to handle H2 flow
Low temperature cryopump seems indispensable (3.7 K or 10 K with sorbent)
Water trapping than anyway guaranteed

## Slide 12: Complete model established
Three sources implemented
First simulations ongoing
With time evolving detailness (cold H2 pumping marionette, cold shieldings pumping water, inhom. distribution on mirror)

## Slide 13: First results
H2 pressure around mirror (with all gas sources, H2 pumping left (50 m), water trapping right (30 m), conductance minimisation upwards) lower as needed
Caused by strong pumping from left cryopump
Can now be reduced in length stepwise (for H2 only, for water full 50 m)
Cold marionette (2 K) influences pressure / pumping (here half p)
For upper tower flow re-justification of minimisation effort

## Slide 14: Conclusions
Source 1: cryopump 80 K for water trapping sufficient
10km beam pipe conditions via low outgassing (instead of high pumping speed)
Source 2: conductance minimisation plus cryopumping in upper tower needed to reduce flow according needs
More precision will come with new model (e.g. more pumping by shields)
Source 3: cryopump for hydrogen needed, water trapped anyway
Largest flow  cryopump lengths and C‘s to be varied (Cryopump with 2 diff. Temp.?)
Total pressure around mirror below requirement, water ice build-up 700 d for 1 ML

## Slide 15: Conclusions
Warm pumping according low outgassing
80 K CP for water only < 30 m
Taylormade CP with 2 diff. T
CP for H2 (10 or 3.7 K – w/o sorbent), < 50 m
Water trapped along 50m with 80 K
Conductance minimisation plus cryopumping in upper tower
To which extend still open
Homogenous water ML after 700 d
Prevention of risky ice removal methods?