## Slide 1
Francesco Sgaramella, INFN – LNF on behalf of the SIDDHARTA-2 collaboration
SIDDHARTA-2 status report
62nd LNF Scientific Committee Meeting November 8, 2021

## Slide 2: SIDDHARTA-2 Collaboration
Silicon Drift Detectors for Hadronic Atom Research by Timing Application
LNF-INFN, Frascati, Italy
SMI-ÖAW, Vienna, Austria
Politecnico di Milano, Italy
IFIN –HH, Bucharest, Romania
TUM, Munich, Germany
RIKEN, Japan
Univ. Tokyo, Japan
Victoria Univ., Canada
Univ. Zagreb, Croatia
Univ. Jagiellonian Krakow, Poland
ELPH, Tohoku University
2

## Slide 3: Contents
Publications since last SC
61st SC recommendations
SIDDHARTINO run outcomes
Activities in – full SIDDHARTA-2 installation
HPGe Detector: test run for kaonic lead (kaon mass)
Future plans
3

## Slide 4: Publications since last SC
M. Miliucci et al., Silicon Drift Detectors system for high precision light kaonic atoms spectroscopy, Meas. Sci. Technol. 32 (2021).
M. Miliucci et al., Low energy kaon-nuclei interaction at DAΦNE:The SIDDHARTA-2 experiment, Il Nuovo Cimento 44 C (2021). Selected communication at 106° SIF Congress (best presentation: Marco Miliucci) for with publication on Rivista de il Nuovo Cimento.
C. Curceanu et al, Kaonic Atoms Measurements at DANE: SIDDHARTA-2 and Future Perspectives, Few Body Syst. 62, 4 (2021).
M. Miliucci et al., Silicon Drift Detectors spectroscopic response during the SIDDHARTA-2 Kaonic Helium run at the DAΦNE collider, arXiv:2111.01572, submitted to Condensed Matter.
M. Miliucci et al., HIGH PRECISION KAONIC ATOMS X-RAY SPECTROSCOPY AT THE DAФNE COLLIDER: THE SIDDHARTA-2 EXPERIMENT (submitted to RAP Conference Proceedings)
4

## Slide 5: Publications since last SC
A. Scordo et al, Efficiency measurements and simulations of a HAPG based Von Hamos spectrometer for large sources, J. Anal. At. Spectrom., 2021, JAAS, 2021, 36, 2485 – 2491, doi: 10.1039/D1JA00214G.
A. Scordo et al, VOXES: a new HAPG mosaic crystal based Von Hamos spectrometer for millimetric sources, RAP conference proceedings, VOL. 6, PP. 1–5, 2021.
M. Miliucci et al., Silicon Drift Detectors Technology for High Precision Light Kaonic Atoms Spectroscopic Measurements at the DAΦNE Collider, in print on AIP-CP.
V. De Leo et al, Reflection efficiency and spectra resolutions ray-tracing simulations for the VOXES HAPG crystal based Von Hamos spectrometer, arXiv:2111.01572, submitted to Condensed Matter.
Kaonic Helium measure: shift and width, in preparation.
Yield kaonic helium in gas, in preparation.
5

## Slide 6: 61st LNF Scientific Committee Meeting
Recommendations SIDDHARTA
“Controlling the background is a critical aspect of this experiment and the committee would like to see the details of the interventions planned by SIDDHARTA/DAFNE for moving towards the aimed -for background level. The committee would appreciate getting this written feedback by the end of June.”
This was one of our main goals in the SIDDHARTINO run, up to its end (18 July) – report sent by LNF Director Report on the Dafne-Siddharta operation May-July 2021 together with a competitive measurement of kaonic helium
6

## Slide 7: Project timeline – since last SciCom
SIDDHARTINO optimization run
2021, June
SIDDHARTINO K-4He run
2021, 24 June – 18 July
Start SIDDHARTA-2 installation: mechanics
2021, August
62nd LNF SciCom 2021, November
SIDDHARTA-2 Installation and tests 2021, September -October
61st LNF SciCom
2021, May
Software and hardware optimization
back. reduction
Different combinations of the degrader thickness and different gas density
Analysis of the SIDDHARTINO data.
Start SIDDHARTA-2 Installation
Installation of SDD, veto and electronics. Update of the DAQ….
Ready for run

## Slide 8: SIDDHARTINO run
VETO-1
8 SDDs arrays
TARGET CELL
K-TRIGGER
LUMINOMETER
Pb LATERAL
SHIELD
He cooling line
VETO-2
Schematic representation of SIDDHARTINO setup
1 Bus
8

## Slide 9: SIDDHARTINO setup (1/6 SDDs)
Phase 1 with SIDDHARTINO:
during the commissioning of DAΦNE:
optimization with the SIDDHARTINO setup
for the K-4He measurement
(with 8 SDD arrays)

## Slide 10: Back. reduction: reinforced shielding around the setup
Lead foil near the beam pipe
Lead bricks around the vacuum chamber
10

## Slide 11: SIDDHARTINO - xray/cm2/pb-1
15 xray/cm2/pb-1
7 xray/cm2/pb-1
Background lowered by a factor 2
reinforced shielding around the setup

## Slide 12: Luminosity measurement to monitor also background
Luminosity detector:
- SIDDHARTA-2 luminometer used for back: kaons/MIPS
- luminosity delivery
Back to plastic scintillators in coincidence with RF/4 signal

## Slide 13: Background levels monitor
Background levels were monitored online by a counter based on Kaon/Mip rate and a second based on Kaon/SDD rate.
Shared with the staff to optimize the background
13

## Slide 14
Optimization of xray/cm2/pb-1 very visible!
6.2 xray/cm2/pb-1
Factor nearly 3
OK for SIDDHARTA-2
15 xray/cm2/pb-1
SIDDHARTINO - xray/cm2/pb-1

## Slide 15: SIDDHARTINO data - Integrated Luminosity
Total integrated luminosity: 54 pb-1
Optimization run: 24 pb-1
Trigger, DAQ, SDD optimization
Kaonic 4He run: 30 pb-1
Degrader optimization, low and high 4He density measure
Kaon monitor and Luminometer measure at the end of SIDDHARTINO run

## Slide 16: SIDDHARTINO - Integrated Luminosity
Total integrated luminosity
luminosity good for physics
86% total efficiency
Pc inefficiency
Pc inefficiency
K-4He run
Optimization run
86% total efficiency
>95% for K4He good runs

## Slide 17: Trigger time window optimization
SIDDHARTINO – Optimization Run
Kaon monitor up
Kaon monitor down
Kaons
MIPS
17

## Slide 18: SDD calibration and energy response
SIDDHARTINO – Optimization Run
SDD calibration run
SDD Stability

## Slide 19: Trigger rejection factor
Sum of all SDDs after individual calibration
Sum of all SDDs after trigger cut
Triggered rejection factor
Events no trigger (5-10 keV) = 11256611
Events with trigger (5-10 keV) = 52
19

## Slide 20: Degrader Optimization
Degrader thickness optimization is fundamental to maximize the number of stopped kaons in the target
Kaon monitor up
Kaon monitor down
the degrader is composed of mylar foil (micron) and is placed below the kaon monitor up
20

## Slide 21: Degrader-1: middle thickness
Luminosity integrated = 6.758 pb-1
Degrader
Boost side
Anti Boost side
SIDDHARTINO DEGRADER #1 ( )
1.67 K-4He xrays/cm2/pb-1
h = 50 Mylar h = 75 Mylar
h = 125 Mylar
21
4 (6.4 keV)

## Slide 22: Degrader-2: middle thickness
Luminosity integrated = 4.577 pb-1
Degrader
Boost side
Anti Boost side
SIDDHARTINO DEGRADER #2 ( )
h = 50 Mylar h = 75 Mylar
1.64 K-4He xrays/cm2/pb-1
22
4 (6.4 keV)

## Slide 23: Degrader-3: middle thickness
Luminosity integrated = 5.219 pb-1
Degrader
Boost side
Anti Boost side
SIDDHARTINO DEGRADER #3 ( )
1.3 K-4He xrays/cm2/pb-1
h = 50 Mylar h = 75 Mylar
23
4 (6.4 keV)

## Slide 24: Degrader-4: middle thickness
Luminosity integrated = 4.753 pb-1
Degrader
Boost side
Anti Boost side
SIDDHARTINO DEGRADER #4 ( )
h = 200 um Mylar
h = 50 Mylar h = 75 Mylar
h = 125 Mylar
h = 200 Mylar
0.4 K-4He xrays/cm2/pb-1
24
4 (6.4 keV)

## Slide 25: Degrader Curve
Deg-1
Deg-2
Deg-3
Deg-4
25

## Slide 26: K-4He low density run: 0.75% liquid helium density -> yields at lowest measured density analyses undergoing -> paper
SIDDHARTINO - K-4He run
26
4
Luminosity integrated = 9.496 pb-1
0.7 K-4He xrays/cm2/pb-1
preliminary

## Slide 27: K-4He shift and width: the most precise measurement in gas!
SIDDHARTINO - K-4He run
Luminosity integrated = 26.05 pb-1
preliminary
27
Paper in preparation
KHe32
KHe42
KHe52

## Slide 28: Report on main activities in towards SIDDHARTA-2
SDD detectors installation
Veto-2 installation
Front-end electronic installation
Veto-1 installation
28

## Slide 29: SDD installation
SDD installed around the target
calibration target
Kapton wall

## Slide 30: SDD installation
Wrap for thermal isolation
30

## Slide 31: Veto-2 installation
Working principle of veto-2 system
31

## Slide 32: Veto-2 installation
Veto-2 single unit
Veto-2 Calibration spectrum
The installation of veto 2 has been completed and the correct operation of each unit has been verified
Each veto-2 unit is equipped with an LED that will allow to calibrate and verify the correct functioning of the system with and without beams
32

## Slide 33: Front-end electronics installation
SDD Front-end connector
SDD power supply connector
Veto2 connectors
SIDDHARTA-2 setup before the installation of electronic components
33

## Slide 34: Front-end electronics installation
SDD Front-end electronics
Electronic Box
Veto-2 Front-end electronics
34

## Slide 35: Front-end electronics installation
Veto2 electronics
SDD power supply
SDD Front-end electronics
35

## Slide 36: SDD calibration spectrum acquired with SIDDHARTA-2
TiK
CuK
BiL
TiK
CuK
BiL
Preliminary calibration
29/10/2021
36

## Slide 37: Veto-1 system installation
Drawing of the veto-1 elements placed around the vacuum
chamber
Working principle of veto-1 system
M. Bazzi et al, 2013 JINST 8 T11003
37
Veto-1: single unit
Veto1: 12 single units

## Slide 38: Veto-1 system installation
Veto-1 system installed around the vacuum chamber
38

## Slide 39
SIDDHARTA-2 setup
Ready for Run
39

## Slide 40: HPGe - feasibility test for the kaonic lead measurement
support structure
Lead shielding
HPGe detector available, Funded by University of Zagreb Croatian Science Foundation project 8570
The HPGe has been transported to LNF from Zagreb
Completed the installation of the support structure and the lead shielding
40

## Slide 41: HPGe - feasibility test for the kaonic lead measurement
Test with 133Ba performed at LNF
41

## Slide 42: HPGe - feasibility test for the kaonic lead measure
Test: 133Ba resolution 1.3 kev at 300 keV
Resolution about 1.3 keV 303 keV
Test with 133Ba performed at LNF
42

## Slide 43: HPGe - feasibility test for the kaonic lead measurement
schematic representation of the apparatus, that will be installed in the hall
HPGe detector ready to be install in the hall
43

## Slide 44: Project timeline – future
Installation of SIDDHARTA-2 setup
2021, September - October
Start Run SIDDHARTA-2 and HPGe parasitic test 2021, November
Continue the run SIDDHARTA-2
Kd
HPGe
2022, from January through all 2022
shutdown for winter holiday 2021, December
𝐃𝐀𝚽𝐍𝐄 shutdown for winter holiday 2021, December
Installation of SIDDHARTA-2 setup
2021, September - October
Start Run SIDDHARTA-2 and HPGe parasitic test 2021, November
Continue the run SIDDHARTA-2
Kd
HPGe
2022, from January through all 2022
SIDDHARTA-2 Kd run: run 1 (300 pb-1) run 2 (500 pb-1) with optimized components
Start of the data taking with 4He to check run condition with respect to SIDDHARTINO run
44

## Slide 45
SIDDHARTA-2 K-d measurement
achievable precision
Kaonic deuterium run in (all) 2022
Monte Carlo for an integrated luminosity
of 800 pb-1
to perform the first measurement of the strong interaction induced energy shift and width of the kaonic deuterium ground state
(similar precision as K-p) !
Significant impact in the theory of strong interaction with strangeness

## Slide 46
SIDDHARTA-2 kaonic deuterium at
shift [eV]
width [eV]

## Slide 47
We anticipate the request for an extension of run with same setup
with solid targets
https://www.lnf.infn.it/esperimenti/siddharta/Kaonic-atoms-post-Kd-SIDDHARTA_final.pdf

## Slide 48
Li
Be
B
Use of present SDDs: Solid target system for light kaonic atoms: e.g. Li – Be - B financed by INFN Nuclear physics (gr 3) as first step towards Future (see Curceanu talk)

## Slide 49
kaonic Li-transitions
3-2 ~15 keV
4-2 ~21 keV
5-2 ~23 keV
4-3 ~ 5 keV
5-3 ~ 8 keV
6-3 ~ 9 keV
5-4 ~2.5 keV
6-4 ~ 4 keV
The energy spectra of light kaonic atom transitions for Li, Be and B targets below 17 keV can achieve a precision below 2-3 eV, for an integrated luminosity of about 150 pb-1 (including calibrations and test).
We anticipate the request of this additional run post-SIDDHARTA-2
Solid target system for light kaonic atoms: e.g. Li – Be – B
KLi
57Co

## Slide 50: Conclusions
Despite the difficult period, we have been able to follow our plan and Sci Com recom. and perform our activities along the schedule @SC61
In particular we: understood and (together with ) succeed to reduce backg such as to start SIDDHARTA-2 run; performed the most precise KHe measurement in gas and the measurement of yields at lowest density
About 10 articles were published – important scientific outcome, 2 are in preparation
We are ready and very motivated to start the SIDDHARTA-2 planned first Kd measurement
We put forward proposal for solid targets measurements with SIDDHARTA-2 setup for 100-150 pb-1 after Kd run

## Slide 51
Luca de Paolis Ph.D. in physics eccellente qualità con lode September 2021

## Slide 52
Thank you!
Part of the SIDDHARTA-2 collaboration

## Slide 53
Special thanks to the accelerator, research and technical divisions, and in particular to the DANE staff and to the LNF Director

## Slide 55: SPARE

## Slide 58
Laboratory activity
M. Iliescu et al, IEEE VOL. 70, 2021. DOI 10.1109/TIM.2021.3068149
MIPs
X-ray
Discovered a correlation between rise time and drift time for the x-ray
New technique to distinguish x-rays from MIP
we are studying the feasibility of applying this technique to the SIDDHARTA-2 experiment

## Slide 59
Laboratory activity