## Slide 1: Silicon Trackers RD_FCC annual meeting 15 December 2021
Attilio Andreazza, Bianca Raciti, Fabrizio Sabatini - Università di Milano and INFN
Filippo Bosi, Fabrizio Palla – INFN Pisa

## Slide 2: The IDEA concept
Central tracking device:
  light Drift CHamber
Silicon detectors for precision measurements
  vertex detector (see Manuel's presentation)
  silicon internal tracker
  silicon wrapper
Thin solenoid with 2T field (according to MDI limits)
Dual readout calorimeter
  supplemented by a pre-shower detector
Muon chambers in the solenoid return yoke

## Slide 3: Silicon Tracker
Strategy is to workout solutions that can fit in in different detector layouts:
  Suitable for FCCee as well as CEPC main detector layouts
  ATLASPIX3 Depleted Monolithic Active Pixel Sensor
  Development of multi-chip modules
  Mechanical structure for long stave layouts
  Designing integration of a full-size system
International collaborations:
  CEPC:
    R&D projects for the Silicon Tracker (see Harald's presentation)
  AIDAInnova:
    WP5: Depleted Monolithic Active Pixel Sensors
    WP10: Advanced Mechanics for Tracking and Vertex detectors
China, Germany, INFN, UK

## Slide 4: ATLASPIX3
Monolithic CMOS
  widespread process allows to produce large areas, fast and cheap
  no hybridization (bump-bonding) needed
  single detection layer, can be thinned keeping high signal efficiency and low noise rate
ATLASPIX3 features
  pixel size 50×150 μm2 (25×165 μm2 feasible)
  up to 1.28 Gbps downlink
  reticle size 20×21 mm2
  TSI 180 nm process on 200 Ωcm substrate
  132 columns of 372 pixels
  digital part of the matrix located on periphery
  both triggerless and triggered readout possible:
    two End of Column buffers
    372 hit buffers for triggerless readout
    80 trigger buffers for triggered readout

## Slide 5: ATLASPIX3
Threshold and noise distributions
  Estimated via s-curves fitting
Threshold uniformity after tuning
  Test measurements with 241Am
Increase of the depletion volume with HV bias
  Amplitude measurements with 90Sr
  Solid shift of the average ToT

## Slide 6: CEPC Baseline layout

## Slide 7: CEPC Baseline layout
INFN Focus

## Slide 8: Multi Chip modules

## Slide 9: Connections: LVDS routing
Mechanical compatibility with ATLAS quad modules (Molex 5025983393)
Differential control signals distribution for SyncRst, Cmd, CkRef, ExtTrigger
Individual differential output for each chip
CMOS level configurations added to data connector

## Slide 10: TDR measurements
Cumulative measure for chip DataOut: impedance
Traces Length = 26.5 mm
Traces Length = 134 mm

## Slide 11: Eye diagram: clock and DataOut
Eye-Diagram 400 mV:
The evaluation of eye-diagram for CkExt is made including Molex cable
For DataOut only the flex is evaluated
DataOut @ 100 Mbit/s
CkExt @ 100 Mbit/s
DataOut @ 500 Mbit/s
CkExt @ 500 Mbit/s
160 mV
380 mV
450 mV
160 mV
180 mV
350 mV
130 mV
190 mV
380 mV

## Slide 12: Assembly procedure
Shown with glass squares: same procedure also used for real module assembly
Gap between chip of 100 um ± 50 um has been achieved

## Slide 13: Testing setup
GECCO readout system developped by KIT
Adapter card designed at the Univesity of Edinburgh
Standard Molex data cable
Custom cable for the power connection
Nexys Video FPGA

## Slide 14: Module characterization
|I leak| < 400 nA for HV > -60 V. Breakdown voltage = -65 V
Current consumption power-up / configured = 1.65 A / 1.33 A for VDD = 1.9 V
Successful fitting of pixel thresholds
Occasional loss of configuration during long scans
Chip 3 can be configured but readout is not working (no wafer probing)

## Slide 15: Lab tests with X-ray tube
Amptek Mini-X2 with silver anode, max energy 50 kV
Linear readout rate from 10 uA – 160 uA at 25 kV without low-energy filters
  5 minutes source runs without biasing voltage
  Missing threshold tuning, set average DAC value
  Rate range: ~1.5 x 104 hits/s to ~ 3.4 x 104 hits/s
  Components on the PCB can be easily identified

## Slide 16: ATLASPIX3 Modules: planning
First 2 multi-chip modules with ATLASPix3 has been operated successfully
Other 7 are being assembled (wire bonding in progress)
Set of ATLASPIX3.1 wafers procured:
  fixes on the main VDDA/VDDD regulators
  on-chip command-clock-recovery
  received 3× 48 chips after dicing and thinning at OPTIM (F)
Designing of a 2nd generation flex hybrid exploiting ATLASPIX3.1 fixes:
  Only one LV supply (currently 3 are needed), exploiting the internal regulator fixes
  Input lines for command and clock (dropping trigger and reset signals)
  Drop of SPI and configuration lines used for debugging module behaviour
  A/C coupling on LVDS lines for compatibility with serial powering
  Use some free space for temperature sensors
Target is building few mini-staves of an outer tracker for FCCee/CepC/ILC

## Slide 17: Long stave mechanics

## Slide 18: Layout overview
Design of the support structure for long stave of Layer 2 SIT
  Possible to implement also for Layer 1 SIT
Inspired to ALICE project, but different specifications
  Easier process (instead of winding process) implemented by WaterJet cut process on carbon fiber laminated (50 µm precision)
  Gluing mask for realization of the 3D truss structure
  Goal of the mechanical structure: max radiation length 0.3% X0
1330 mm

## Slide 19
Laminated plate Carbon Fiber: M46J
N.4 unidirectional layer 0-90-90-0
Thickness: 0.5 mm
Profile of the single plane truss structures
Maximum dimensions of the cutting surface under the Waterjet machine:
580x465 mm2

## Slide 20: Long stave layout

## Slide 21: Gluing truss mask for half stave
Truss Structure
Lateral Positioning Brake
Lateral Precision Support
Precision Pin
Upper Positioning Brake
Precision Pin
Upper Mask
Lateral Mask
665

## Slide 22: Gluing truss mask for long stave
Lateral Precision Support
Upper Mask
Long Truss Structure
Precision Pin
1330
Lateral Mask
Lateral Mask
Upper positioner CF stiffness plate
Stiffness CF Plate
Lateral positioner CF stiffness plate
Lateral positioner CF stiffness plate
Upper middle support
Lateral middle support
Upper middle support
Lateral middle support

## Slide 23: Cold plate

## Slide 24: Populated cold plate

## Slide 25: Complete long stave

## Slide 26: Stave Mechanics: planning
Done in 2021:
  Designed the long stave parts
  Finished to design the long stave gluing mask
  Ordered the carbon fiber material
Next steps in 2022:
  Manufacturing of the Gluing Mask and the end part of the 3D truss and cold plate in peek material
  Order WaterJet cutting operation
  Assembly the Long Stave structure
  Assembly of the cold plate
  Measure the sagitta of the long stave and thermo-mechanical properties of the cold plate in Pisa lab

## Slide 27: services integration

## Slide 28: Si tracker: system considerations
Complete system consists of 900'000 cm2 area / 4 cm2 chip = 225k chips (56k quad-modules)
  aggregation of several modules for data and services distribution is essential
  inner tracker will be 5--10% of this
Data rate constrained by the inner tracker
  average rate 10-4 - 10-3 particles cm-2 event-1 at Z peak
  assuming 2 hits/particle, 96 bits/hit for ATLASPIX3
  640 Mbps link/module (assuming local module aggregation) provides ample operational margin
  16 modules can be arranged into 10 Gbps fast links: 3.5k links
    can also assume 100 Gbps links will be available: 350 links
DAQ architecture
  triggerless readout will fit the data transmission budget but requires off-chip re-ordering of data
  triggered readout will be simpler and would also reduce the bandwidth occupancy
Power consumption
  ATLASPIX3 power consumption 150 mW/cm2
  600 mW/chip → 2.4 W/module → total FE power 130 kW
  additional power for on detector aggregation and de-randomizations ~2W/link

## Slide 29: Stave Electrical Bus
Power IN/OUT
Data IN/OUT
HV
Distribute power and data signals along the stave
Assume minimal I/O connection on chip:
  All biases generated internally by shunt-LDO regulators
  chip-to-chip data transmissions: local data aggregation on module
  clock data recovery
Requirements:
  LVDS command input
  LVDS data output at 640 Mbps on ~700 mm (half)stave length
  Serial powering assuming 0.5 A/chip, 2 A/module
  HV distributed in parallel to all modules
Integrated signal and power bus:
  Power distribution and return layers
  Signal lines on top and bottom layers
  Interconnection by soldering or wire bonding
Alternative under study:
  separate power cables + twinax for signal (the LHC way)

## Slide 30
Signals:
LVDS trace width = 200 µm
resistance for a length of 70 cm ̴ 5 Ω
Stack-up minimizes cable thickness, but bottom signal lines face module hybrid circuit
Power:
Plane width = 14 mm
resistance for 70 cm ̴ 0.08 Ω
current I ̴2 A (@ 20 + 3 ºC)
}
}
Total thickness 372 µm
Total copper 36 µm
Modules 0-7
Modules 8-F
Serial power bus

## Slide 31: Conclusions
INFN work on RD_FCC SiTracker progressing well within the CEPC Framework
  sharing of parts and ATLASPIX3 testing
  parallel development of structures for the different layers of the tracker
First multi-chip module(s) assembled
  Build a 2nd generation based on ATLASPIX3.1 in 2022
Developed the full design of a long stave for the outermost layers of the SiTracker
  Realization of prototypes and thermo-mechanical characterization in 2022

## Slide 32: backup

## Slide 33: Physics requirements
Impact parameter resolution
Particle identification capability (p/K/p)
Momentum resolution
b/c/g/t tagging
Flavour physics
Recoil mass determination
M. Selvaggi on Tuesday
J. Eysermans on Tuesday
Example:

## Slide 34: IDEA: the vertex region
High precision impact parameter reconstruction with low mass vertex detector
  at least 20 mm granularity
  thickness < 0.3% of radiation length
  low power <20 mW/cm2 to minimize services
Supplemented by coarser/faster silicon detectors in front of the drift chamber
Depleted Monolithic Active Pixels sensors
  not necessarily the same technologies for both: different requirements
  present technologies are very promising
  R&D on different approaches (ARCADIA, ATLASPIX3)

## Slide 35: Si Wrapper
Solenoid
DCH
Si Wrapper
Precision silicon layer around the central tracker
Functionalities:
  momentum resolution
  extend tracking coverage in the forward/backward region by providing an additional point to particle with few measurements in the drift chamber
  precise and stable ruler for acceptance definition
Covered area ~90 m2
Suitable technologies:
  microstrips (2 layers)
  double sided microstrip
  DMAPS → single layer, high resolution on both coordinates, maybe simpler integration

## Slide 36: Flex Stackup and power integrity
In this initial version emphasis is on signal integrity, rather than minimizing material:
  4 layers
  External layers copper: 43 um
  Inner layers copper: 18 um
  Total thickness: 565 um
  Via diameter: 300 um
  Via hole size: 150 um
100 ohm impedance match on differential lines on top and inner layers
Simulation results for VDD (ref. GND)
  Max Voltage Drop: 2.7 mV
  Max Current Density: 13.9 A/mm2
  Max Via Current: 137.0 mA
Power connector BM25: VDD, GND, HV, VGATE, VLVDS
Power Integrity simulation parameters:
  Voltage source: 1.8 V
  Current sink: 500 mA per chip
  Max voltage drop: 3 mV
  Max current density: 15 A/mm2