## Slide 1
Luigi Celona
Future beams at LNS
Nuclear Physics Mid Term Plan in Italy
LNS – Session
Catania, April 4th-5th 2022
Paolo Russotto
INFN-LNS, Catania, Italy
INFN-LNS, Catania, Italy

## Slide 2
Luigi Celona
LNS LAYOUT AFTER THE UPGRADING

## Slide 3
Tandem + Cyclotron beam time
About 430 BTU per year delivered by each accelerator
(excluding beam time preparation)
35 - 40 experiments per year, including the proton therapy sessions
Beam time lost for failures:
Tandem: < 2%
Cyclotron: < 4%
Luigi Celona
Tandem & Cyclotron Beam Time

## Slide 4
1H, 2H
6Li, 7Li
9Be, 10Be
10B, 11B
12C, 13C
14N
16O, 17O, 18O
19F
58Ni, 60Ni
63Cu, 65Cu
70Ge
79Br
93Nb
116Sn, 120Sn
127I
197Au
Tandem Beam Menu
Maximum High Voltage ≈ 13.5MV
Pelletron charging system
HV stability ≈ 10-4
Noble gases beam development in progress
Actions: Replacement of obsolete parts (electronics, power, automation) mandatory to permit future safe and reliable operations
23Na
24Mg, 25Mg
27Al
28Si, 29Si
32S, 34S
35Cl, 37Cl
40Ca
Luigi Celona
Tandem Beams

## Slide 5
Long half-life isotopes in batch-mode
@ 47 MeV
I≈10 nA for a few days
Contamination of 10B≈ 0.1%
10Be (T1/2 = 1.39×106 y) Tandem beam has been produced in batch-mode, in collaboration with PSI (Zurich)
10B≈0.1%
10Be
DE(ch)
E (ch)
Next possible beam: 26Al (T1/2=7.17×105 y)
Batch-mode beam development is foreseen for the next years.
Luigi Celona
Batch mode operation with Tandem

## Slide 6
Superconducting Cyclotron
Operating 1994 - 2020
EMAX ~ 80 AMeV for lighter ions
EMAX ~ 25 AMeV for heavier ions (i.e. Au36+)
Kbend =800 - Kfoc=200
Pole radius: 90 cm – Mag. field: 2.2 - 4.8 T
RF range: 15-48 MHz
Since 1999
Two ECR ion sources: CAESAR and SERSE
June 2020 last experiment, disassembly for the upgrading started in November.
Luigi Celona
LNS K800 Superconducting Cyclotron

## Slide 7
Matching Point at Achromatic Waist
New Extraction line
Cyclotron Upgrade
Instantaneous change of the magnetic rigidity, when the charge state of the ion is suddenly increased crossing a thin carbon foil.
Beam extraction by stripping
Efficiency >99%
Luigi Celona
Extraction by stripping

## Slide 8
Cyclotron Beams Menu
AX E (AMeV)
H2+ 62,80
H3+ 30,35,45
2D+ 35,62,80
4He 25,62,80
He-H 10, 21
9Be 45
11B 55
12C 23,62,80
13C 45,55
14N 62,80
16O 21,25,55,62,80
18O 15,55
19F 35,40,50
20Ne 20,40,45,62
24Mg 50
27Al 40
36Ar 16,38
40Ar 15,20,40
Chart: Mass (a.m.u.)
| 2 | 20 | 58.6 | 120 | 117.3 | 240
 | 80 | 78.4 | 59.2 | 41.6 | 42 | 18
AX E (AMeV)
40Ca 10,25,40,45
42,48Ca 10,45
58Ni 16,23,25,30,35,40,45
62,64Ni 25,35
68,70Zn 40
74Ge 40
78,86Kr 10
84Kr 10,15,20,25
93Nb 15,17,23,30,38
107Ag 40
112Sn 15.5,35,43.5
116Sn 23,30,38
124Sn 15,25,30,35
129Xe 20,21,23,35
197Au 10,15,20,21,23
208Pb 10
Luigi Celona
Cyclotron beams

## Slide 9
Ion | Energy | Isource | Iextr | Iextr | Pextr
 | MeV/u | emA | emA | pps | watt
12C | 30 | 200 | 45 | 4.71013 | 2700
12C | 45 | 400 | 90 | 9.41013 | 8100
12C | 60 | 400 | 90 | 9.41013 | 10800
18O | 20 | 400 | 80 | 6.21013 | 3600
18O | 29 | 400 | 80 | 6.21013 | 5220
18O | 45 | 400 | 80 | 6.21013 | 8100
18O | 60 | 400 | 80 | 6.21013 | 10800
18O | 70 | 200 | 34 | 2.71013 | 5400
20Ne | 28 | 400 | 85 | 5.31013 | 4800
20Ne | 70 | 400 | 85 | 5.31013 | 10280
40Ar | 60 | 400 | 77 | 2.71013 | 10280
Cyclotron Upgrade: expected currents by stripping
Beam extraction by stripping: Efficiency >99%
Luigi Celona
High intensity beams with cyclotron through extraction by stripping

## Slide 10
Our experience: FRIBs
Paolo Russotto
Text
At INFN-LNS RIBs were produced, since 2001, using the FRIBs (in Flight Radioactive Ion Beams at LNS) facility through the In-Flight fragmentation method (primary beam accelerated by CS + 9Be target), employing a maximum beam power of 100 W
Two 45° dipoles of the beam line for the fragments selection
production target
Tagging system in the CHIMERA beam line
Lombardo I. et al., Nucl. Phys. B, 215 (2011) 272
RIBs produced: from 6He to 68Ni with max intensity of ≈ 105 pps

## Slide 11
Our experience: FRIBS
Paolo Russotto
Text
ΔE (MeV)
ToF (ns)
18O(55 AMeV) + 9Be(1500 um)
Bρ=2.78Tm
A/Z=3
6He
9Li
12Be
15B
18C
A/Z=2.66
16C
8Li
Di-proton decay from 18Ne excited states
G. Raciti et al., PRL 100 192503 (2008)
N.S. Martorana et al, PLB 2018 in press
Isoscalar excitation of Pygmy resonance in 68Ni
68Ni coinc.
background
After background subtraction
Exotic nuclei cluster structure: 10Be->6He+4He
D. dell’Aquila et al., PRC 93, 024601 (2015)

## Slide 12
Our experience: FRIBs
Paolo Russotto
Text
Two 45° dipoles of the beam line for the fragments selection
production target
Al (1000 µm) degrader
In specific cases, an aluminum degrader, placed between the two 45° dipoles of the fragment separator, was used to obtain fragmentation beams with high purity of a particular isotope
DSSSD 16x 16 strips
+ plastic scintillators
13C (50 enA) + 9Be @ 55 AMeV
RIBs with a 11Be purity of 95 %

## Slide 13
Our future: FraISe
Paolo Russotto
Text
Main features:
4 dipoles, 6 quadrupoles and 2 sextupoles, arranged in two symmetric branches, to ensure optimal achromatic condition
maximum magnetic rigidity 3.2 Tm
momentum acceptance ±1.2%
solid angle acceptance ±2.5 msr
5 m dispersion at symmetry plane, energy resolving power
thanks to high energy dispersion value at the symmetry plane, it will allow to deliver stable beams with an energy spread of 0.1 %
Degrader and/or selection slits
Rotating Target
CLIM (GANIL)

## Slide 14
Our future: FraISe
Paolo Russotto
First order envelope calculated in case of x-x' maximum acceptance
contact A.D. Russo for further info

## Slide 15
Our future: FraISe
Paolo Russotto
Text
14
Also, a revision and improvement of the diagnostics and tagging systems are needed to measure features of the RIBs  the systems will be versatile and useful for FRAISE and other facilities
Inside a Fragment Separator:
Need of a point-to-point measurement of cocktail intensity, relative composition, energy distribution, 2D profile, angular distribution during optimization
Monitoring of beam properties, start time for event-by-event ToF/energy measurement during data taking
In the final set-up point:
Need of event-by-event tagging of cocktail beam and trajectory measurement
SiC is the new emerging technology for the future (low consumption, radiation-hard) sensing and electronic devices fabrication
In the last years R&D on these materials and technologies was carried out @ INFN Tudisco S. et al., Sensors 2018, 18, 2289
A feasibility study, in synergy with Research Division, has already started, performing simulations and preliminary tests in order to evaluate the possibility of using SiC detectors
What we want to develop:
array of detectors based on SiC technology, where the single detection unity pad will be 5 × 5 mm2 and 100 µm thick fully depleted SiC rad-hard multi-pad sensors: up to 107 pps over  72 channels with Δt ≈ 200 ps (0.1% precision on energy for 20 m base-of-flight) with 200 µm inter-pad dead zone, 10% dead area
5 mm
60 mm
30 mm
Side View

## Slide 16
Our future: FraISe
Paolo Russotto
Text
Some refs:
P. Russotto et al., J. Physics: Conf. Ser., 1014 (2018) 012016;
N.S. Martorana, Nuovo Cimento 44 C (2021) 1 and LNS report 2019-2020;
F. Risitano, Master thesis Univ. Of Messina 2020 and LNS report 2020;
A.D. Russo et al., Nucl. Instrum. Methods B, 463 (2020) 418.
F. Risitano, in press on Nuovo Cimento C
N.S. Martorana, Proceedings of IWM-EC 2021, to be published in Nuovo Cimento C
web: https://potlns.lns.infn.it/it/motivazioni-scientifiche/fraise.html
Studied cases
In the following:
-Al 100 mm homogenous degrader on symmetry plane
-100 mm SiC tagging detector at the exit

## Slide 17
Our future: FraISe
Paolo Russotto
Text
12C6+ @ 60 AMeV 2 kW on ≈2500 um 9Be target
 |  |  |  | 17Ne | 18Ne | 19Ne | 20Ne | 21Ne | 22Ne | 23Ne | 24Ne | 25Ne | 26Ne | 27Ne | 28Ne
 |  |  |  |  | 17F | 18F | 19F | 20F | 21F | 22F | 23F | 24F | 25F | 26F | 27F
 |  | 13O | 14O | 15O | 16O | 17O | 18O | 19O | 20O | 21O | 22O | 23O | 24O |  | 
 |  | 12N | 13N | 14N | 15N | 16N | 17N | 18N | 19N | 20N | 21N | 22N | 23N |  | 
9C 4.0E5 45 | 10C 1.2E7 43 | 11C 2.2E8 44 | 12C | 13C | 14C | 15C | 16C | 17C | 18C | 19C | 20C |  | 22C |  | 
8B 3.1E6 42 |  | 10B | 11B | 12B | 13B | 14B | 15B |  | 17B |  | 19B |  |  |  | 
7Be 1.5E7 43 |  | 9Be | 10Be 1.6E7 50 | 11Be | 12Be |  | 14Be |  |  |  |  |  |  |  | 
6Li | 7Li | 8Li 4.2E6 50 | 9Li 8.9E5 51 |  | 11Li |  |  |  |  |  |  |  |  |  | 
 | 6He 2.1E6 51 |  | 8He 1.8E4 51 |  |  |  |  |  |  |  |  |  |  |  | 
Expected yield (pps)
Energy after the exit slit (AMeV)

## Slide 18
Our future: FraISe
Paolo Russotto
Text
12C6+ @ 60 AMeV – 18O8+ @ 70 AMeV 2 kW on ≈ 2500-1500 um 9Be target
 |  |  |  | 17Ne | 18Ne | 19Ne | 20Ne | 21Ne | 22Ne | 23Ne | 24Ne | 25Ne | 26Ne | 27Ne | 28Ne
 |  |  |  |  | 17F | 18F | 19F | 20F | 21F | 22F | 23F | 24F | 25F | 26F | 27F
 |  | 13O 7.2E4 54 | 14O 1.4E6 40 | 15O 2.8E7 54 | 16O | 17O | 18O | 19O 4.4E6 50 | 20O | 21O | 22O | 23O | 24O |  | 
 |  | 12N 1.2E6 49 | 13N 2.3E7 50 | 14N | 15N | 16N 6.9E8 53 | 17N 3.2E8 57 | 18N | 19N | 20N | 21N | 22N | 23N |  | 
9C 4.0E5 45 | 10C 1.1E7 43 | 11C 2.2E8 44 | 12C | 13C | 14C 1.1E8 59 | 15C 4.0E7 59 | 16C 1.4E7 60 | 17C 1.2E5 58 | 18C 4.8E2 55 | 19C | 20C |  | 22C |  | 
8B 3.1E6 42 |  | 10B | 11B | 12B 2.6E7 57 | 13B 7.5E6 58 | 14B 1.4E6 60 | 15B 2.6E5 51 |  | 17B |  | 19B |  |  |  | 
7Be 1.5E7 43 |  | 9Be | 10Be 1.6E7 50 | 11Be 1.5E6 58 | 12Be 2.8E5 60 |  | 14Be 3.0E3 63 |  |  |  |  |  |  |  | 
6Li | 7Li | 8Li 4.2E6 50 | 9Li 8.9E5 51 |  | 11Li 3.3E3 60 |  |  |  |  |  |  |  |  |  | 
 | 6He 2.1E6 51 |  | 8He 1.8E4 51 |  |  |  |  |  |  |  |  |  |  |  | 
Notes:
13C will allow: 12B 1.2E8 pps
16O will allow: 15O 2.7E8 pps, 14O 1.3E7 pps, 13O 4.2E5 pps
Primary beams at lower energy (≈30 AMeV) and thinner target will give about yield lower by ≈ 1 order of magnitude and final energies of 15-25 AMeV
Expected yield (pps)
Energy after the exit slit (AMeV)

## Slide 19
Our future: FraISe
Paolo Russotto
Text
12C6+ @ 60 AMeV - 18O8+ @ 70 AMeV - 20Ne10+ 2 kW @ 70 AMeV on 2500-1500-1250 um 9Be target
 |  |  |  | 17Ne 8.7E5 53 | 18Ne 3.1E7 51 | 19Ne 6.0E8 52 | 20Ne | 21Ne | 22Ne | 23Ne | 24Ne | 25Ne | 26Ne | 27Ne | 28Ne
 |  |  |  |  | 17F 1.7E8 50 | 18F | 19F | 20F 9.5E6 55 | 21F | 22F | 23F | 24F | 25F | 26F | 27F
 |  | 13O 7.2E4 54 | 14O 1.4E6 40 | 15O 2.8E7 54 | 16O | 17O | 18O | 19O 2.3E6 39 | 20O | 21O | 22O | 23O | 24O |  | 
 |  | 12N 1.2E6 49 | 13N 2.3E7 50 | 14N | 15N | 16N 6.9E8 53 | 17N 3.2E8 57 | 18N 3.7E6 57 | 19N | 20N | 21N | 22N | 23N |  | 
9C 4.0E5 45 | 10C 1.1E7 43 | 11C 2.2E8 44 | 12C | 13C | 14C 1.1E8 59 | 15C 4.0E7 59 | 16C 1.4E7 60 | 17C 1.2E5 58 | 18C 4.8E2 55 | 19C | 20C |  | 22C |  | 
8B 3.1E6 42 |  | 10B | 11B | 12B 2.6E7 57 | 13B 7.5E6 58 | 14B 1.4E6 60 | 15B 2.6E5 51 |  | 17B |  | 19B |  |  |  | 
7Be 1.5E7 43 |  | 9Be | 10Be 1.6E7 50 | 11Be 1.5E6 58 | 12Be 2.8E5 60 |  | 14Be 3.0E3 63 |  |  |  |  |  |  |  | 
6Li | 7Li | 8Li 4.2E6 50 | 9Li 8.9E5 51 |  | 11Li 3.3E3 60 |  |  |  |  |  |  |  |  |  | 
 | 6He 2.1E6 51 |  | 8He 1.8E4 51 |  |  |  |  |  |  |  |  |  |  |  | 
Expected yield (pps)
Energy after the exit slit (AMeV)

## Slide 20
Some physics cases
Al 100 µm homogenous wedge on the symmetry plane
100 µm SiC tagging detector at the exit
LISE++ simulations 18O primary beam at 70 MeV/nucleon, 2 kW on a 9Be target (1500 µm)
Simulation of spatial distribution of beam components, using a SiC detector placed after the exit slit
14Be: 69 %
3.0 103 pps
11Li
8He
Our future: FraISe
Paolo Russotto
14Be
11Li
8He

## Slide 21
Some physics cases
Al 100 µm homogenous wedge on the symmetry plane
100 µm SiC tagging detector at the exit
Simulation of spatial distribution of beam components, using a SiC detector placed after the exit slit
LISE++ simulations 18O primary beam at 70 MeV/nucleon, 2 kW on a 9Be target (2000 µm)
16C: 97 %
1.4 107 pps
13B
11Be
14B
18N
Our future: FraISe
Paolo Russotto
18N
13B
14B
16C

## Slide 22
Chart: Carbon isotopes expected yield
| 9 | 10 | 11 | 14 | 15 | 16 | 17 | 18
 | 380000 | 11000000 | 220000000 | 89000000 | 37000000 | 13000000 | 120000 | 440
Chart: Carbon isotopes expected purity
| 9 | 10 | 11 | 14 | 15 | 16 | 17 | 18
 | 28 | 99 | 99 | 56 | 99 | 99 | 9 | 1
Chart: Nytrogen isotopes expected yield
| 12 | 13 | 16 | 17 | 18 | 19
 | 2600000 | 18000000 | 540000000 | 270000000 | 4200000 | 4200
Our future: FraISe
Paolo Russotto
Chart: Nytrogen isotopes expected purity
| 12 | 13 | 16 | 17 | 18 | 19
 | 55 | 59 | 93 | 97 | 55 | 0.1

## Slide 23
Our future: FraISe
Paolo Russotto
Text
40Ar18+ @ 70 AMeV 2 kW on 500 um 9Be target
 |  |  |  | 35K | 36K 6.6E3 48 | 37K 8.2E4 48 | 38K 6.3E5 49 | 39K | 40K | 41K | 42K 8.2E5 32 | 43K 1.7E3 33 | 44K
 | 31Ar | 32Ar | 33Ar | 34Ar | 35Ar 8.9E5 45 | 36Ar | 37Ar 5.2E7 39 | 38Ar | 39Ar 7.0E8 39 | 40Ar | 41Ar 7.9E6 34 | 42Ar 1.5E4 34 | 43Ar
 |  | 31Cl | 32Cl 2.7E4 38 | 33Cl 7.1E5 33 | 34Cl 8.1E6 34 | 35Cl | 36Cl | 37Cl | 38Cl 4.5E8 35 | 39Cl 2.0E8 35 | 40Cl 3.6E6 30 | 41Cl 3.2E3 34 | 42Cl
28S | 29S | 30S 4.2E4 48 | 31S 1E6 49 | 32S | 33S | 34S | 35S 1.1E8 35 | 36S | 37S 3.9E7 36 | 38S 1.2E7 40 | 39S 1.1E5 40 | 40S 3.2E2 39 | 41S
27P | 28P 5.8E4 42 | 29P 1.4E6 43 | 30P 1.1E7 43 | 31P | 32P 5.2E7 40 | 33P 6.7E7 48 | 34P 3.9E7 44 | 35P 1.5E7 46 | 36P | 37P 8.2E5 50 | 38P 7.9E3 48 | 39P | 40P
26Si | 27Si 9.7E5 43 | 28Si | 29Si | 30S | 31Si 3.5E7 45 | 32Si 1.3E7 48 | 33Si 3.5E6 52 | 34Si 1.0E6 52 | 35Si 1.9E5 49 | 36Si 2.5E4 49 | 37Si | 38Si | 39Si
25Al 9.2E5 44 | 26Al 5.4E6 44 | 27Al | 28Al 2.0E7 45 | 29Al 1.2E7 45 | 30Al 4.4E6 45 | 31Al 1.1E6 52 | 32Al 1.6E5 41 | 33Al 2.5E4 41 | 34Al 2.9E3 41 | 35Al 3.5E2 41 | 36Al | 37Al | 38Al

## Slide 24
Our future: FraISe
10 20 30 40 50 60 70 80 90 100 150 200
FAIR-GSI
Paolo Russotto
ISOLDE
SPIRAL2-GANIL
200
150
100
90
80
70
60
50
40
30
20
10
0
E/A (MeV)
FRIB-MSU
BIGRIPS-RIKEN
LISE-GANIL
RIPS-RIKEN
A
SPES-LNL
ISOL: only longer lifetimes, better beam quality
FRAISE
In-flight: also shorter lifetimes
Complementarity!
FraISe with TANDEM beams after developing a cryogenic gas targets (p,d,3He…)

## Slide 25
Our future: FraISe
Paolo Russotto
Text
(some) other cases of relevant interest:
58,64Ni ->A≈60 region
24Mg, 27Al ->Al, Mg, Na, Ne, F isotopes
32S ->S, P, Si, Al isotopes
13C->light n-rich isotopes
16O->light n-poor isotopes
70Zn ->A≈68 region
36Ar ->A≈34 n-poor isotopes

## Slide 26
Conclusion & Perspectives
Several infrastructures (CS, Tandem, Sources) which represented the core of the LNS nuclear research activities are suffering from ageing. Important maintenance and development activities are needed to ensure their use for the next decades.
The Tandem beam menu will be enriched with the possibility to accelerate noble gas beams and with the production of long half life isotopes. The Cyclotron beam menu will include high intensity ion beams through the extraction by stripping.
The upgrading of the entire infrastructure and the offer of new beams will open new perspectives and to attract new users (at least we hope !).
The cyclotron upgrading works are proceeding with some delays due to the global pandemic situation. Detailed plans of commissioning of the major subsystems and of the Cyclotron are in preparation.
We plan to efficiently produce neutron-poor and neutron-rich light RIBs of A<=20 and around A=36 at Fermi energies
Production of RIBs of A≈20-34 and, expecially, A≈40-70 needs to be deeply studied and tested.
Conclusions & Perspectives
Luigi Celona & Paolo Russotto

## Slide 28
 |  |  |  | 22Al | 23Al | 24Al | 25Al | 26Al | 27Al | 28Al | 29Al | 30Al | 31Al | 32Al | 33Al
 |  |  | 20Mg | 21Mg | 22Mg | 23Mg | 24Mg | 25Mg | 26Mg | 27Mg | 28Mg | 29Mg | 30Mg |  | 
 |  |  |  | 20Na | 21Na | 22Na | 23Na | 24Na | 25Na | 26Na | 27Na | 28Na | 29Na |  | 
 |  | 17Ne | 18Ne | 19Ne | 20Ne | 21Ne | 22Ne | 23Ne | 24Ne | 25Ne | 26Ne | 27Ne | 28Ne |  | 
 |  |  | 17F | 18F 9.8E7 36 | 19F | 20F 4.2E8 37 | 21F 1.6E8 42 | 22F | 23F | 24F | 25F | 26F | 27F |  | 
13O | 14O | 15O | 16O | 17O | 18O | 19O 3.2E7 40 | 20O 9.2E6 43 | 21O 8.9E4 40 | 22O 3.0E2 43 | 23O | 24O |  |  |  | 
12N | 13N | 14N | 15 N | 16N | 17N | 18N 1.5E6 40 | 19N 3.2E5 43 | 20N 2.7E3 42 | 21N | 22N | 23N |  |  |  | 
11C | 12C | 13C | 14C | 15C | 16C | 17C | 18C | 19C | 20C |  | 22C |  |  |  | 
22Ne (50 AMeV) @ 2 kW on 9Be target
Paolo Russotto
Our future: FraISe

## Slide 29
24Mg (50 AMeV) @ 2 kW on 9Be target
 |  |  |  | 22Al | 23Al | 24Al | 25Al | 26Al | 27Al | 28Al | 29Al | 30Al | 31Al | 32Al | 33Al
 |  |  | 20Mg 8.6E6 37 | 21Mg 3.5E5 37 | 22Mg 1.2E7 38 | 23Mg 3.0E8 35 | 24Mg | 25Mg | 26Mg | 27Mg | 28Mg | 29Mg | 30Mg |  | 
 |  |  |  | 20Na 3.8E6 35 | 21Na 7.6E7 35 | 22Na 3.2E8 36 | 23Na | 24Na | 25Na | 26Na | 27Na | 28Na | 29Na |  | 
 |  | 17Ne | 18Ne | 19Ne | 20Ne | 21Ne | 22Ne | 23Ne | 24Ne | 25Ne | 26Ne | 27Ne | 28Ne |  | 
 |  |  | 17F | 18F | 19F | 20F | 21F | 22F | 23F | 24F | 25F | 26F | 27F |  | 
13O | 14O | 15O | 16O | 17O | 18O | 19O | 20O | 21O | 22O | 23O | 24O |  |  |  | 
12N | 13N | 14N | 15 N | 16N | 17N | 18N | 19N | 20N | 21N | 22N | 23N |  |  |  | 
11C | 12C | 13C | 14C | 15C | 16C | 17C | 18C | 19C | 20C |  | 22C |  |  |  | 
Paolo Russotto
Our future: FraISe

## Slide 30
 |  |  |  | 22Al | 23Al 9.5E4 37 | 24Al 2.8E6 41 | 25Al 5.6E7 41 | 26Al 5.1E8 34 | 27Al | 28Al | 29Al | 30Al | 31Al | 32Al | 33Al
 |  |  | 20Mg | 21Mg | 22Mg | 23Mg | 24Mg | 25Mg | 26Mg | 27Mg 4.9E6 40 | 28Mg | 29Mg | 30Mg |  | 
 |  |  |  | 20Na | 21Na | 22Na | 23Na | 24Na 8.1E7 39 | 25Na 2.5E7 39 | 26Na | 27Na | 28Na | 29Na |  | 
 |  | 17Ne | 18Ne | 19Ne | 20Ne | 21Ne | 22Ne | 23Ne 7.9E6 43 | 24Ne 1.9E6 40 | 25Ne | 26Ne | 27Ne | 28Ne |  | 
 |  |  | 17F | 18F | 19F | 20F | 21F | 22F 5.7E5 40 | 23F 5.9E4 43 | 24F | 25F | 26F | 27F |  | 
13O | 14O | 15O | 16O | 17O | 18O | 19O | 20O | 21O | 22O | 23O | 24O |  |  |  | 
12N | 13N | 14N | 15 N | 16N | 17N | 18N | 19N | 20N | 21N | 22N | 23N |  |  |  | 
11C | 12C | 13C | 14C | 15C | 16C | 17C | 18C | 19C | 20C |  | 22C |  |  |  | 
27Al (40 AMeV) @ 2 kW on 9Be target
Paolo Russotto
Our future: FraISe

## Slide 31
 |  |  |  |  |  | 28S | 29S | 30S 9.6E6 39 | 31S 2.7E8 39 | 32S | 33S | 34S | 35S | 36S
 |  |  |  |  |  | 27P 7.9E4 34 | 28P 2.9E6 33 | 29P 7.0E7 35 | 30P 3.7E8 35 | 31P | 32P 7.2E6 40 | 33P 6.8E3 39 | 34P | 35P
 |  |  | 23Si | 24Si | 25Si | 26Si 1.1E6 39 | 27Si 2.0E7 39 | 28Si | 29Si | 30Si | 31Si 6.1E5 40 | 32Si 2.2E3 40 | 33Si | 34Si
 |  |  | 22Al | 23Al | 24Al | 25Al | 26Al | 27Al | 28Al 4.0E7 41 | 29Al 1.0E7 41 | 30Al 8.8E4 40 | 31Al | 32Al | 33Al
 |  | 20Mg | 21Mg | 22Mg | 23Mg | 24Mg | 25Mg | 26Mg | 27Mg 5.6E6 41 | 28Mg 6.6E5 41 | 29Mg 6.4E3 40 | 30Mg |  | 
 |  |  | 20Na | 21Na | 22Na | 23Na | 24Na | 25Na 2.6E6 41 | 26Na 3.6E5 41 | 27Na 2.8E4 41 | 28Na | 29Na |  | 
 | 17Ne | 18Ne | 19Ne | 20Ne | 21Ne | 22Ne | 23Ne | 24Ne | 25Ne 1.2E4 41 | 26Ne 8.7E2 42 | 27Ne | 28Ne |  | 
 |  | 17F | 18F | 19F | 20F | 21F | 22F | 23F | 24F | 25F | 26F | 27F |  | 
32S (50 AMeV)@ 2 kW on 9Be target
Paolo Russotto
Our future: FraISe

## Slide 32
36Ar (40 AMeV) 2 kW on 9Be target
ù |  |  |  | 35K 6.1E4 36 | 36K 4.2E6 37 | 37K 3.8E6 37 | 38K 6.3E5 37 | 39K | 40K | 41K | 42K | 43K | 44K
 | 31Ar | 32Ar | 33Ar 1.9E5 37 | 34Ar 8.2E6 37 | 35Ar 2.7E8 38 | 36Ar | 37Ar 2.9E6 38 | 38Ar | 39Ar | 40Ar | 41Ar | 42Ar | 43Ar
 |  | 31Cl 5.6E4 37 | 32Cl 2.3E6 38 | 33Cl 5.9E7 38 | 34Cl 3.2E8 38 | 35Cl | 36Cl | 37Cl | 38Cl | 39Cl | 40Cl | 41Cl | 42Cl
28S | 29S | 30S | 31S | 32S | 33S | 34S | 35S | 36S | 37S | 38S | 39S | 40S | 41S
27P | 28P | 29P | 30P | 31P | 32P | 33P | 34P | 35P | 36P | 37P | 38P | 39P | 40P
26Si | 27Si | 28Si | 29Si | 30Si | 31Si | 32Si | 33Si | 34Si | 35Si | 36Si | 37Si | 38Si | 39Si
25Al | 26Al | 27Al | 28Al | 29Al | 30Al | 31Al | 32Al | 33Al | 34Al | 35Al | 36Al | 37Al | 38Al
Paolo Russotto
Our future: FraISe

## Slide 33
Our future: FraISe
Paolo Russotto
Text
32
Some physics cases
14Be: 63 %
11Li
8He
Al 100 µm homogenous wedge on the symmetry plane
100 µm SiC tagging detector at the exit
LISE++ simulations 18O primary beam at 70 MeV/nucleon, 2 kW on a 9Be target (1250 µm)
Simulation of spatial distribution of beam components, using a SiC detector placed after the exit slit
3E3 pps
14Be
11Li
8He
∆E-ToF plot

## Slide 34
Our future: FraISe
Paolo Russotto
Text
33
N.S. Martorana - martorana@lns.infn.it
4/1/2022
33
Some physics cases
Al 100 µm homogenous wedge on the symmetry plane
100 µm SiC tagging detector at the exit
Simulation of spatial distribution of beam components, using a SiC detector placed after the exit slit
16C: 85%
LISE++ simulations 18O primary beam at 70 MeV/nucleon, 2 kW on a 9Be target (1250 µm)
∆E-ToF plot
1.4E7 pps

## Slide 35
34
Some physics cases
Al 100 µm homogenous wedge on the symmetry plane
100 µm SiC tagging detector at the exit
Simulation of spatial distribution of beam components, using a SiC detector placed after the exit slit
68Ni: 52%
7.5E5 pps
LISE++ simulations 70Zn primary beam at 40 MeV/nucleon, 1 kW on a 9Be target (500 µm)
∆E-ToF plot
Paolo Russotto
Our future: FraISe

## Slide 36
Our future: FraISe
Paolo Russotto
First order envelope calculate in case of x-x' maximum acceptance
Momentum separation at FRAISE symmetry plane

## Slide 37
 |  |  |  |  |  |  | 20Ne | 21Ne | 22Ne |  |  |  |  |  | 
 |  |  |  |  |  |  | 19F |  |  |  |  |  |  |  | 
 |  |  |  |  | 16O | 17O | 18O |  |  |  |  |  |  |  | 
 |  | 12N 2.6E6 43 | 13N 6.6E5 41 | 14N | 15 N |  |  |  |  |  |  |  |  |  | 
9C 3.8E5 40 | 10C 1.1E7 42 | 11C 2.2E8 44 | 12C | 13C | 14C 1.5E3 40 |  |  |  |  |  |  |  |  |  | 
8B 3E6 42 |  | 10B | 11B | 12B 3.7E6 48 | 13B 2.5E3 42 |  |  |  |  |  |  |  |  |  | 
7Be 1.5E7 45 |  | 9Be | 10Be 1.6E7 48 | 11Be 1.4E5 45 |  |  |  |  |  |  |  |  |  |  | 
6Li | 7Li | 8Li 4.2E6 50 | 9Li 8.9E5 51 |  |  |  |  |  |  |  |  |  |  |  | 
 | 6He 2.2E6 49 |  | 8He 2E4 50 |  |  |  |  |  |  |  |  |  |  |  | 
12C6+ @ 60 AMeV 2 kW on 2500 um 9Be
Expected yield (pps)
Energy after the tagging detector (AMeV)

## Slide 38
 |  |  |  | 17Ne | 18Ne | 19Ne | 20Ne | 21Ne | 22Ne | 23Ne | 24Ne | 25Ne | 26Ne | 27Ne | 28Ne
 |  |  |  |  | 17F | 18F | 19F | 20F | 21F | 22F | 23F | 24F | 25F | 26F | 27F
 |  | 13O 6.3E4 56 | 14O 1.3E6 56 | 15O 2.4E7 57 | 16O | 17O | 18O | 19O 3.2E6 57 | 20O 5.8E3 53 | 21O | 22O | 23O | 24O |  | 
 |  | 12N 9.5E5 57 | 13N 1.7E7 59 | 14N | 15 N | 16N 5.4E8 60 | 17N 2.7E8 60 | 18N 4.2E6 61 | 19N 4.2E3 55 | 20N | 21N | 22N | 23N |  | 
9C | 10C | 11C | 12C | 13C | 14C 8.9E7 60 | 15C 3.7E7 61 | 16C 1.3E7 61 | 17C 1.2E5 58 | 18C 4.4E2 55 | 19C | 20C |  | 22C |  | 
8B |  | 10B | 11B | 12B 2.0E7 61 | 13B 7.2E6 61 | 14B 1.5E6 61 | 15B 2.9E5 62 |  | 17B 4 56 |  | 19B |  |  |  | 
7Be |  | 9Be | 10Be 4.4E6 61 | 11Be 1.4E6 61 | 12Be 2.4E5 62 |  | 14Be 3E3 62 |  |  |  |  |  |  |  | 
6Li | 7Li | 8Li 8.2E5 63 | 9Li 2.3E5 62 |  | 11Li 3E3 62 |  |  |  |  |  |  |  |  |  | 
 | 6He 2.7E5 66 |  | 8He 5.2E3 64 |  |  |  |  |  |  |  |  |  |  |  | 
18O8+ @ 70 AMeV 2 kW on 1500 um 9Be

## Slide 39
 |  |  |  | 17Ne | 18Ne | 19Ne | 20Ne | 21Ne | 22Ne | 23Ne | 24Ne | 25Ne | 26Ne | 27Ne | 28Ne
 |  |  |  |  | 17F | 18F | 19F | 20F | 21F | 22F | 23F | 24F | 25F | 26F | 27F
 |  | 13O 3.3E3 15 | 14O 7.9E4 16 | 15O 1.9E6 16 | 16O | 17O | 18O | 19O 4.6E5 19 | 20O 8.7E2 20 | 21O | 22O | 23O | 24O |  | 
 |  | 12N 7.5E4 17 | 13N 1.5E6 17 | 14N | 15 N | 16N 7E7 20 | 17N 3.6E7 20 | 18N 7.4E6 17 | 19N 6E2 21 | 20N | 21N | 22N | 23N |  | 
9C | 10C | 11C | 12C | 13C | 14C 1.2E7 20 | 15C 4.8E6 21 | 16C 1.7E6 21 | 17C 1.6E4 21 | 18C 7.7E1 21 | 19C | 20C |  | 22C |  | 
8B |  | 10B | 11B | 12B 2.7E6 21 | 13B 8.3E5 21 | 14B 1.9E5 22 | 15B 3.4E4 22 |  | 17B |  | 19B |  |  |  | 
7Be |  | 9Be | 10Be 6E5 22 | 11Be 1.6E5 22 | 12Be 3.3E4 22 |  | 14Be 3.6E2 23 |  |  |  |  |  |  |  | 
6Li | 7Li | 8Li 1.2E5 25 | 9Li 3E4 25 |  | 11Li 4E2 23 |  |  |  |  |  |  |  |  |  | 
 | 6He 4.3E4 27 |  | 8He 7.3E2 25 |  |  |  |  |  |  |  |  |  |  |  | 
18O8+ @ 29 AMeV 2 kW on 500 um 9Be

## Slide 40
 |  |  |  | 17Ne 8.E5 56 | 18Ne 2.6E7 56 | 19Ne 4.9E8 57 | 20Ne | 21Ne | 22Ne | 23Ne | 24Ne | 25Ne | 26Ne | 27Ne | 28Ne
 |  |  |  |  | 17F 1.3E8 57 | 18F | 19F | 20F 8.5E6 59 | 21F 8.6E3 53 | 22F | 23F | 24F | 25F | 26F | 27F
 |  | 13O 1.2E5 57 | 14O 3.3E6 57 | 15O 1.4E8 58 | 16O | 17O | 18O | 19O 6.8E5 56 | 20O 2.4E3 54 | 21O | 22O | 23O | 24O |  | 
 |  | 12N 1.3E6 57 | 13N 1.8E7 58 | 14N | 15 N | 16N | 17N | 18N | 19N | 20N | 21N | 22N | 23N |  | 
9C | 10C | 11C | 12C | 13C | 14C | 15C | 16C | 17C | 18C | 19C | 20C |  | 22C |  | 
8B |  | 10B | 11B | 12B | 13B | 14B | 15B |  | 17B |  | 19B |  |  |  | 
7Be |  | 9Be | 10Be | 11Be | 12Be |  | 14Be |  |  |  |  |  |  |  | 
6Li | 7Li | 8Li | 9Li |  | 11Li |  |  |  |  |  |  |  |  |  | 
 | 6He |  | 8He |  |  |  |  |  |  |  |  |  |  |  | 
20Ne10+ @ 70 AMeV 2 kW on 1250 um 9Be

## Slide 41
 |  |  |  | 35K 1.7E2 44 | 36K 6.6E3 45 | 37K 8.2E4 45 | 38K 6.3E5 45 | 39K | 40K | 41K | 42K 9.1E5 46 | 43K 1.8E3 45 | 44K
 | 31Ar | 32Ar 7E1 45 | 33Ar 1.5E3 46 | 34Ar 3.2E4 46 | 35Ar 7.5E5 47 | 36Ar | 37Ar 6.8E7 47 | 38Ar | 39Ar 8.2E8 48 | 40Ar | 41Ar 7.6E6 47 | 42Ar 1.5e4 47 | 43Ar
 |  | 31Cl 1.7E3 46 | 32Cl 3.9E4 47 | 33Cl 1E6 49 | 34Cl 1.1E7 49 | 35Cl | 36Cl | 37Cl | 38Cl | 39Cl 2.2E8 49 | 40Cl 3.5E6 49 | 41Cl 4E3 49 | 42Cl
28S | 29S 1.8E3 47 | 30S 4.2E4 48 | 31S 1E6 49 | 32S | 33S | 34S | 35S 1.3E8 49 | 36S | 37S 5E7 49 | 38S 1.5E7 49 | 39S 1.5E5 49 | 40S 4.1E2 48 | 41S
27P 1.8E3 47 | 28P 4.2E4 47 | 29P 9.5E5 48 | 30P 7.8E6 48 | 31P | 32P 6.6E7 49 | 33P 5.5E7 49 | 34P 3.5E7 49 | 35P 1.3E7 49 | 36P 3.9E6 49 | 37P 8E5 50 | 38P 7.8E3 49 | 39P 1.5E1 48 | 40P
26Si 4E4 48 | 27Si 7.1E5 50 | 28Si | 29Si | 30S | 31Si 2.8E7 49 | 32Si 1.1E7 50 | 33Si 3.5E6 50 | 34Si 1E6 50 | 35Si 1.7E5 50 | 36Si 2.5E4 50 | 37Si 2.5E2 50 | 38Si | 39Si
25Al 6.7E5 51 | 26Al 3E6 51 | 27Al | 28Al 1.6E7 50 | 29Al 1.1E7 50 | 30Al 5.9E6 50 | 31Al 1.1E6 50 | 32Al 2.2E5 50 | 33Al 3.1E4 50 | 34Al 4.3E3 50 | 35Al 5.5E2 50 | 36Al 5 50 | 37Al | 38Al
40Ar18+ @ 60 AMeV 2 kW on 500 um 9Be

## Slide 42
Our future: FraISe
Paolo Russotto
Text
Some refs:
P. Russotto et al., J. Physics: Conf. Ser., 1014 (2018) 012016;
N.S. Martorana, Nuovo Cimento 44 C (2021) 1 and LNS report 2019-2020;
F. Risitano, Master thesis Univ. Of Messina 2020 and LNS report 2020;
A.D. Russo et al., Nucl. Instrum. Methods B, 463 (2020) 418.
F. Risitano, in press on Nuovo Cimento C
N.S. Martorana, Proceedings of IWM-EC 2021, to be published in Nuovo Cimento C
Studied cases
In the following:
-Al 100 um homogenous degrader on symmetry plane
-100 um SiC tagging detector at the exit
Summer 2019
Start Construction Site
Summer 2022
Closing of Construction Site
Jan.–Mar. 2023
Tandem beam
Fall 2023
CS preparation/operation