## Slide 1: STT Technical Basics
C. Montanari
FNAL – INFN Pavia
DUNE-IT Meeting – November 12, 2021

## Slide 2: SAND’s STT – Reference Concept
  SAND’s Straw Tubes Tracker (STT) is organized as a sequence of straw tubes planes interleaved with thin targets made either of graphite (pure Carbon) or polyethylene (C2H4) and transition radiation foils.
LAr target
(GRAIN)
XXYY configuration

## Slide 3: SAND’s STT – Reference Concept – main parameters
  Target mass (fiducial): 4700 kg (C2H4) + 504 kg (graphite)
  Straws diameter: 5 mm
  Max straws length: 4000 mm
  Straws thickness: 20 µm
  Number of channels: ≈ 220000
  2-views configuration: XXYY
  Gas mixture: Xe/CO2 (70/30) for C2H4 target modules and Ar/CO2 (70/30) for graphite modules
  Operating pressure: 1.9 bar abs
  Nominal space resolution: 100 µm (this is my understanding)

## Slide 4: Straw Tubes Detectors: 1 – Straw Tubes Tracker for Compass
  Built between 2001 and 2004
  3 straws orientation: 0 (vertical), 10°, 90°
  Max straws length: 3652 mm
  Straws diameter: 6 mm and 9.5 mm (≈1/2,≈1/2)
  Total number of channels: 12440
  Gas mixture: Ar/Co2/CF4 (74/6/20)
  Operating pressure: unknown
  Nominal space resolution: 200 µm
Cross-section of a double layer
Straw tube layout: inner layer Kapton XC (40 µm)
Glue film: 7 µm ; outer layer aluminized Kapton (12 µm)
Detail of the end plug of the straw tubes
V.N. Bychkov, et al. NIM A 556 (2006) 66-79

## Slide 5: Straw Tubes Detectors: 2 – Straw Tubes Tracker for COMET
  Detector in the prototyping phase
  2 straws orientation: xxyy
  Max straws length: ≈ 1300 mm
  Straws diameter: 9.8 mm
  Straw thickness: 20 µm
  Total number of channels: ≈ 2650
  Gas mixture: Ar/C2H6 (50/50) possible alternatives under investigation
  Operating pressure: 1 bar abs (N.B. the straw tubes will be in a vacuum chamber)
  Nominal space resolution: 200 µm
Full size prototype
Straight ultrasonic welding of the straws
H. Nischiguchi, et al. NIM A 845 (2017) 269-272

## Slide 6: Straw Tubes Detectors: 3 – Central Straw Tubes Tracker for PANDA
  Detector not yet in operation
  3 straws orientation: 0 (longitudinal), +3°, -3° (all double layers)
  Straws length: ≈ 1500 mm
  Straws diameter: 10 mm
  Straw thickness: 27 µm
  Total number of channels: 4636
  Gas mixture: Ar/CO2 (90/10)
  Operating pressure: 2 bar abs
  Nominal space resolution: 150 µm
Pressure stabilized straw tubes pack
Lead brick
Individual tubes built and pressurized before assembling
P. Gianotti, et al. arXiv:1307.4537v1 (2013)

## Slide 7: Straw Tubes Detectors: 4 – ATLAS TRT Barrel Detector
  Detector built between 1998 and 2003 (by 3 US groups
  1 straws orientation
  Straws length: ≈ 1440 mm
  Straws diameter: 4 mm
  Straw thickness: 80 µm
  Total number of channels: 52544
  Gas mixture: Xe/CO2/O2 (70/27/3)
  Operating pressure: 3 bar abs
  Measured space resolution: 130 µm
Detail of end plugs and gas manyfold
ATLAS TRT Coll. JINST 3 P02013 ; P02014

## Slide 8: SAND STT : Challenges
  Production and detection of transition radiation:
    construction of radiator based on 15 µm thick up to 4 x 4 m2 foils
    use of Xe + high pressure
  Number of STT channels
  Use of thin walls thickness (20 µm)
  Definition of thermal and humidity operative conditions (mechanical properties of the straws show a significant dependence on temperature and humidity).
  Definition of minimal requirements for mechanical alignment
  Definition of minimal requirements for straw tubes reliability

## Slide 9: SAND STT : path towards an engineering design
  Identify a team of engineers, with a lead engineer and a leading detector expert physicist that starts designing a production process (it is recommended that lead engineer and lead physicist are INFN).
  Establish a combined group between the engineering team and the team currently working on detector simulations with the objective to clearly define some of the critical detector parameters. In particular:
    The need of transition radiation
    The maximum size of the straw tubes
    The maximum thickness of the straw tube walls and the corresponding limitations in terms of material composition
    The minimal requirements on mechanical alignment
    Any other appropriate requirement coming from the engineering team
  An appropriate deadline for the above process is May 2022.
  From May 2022 to the end of 2022, an engineering design of the STT production should then be achieved, followed by the production of the first full scale prototype in 2023.
  Dedicated tests on materials and procedures have to proceed in parallel with the engineering design and the prototype production.
  Mass production should start in 2024, with an available time of about 5 years for completion (teams for this task are, at least dominantly, non INFN).