## Slide 1
Tracking the magnetic field in the Fermilab Muon g-2 experiment
René Reimann for the Muon g-2 collaboration
ICHEP 2022, Bologna
Jun 7th , 2022

## Slide 2: Muon g-2
magnetic moment
spin
proportionality constant
Figure: Zoltan Fodor
Hadronic vacuum polarization dominates theoretical uncertainty.
Dispersive and lattice QCD approach deviate
Run 1 result consistent with BNL measurement

## Slide 3: Measurement principle
Magnetic storage ring
spin precession
cyclotron motion
spin polarized muons
Measure energy of decay e+
event rate varies with
measured using nuclear
magnetic resonance (NMR)
spin precession of protons
Notes: $$ \underbrace{\omega_S - \omega_C}_{\omega_a} = \underbrace{\frac{g_\mu - 2}{2}}_{a_\mu} \frac{e}{m_\mu} B $$

## Slide 4: Extracting aµ
Spatial distribution of
magnetic field
Transient magnetic fields
Calibration
Clock blinding
Muon beam dynamics corrections
Spatial muon distribution
Anomalous spin
precession frequency
Talk by A. Driutti Accelerators, Jul 7, 9:30AM
Talk by L. Cotrozzi Quarks & Lepton Flavor Physics
Jul 8, 11:32
external measurements known to 25ppb

## Slide 5: Superconducting storage ring magnet
3 cryostats with 4 superconducting coils (5300 A)
1.45 T vertical magnetic field
90 mm muon storage region
180 mm gap for vacuum chambers
µ+

## Slide 6: Trolley System
17 NMR probes
Measures spatial field distribution in storage region
Pulled through ring every ~3 days

## Slide 7: Spatial distribution of field
Phys. Rev. A 103, 042208 (2021)
azimuthal slice
dipole
quadrupole
sextupole
octupole

## Slide 8: Trolley measurements
Phys. Rev. A 103, 042208 (2021)
>8000 azimuthal locations
Trolley measures spatial distribution, but can not measure while muon beam

## Slide 9: Fixed Probe System
  72 azimuthal location (stations)
  allows to extract 4 to 5 multipole moments
  tracks field drift 24/7
  measures field differences
aluminum

## Slide 10: Trolley Footprint Removal
trolley electronics disturbs field (footprint)
veto measurements
interpolate from neighboring probes
Phys. Rev. A 103, 042208 (2021)

## Slide 11: Time tracking
Phys. Rev. A 103, 042208 (2021)

## Slide 12: Time tracking
Phys. Rev. A 103, 042208 (2021)

## Slide 13: Time tracking
drifts in higher order moments lead to tracking offset
Phys. Rev. A 103, 042208 (2021)
M

## Slide 14: Time tracking
drifts in higher order moments lead to tracking offset
Phys. Rev. A 103, 042208 (2021)
M

## Slide 15: Tracking Uncertainty
Fixed Probe drift: Random walk
End point known: Brownian bridge model
Uncertainty vs time
no second Trolley run
Improvements
improved position determination
continues azimuthal treatment (virtual trolley, Fourier method)
improved trolley footprint removal
more trolley runs
improved field stability by temperature regulation

## Slide 16: Trolley Probe Calibration
Absolute calibrated water probe
Cross-calibrated at Argonne National Lab test magnet
Probe can be placed in ring by 3D translation stage
Swap trolley and calibration probe to get calibration constant
Derive calibration constants for each trolley probe
Improvements
Study of temperature effects
Calibration twice a year with automated procedure
Consistent results

## Slide 17: Kicker transient magnetic field
Kicker used to place beam on storage orbit
Kicker pulse induces 22mT field in radial direction
Measurement based on optical faraday rotation
Improvements
Reduced uncertainties due to vibration mitigation
Second independent magnetometer ready to go

## Slide 18: Beam related magnetic field transients
Pulsing electrostatic quadrupoles for beam confinement leads to magnetic field transient.
Only measured after run 2  conservative estimates
Full mapping of ring between run 4 and run 5

## Slide 19: Beam related magnetic field transients
Pulsing electrostatic quadrupoles for beam confinement leads to magnetic field transient.
Only measured after run 2  conservative estimates
Full mapping of ring between run 4 and run 5
µ present
Improved understanding

## Slide 20: Muon weighted average magnetic field
Using tracker profiles and beam dynamics simulation
Improvements
Better placement of beam, due to replacing broken resistors
Better placement of beam, due to stronger kick
CBO reduction due to quad RF (run 5)

## Slide 21: Summary
First time a three-way comparison of aµ is possible, very exciting
Run 2 / 3 analysis on-going
Magnetic field tracked by trolley system (spatial distribution) and fixed probe system (drift)
Probes are calibrated with absolute calibrated water probe twice a year
Detailed measurement campagnes to measure transient magnetic fields from kickers and quads
Improvements in running conditions (temperature stability), data processing (position reconstruction) and analysis
Exciting times ahead!
Thank you
Notes: \documentclass{article}
\usepackage{amsmath}
\pagestyle{empty}
\begin{document}
\begin{tabular}{lrr}
\hline
\hline
Quantity & Correction Terms & Uncertainty \\
& (ppb) & (ppb) \\
\hline
$\omega_a^m$ (statistical) & - & 100 \\
$\omega_a^m$ (systematic) & - & - \\
\hline
Total systematic & - & 100 \\
Total fundamental factors & - & 25 \\
Totals & - & 140 \\
\hline
\hline
\end{tabular}
\end{document}

## Slide 22: Backup

## Slide 23: Magnetic Field Analysis Overview
calibration
quality cuts
field tracking
muon weighting
transients

## Slide 24: Uncertainty budget
Technical Design Report goal
  Total uncertainty 140 ppb
  Total systematic uncertainty 100 ppb
  Magnetic field uncertainty 70 ppb
Dominant magnetic field uncertainty due to transient fields from quadrupole and kicker operations
  Conservative estimate for run 1
  Detailed investigation ongoing
Reduce tracking uncertainty to achieve overall goal
Run 1 uncertainties

## Slide 25: Magnetic field stability
Hall temperature changes caused field changes
See diurnal field variation
Influences magnetic field systematic

## Slide 26: Magnetic field stability
Hall temperature changes caused field changes
See diurnal field variation
Influences magnetic field systematic
before
after
Magnet insulation

## Slide 27: Magnetic field stability
Hall temperature changes caused field changes
See diurnal field variation
Influences magnetic field systematic
before
after
Magnet insulation

## Slide 28: Magnetic field stability
Hall temperature changes caused field changes
See diurnal field variation
Influences magnetic field systematic
Upgrade Air Conditioning System
before
after
Magnet insulation

## Slide 29: Magnetic field stability
Hall temperature changes caused field changes
See diurnal field variation
Influences magnetic field systematic
Upgrade Air Conditioning System
before
after
Magnet insulation
Improved operating conditions

## Slide 30: Run 1 Result
Muon g-2 collaboration published Run 1 result B. Abi et al. (Muon g−2 Collaboration) Phys. Rev. Lett. 126, 141801, 2021
Uncertainty in theory calculation dominated by calculation of hadronic vacuum polarization
Dispersive approach, 4.2σ tension T. Aoyama et al., Phys. Rept. 887 (2020) 1-166
Lattice QCD approach , 1.5σ tension Borsányi et al., Nature 593, 51–55, 2021 and arXiv:2002.12347
Figure: Zoltan Fodor

## Slide 31: Magnetic Storage Ring
In order to measure to the required precision:
Keep the field as uniform as possible
  passive & active shimming
Keep the field as stable as possible
  power supply feedback & temperature stabilization
Measure the field experienced by the muons
Track drifts during the times when muons are present
Calibrate the field measurements with a well-understood measurement standard
B = 1.45 T