## Slide 1: SEM Meeting
INFN-LNF
Filippo Rosatelli
06/12/2021

## Slide 2
ATLAS ITk – Cabling
Activities:
Update the Layer 2 routing in End caps (WIP). Waiting news from ATLAS collaboration.
EC L2 NOW
HV/LV
DATA

## Slide 3
ATLAS ITk –Data feedthrough
Activities:
Test on different prototypes to verify the issues connected on filling process.
Improve the solution adopted.
Design the new 1:1 scale prototype for test (WIP)

## Slide 4
ATLAS ITk –Leak test
Activities:
Production of samples for test O-ring leak.
O-ring Leak check test performed.
Sent the three samples to US facility for irradiation up to 6 MGy.
Migration to 3D experience.
4MGy
6MGy
4MGy
6MGy
Prototype tested

## Slide 5
LEAK TEST RESULTS
Sample n° | Leak rate [mbar l/s] He std after 6 h
1 | 5,2E-06
2 | 4,28E-06
3 | 4,31E-06
Sample n° | Leak rate [mbar l/s] He std after 24 h
1 | 5,42E-06
2 | 4,6E-06
3 | 4,62E-6
Chart: Leak vs Time
| 0.16666666666666699 | 0.33333333333333331 | 0.5 | 1 | 2 | 5 | 10 | 15 | 20 | 30 | 60 | 90 | 120 | 180 | 210 | 240 | 270 | 330 | 360 | 390
1 | 1.3e-12 | 1.3e-12 | 1.6e-12 | 1.5e-12 | 1e-09 | 7e-08 | 4.2e-07 | 8.8e-07 | 1.3e-06 | 2e-06 | 3.05e-06 | 3.53e-06 | 3.86e-06 | 4.4e-06 | 4.5e-06 | 4.7e-06 | 4.8e-06 | 5.1e-06 | 5.2e-06 | 5.3e-06
2 | 1.1e-09 | 1.1e-09 | 1.1e-09 | 1.12e-09 | 1.6e-09 | 4e-08 | 2.8e-07 | 6.1e-07 | 9.7e-07 | 1.57e-06 | 2.42e-06 | 2.85e-06 | 3.12e-06 | 3.56e-06 | 3.7e-06 | 3.86e-06 | 4e-06 | 4.2e-06 | 4.28e-06 | 4.35e-06
3 | 1.1e-09 | 1.1e-09 | 1.1e-09 | 1.1e-09 | 6.3e-09 | 4.1e-08 | 2.7e-07 | 6.2e-07 | 1e-06 | 1.66e-06 | 2.7e-06 | 3.13e-06 | 3.4e-06 | 3.78e-06 | 3.85e-06 | 4e-06 | 4.14e-06 | 4.23e-06 | 4.31e-06 | 4.4e-06

## Slide 6
CYGNO - LIME
Activities:
Design a new regulation system for CMOS camera.
Production of components (WIP)
Support to the experiment.
Order of commercial part.
GEM

## Slide 7
CYGNO - MANGO
Activities:
Design the support system for CMOS camera placed in front of the vacuum window .
Production of components (WIP)