## Slide 1: Super-B: Second order of momentum compaction.
Sasha Novokhatski
SLAC National Accelerator Laboratory
XV Super B General Meeting
December 14 – December 17, 2010
California Institute of Technology, USA

## Slide 2: Super-B parameters. March 3, 2010
(Bold: computed values) |  | Base Line |  | Low Emittance |  | High Current |  | Tau/Charm (prelim.) | 
Parameter | Units | HER (e+) | LER (e-) | HER (e+) | LER (e-) | HER (e+) | LER (e-) | HER (e+) | LER (e-)
Energy | GeV | 6.7 | 4.18 | 6.7 | 4.18 | 6.7 | 4.18 | 2.58 | 1.61
Circumference | m | 1258.4 |  | 1258.4 |  | 1258.4 |  | 1258.4 | 
Bunch length (zero current) | mm | 4.69 | 4.29 | 4.73 | 4.34 | 4.03 | 3.65 | 4.75 | 4.36
Bunch length (full current) | mm | 5 | 5 | 5 | 5 | 4.4 | 4.4 | 5 | 5
Beam current | mA | 1892 | 2447 | 1460 | 1888 | 3094 | 4000 | 1365 | 1766
N. Buckets distance |  | 2 | 2 | 2 | 2 | 1 | 1 | 1 | 1
Ion gap | % | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
RF frequency | Hz | 4.76E+08 | 4.76E+08 | 4.76E+08 | 4.76E+08 | 4.76E+08 | 4.76E+08 | 4.76E+08 | 4.76E+08
Revolution frequency | Hz | 2.38E+05 |  | 2.38E+05 |  | 2.38E+05 |  | 2.38E+05 | 
Harmonic number | # | 1998 |  | 1998 |  | 1998 |  | 1998 | 
Number of bunches | # | 978 |  | 978 |  | 1956 |  | 1956 | 
N. Particle/bunch | # | 5.08E+10 | 6.56E+10 | 3.92E+10 | 5.06E+10 | 4.15E+10 | 5.36E+10 | 1.83E+10 | 2.37E+10
Bunch current | mA | 1.935 | 2.502 | 1.493 | 1.930 | 1.582 | 2.045 | 0.698 | 0.903
Energy Loss/turn | MeV | 2.11 | 0.865 | 2.11 | 0.865 | 2.11 | 0.865 | 0.4 | 0.166
Momentum compaction |  | 4.36E-04 | 4.05E-04 | 4.36E-04 | 4.05E-04 | 4.36E-04 | 4.05E-04 | 4.36E-04 | 4.05E-04
Energy spread (zero current) | dE/E | 6.31E-04 | 6.68E-04 | 6.31E-04 | 6.68E-04 | 6.31E-04 | 6.68E-04 | 6.31E-04 | 6.68E-04
Energy spread (full current) | dE/E | 6.43E-04 | 7.34E-04 | 6.43E-04 | 7.34E-04 | 6.43E-04 | 7.34E-04 | 6.94E-04 | 7.34E-04
CM energy spread | dE/E | 5.00E-04 |  | 5.00E-04 |  | 5.00E-04 |  | 5.26E-04 | 
Energy acceptance |  | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01
Synchrotron frequency | kHz | 3.01 | 2.8 | 2.97 | 2.77 | 3.54 | 3.26 | 2.96 | 2.77
Synchrotron tune |  | 0.0126 | 0.0118 | 0.0125 | 0.0116 | 0.0148 | 0.0137 | 0.0124 | 0.0116
SR power loss | MW | 3.99 | 2.12 | 3.08 | 1.63 | 6.53 | 3.46 | 0.55 | 0.29
RF Wall Plug Power (SR only) | MW | 12.22 |  | 9.43 |  | 19.98 |  | 1.68 | 
Total RF Wall Plug Power | MW | 17.08 |  | 12.72 |  | 30.48 |  | 3.11 | 
Number of cavities |  | 12 | 8 | 12 | 8 | 20 | 12 | 6 | 4
Number of Klystrons |  | 6 | 4 | 6 | 4 | 10 | 6 | 3 | 2
Total Number of klystrons |  | 10 |  | 10 |  | 16 |  | 5 | 
RF Voltage | MV | 7.01 | 5.25 | 6.88 | 5.13 | 9.3 | 7.2 | 2.54 | 1.94
Rs | MW |  |  |  |  |  |  |  | 
Q0 |  |  |  |  |  |  |  |  | 
b |  |  |  |  |  |  |  |  | 

## Slide 3: Momentum compaction
Small momentum compaction means small
Quasi-isochronous ring

## Slide 4: Example of a quasi-isochronous lattice
Yuri Nosochkov

## Slide 5: When it is small?
Consider only first and second order
or

## Slide 6: Two stable fixed points
without wake fields

## Slide 7: Head-tail growth rate
If energy loss decreases with a bunch length,
than we have instability without any threshold for a positive sign of

## Slide 8: Strong Heat –Tail Instability

## Slide 9: Linear feedback. Bunch position.

## Slide 10: Bunch length and energy spread

## Slide 11: Super B. Wake potential of a 5 mm bunch (Base line).
Loss factor = 11 V/pC
Chart: Toal wake potential [V/pC]

## Slide 12: Bunch lengthening in Super-B. Base line

## Slide 13: Bunch lengthening in Super-B.
LER
Chart: Bunch charge [nC]
| 0 | 3 | 6 | 9 | 10.5 | 12 | 15 | 18 | 21 | 24 | 27 | 30 | 33 | 36 | 39 | 42 | 45 | 48
bunch length | 4.29 | 4.51 | 4.73 | 4.92 | 5.02 | 5.1 | 5.27 | 5.43 | 5.58 | 5.73 | 5.86 | 5.99 | 6.12 | 6.24 | 6.35 | 6.53 | 6.71 | 6.85
dE/E | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1.0273 | 1.0585 | 1.0718

## Slide 14: Adding second part of momentum compaction

## Slide 15: Adding second part of momentum compaction
Check for a negative value -0.05. It is stable.

## Slide 16: Saw-tooth type instability
Check for a positive value +0.05. It is unstable.

## Slide 17: Summary
Second part of momentum compaction may play important role in the longitudinal beam dynamics for low compaction machines.
There is no instability threshold for a positive value of
It is necessary to check that second part of the momentum compaction of the Super-B lattice has the right sign, or at least less than 0.05, if it is positive.