## Slide 1: Supercomputing IR wakes
My adventures in super computing: first results
Introduce SLAC Advanced Computing Department parallel Finite Element Method electromagnetic time domain solver (t3p) as a tool for IR wakefield computation.
Compare with gdfidl** finite integration techniques (MAFIA)
Consider simple intersecting tubes as a generic model for an IP
* http://www.slac.stanford.edu/grp/acd/ace3p.html
** http://www.gdfidl.de/

## Slide 2: wake potential basics
bunch particles are a rigid relativistic line charge of gaussian intensity distribution
at the pipe boundaries image charges move with the bunch
electromagnetic “wake” fields are generated by the image charges as they move along changing boundaries.
wake fields

## Slide 3: wake potential basics
following particles within the bunch feel the wake fields caused by the previous particles
wake potential is the accumulated voltage seen by particles as the bunch traverses the structures
bunch
longitudinal
wake potential

## Slide 4: energy loss and loss factor
bunch l(s)
longitudinal
wake potential W(s)
energy lost by the bunch to the structure is given by
with longitudinal loss factor [V/pC]:
Power loss by the beam currents I and bunch spacing t :

## Slide 5: software features
gdfidl
  FIT
  Napoly
  serial to small cluster
  loss factors
  absorbing boundaries
t3p
  FEM
  direct
  massively parallel NERSC
  not yet implemented
  absorbing boundaries
  visualization: CUBIT, Paraview

## Slide 6: mesh
radius 10 mm
angle 66 mR
length 1 m
conformal vs staircase
loss factor vs mesh size
8mm bunch length
gdfidl
cubit

## Slide 7: beam’s eye view
Notes: CUBIT animation.

## Slide 8: stability
both programs exhibit numerical instability for certain mesh and time step parameters
these runs are not considered
t3p sensitivity to internal surface meshing. Many ways to make bad triangles

## Slide 9
solver | Mesh [mm] | dt[ps] | kz | loss | Bunch length[mm] | order | solver |  | stability
t3p | 2 | 0.5 | -5.43E-05 | -5.43E-17 | 8 | 2 |  |  | stable
t3p | 2 | 0.3 | -1.02E-04 | -1.02E-16 |  | 2 |  |  | stable
t3p | 3 | 0.5 | -2.54E-04 | -2.54E-16 | 8 | 2 | CG |  | stable
t3p | 2 | 1 | -3.81E-04 | -3.81E-16 | 8 | 2 | CG |  | stable
t3p | 1 | 1 | 2.69E-04 | 2.69E-16 | 8 | 2 | CG |  | unstable
t3p | 3 | 1 | -1.93E-05 | -1.93E-17 | 8 | 2 | CG |  | stable
t3p | 4.2 | 1 | -6.49E-04 | -6.49E-16 | 8 | 2 | CG |  | stable
gdfidl | 1 | 1 | -1.10E-03 | -1.10E-15 | 8 |  |  | napoly | stable
gdfidl | 1 | 1 | -1.88E-03 | -1.88E-15 | 8 |  |  | no | stable
gdfidl | 2 | 1 | -3.35E-03 | -3.35E-15 | 8 |  |  |  | unstable
gdfidl | 2 | 2 | -7.36E-03 | -7.36E-15 | 8 |  |  | no | unstable
gdfidl | 2 | 3.6 | -5.26E-03 | -5.26E-15 | 8 |  |  | no | unstable
gdfidl | 1 | 0.9 | -7.53E-04 | -7.53E-16 | 8 | NA | NA | napoly | stable
gdfidl | 2 | 0.5 | -2.80E-03 | -2.80E-15 | 8 |  |  | napoly | unstable
gdfidl | 0.5 | 0.9 | 1.24E-03 | 1.24E-15 | 8 |  |  | napoly | stable
gdfidl | 0.5 | 0.4 | -5.50E-04 | -5.50E-16 | 8 | NA | NA |  | stable
gdfidl | 0.5 | 0.25 | -7.88E-04 | -7.88E-16 | 8 |  |  | no | stable
gdfidl | 1 | 1 | -1.75E-03 | -1.75E-15 | 8 | NA | NA |  | stable
gdfidl | 2 | 1 | -3.45E-03 | -3.45E-15 | 8 | NA | NA |  | unstable
stability

## Slide 10: longitudinal loss factors
vs mesh size
vs time

## Slide 11: discussion
comparison with Super B IR model for s = 8 mm with gdfidl:
kzSuperB~-10.8s -2.6 = -0.048 V/pC
speed up with supercomputing?
  gdfidl 0.5 mm/1ps: 1 hr 1-2 CPU
  t3p 1 mm/1ps: 9 hrs + queue time 128 nodes, 4 CPU/node
Longitudinal wake intensity for gdfidl changes with mesh size

## Slide 12: transverse wakes
implemented in gdfidl but not t3p

## Slide 13: next steps
More exhaustive study
Napoly integration
Automatic calculation of important parameters
  transverse wakes
  loss factors
Beam offset
import SuperB geometry (stl)
Bunch length studies
beam pipe size and IP angles
optimize loads. More nodes for dense mesh

## Slide 14: Conclusion
loss factor for round tubes is small compared to model of the Super B IR
Convergence is slightly better with t3p for this study
More exhaustive study needed