## Slide 1: PLASMA MODELING BY PIC SIMULATIONS
Alessio Galatà
Pandora Collaboration Meeting, LNS 16-17/12/2021

## Slide 2: COMPLETE PLASMA DESCRIPTION
ELECTROMAGNETIC SIMULATIONS
ELECTRON DYNAMICS
SELF-CONSISTENT APPROACH
IONS DYNAMICS INCLUDING CSD BUILD-UP AND CONFINING ELECTROSTATIC FIELD
MICROWAVE ABSORPTION IN AN ANISTOTROPIC AND DISPERSIVE MEDIUM
ENERGY GAIN DUE TO ECR
ENERGY REDISTRIBUTION DUE TO COLLISIONS
COLLISIONAL DIFFUSION
IONIZATION
CHARGE EXCHANGE
COLLISIONAL DIFFUSION
BUILD UP OF CSD
OVERALL CHARGE NEUTRALITY
BUILD UP OF AN ELECTROSTATIC POTENTIAL RESPONSIBLE FOR CONFINEMENT

## Slide 3: INFN SIMULATION TOOL
FULLY 3D TRACKING CODE FOR IONS AND ELECTRONS
PRECISE ELECTROMAGNETIC CALCULATIONS (COMSOL+MATLAB)
INCLUDES ELASTIC COULOMB COLLISIONS RESPONSIBLE FOR PARTICLES DIFFUSION
PLASMA FINE STRUCTURE IS AUTOMATICALLY OBTAINED
CAN CREATES DISTRIBUTION MAPS OF ANY PHYSICAL QUANTITY
ATOMIC PROCESS CAN BE EASILY IMPLEMENTED
BENCHMARKED WITH EXPERIMENTS
CAN DEMONSTRATES OBSERVED EXPRIMENTAL EVIDENCES (THE FREQUENCY TUNING EFFECT)
BUILD-UP OF CSD

## Slide 4: SELF CONSISTENT APPROACH
THE ELECTROMAGNETIC FIELD DISTRIBUTION AND THE PLASMA INFLUENCE EACH OTHER IN A CLOSED LOOP
TRACKING
Tstep=10-12 s
Tspan=40 µs
N=40000 electrons
Elastica e-e collisions included

## Slide 5: SELF CONSISTENT APPROACH
ELECTROMAGNETIC SIMULATIONS
ELECTROMAGNETIC FIELD IN ECRIS PLASMA
SOLUTION OF MAXWELL’S EQUATIONS IN COMSOL USING MUMPS DIRECT SOLVER
COLD PLASMA ANISOTROPIC TENSOR FOR THE MAGNETIZED PLASMA COMPUTED IN MATLAB
SOLUTION OF THE WAVE EQUATION WITH AN ADAPTATIVE MESH
non homogeneous dielectric permittivity Tensor depends on local electron density and magnetic field

## Slide 6: SELF CONSISTENT APPROACH
ELECTROMAGNETIC SIMULATIONS
CONSTITUTIVE RELATIONS
3D COLD PLASMA MODELING: PLASMA AS A DISPERSIVE MEDIUM WITH COLLISIONS
DERIVATION OF CONDUCTIVITY TENSOR
Random thermal motion neglected
( vφ >>vth)
COLLISION FREQUENCY ωeff ACCOUNTS FOR THE COLLISION FRICTION, MODELS THE WAVE DAMPING AND RESOLVES THE SINGULARITY OF SOME ELEMENTS OF TENSOR
where
MAXWELL’EQUATIONS

## Slide 7: SELFCONSISTENT APPROACH
ELECTROMAGNETIC SIMULATIONS
NON-SYMMETRIC 3D MAGNETOSTATIC FIELD
OFF-DIAGONAL ELEMENTS DUE TO 3D MAGNETIC FIELD
ASSUMING A NON UNIFORM MAGNETOSTATIC FIELD THE DIELECTRIC TENSOR IS:
NON-UNIFORM “LOCAL” DIELECTRIC TENSOR

## Slide 8: SELF CONSISTENT APPROACH
ELECTROMAGNETIC SIMULATIONS
14.521 GHz
14.324 GHz
ELECTROMAGNETIC FIELD AT THE END OF THE SELF-CONSISTENT LOOP
INTENSIFICATION OF THE ELECTRIC FIELD AT THE RESONANCE
32 kV/m
12 kV/m
ELECTRIC FIELD ON AXIS

## Slide 9: SELF CONSISTENT APPROACH
FORWARD DIFFERENCE METHOD
v(t+1)=v(t) + a*Tstep  x(t+1)=x(t)+ v(t+1)*Tstep
RELATIVISTIC BORIS METHOD (LEAPFROG)
EVENTUAL EXTERNAL EM FIELD
e-e COLLISIONS: LANGEVIN EUQATION
ΔvLang= v(t+1)-v(t)= - νsv(t)*Tstep+vrand
NUMERICAL IMPLEMENTATION
DIFFUSION
SLOWING DOWN
DIFFUSION COEFFICIENTS
v(t+1)=v(t) - νs*v(t)*Tstep+vrand + q*[v(t)xB]

## Slide 10: SELF CONSISTENT APPROACH
THE FOKKER PLANK EQUATION
DYNAMICAL FRICTION
PERP. DIFFUSION D⊥
PAR. DIFFUSION D//
INDEPENDENT VARIABLE

## Slide 11: SELF CONSISTENT APPROACH
REALISTIC PLASMA DESCRIPTION
THE PLASMA CONCENTRATES INSIDE THE RESONANCE SURFACE
THE PLASMOID HALO STRUCTURE IS AUTOMATICALLY FORMED
THE PLASMOID HAS AN ITS OWN STRUCTURE
DENSITY DISTRIBUTION
RADIAL DENSITY DISTRIBUTION

## Slide 12: SELF CONSISTENT APPROACH
ENERGY DISTRIBUTION
MAXIMA LOCALIZED ON THE RESONANCE SURFACE
THE DISTRIBUTION REFLECTS THAT OF THE ELECTROMAGNETIC FIELD
AVERAGE ELECTRON ENERGY
SPATIAL DISYRIBUTION OF DIFFERENT ELECTRONS POPULATIONS

## Slide 13: SELF CONSISTENT APPROACH
FREQUENCY TUNING
EVIDENCE OF THE INFLUENCE OF THE FREQUENCY ON THE PLASMA STRUCTURE
14.521 GHz
14.324 GHz

## Slide 14: SELF CONSISTENT APPROACH
FREQUENCY TUNING: DENSITY PROFILES
14.521 GHz
14.324 GHz
THE FREQUENCY INFLUENCE THE ELECTRONS DISTRIBUTION INSIDE THE PLASMOID

## Slide 15: SELF CONSISTENT APPROACH
IT IS POSSIBLE TO OBTAIN OCCUPATION MAPS IN ANY ENERGY RANGE!
THE FREQUENCY AFFECTS THE ELECTRONS DENSITY AND ENERGY DISTRIBUTIONS
ENERGY DISTRIBUTION

## Slide 16: BUILD-UP OF CSD
PRELIMINARY RESULTS
CALCULATION OF OXYGEN CSD
ELECTRON DENSITY AND ENERGY FROM PREVIOUS SIMULATIONS
EACH CHARGE Z MOVES IN APLASMA MADE OF CHARGES 1…Z-1
ONLY IONIZATIONS UP TO 5+(NO CEX)
Tspan=10*<τioniz(z)>
O1+
O5+
O2+
O3+
O4+
ECR RESONANCE
RESULTS AGREE WITH THE EXPERIMENTAL EVIDENCE OF PROGRESSIVE IONS CONCENTRATION ON AXIS
MORE DETAILS ON THE COMPLETE APPROACH GIVEN BY B. MISHRA

## Slide 17: IONS DYNAMICS
1+BEAM INJECTION: CB TECHNIQUE
E1+=1*V keV
VCB = +(V + ΔV) kV
ΔV
SIMULATION OF 1+ IONS INJECTION
PLASMA DISTRIBUTION FROM SC CALCULATIONS
COULOMB COLLISIONS THORUGH LANGEVIN EQUATION
IONIZATION WITH A MC APPROACH
LOTZ FORMULA
ECR SOURCE

## Slide 18: ECR-CB MODELING
AGREEMENT WITH EXPERIMENTS (CB @ LPSC)
Experiment
simulations
REPRODUCTION OF EFFICIENCY CURVES FOR HEAVY AND LIGHT IONS
Na
Rb

## Slide 19: ECR-CB MODELING
DYNAMICS OF THE PROCESS
BALLISTIC OF THE PROCESS
IONS INJECTION AND CAPTURE
ENERGY RELEASED IN THE PLASMA

## Slide 20: CONCLUSIONS
THE NUMERICAL CODE DEVELOPED WITHIN PANDORA IS ABLE TO DESCRIBE ELECTRONS MOTION
IS ABLE TO GIVE SPATIAL DISTRIBUTION OF RELEVANT QUANTITIES (DENSITY, ENERGY)
HAS BEEN BENCHMARKED WITH EXPERIMENTS
THE IMPLEMENTATION OF IONS’ CSD WILL GIVE A COMPLETE DESCRITPION OF THE ECR PLASMA
CAN BE CONSIDERED A PREDICTIVE TOOL FOR EVENTUAL VIRTUAL EXPERIMENTS
THE CODE IS READY FOR FUTURE UPGRADE OF THE FACILITY (CHARGE BREEDING)
NEXT STEP: HEATING BY MULTIPLE FREQUENCIES (WE ALREADY KNOW HOW TO DO IT!)

## Slide 21: THANK YOU VERY MUCH FOR YOUR ATTENTION