## Slide 1
Present and future

## Slide 2
Magnetic compression
Undulators
Acc. SC modules
Gun
< 500 m
Why ACTIS?
Requirements for MariX FEL:
High rep. rate (1 MHz)
EFEL= 2-5 keV 3 GeV linac
Linac > 1 km
Gun
2
Reduced costs
Reduced environmental impact
Bubble Arc-Compressor
Notes: To understand the reasons behind the birth of ACTIS we have to introduce a machine that was studied in the last years in Milano, the MariX FEL A light source characterized by high rep rate and high photon energy. The high rep rate desired by users requires working in CW mode and adopting superconducting cavities.
Also high photon energy was required and this implied t build a 3 GeV linear machine. whose lattice is composed of a long series of cryomodules and magnetic compression stages between them. The total length of a machine like this is higher than 1 km, MariX was designed to fit into the new University of Milan Scientific Campus ad its dimensions should not exceed 500 m.
For this reason we adopted a new geometry (*****) of the machine by folding its lattice and exploiting the long cryogenic booster to accelerate twice the beam. This can be done adopting standing wave RF in the accelerating cavities. The compression happens in a long arc compressor bubble shaped that U-turns the e-beam.
***
and enables the machine to achieve low cost

## Slide 3
Arcs in MariX
Instruments, 3 (Sep. ‘19)
PRAB, 22 (Nov. ‘19)
Gun
< 500 m
MariX
3
J. Phys.: Conf. Ser., 1569 (2020)
NO EXPERIMENTAL DEMONSTRATION
Notes: This kind of devices have been studied previously by Di Mitri who also collaborated in MariX Project. Despite the theory of arc compressors is solid, an experimental demonstration have still to be provided. The aim of the project is to demonstrate that arcs can be used as efficient magnetic compressors.

## Slide 4
Grant awarded
4
- Call N. 21188/2019
Grant start: February 2020
Notes: I proposed ACTIS at a call for young researchers and won a grant that started in February 2020 And Solaris was proposed as the perfect site to test the behavior of Arc Compressors

## Slide 5
Solaris, the animation
15 ps
1 ps
Synchrotron Radiation (SR) SX-NIR
Coherent Synchrotron Radiation (CSR) FIR-THz
Coherent Transition Radiation (CTR)
5
Notes: In fact @ Solaris a ring composed by 12 double band achromats is injected by a long linac and is able to produce MariX like e-bunches. The linac will be used to chirp the beam (introduce a longitudinal energy correlation) *** and inject it into the ring when it will be compressed during one turn of it. Beam lenght measurements will be performed with two separate detectors that have been studied … one @ the end of the linac and one after the the 12Th DBA

## Slide 6
Collaboration
6
Proposing Institution.
Strongly interested in the physics of MariX Arc Compressor.
Provides the machine, the local expertise, experience in SR detection.
Experience in arc compressors beam dynamics, and synchrotron machines.
SPARC_LAB collaboration on coherent THz radiation detection.
INFN Milano
Solaris Synchrotron
Elettra - S.T. S.C.p.a.
INFN Frascati
Notes: The ACTIS collaboration is composed by 4 main actors:

## Slide 7
Work packages and time schedule
Notes: This gantt chart was proposed 2 years ago and shows the 4 main activities of this project Thi first is a simulative activity aimed to build reliable simulations of the machine The second was dedicated to the design and procurement of the beam length detectors and their components
The third is a development activity of a code we use as optimizer of beam dynamics and will help to individuate the correct working point
The forth is the experimenal activity.
Without COVID we would have been here

## Slide 8
Pandemic legacy
8
Several activities were delayed
5 orders delayed (3 completed)
Missions completely cancelled.
Simulations become more extensive than expected.
ACTIS activities where extended up to 12/2022
Notes: But the reality is that several activities have been delayed.
2 of five material orders (for detectors and computational activity) have yet to be completed.
Missions as we know have been cancelled several times.
I underestimated the workload of the simulative activity mainly because I thought that simulations of the machine were previously available at Solaris. And I did not budget the time required for the creation of a model of the low energy machine. However, considering the special situation the experiment have been extended to all 2022.

## Slide 9
Detectors
Notes: I will now move on to description of the beam length detectors sudied in the context of this experiment

## Slide 10
Sub-THz detector
To dump
OTR
e-beam
Parabolic mirror
Schottky
diodes
Sub- THz
Collimated beam
Slit
1
2
Breadboard
Parab. Mirror + Mountings
(Thanks to E. Chiadroni)
OTR from Frascati
Schottky diodes (2 freq.)
1-axis movement
2
1
1
1
A. Curcio et al., “Beam-based sub-THz source at the CERN linac electron accelerator for research facility” PRAB 22, 020402 (2019)
Sellers:

## Slide 11
THz detector
Bending magnet
Parabolic mirror
Pyroelectric detector
Focused THz
3-axis kinematics
Band-pass filter wheel
CSR - THz
Breadboard
Parab. Mirror + kinematics + Mountings
(Thanks to E. Chiadron)
Filter Wheel
Custom THz BP filters
Pyroelectric sensor + Focusing
Assembled 3-axis movement
1
2
3
1
1
3
1
2
1
Sellers:

## Slide 12
Situation
Workstation
Mirrors & mechanics
Ad hoc THz BP filters
Design completed
Awaiting final quotation
Pyroelectric sensor
Schottky diodes (2 frequencies)
bureaucracy almost completed
Orders Requests
sent
Notes: Here we see a recap of the orders state. Everithing have been delayed by the situation but computational resources have arrived together with half of the instrumentation for the detectors. The last two orders are proceeding and I hope will be concluded in the near future.

## Slide 13
It’s real!
Notes: Here I’m showing some of the goods that have arrived: - the Multicore Workstation
Some of the kinematics for the THz detector
And the most surprising one: Lab snacks from THORLABS! Below that you can see one of the breadboards.

## Slide 14
Simulations
Notes: I will now summarize what have been done to build a machine model taking into account Space-charge

## Slide 15
Complete simulation of the full machine.
Codes
GIOTTO (Genetic Interface for OpTimizing Tracking with Optics), INFN, Milano
Integration with ASTRA
Multi objective opt.
Fast solutions explorer
Statistic mode (jitters)
ASTRA (A Space-Charge Tracking Algorithm), Desy
ELEGANT (Electron Generation And Tracking), APS, Argonne National Laboratory
Low energy beamline
High energy beamline
Developed features:
Multi-position optimization
Rotated frames handling
Calculation of dispersion
Notes: We’ll use GIOTTO, a multi objective GA developed in our group to perform Genetic a optimization of BD thanks to its ability to drive Astra.

## Slide 16
Starting point
I tried to build a reliable simulation of the Linac with ASTRA. Starting point:
An elegant lattice of the linac and one of the ring.
A simulation from elegant @ 95 MeV with an ideal input bunch.
Bunch
Notes: The “Linac Report v 7.7” considers a different gun max field (125 MV/m instead of 80, +56%).

## Slide 17
Comparison
Z [m]
σx/y [mm]
Lattice alignment after tuning quadrupoles bores radii and using original cavity field:
Notes: In fact I started from this bunch to sync. the Astra results with elegant ones

## Slide 18
Injector
RF
Thermionic RF-Gun
½ + ½ +1 cells structure in π/2 mode
Short - Solenoids
S-band TW
Beam Chopper
15 cm long stripline pair
Energy filter
120° total bending

## Slide 19
Cut after gun
E [MeV]
z [m]
E [MeV]
z [m]
z [m]
X [m]
z [m]
X [m]
Beam Cut (7.1 %)
σx = 0.910 mm
σs = 8.68 mm
εn,x = 5.2 mm mrad
<E> = 2.34 MeV, Esp = 197KeV
Q = 106 pC / 6.78 kMP
Dz [m]
I [kA]
Slice Current (500 µm bins, 54 slices)

## Slide 20
Chopper slit
Survived: 71% (75 pC)
Aperture radius: 2 mm

## Slide 21
Filter simulation
It is difficult to deal with back-propagating bunches in Astra
Development of GIOTTO and Postprocessor to better deal with rotated bunches.
We requested an ad hoc modification of ASTRA to K. Floettmann.
Notes: The beam enters oblique way

## Slide 22
Filter dynamics
Z[m]
Z[m]
ε [mm mrad]
After correction of the horizontal offset of quads and aperture.

## Slide 23
Booster size match
RF
RF
RF
RF
RF
Line: 35.12 m
UNIT 1
UNIT 2
UNIT 3
I will have to match beam spotsizes measured along the line in several points
Giotto is now capable of doing it (multi-markers optimization)
Elegant line is correctly aligned to Astra elements (Cavities and quad bores)
RF
εn,x | 3.3 mm mrad
εn,y | 3.0 mm mrad
Emittance is spoiled by high transverse dimensions.
Transverse dynamics after filter is difficult to control.
Notes: The setting obtained is the following, emittance is spoiled by chromatic aberrations induced by the big transverse dimension in part of the booster. However, I am confident that this solution can be improved with some more work.

## Slide 24
Ring model
24
Courtesy of I. Drebot
Notes: After we will move on the elengant transport into the ring. The lattice is available and here you can see its 3D-geometry created by Illya Drebot. The TL have still to be added.

## Slide 25
What Next?
Notes: To end this presentation, I would like to share what I think should be the next steps.

## Slide 26
Simulations
Final refining of linac optimization.
In elegant transport beam into the transfer line - matching to the ring DBA.
Transport into 12 DBA (1 ring turn).
Simulate beam chirp & verify compression.
26

## Slide 27
Detectors
27
Compression experiments should be performed in second half of ‘22
Wait for last two orders.
Assemble and align the detectors in Frascati. (with E. Chiadroni)
Shipment of detectors to Solaris

## Slide 28
A possible ‘22
Notes: This gantt is showing how the remaining activities could be organized in time The machine model will be completed in the first 2 months. And the WP for maximum compression will be investigate in the following two months. I suppose the apparat preparation will be completed in the first half of the here to move of the compression experiments in the first half.

## Slide 29
SOLARIS DBA

## Slide 30
Bonus material

## Slide 31: Credits
Special thanks to all the people who made and released these resources for free:
Presentation template inspired by SlidesCarnival
Icons from Flaticon

## Slide 32
Workstation
I studied an optimal configuration of the machine given funds (8 k€) and requirements (High number of CPUs) fast and big Memory and Hard Drives.
Asked 5 companies for quotations of the setup
Computer Specialist (not on mepa)
E4
DPS Informatica
Bologna Computer SNC (minor price)
Virtual Logic
AMD Ryzen Threadripper 3990x (4.0 k$)
64 Cores, 128 Thread (Clock 2.9GHz / 4.3GHz)
G-Skill 256 GB RAM DDR4 3200 MHz
Tower Workstation
After almost 6 months (Jul)
SHOULD ARRIVE BY DAYS!

## Slide 33
Thorlabs order is the first one concluded!
Wrong destination (Milan instead of LNF)
The order was scattered in 6 tranches with 6 receipts
One element was wrong
The motorized pieces had to be tested in Milan by me
Everything has been repackaged and shipped to LNF
Orders!

## Slide 34
Gun simulation
Z [m]
E
@ the cathode
Laser: Flat Top
Q = 1.5 nC / 105 MacroP
1000 K / 0.1 eV Therm. emit
σr = 0.75 mm

## Slide 35
Chopper effect
1 ns
1 ns
1 ns
1 ns
1 ns
1 ns
1 ns
1 ns
9x
9x
9x
9x
9x
9x
9x
9x
10 ns, 100 MHz
…
Selects 1 macro-bunch every 10 ns (100 MHz operation)
100 ns (10 Macro-bunch)
Gate of 100 ns
333 ps

## Slide 36
Filter test
Total charge was too high (discussion with Curcio)
Aperture radius had to be increased (asked the real value to Adriana)
The plane of the final quadrupoles intersects the trajectory (Astra modified by Klaus F.)
Space charge needs a very big 3-d mesh (beam is long and dispersion enlarges hor. dimension a lot). Slow down
Beam centroid strongly off-center when the beam is dispersed leading to offsets in the quads and aperture (other dispersion).
When dispersion closed the beam divergence was too big for safe travel through quad bore.
Reference orbit
Slit
Why took so long? (5 months intead of 2)
Z [m]
X [m]
Start
Solenoid
Quads
Bends

## Slide 37
Cavity studies
PSI TW Cavity
Freq: S-band 2998.55 MHz
Cell L: 99.959 mm
Total: 156 cells - 5.2 m
LIL TW Cavity
Freq: S-band 2998.55 MHz
Cell L: 99.981 mm
Total: 156 cells - 5.2 m
Z [m]
L-Field [A.U.]