## Slide 1
霍迪 Huo = Dieter HH Hoffmann on behalf of p11B project team of Xi’An Jiaotong University, School of Physics, Xi’An, China PI: Yongtao Zhao Hebei Key Laboratory of Compact Fusion, Langfang 065001, China
ENN Science and Technology Development Co., Ltd., Langfang 065001, China CSO: Martin Peng Institute of Modern Physics, CAS, Lanzhou, China PI: Rui Cheng Shanghai Inst. Of Applied Nucl. Phys., Shanghai, China PI: Guoqiang Zhang
Proton Boron Fusion with respect to Accelerator Driven High Energy Density Science
2nd International Workshop onProton-Boron Fusion Catania 2022
Notes: Introductory remarks about the collaboration

## Slide 2
A few remarks on my opinion on fusion energy in general and more so on p11 B Fusion

## Slide 3
Motivation and Introductory Remarks: Magnetic Confinement Fusion
May 28, 2021: The Experimental Advanced Superconducting Tokamak achieved a world record for Temperature and confinement time
Another remarkable achievement (59 MJ)is reported
From JET in a DT experiment in 2021
Notes: Fusion is making progress, however slow. My remark and personal opinion is that Fusion will not help to solve any current energy and environmental problems. It is for the future and in my mind not in 10 or 40 years. Kstar in Korea similar values

## Slide 4
Courtesy of:Laszlo Cszernai, 2019
2021 fusion energy 1.8 MJ
Notes: Very little of the original 422 MJ arrives at the target

## Slide 5
What is the reason for this discrepancy ?
Probably a number of reasons among them:
Insufficient knowledge of Laser Plasma Interaction Hydrodynamics in radiation dominated regime (needs relativistic corrections) Underestimation of role of instabilities (fuel mix) Energy deposition of -particles in degenerate matter Non-optimum hohlraum configuration
From the scientific and technology point of view the NIF program is a success story

## Slide 6
Challenges of p11B Fusion
11B(p,α)2α Reaction

## Slide 7
Programme
Introductory remarks
Understanding the abundance of 11B p11B Fusion Experiments a) at accelerators b) using high power laser radiation Conclusion and Outlook
Notes: Probable topics for the talk

## Slide 8
兰州重离子加速器
国家实验室
（1991年国家计委批准成立）
IMP Lanzhou
Institute of Applied Nuclear Physics
HIAF
Hefei Synchrotron
ENN Langfang

## Slide 9
Abundence of Elements in the solar system
Review of Mod. Phys 93.015002

## Slide 10
Simulated r-abundance normalized to solar
B 5.101980e-09 3.133204e-11
Ba 3.304903e-10
R-process simulation for Boron by Bowen Jiang (GSI) 28.07.2021

## Slide 12: EXL-50 @ ENN Langfang
Project started from October 2018.
First plasma achieved in August 2019.

## Slide 13
EXL-50 solenoid-free startup experiment
Fast camera 1280X800
ECRH heating：2.45GHz: 5~8kW，28GHz: 35kW
Ip (kA)
ne (1017m-2)
solenoid-free current drive: >1.2A/W

## Slide 14
Optimal Fuel Mixture
The large bremsstrahlung radiation is mainly caused by the high effective charge number Zeff
An effective way to reduce Zeff is to adjust the fuel mix ratio :
J.R. Roth ‘87

## Slide 15
Number Reduction Reduction in T Gain
0.5 0.5 0.25 770
0.6 0.4 0.24 4% 20% 739
0,7 0,3 0.21 16 % 40% 647
0.8 0.2 0.16 36% 60% 493
Applied to of p11B fuel mixture we obtain a reduction from 2,4
Notes: With the same procedure applied to P11B the effective Z would vary from

## Slide 16
The optimal fuel mixture can be obtained by minimizing the following ratio against x and T
Optimal fuel mixture:
Relativistic corrections impose constraint on temperature
p-11B plasma can be ignited with the new cross section
Optimal Fuel Mixture
McNally ’82; Rider ’95 & ‘97; Nevins ‘98

## Slide 17
Caveats
Relativistic correction becomes inaccurate at high temperature
  Overestimated the radiation power by a factor of 2~3
  Fully relativistic bremsstrahlung is needed for high temperature
Impurity radiation, controlling of 4He ash
McNally ’82; Rider ’95 & ‘97;
Nevins ’98; Dawson ‘81

## Slide 18
1、 技术研发进展与过程改进（硼靶制备项目）
18
2.氢硼靶制备：
  完成新的CVD平台搭建：真空系统改造和维修、气体系统管路焊接和安装、控制系统配置
  完成新的CVD平台性能初步测试
CVD实验平台
原理图
抽气系统
真空腔
电极

## Slide 20
1.纳米厚度硼靶制备：
完成500纳米厚硼靶制备技术开发
均匀的硼膜
脱膜
捞到靶托上的硼膜
硼膜
1、主要工作进展（硼靶制备项目）
Uniform distributed Boron film
Take off the film
Boron film on the target holder

## Slide 21
Notes: Accelerator in China

## Slide 22
The Fairy Tale of 3 Alphas at 2.9 MeV

## Slide 23
5.8 MeV
2,9 MeV
The p11B Fusion Reaction at
Notes: There used to be a misconception about the 3 alpha particles. One alpha particle is at 5.8 MeV called Alpha 1 the 2 other originate from a 2 particle decay of Be and they share the 2.9 statistically, which gives rise to a continuum in the spectrum

## Slide 24
Proton-Boron Tumor Therapy

## Slide 26
p(11B,3α)12 C Experiment Inst. Modern Physics CAS, Lanzhou, China
Date | Energy | Current | Detector Angle | Remarks
7月6日 | 160keV | 280nA | 0 | High count rate 13 s
7月7日 | 170keV | 36nA | 65 | Low count rate for 2 h
P->

## Slide 27
Measured Alpha Spectrum at 560 keV Proton Energy
Measurement at SINAS (Shanghai) by ENN-XJTU- IMP collaboration
Notes: Measured spectrum in Shanghai at 560 keV proton energy.. Alpha 0 a rare event also visible

## Slide 29
Experiments at IMP Lanzhou at very low proton energy (160 keV regime)
CR 39 tracks

## Slide 31
Plasma generation from laser heated Hohlraum for experiments at the XG-III laser facility of the Laser Fusion Research Center in Mianyang we plan to use this set-up for opacity measurements also
Bubo Ma et al. with Yongtao Zhao accepted for publication by Astrophysical Journal (July 2020
Notes: The target was used to simulate a special white dwarf atmosphere. In my mind it is also perfectly suited for opacity measurement that we need for Boron atmosphere

## Slide 32
Laser: ps-120J, 0.8ps, 10μm;
ns-150J, 2ns, 100μm, 532nm;
ns ahead of ps by 8ns
Target: 20% B-CHO foam；density- 2mg/cc,
diameter-1mm，length-1mm
10μm Cu solid foil for laser acc.
ps laser accelerates intense proton beam (TNSA)
ns laser heats the boron-CHO foam
XGIII experimental setup and target design

## Slide 33
Experimental Results and Analysis
Energy spectra of α particles from CR39 with Al foils (5-40μm)

## Slide 34
alpha yield normalized by beam intensity for plasma and cold foam

## Slide 35
The α yield from plasma is generally 1~2 orders higher than that from the cold foam.
Nonlinear increase of alpha particle yield with proton beam intensity
Summary and Outlook
Alpha spectra depend on proton energy
Alpha yield depends on Hydrogen Boron ratio of the target
All of this needs further verification

## Slide 36
To Do List:
1:Remeasure the fusion cross section up to about 10 MeV 2: If possible measure under plasma conditions
3: Study the influence of magnetic fields 4:Opacity measurements on p11B plasma
5: Experimental and theoretical data on EOS
6: make better Boron Targets and Boron Hydrogen Targets

## Slide 37
Problems for p11B energy production
p11B in the Inertial Confinement scheme needs extremely high compression to about
( Weaver et al. LLNL 1973)
It will be extremely difficult to produce a Boron
pellet with the required surface roughness
We need an efficient driver to do the compression work
Notes: Due to my experience with Boron targets it needs a huge effeort to produce Boron inertial fusion targets with the required surface roughness. It seems to be a technical problem but is probably not easy to achieve