## Slide 1: High sensitivity Thomson spectrometry in experiments of laser-driven low-rate neutron-less fusion reactions
M. Scisciò1, G. Di Giorgio1, P.L. Andreoli1, M. Cipriani1, G. Cristofari1, R. De Angelis1, M. Salvadori1, G. A. P. Cirrone2, L. Giuffrida3, D. Margarone3,4, G. Milluzzo2, G. Petringa2 & F. Consoli1
1ENEA, Fusion and Nuclear Safety Department - C. R. Frascati, 00044 Frascati, Italy
2Laboratori Nazionali del Sud, Istituto Nazionale di Fisica Nucleare (LNS-INFN), 95125 Catania, Italy
3ELI Beamlines, Institute of Physics of the Czech Academy of Sciences, 25241 Dolni Brezany, Czech Republic
4Queen's University Belfast, School of Mathematics and Physics, BT7 1NN Belfast, United Kingdom
2nd International Workshop on Proton-Boron Fusion
Sept. 5-8, 2022
Catania, Italy

## Slide 2: 11B(p,α)2α fusion reaction
11B(p,α)2α nuclear fusion reaction: MeV
No/few neutrons are produced
No need for radioactive reactant
Energetic alpha particles are obtained
Not only for energy production:
interest for both medical applications and astrophysics research
Fusion reaction initiated by high energy lasers,
two main schemes are adopted:
“In target”
“pitcher-catcher”
Kimura et al., Phys. Rev E 79, 038401 (2009)
Nuclear fusion rates are determined by the produced alphas:
needs for an effective way for the detection and characterization of the produced alpha particles.
F. Consoli et al. Front. Phys. 8, (2020) 561492
P. Cirrone et al. Sci. Rep. 8 (2018) 1141

## Slide 3: The detection of α-particles is a challenging task
F. Consoli et al. Front. Phys. 8, (2020) 561492
Thomson spectrometers (TS)
■ Ion discrimination according to mass-to-charge ratio
■ Spectrum reconstruction
■ α trace overlaps with fully stripped ions (C6+, N7+…)
■ Sensitive to EMP and ionizing radiation noise
Time Of Flight (TOF)
■ Provide prompt information on velocity distribution
■ Spectrum reconstruction
■ Does not allow for particle discrimination
■ Sensitive to EMP noise
Solid State Nuclear Track Detector (SSNTD)
■ Ion discrimination
■ ■ Spectrum reconstruction is challenging
■ Strong background
Typical diagnostics for p-B experiments:
EMP radiation
ionizing radiation
particle radiation

## Slide 4: Thomson spectrometer working principle
M. Scisciò et al. J. Inst. 17, (2022) C01055
Each parabolic trace corresponds to one ratio.
: their contribution to the retrieved signal is on this parabola, together with all the other ions with the same mass-to-charge ration, e.g. C+6 ions.
Typical traces generated by the particles on the detector
with
y

## Slide 5: The TS designed at ENEA - Frascati
Internal (external) pin-hole diameter | 0.35 mm (2 mm)
Dipole length L | 25 mm
Dipole gap | 5 mm
Magnetic field B | 0.405 T
Max. electric field E | 1.56 MV/m
Drift space LD | 197 mm
Deflecting assembly
Two-pinhole assembly
External case
Adjustment supports
Detector and laser alignment
High-voltage connectors
Compact dimensions for in-chamber use
EMP shielding allows positioning close to the target
Medium size pinhole system for high sensitivity
Optimized for proton energies up to 10 MeV
Can be equipped with both IPs or CR-39
G. Di Giorgio et al., J.Inst. 15, C10013 (2020)
F. Consoli et al., J.Inst. 11, C05010 (2016)

## Slide 6: PALS experimental campaign: setup
Experimental setup at the PALS facility: “in-target” scheme
Laser parameters:
Wavelength λ = 1315 nm
Pulse duration 350 ps
Pulse energy between 600 J and 700 J Intensity on target
The maximum voltage applied to the electrodes of the TS was of ΔV = 4 kV (resulting in an electric field E ≈ 0.78 MV/m).
Target: 10 µm thick plastic foil, doped with 11B.
Detector on TS: BAS-TR type Imaging Plate with no filter on the sensitive surface.
Device at close proximity to the target, inside the target chamber.
External lead slit

## Slide 7: PALS experimental campaign: IP scan
2.34
1.72
1.31
1.04
0.84
0.70
1.24
0.98
0.80
0.66
0.56
0.48
0.41
Obtained Imaging Plate scan:
No digital enhancing used!
Comparison:
Obtained traces when no special shielding against EMP and other background noise is used. Here, the TS was placed at 1.5 m from the target, outside the chamber.
L. Giuffrida et al., Physical Review E 101, 013204 (2020)
IP type: BAS TR (no filter)
Shot #56027 :
Protons = 1.24 MeV
Alphas = 2.34 MeV
Laser energy 661 J

## Slide 8: Analysis on the obtained signal and background noise level
Signal generated by the particles:
Background :
Proton energy [MeV]
Evaluation of the signal (black-level of the retrieved trace) and background (black-level adjacent to the trace), as a function of the particle energy, according to

## Slide 9: Analysis on the obtained signal and background noise level
Proton energy [MeV]
Integrated PSL values
Proton energy [MeV]
Signal-to-background-ratio for trace (protons)
Energy range 0.1-0.7 MeV : SBR>100
Up to energy 1.1 MeV : SBR>10
At = 1.2 MeV : SBR>4

## Slide 10: Analysis on the obtained signal and background noise level
Integrated PSL values
Alpha particles energy [MeV]
Alpha particles energy [MeV]
Signal-to-background-ratio for trace (in case of signal generated by particles)
Energy range 0.2-0.5 MeV : SBR>2
From 0.5 MeV up to = 2.4 MeV : SBR>3

## Slide 11: Obtained spectrum for the trace
Calibration data for TR IPs are available only for energies above 350 keV (red)
[T. Bonnet et al., Review of Scientific Instruments 84, 013508 (2012)]
For lower energies (black), a linear response was used.
Particle spectrum
Used calibration curve for TR type IPs

## Slide 12: Obtained spectrum for the trace
Case where the signal is generated by particles only.
Calibration of TR type IPs available only for >800 keV: C. G. Freeman et al., Review of Scientific Instrument 79, 073301 (2011).
For lower energies a linear response was used.
Case where the signal is generated by C+6 ions only.
Calibration of TR type IPs is a polynomial fit of exp. data in D. Doria et al., Review of Scientific Instruments 86, 123302 (2015)

## Slide 13: Obtained spectrum for the trace
Case where the signal is generated by particles only.
Calibration of TR type IPs available only for >800 keV: C. G. Freeman et al., Review of Scientific Instrument 79, 073301 (2011).
For lower energies a linear response was used.
Case where the signal is generated by C+6 ions only.
Calibration of TR type IPs is a polynomial fit of exp. data in D. Doria et al., Review of Scientific Instruments 86, 123302 (2015)
This is for particle detected outside plasma. What was inside?
This is for particle detected outside plasma. What was inside?

## Slide 14: Obtained spectra for a pair of similar shots
Comparison of two shots with the same exp. setup.
Shot #56025 -
Shot #56027 -
Spectra for the trace (protons)
Spectra for the trace (alphas)
Spectra for the trace (C+6 ions)

## Slide 15: Summary and remarks
The ENEA Thomson Spectrometer successfully implemented in a p-B fusion experiment:
Implementation at close distance to the target (d=367 mm)
Good EMP shielding (non oscillating traces)
Signal-to-background ration proves good shielding against ionizing radiation (outside&inside) and particle noise
Analysis of the and traces and evaluation of the obtained particle spectra
Results and analysis submitted to Laser and Particle Beams special issue Advances In the Study of Laser-Driven Proton-Boron Fusion
Open / work-in-progress issues:
Imaging plate calibration is necessary for particles at low energies
The distinction of -particles from other ions requires additional techniques (e.g. CR-39 detectors, differential filtering system)

## Slide 16: Acknoledgment
This work has been carried out within the framework of the EUROfusion Consortium, funded by the European Union via the Euratom Research and Training Programme (Grant Agreement No 101052200 — EUROfusion). Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the European Union or the European Commission. Neither the European Union nor the European Commission can be held responsible for them. The involved teams have operated within the framework of the Enabling Research Project: ENR-IFE.01.CEA “Advancing shock ignition for direct-drive inertial fusion”
.

## Slide 17
Thank you
for your attention!
Massimiliano Scisciò - massimiliano.sciscio@enea.it
Fabrizio Consoli - fabrizio.consoli@enea.it