## Slide 1
WG-3: Microdosimetry
PoliMi, LNL, LNS, TIFPA
4th Annual NEPTUNE Collaboration Meeting
9th September 2022
NEPTUNE
Nuclear process-driven Enhancement of Proton
Therapy UNrav Eled

## Slide 2
Detectors
Mini-TEPC (LNL)
Silicon Telescope (PoliMi)
MicroPlus probe (LNS)
Silicon Carbide Detector (LNS)
Measurements of microdosimetric spectra across the proton Bragg peak with detectors with tissue-equivalent (TE) walls/converters unloaded and loaded with boron.
Proton irradiations performed at LNS (CATANA) and TIFPA.

## Slide 3
Experimental set-up at CATANA
62 MeV modulated proton therapy beam: range of 2.9 cm and modulation width of 1.1 cm
Measurements performed at different positions along the Spread‒Out Bragg Peak, corresponding to positions of clinical relevance (entrance, proximal, central, and distal end of the SOBP)

## Slide 4
Reproducibility tests with mini-TEPC
Stability of the sealed mini-TEPC checked at 6 positions
Light blue: first shift of measurements
Red: second shift four months later
No significant difference detected

## Slide 5
Reproducibility tests with mini-TEPC
yD models total LET-dose
Three measurements campaigns
Full SOPBP characterization

## Slide 6
Results: comparison between mini-TEPC and silicon telescope
Mini-TEPC
Silicon telescope

## Slide 7
Results: comparison between mini-TEPC and silicon telescope

## Slide 8
Results: comparison between mini-TEPC and FWT LET1/2
Mini-TEPC
(LNL)
FWT LET1/2
(TIFPA)

## Slide 9
Results: comparison between mini-TEPC and FWT LET1/2
Mini-TEPC
FWT LET1/2
PILE UP !

## Slide 10
Results: MicroPlus probe

## Slide 11
Results: Silicon Carbide Detector
Preliminary results

## Slide 12
Results: comparison between sim and exp
Experimental dose (blue dotted line) and simulated (blue line) is reported. The simulated fluence of primary protons corresponds to the black dotted lines. Circles refer to the yD obtained with the MicroPlus probe, squares to the measurements performed with the mini-TEPC and triangles with the Silicon telescope. Simulated LET is reported as well: green points corresponds to the LET-dose total, pink line to the LET-track primary and green line to the LET-dose primary.

## Slide 13
Boron targets for solid state microdosimeters
Preliminary PMMA foils containing boron have been designed and produced. The converter is produced by depositing a thin layer (tens of 𝜇m) of boron carbide (B4C) on a 50 𝜇m PMMA foil through a chemical procedure.
The thickness of the deposited boron has been optimized for minimizing the yield of alpha particles undergoing self-absorption inside the converter (in order to maximize the yield of detectable alpha particles).
Other converters employing natural and enriched (in B-11) boric acid are being studied and will be fabricated in the next months.

## Slide 14
Preliminary measurements at CATANA with natural Boron

## Slide 15
Preliminary measurements at CATANA with natural Boron
Without boron
Silicon telescope
With boron

## Slide 16
New boric acid targets enriched in B-10 or B-11 @CATANA
#85 gafchromic films for reproducing 28.05 mm in water
Boric (99 % B-11 or B-10) acid (H3BO3) target

## Slide 17
Scatter plots
No B
B-10
B-11

## Slide 18
Energy spectra

## Slide 19
Microdosimetric spectra
Detected alpha per primary proton: 1.0e-3 (B-10) and 1.2e-4 (B-11)
Contribution to the dose: 1.3 % (B-10) and 0.12 % (B-11)

## Slide 20
Microdosimetric spectra of alpha particles
Detected alpha per primary proton:
7.6⋅10-5 ± 23.6% without any converter
1.0⋅10-3 ± 9.8% for 10B
1.2⋅10-4 ± 7.0% for 11B
Dose-mean lineal energies:
120.4 keV/μm ± 23.0% for 10B
122.2 keV/μm ± 13.0% for 11B

## Slide 21
Development of new boron targets
Pulsed Laser Deposition Technique (PLD)
Micro- and Nanostructured Materials Lab (NanoLab) @ PoliMi
Optimization via FLUKA simulations

## Slide 22
Monolithic silicon telescope
Scatter plots for particle discrimination
Measurements @INFN-LNL – CN accelerator
Monoenergetic proton beams: 2 and 2.5 MeV
5 μm Boron layer on a 55 μm PMMA substrate
High Vacuum conditions

## Slide 23
Preliminary results @INFN-LNL – CN accelerator
2 MeV protons
2.5 MeVprotons

## Slide 24
Measurements @INFN-LNL – CN accelerator
Experimental
Simulated (FLUKA)
2 MeV
protons
Threshold
alpha/ protons
3.92 x
alpha/ protons
1.41 x

## Slide 25
Measurements @INFN-LNL – CN accelerator
Second set-up: detector out-of-field (60°)
Collimated proton beam
5 μm Boron layer on a 55 μm PMMA substrate
High Vacuum conditions
Faraday cup

## Slide 26
Measurements @INFN-LNL – CN accelerator
2 MeV protons

## Slide 27
Measurements @INFN-LNL – CN accelerator
Preliminary result: new boron target

## Slide 28
Test of Boron loaded TEPC @PoliMi
Avalanche-confinement TEPC:
Simulated site sizes in the range 1 μm - 25 nm
Different TE walls loaded/unloaded with Boron
Microdosimetry at nanometric level
Test inside the thermal neutron facility @PoliMi

## Slide 29
Test of Boron loaded TEPC @PoliMi
300 nm
50 nm
Peak from the Boron Neutron Capture reaction

## Slide 30
Test of Boron loaded TEPC @LNL
Simulated site sizes 1 μm
TE walls loaded/unloaded with Boron
bismuth window
MUNES neutron field at CN-LNL
no 10B
100 ppm 10B
Caratterizzato il rivelatore e la metodologia per discriminare le diverse componenti.

## Slide 31
Peak from the Boron Neutron Capture reaction
Test of Boron loaded TEPC @LNL

## Slide 32
Test of Boron loaded TEPC @LNL
Dose fractions
Le alpha sono ben visibili oltre la proton-edge a ~ 150 keV/mm

## Slide 33
LNS Activity: Current state
Silicon (MicroPlus probe)
Experimental runs w/o boron:
  60 MeV proton beam (CATANA)
  30 MeV proton beam (REZ)
Experimental runs with alpha:
  60 AMeV 4He beam (LNS)
To do:
  Experimental shifts in Trento to evaluate the response of the silicon detector with and without targets of 19F and 11B
  Experimental shift @LNL to check the detector calibration
Silicon Carbide:
A prototype was realized and electrically tested;
The detector was tested with 60 MeV (CATANA) and 30 MeV (REZ) of proton beam
The detector was entirely simulated with Geant4.
The detector response was compared with the Silicon (MicroPlus probe)

## Slide 34
Experimental run @Ústav Jaderné Hyziky av ČR (CZ)
30 MeV proton beam w/o boron

## Slide 35
Attività di microdosimetria con TEPCs – Laboratori Nazionali di Legnaro
Nell’ambito del progetto R4I 4MiCA abbiamo potuto costruire nuovi rivelatori. Uno di questi ha le pareti di plastica A150 miscelata a 500 ppm di Boro naturale (400 ppm di Boro11).
Sono state fatte due campagne di misura a Trento (Febbraio e Maggio 2022), sul fascio da 70 MeV, utilizzando due rivelatori uguali, uno con pareti borate e l’altro con pareti non borate.

## Slide 36: Risultati: misure sul fascio da 70 MeV senza e con Boro
Con ciascun rivelatore sono state effettuate diverse misure, una con il rivelatore nudo e una dopo spessori variabili di acqua solida (precisamente 1 cm, 2 cm, 2.5 cm, 3.15 cm). Non si nota differenza significativa negli spettri.

## Slide 37: Risultati: misure sul fascio da 70 MeV senza e con Boro
Senza Boro
Con Boro
Con ciascun rivelatore sono state effettuate diverse misure, una con il rivelatore nudo e una dopo spessori variabili di acqua solida (precisamente 1 cm, 2 cm, 2.5 cm, 3.15 cm). Non si nota differenza significativa negli spettri.

## Slide 38
Risultati: fascio da 70 MeV, senza e con Boro
Nessuno spessore
+ 1 cm
La visualizzazione doppio log evidenzia i rari eventi ad alti valori di y.

## Slide 39
Risultati: fascio da 70 MeV, senza e con Boro
+ 2 cm
+ 2.5 cm
La visualizzazione doppio log evidenzia i rari eventi ad alti valori di y.

## Slide 40
Risultati: fascio da 70 MeV, senza e con Boro
+ 3.15 cm
La visualizzazione doppio log evidenzia i rari eventi ad alti valori di y.
p-edge
La probabilità di eventi alto y è di
(1.0±0.3)×10-5 in assenza di Boro
(0.8±0.1)×10-5 nel rivelatore con Boro.
Differenze non statisticamente significative

## Slide 41: Additional slides

## Slide 42
Detectors
Mini-TEPC (LNL)
New mini‒TEPC developed at LNL (same design as the previous TEPC published earlier), but with modified gas and vacuum ducts to improve the counter cleaning from plastic degassing as well as washing and gas filling procedures. It operates in gas‒steady modality
Cylindrical sensitive volume 0.9 mm (diameter and height)
0.35 mm‒thick A‒150‒cathode wall
0.35 mm Rexolite® insulator
0.2 mm‒thick titanium sleeve
(total external diameter of 2.7 mm)
Silicon Telescope (PoliMi)
∆E stage (about 2 μm in thickness) acts as a solid state microdosimeter and E residual-energy stage (500 μm in thickness) gives information on the energy and the type of the impinging particle
The type of the impinging particle is discriminated through a scatter-plot
An optimized event-by-event correction is performed by measuring the residual energy deposited in the E-stage

## Slide 43
Detectors
It contains several microdosimeter detectors with different-sized sensitive volumes (SVs) that can be selected independently
It is fabricated using silicon-on-insulator wafers with 10 µm thick silicon active volume.
Each microdosimeter detector is fabricated using 3D-mesa technology and has a silicon substrate of area 0.6 mm x 0.8 mm with a single, silicon 3D SV of rectangular-parallelepiped shape on top of silicon oxide.
MicroPlus probe (LNS)
The Silicon detectors used was designed by IMM-INFN and manufactured by ST-Microelectronics (STM) in Catania
The detector has a 0.3 μm thick p-layer and a 10 μm thick n-layer. The detector has an active area of about 10 x 10 mm2, and was mounted on PCB board designed to be housed in an aluminum box.
Silicon Carbide Detector (LNS)

## Slide 44
Monte Carlo simulation
The CATANA transport beamline is simulated with Hadrontherapy, a free and open source application currently available inside the public release of the Geant4 Monte Carlo code.
A completely new module was used to calculate the track‒averaged LETT and the dose‒averaged LETD of the specific modulated Bragg peak used. To calculate LETT and LETD at a given water depth, the track-mean and the dose-mean LET values of each particle were weighted with their relative frequency and dose contribution, respectively. The following equations were used:
where Ld(z) is the LETD at the depth z in the water phantom, Selj is the electronic stopping power of the particle j of energy E and 𝛗Ej(z) is the number of particles of type j that have energy E at depth z.

## Slide 45
Depth-dose profile at CATANA

## Slide 47
Measurements @INFN-LNL – CN accelerator
Alpha spectrum
alpha/ protons
exiting the target
≈ 6.0 x