## Slide 1: Impact of the beam rate at CNAO
Marco Bon - 31/05/2022
Marco Bon

## Slide 2: Introduction
The aim of this presentation is to show the impact of the beam rate on the Z-ID and on the trigger efficiency using data taken from CNAO in November 2021
Beam: Carbon ions with
1) E=200 Mev/N, Target: C, C2H4, Events (for cross section measurement)
2) E=(150, 300, 400)MeV/N, Target: C, Events (for calibration purposes)
Marco Bon

## Slide 3: Charge in the central bars
Marco Bon
In the central bars (8-9-10) we don’t see clearly the expected peaks
200 MeV/u — All run
DATA
DATA
DATA

## Slide 4: Charge in bars 7-11
For the “lateral” bars we don’t have the same effect
200MeV/N — All runs
Marco Bon
DATA
DATA

## Slide 5: Beam rate
In order to understand the problem we studied the rate.
200 MeV/u — All run
Marco Bon
Values of the order of MHz
1st NIGHT
E (MeV/u) | Runs | Trigger | Mean beam rate (kHz)
200 | 751-865 | MB | 20.1
200 | 1000-1093 | MB | 23.8
200 | 1100-1446 | MB+frag | 67.9
2nd NIGHT
200 | 2000-2091 | MB | 18.6
200 | 2100-2470 | MB | 18.4
200 | 2500-2959 | MB | 13.7
200 | 3300-3969 | MB+frag | 95.8
200 | 4000-4226 | MB+frag | 65.3
3rd NIGHT
200 | 10000-10035 | MB+frag | 54.9
200 | 10900-11069 | MB | 15.9
150 | 10650-10893 | MB | 93.2
150 | 10200-10624 | MB+frag | 175
300 | 11100-11231 | MB | 57.6
300 | 9660-9859 | MB+frag | 165
400 | 11300-11475 | MB | 21.5
400 | 9200-9957 | MB+frag | 52.1

## Slide 6: Pile-up estimation
Because of this high rate we tried to quantify the pile up with the start counter
Marco Bon
1st NIGHT
E (MeV/u) | Runs | Trigger | Mean beam rate (kHz)
200 | 751-865 | MB | 20.1
200 | 1000-1093 | MB | 23.8
200 | 1100-1446 | MB+frag | 67.9
2nd NIGHT
200 | 2000-2091 | MB | 18.6
200 | 2100-2470 | MB | 18.4
200 | 2500-2959 | MB | 13.7
200 | 3300-3969 | MB+frag | 95.8
200 | 4000-4226 | MB+frag | 65.3
3rd NIGHT
200 | 10000-10035 | MB+frag | 54.9
200 | 10900-11069 | MB | 15.9
Pile-up (%)
0.49
0.50
1.62
0.48
0.50
0.42
2.27
1.71
1.71
0.46
2C
1C
3C
…
t (ns)
Amplitude (mV)
ST waveform
STCharge

## Slide 7: Pile-up estimation
The fraction of pile up events depends on the beam rate and it varies between 0.4% and 2.5% within all the acquired runs
The estimated pile-up is not enough to justify the absence of peaks in the central bars
Marco Bon

## Slide 8: TW Amplitude vs rate for the central bars
Marco Bon
At high rates the TW is not able to correctly compute the charge
200 MeV/u — All runs
Beam rate(kHz)
Amp chA (mV)
ZOOM

## Slide 9: TW Amplitude vs rate for the lateral bars
Marco Bon
For the “lateral” bars we don’t have the same effect
200 MeV/u — All runs

## Slide 10: Energy loss calibration
Marco Bon
DATA
MC
Calibration used for GSI data does not fit well on CNAO data. In order to calibrate the charge with the Eloss_MC for all bars separately Birks law was used.
For the central bars, most affected by the high beam rate, to make the peaks more visible, a cut was placed on the charge distributions, imposing that Beam_Rate<1kHz

## Slide 11: Energy loss calibration
Marco Bon
The calibration works quite well. Here is reported the Eloss of the whole layer 1 after calibration compared with the MC
200 MeV/u - All runs

## Slide 12: Introducing the rate into MC simulation
In order to parameterize the Eloss response to the beam rate, we did a smearing of the MC based on experimental data.
To do this, we studied the average Carbon peak value of the central bars as a function of the beam rate.
Marco Bon
ProfileX( )
DATA

## Slide 13: Introducing the rate into MC simulation
Marco Bon
200 MeV/u — Only MB

## Slide 14: Z identification
In order to apply the Z reconstruction algorithm we have to find the Bethe-Bloch parameters
Only the primary fragments produced in the interaction of the beam with the TG are considered.
Marco Bon
MC

## Slide 15: Z identification - no rate
Marco Bon
We studied the performance of Z-ID on the reconstructed hit with only the experimental resolution (NO RATE)

## Slide 16: Z identification - rate
Marco Bon
13kHz
96kHz
55kHz
At 13kHz the rate effect on the reconstructed hit is not too evident

## Slide 17: Trigger efficiencies
Marco Bon
We also studied the impact of the beam rate on trigger efficiency using the calibrated and reconstructed data
number of points acquired with the MB trigger that would have fired the fragmentation trigger.
number of points acquired with the MB trigger

## Slide 18: Trigger efficiencies -13 kHz
Marco Bon
1kHz cut
We focused our attention on the run in which the mean beam rate was 13kHz
For boron, the results are different from those of Lorenzo Marini's work, but taking the events below 1kHz, even with reconstruction (point), we get the same values.
200 MeV/u — run (2500-2959)
DATA
DATA

## Slide 19: Conclusions
Marco Bon
The fraction of pile up events is small (0.4%-2.5%)
We introduced in the MC simulation the effect of the beam rate to study
1. the performance of the Z-ID on the reconstructed hit
2. the trigger efficiency
We are trying to apply the efficincies to fragmentation data to recover the MB ones. At the moment there are some discrepances that we are checking…
At 13kHz the rate effect is not too evident
At 13kHz for boron fragments the trigger efficiency varies from 0.85 to 0.99 with a cut on the beam rate of 1kHz

## Slide 21: Conclusions
Marco Bon
The fraction of pile up events is small (0.4%-2.5%)
We introduced in the MC simulation the effect of the beam rate to study
We studied the performance of Z-ID on the reconstructed hit. With a mean beam rate of 13kHz the (VUOI CHE QUANTIFICO QUANTO PERDIAMO IN EFFICIENZA DI RICOSTRUZIONE PER I SINGOLI FRAMMENTI a 13khZ? ACCENNO QUALCOSA SUI 55 E 96 KHZ?) rate effect is not too evident
We studied the impact of the beam rate on trigger efficiency. For a run in which the mean beam rate is 13 kHz, for boron fragments the trigger efficiency varies from 0.85 to 0.99 with a cut on the beam rate of 1kHz. It is important to understand this behavior since the value of the trigger efficiency actively participates in the computation of the cross section.

## Slide 22: Spill structure
Marco Bon
Rate MB (Hz)
t (s)
Even within the same run, the beam rate has many fluctuations
Spill structure

## Slide 23: ST summed signal
In order to tag the pile up events, we used the ST
The ST has 8 channels. To compute the charge, the summed signal is integrated
The mean and standard deviation of the amplitudes of the first part of the signal were taken in order to remove the positive overshoot induced by a high pass filter.
The signal integral is computed excluding the samples with
Marco Bon
t (ns)
Amplitude (mV)

## Slide 24: Pile-up estimation -1
E= 150MeV/N (MB)
With the ST we are able to tag the pile-up events.
The fraction of pile up events depends on the beam rate and it varies between 0.5% and 3% within all the acquired runs
Marco Bon
2C
1C
3C
…
After removing the positive overshoot

## Slide 25: Selection on beam rate
Since we knew of the presence of high rate, we tried to put a cut directly on the beam rate
150MeV/N (MB)
Mean beam rate= 93kHz
We have normalized the distributions to see how the shape changes
By applying the cuts we’ve lost:
1) 1kHz->96% of the events
2) 10kHz->46% of the events
3) 50kHz-> 24% of the events
Marco Bon

## Slide 26: Beam rate -3
Since we knew of the presence of high rate, we tried to put a cut directly on the beam rate
E=200 MeV/N (MB)
Marco Bon
Without cut
Beam_rate<10 kHz
Beam_rate<1 kHz

## Slide 27: Beam rate -3
If we impose cuts on the Beam_rate, the charge distributions improve slightly
E=200 MeV/N (MB)
Marco Bon
Without cut
Beam_rate<50 kHz
Beam_rate<100 kHz

## Slide 28
Marco Bon

## Slide 29
Marco Bon
200MeV/N

## Slide 30: Introducing the rate into MC simulation
Without the rate, in order to introduce the sperimental resolution, a random value, taken from a Gaussian with G(mean=0, ), is summed to the MC_true
In order to parameterize the Eloss response to the beam rate, the mean value of the Eloss at fixed rate was taken:
Marco Bon
ProfileX( )

## Slide 31: Introducing the rate into MC simulation
To implement our dependent-rate model, we performed a fit with the function:
Marco Bon

## Slide 32: Introducing the rate into MC simulation
From this distribution, a random value “r” is extracted from the rate distribution. To this random value is associated a smeared E(r).
Let E(1) be the value of energy when the rate is 1kHz, it is possible to define the shift in energy caused by the beam rate
shift = E(r) - E(1)
Marco Bon
.
E(r)
E(1)
r
With this value it is possible to introduce the smearing caused by the rate in the MC simulation by summing a random value from a Gaussian with
G(mean= shift, )
to the MC_true

## Slide 33: Introducing the rate into MC simulation
Marco Bon
200 MeV/u — Only MB

## Slide 34: Introducing the rate into MC simulation
To implement our dependent-rate model, we performed a fit with the function:
Marco Bon
p0 | 44.8
p1 | 5.9
p2 | 2.7 E4
p3 | -1.9 E-5
p4 | 2.7 E-12

## Slide 35: Trigger efficiencies
Marco Bon

## Slide 36: Z reconstruction
MB
Marco Bon

## Slide 37: Z reconstruction
Marco Bon
MB+frag

## Slide 38: Z identification
Marco Bon
By losing efficiency in reconstructing the Z on the single hit, when reconstructing the point (requiring that the Z of the two layers match), you lose statistics
Rate (kHz) | Entries | Normalization
13 | 1.85 E7 | 1
55 | 1.56 E7 | 0.84
96 | 1.38 E7 | 0.74
MC

## Slide 39: Z reconstruction
Marco Bon

## Slide 40: Z identification
Marco Bon
By losing efficiency in reconstructing the Z on the single hit, when reconstructing the point (requiring that the Z of the two layers match), you lose statistics
Rate (kHz) | Entries | Normalization
13 | 1.85 E7 | 1
55 | 1.56 E7 | 0.84
96 | 1.38 E7 | 0.74
MC