## Slide 1: COLD Lab activity report
Claudio Gatti
63nd LNF Scientific Committee – May 2022

## Slide 2
COLD - Cryogenic Laboratory for Detectors
Axion Experiments
Superconducting Quantum Devices
Superconducting Cavities
Magnetic Measurements
QUAX – QUest for AXions
Search for galactic axions with Sikivie’s Haloscopes at 10 GHz (Ongoing experiments at LNL and LNF).
(K)FLASH
Search for galactic axions with a Sikivie’s Haloscope at 100 MHz (Design Study).
DART WARS (Detector Array Readout with Travelling Wave AmplifieRS)
Development of wide band quantum amplifiers for multi-channel detector readout (Ongoing).
EXPERIMENTS
Superconducting Devices
SIMP (Single Microwave Photon detectors)
Development of single-microwave photon detector (Ends 2021)
Qub-IT Quantum Sensing with superconducting qubits (Started 2022).
Supergalax FET H2020 Project
SC-qubits array photon-detector for axion experiments
SQMS USA DOE Project
Superconducting Quantum Materials and Systems
SC materials for cavities

## Slide 3: outline
QUAX - Galactic Axion Search at 10 GHz (35-50 meV)
FLASH - Galactic Axion Search at 100 MHz (0.5-1.5 meV)

## Slide 4
Wilczek’s seminar on February 2022

## Slide 5: Resonant Cavity - Cu 8.5 GHz
Simulations S. Tocci
Technical design S. Lauciani
Fabrication LNF workshop
Chemical polishing LNL

## Slide 6: Tuning
Type | Q | C010
Ideal | 117,000 | 0.669
Allumina | 114,000 | 0.665
Copper | 114,000 | 0.666
Cu Disk | 115,000 | 0.663
Allumina
Copper
Cu Disk
~200 MHz scan

## Slide 7: Superconductive Cavity: Nb3Sn (SQMS)
Design di M. Checchin (FNAL)
Tuning S.Tocci
Technical design S. Lauciani
Fabrication in progress at FNAL

## Slide 8: Test of 9T Magnet
New 9T NbTi magnet from AMI succesfully installed in the cryostat
I=10 Ampere/Tesla
Succesfully ramped to 5 T (50 Amps) and set in persistent mode
Above 50 amps, the temperature of the 4K plate increases by more than 1K
New Pulse Tube (~1.5 W@ 4K) purchased. Delivery expected this summer

## Slide 9: B Field Shield For SC Electronics
Shield simulation G. Iannone (Salerno)
Lead B-field shield
B-field shield

## Slide 10: New Sample Holder
Simulations by Nassim Chikhi, CNR (Supergalax)
Simulation of “cavity” mode removal by pillars

## Slide 11: Quantum Limited Amplification: Flux JPA (QubIT)
DC Squid
Coupling capacitor (20 fF)
Signal line
Pump line
Circuit design LNF
Chip design FBK
E.M. simulation Uni Fi
Device simulation Salerno
Fabrication FBK/CNR-IFN
Resonator l/4
First device at 8.5 GHz in fabrication now at FBK!

## Slide 12: Sensitivity of LNF Haloscope
Gagg 90% cl | Tnoise | Q | B(T)
1.6×10-13 | 8 K (HEMT) | 120,000 Cu Cavity | 5
9×10-14 | 8 K (HEMT) | 120,000 Cu Cavity | 9
2×10-14 | SQL (JPA) | 120,000 Cu Cavity | 9
1.3×10-14 | SQL (JPA) | 300,000 SC Cavity | 9
Gagg(KSVZ)=1.3×10-14 GeV-1
ma=35 meV
1h data taking
Multi-cavity: with 4 cavities at differet frequencies, 4 times the scan speed with same sensitivity.
 Ready for the first experimental run (Summer 2022)!
 After new Pulse Tube commissioning
 With JPA
 With SC cavity

## Slide 13: Single Photon Detection
IEEE TRANSACTIONS ON APPLIED SUPERCONDUCTIVITY, VOL. 32, NO. 4, JUNE 2022
Observed Resonant Activation of a CBJJ
Two resonators coupled by 5 qubits
Test at LNF in preparation (end of May)
SIMP
A. Rettaroli Ph.D. Thesis “Study of devices based on Josephson junctions for galactic axion search” Uni Roma Tre (2022)

## Slide 14: FLASH Finuda magnet for Light Axion SearcH
Galactic axion search at 100 MHz (0.4-1.1 mev)

## Slide 15: The Flash
FLASH - Finuda magnet for Light Axions SearcH
Proposal of a large Haloscope
Search of galactic axions in the mass range 0.5-1.5 meV
Large volume RF Cavity (4 m3)
Moderate magnetic field (1.1 T)
Copper rf cavity Q~500,000
T 4.5 K
Experiment | w B2 V Q (rad T2m3/s) (×1015)
The FLASH | 1.5
ADMX | 5
HAYSTAC | 0.2

## Slide 16: THE FLASH Frequency Tuning - LF
L=1200 mm
Φrod=230mm
Rcav=1050 mm
From 117 to 206 MHz
Simulations S.Tocci

## Slide 17: THE FLASH Frequency Tuning - HF
From 206 to 360 MHz (preliminary)
Rcav=590 mm
L=1200 mm
Φrod=120 mm

## Slide 18
Generated with https://github.com/cajohare/AxionLimits by Ciaran O’Hare
FLASH sensitivity 0.5 – 1.5 meV

## Slide 19
Generated with https://github.com/cajohare/AxionLimits by Ciaran O’Hare
With projections from other experiments

## Slide 20
https://indico.cern.ch/e/MHzHaloscope
Two days workshop to discuss physics opportunities at 100-500 MHz Haloscopes
115 registered people
FLASH (Design study;120-1360 MHz; 4K;1.1T)
Baby Iaxo-RADES (Design study; 200-500 MHz; 6K; 2.5 T)
ADMX Low Frequency (Design study, 9T MRI magnet, 100 mK, 160-500 MHz)
DMRadio-ABRACADABRA (TDR in preparation; 4 T; mK; 5-200 MHz)

## Slide 21: High Frequency Gravitational Waves
arXiv:2112.11465

## Slide 22: Sensitivity to HFGW
Mode | Resonant Frequency [MHz] | Q factor (@4°K)
TE111 | 150.4 | 711e3
TE112 | 263.5 | 871e3
TE211 | 186.9 | 735e3
TE212 | 285.9 | 817e3
arXiv:2112.11465

## Slide 23: Sensitivity to HFGW
Mode | Resonant Frequency [MHz] | Q factor (@4°K)
TM010 | 109.5 | 626e3
TM011 | 166.1 | 526e3
TM012 | 272.3 | 752e3
TM110 | 174.4 | 790e3
TM111 | 214.5 | 598e3
TM112 | 304.7 | 712e3
TM210 | 233.7 | 915e3
TM211 | 264.9 | 664e3
TM212 | 342.1 | 755e3

## Slide 24: Sensitivity to HFGW
arXiv:2112.11465
Mode | TM012
frequency | 270 MHz
hn | 0.14
B0 | 1.1 T
Vcav | 4.15 m3
Q0 | 7×105
Tsys | 4.9 K
Dn | 10 kHz
tint | 1 min
FLASH
FLASH strain sensitivity h0 ~ 4×10-22

## Slide 25: Plan for the Test of the Finuda Magnet
Revision of He Buffer
Revision of safety valves
September
Test of pumping system
June
Elongation of He transfer line
Repair of control panel
New cooling system of magnet power supply and test
Endcaps closing
September
July
September 2022- January 2023
January 2023
September - October

## Slide 26: Conclusion
Ready for the first QUAX@LNF run with sensitivity 10×KSVZ (June-July)
Roadmap to KSVZ:
  Tuning system
  Quantum limited amplification (JPA/TWPA)
  Superconducting cavity (Nb3Sn, NbTi, YBCO)
  Multicavity
  Single microwave photon counters (CBJJ, SC qubits)
Estimate of FLASH sensitivity to axions and HFGW with e.m. simulations
Large attendace at 100 MHz Haloscopes Workshop!
Ongoing work to prepare the test of the FINUDA magnet at beginning of 2023