## Slide 1: SRF Photoelectron Source Development for BERLinPro
TTC-meeting Februar 28 – March 3 2011 – Milano, Italy
O. Kugeler (based on talk given by A. Neumann)

## Slide 2: Path towards a Photoinjector for BERLinPro
max. beam energy | 100 MeV
max. current | 100 mA
nominal bunch charge | 77 pC
max. rep. rate | 1.3 GHz
normalized emittance | < 1mm mrad
cryo load @ 1.8K | 240 W
ERL challenges:
  Optics design
  HOM excitation, beam break up
  Bunch length manipulation
  Beam loss
  Timing jitter
  Field control
But: The beam quality is determined by the source
Booster
Main linac
Undulator
Beam dump
Merger
Return arcs
RF Photoinjector
Goals for ERL demonstrator
No source has ever reached these parameters
 Workshop at HZB with leading experts in 2009: Decision for SC RF Photoinjector
ERL: Combine high beam quality of linac with high average current of storage rings
Gun

## Slide 3: SC RF photoinjector principle
- 1.6 cell TESLA structure with backplane
at the equator; EM design by
Jacek Sekutovicz: Highest fields at Cathode region
TTF-III Input coupler
Pick-up probe
Pb-Cathode
Excited p-TM010 mode
Reaching ERL parameters is a complex task and challenge
follow a three stage approach

## Slide 4: The three stage approach
Stage A (Beam dynamics):
Study beam dynamics of SC RF photoinjector:
  Emittance
  Field levels
  Stability
Starting point for SC design and operation of SRF gun
no tuner. Sync with feeback loop on laser rep-rate
Stage B (Peak Brightness):
Study + develop cathode insert into SC injector (choke filter):
Lifetime + quantum efficiency of cathode materials
Reliable cathode replacement scheme
Stage C (High avg. Current):
SC design for ERL design current
High power operation
HOM damping
Cathode lifetime
Started here

## Slide 5: Stage A Gun with Diagnostic beamline at HZB
SC Solenoid
(Niowave)
SC Cavity
Mass Spectrometer
Viewscreens
Dipole magnet
THz diagnostics
SQ
Faraday Cups
Stripline BPM,
ICT
HoBiCaT
cryostat
First time operated fully SC photoinjector ensemble (SC Cathode, Cavity & Solenoid)

## Slide 6: Extension of the HoBiCaT Cavity Test Facility
Laser
hut
Laser beamline
HoBiCaT cryostat
Diagnostic
e- beamline
C
o
n
t
r
o
l
ro
o
m
IOT (CPI, cw, 17kW)

## Slide 7: The Collaboration for the Stage A injector
Cathode Laser cleaning
QE measurements
Cavity
electro-magnetic design
Pb Cathode
deposition
Cavity fabrication,
treatment and testing
Laser design
and fabrication
Project planning
Cavity mechanical design,
Setup of test facility,
Beam physics program

## Slide 8: Mechanical design: Countermeasures to increase field stability
Beam quality dominated by field stability
Field stability in SC cavity: Avoid detuning (deformation) of the cavity
F
Backwall stiffening
Detuning in Hz/mbar
Combined FEM mechanical and
Electro-magnetic field simulations
 low deformation (detuning) design
ANSYS simulation

## Slide 9: Cavity fabrication at Thomas Jefferson Lab
Status Anfang des Jahres:
Stiffening ring
Pick-up Port
„Helium vessel endplate“
Passive stiffening
System: “Spider“
Cavity backwall for
cathode
Cavity half-
cells
Cavity tuning setup at JLab
Fundamental power
coupler port
Cavity in helium vessel
All pictures courtesy
of Peter Kneisel

## Slide 10: Cathode deposition at IPJ Andre Soltan Swierk
Plasma arc
depositon setup
in 30° configuration
16 x 5min depositions result
in a few hundred nm thick
Pb cathode film
Pb cathode film
Cavity with helium vessel
Mask to protect cavity

## Slide 11: Cavity vertical tests at Jlab: Current status
                Acceptance tests for SC cavity: Rsurf or Q0 as function of peak field
                Test after fabrication, tuning and several treatments:
                Peak fields > 40 MV/m, light field emission at highest fields
                Cathode deposition
                First cathode was lost
                Second cathode depositon
Final vertical test with cathode:
Fields above ERL operating range
Surface resistance below cryogenics limits  Cavity ready for beam production!
ERL operation

## Slide 12: Outlook: Near future
Installation of cavity, solenoid and beamline in HoBiCaT
Cold test of solenoid
Installation and commissioning of laser
First horizontal RF tests:
  Q0(Eacc), cryogenic tests
  LLRF field control: Field stability
  Test with laser and RF, synchronization
First beam on viewscreen by spring 2011
Start design of Stage B in collaboration with FZD (HZDR), DESY and TU Dortmund
People involved:
W. Anders, M. Dirsat, A. Frahm, A. Jankowiak, T. Kamps, J. Knobloch, O. Kugeler, A. Neumann, T. Quast, J. Rudolph,
M. Schenk, M. Schuster, Helmholtz-Zentrum Berlin für Materialien und Energie GmbH, Berlin, Germany
T. Rao, J. Smedley, BNL, Upton, Long Island, New York, USA
J. Sekutowicz, DESY, Hamburg, Germany
P. Kneisel, JLAB, Newport News, Virginia, USA
R. Nietubyc ,The Andrzej Soltan Institute for Nuclear Studies, Swierk/Otwock, Poland
I. Will, MBI, Berlin, Germany + the support of many more…….
almost done
almost done