## Slide 1: CCE & Charge Sharing vs External Capacitor in HERD SCD
Rui Qiao; Wenxi Peng; Ke Gong

## Slide 2: Background: CCE & Charge sharing when hitting readout strip
For 5% charge sharing ratio, FOOT-150 has lowest CCE, IHEP-25/IHEP-60/FOOT-320/AMS has similar CCE around 80~85%.
The coupling cap was around 30~50 pF correspondingly.

## Slide 3: Background: Hitting readout strip and floating strip
Small coupling capacitance can improve charge sharing, but decrease CCE.
Lower CCE with hitting float strip than readout strip.
Seed ch.
Seed+1 ch.
Seed+2 ch.
Seed ch.
Seed+1 ch.
Seed+2 ch.
DAMPE:
Hitting
readout strip
DAMPE:
Hitting
float strip

## Slide 4: Requirement of coupling capacitor
Z | Signal
Proton Z=1 | Small signal ~3.67 fC (@ 0 deg)
Iron Z=26 | Large signal ~4270 fC (@ 30 deg)
Impact position | Signal
Float strip | Small CCE (60% for DAMPE)
Readout strip | Large CCE (100% for DAMPE)
Z | Impact position | Signal | Requirement
Proton Z=1 | Float strip | Smallest signal | Enough SNR
Iron Z=26 | Readout strip | Largest signal | Large Dynamic

## Slide 5: Analyze procedure:
Channel CCE simulation:
Hitting readout strip
Channel CCE simulation:
Hitting float strip
Interpolation of CCE with different
impact position
Channel amplitude simulation:
interpolated impact position
Deposited charge simulation
SPICE
PYTHON

## Slide 6: SPICE simulation
Parameter | Value
Readout chn. | 7
Charge inject position | Chn 3 ~ Chn. 4
Notes: 来源：G:\keyan\科研任务\211212_硅微条模拟\MyMultisim\220303_模拟IHEP SCD外接电容的影响_覆盖到Inter3\25um条宽\总电路.png

## Slide 7: Cross-check using AMS-02 results
The x side of AMS-02 has readout pitch of 110 um, similar to AMS-Upgrade which is 109 um.
IP~0.3; Angle~10°; coupling cap~70pF
Notes: 来源：Y. Jia, Q. Yan, V. Choutko et al. Nuclear Inst. and Methods in Physics Research, A 972 (2020) 164169
G:\keyan\科研任务\211212_硅微条模拟\220315_Channel response vs External Capacitor in HERD SCD\PNG_AMS-02\Check_AMS-02_Result.png

## Slide 8: Channel CCE vs impact position: large coupling capacitance
Detector: IHEP-60um
Coupling cap.: 500 pF
IP=0: hitting readout strip
IP=0.5: hitting float strip
Extreme small charge sharing ratio hitting readout strip
Hitting
Readout Strip
Hitting
Float Strip
Hitting
Readout Strip
Notes: 来源：G:\keyan\科研任务\211212_硅微条模拟\220301_Channel response vs External Capacitor in HERD SCD\PNG_channel_vs_ip\IHEP-60_500pF.png

## Slide 9: Channel CCE vs impact position: different coupling capacitance
The impact of small coupling capacitance:
Advantage: larger charge sharing ratio with hitting readout strip.
Disadvantage: smaller CCE with hitting float strip.
500 pF
Coupling
capacitance
Hitting
Readout Strip
Hitting
Float Strip
Hitting
Readout Strip
10 pF
Coupling
capacitance
Hitting
Readout Strip
Hitting
Readout Strip
Hitting
Float Strip
Notes: 来源：G:\keyan\科研任务\211212_硅微条模拟\220301_Channel response vs External Capacitor in HERD SCD\PNG_channel_vs_ip\*

## Slide 10: Charge Inject: From proton (Z=1) to iron (Z=26)
Detector: FOOT-150um
Coupling cap.: 500 pF
IP=0, hitting readout st.
Extreme small charge sharing ratio hitting readout strip
Z=1
Z=26
Readout strip
500 pF
Notes: 来源：G:\keyan\科研任务\211212_硅微条模拟\220301_Channel response vs External Capacitor in HERD SCD\PNG_channel_vs_energy\*

## Slide 11
 | AMS-02 | AMS升级
厚度 [um] | 320 | 
条宽 [um] | 12 | 
读出pitch [um] | 110 | 109
读出周期 | 每4条读1条 | 
耦合电容 | 单个Ladder 760pF 每个Sensor约70pF | 15~1000 pF可调 选择70 pF

## Slide 12
Float strip
500 pF
Read strip
500 pF
Z=1
Z=1
Z=26
Z=26
Float strip
10 pF
Read strip
10 pF
Z=1
Z=1
Z=26
Z=26
Notes: 来源：G:\keyan\科研任务\211212_硅微条模拟\220301_Channel response vs External Capacitor in HERD SCD\PNG_channel_vs_energy\*

## Slide 13: CASE 1: Proton(Z=1) hitting float strip
For DAMPE SCD, we use 3.5*sigma to trigger the cluster finding algorithm, and use 1.5* sigma to end the cluster.
For HERD SCD, the SNR of the maximum channel should be large enough for the cluster finding efficiency if data compression is in need.
Proton hitting float strip has the minimum CCE, as well as the minimum cluster finding efficiency

## Slide 14: CASE 1: Proton(Z=1) hitting float strip
The thin FOOT-150um detector has lowest SNR.
The threshold of SNR puts a lower limit on coupling capacitance.
Project | Ladder length (cm) | Noise Level (fC)
DAMPE STK | 40 | ~0.18
HERD SCD | 90 | ~0.41
2σ
3σ
Notes: 来源：G:\keyan\科研任务\211212_硅微条模拟\220301_Channel response vs External Capacitor in HERD SCD\PNG_MIPs_Z1_Z26\max_amp_with_floating_Z1.png

## Slide 15: CASE 2: Iron(Z=26) hitting readout strip
The electronics expert suggest the non-linear response is not reliable.
The total signal amplitude without saturation as large as possible.
Read strip
500 pF
Z=1
Z=26
Read strip
10 pF
Z=1
Z=26
Notes: 来源：G:\keyan\科研任务\211212_硅微条模拟\220301_Channel response vs External Capacitor in HERD SCD\PNG_channel_vs_energy\*

## Slide 16: CASE 2: Iron(Z=26) hitting readout strip
Zoom A: total amplitude without saturation increase with smaller coupling capacitance.
Zoom B: total amplitude without saturation drop with extreme small coupling capacitance.
Zoom
A
Zoom
B
Notes: 来源：G:\keyan\科研任务\211212_硅微条模拟\220301_Channel response vs External Capacitor in HERD SCD\PNG_MIPs_Z1_Z26\total_amp_with_readout_Z26.png

## Slide 17: Combining Proton(Z=1) and Iron(Z=26)
Z=1, float strip
Z=26, readout strip
Higher SNR
With
Larger capacitance
Larger Signal
With
Medium capacitance
Notes: 来源：G:\keyan\科研任务\211212_硅微条模拟\220301_Channel response vs External Capacitor in HERD SCD\PNG_MIPs_Z1_Z26\*

## Slide 18: Combining Proton(Z=1) and Iron(Z=26)
Higher SNR
For Z=1
Larger signal
For Z=26
The IHEP-60 & AMS-Up have better performance to compromise Z=1 & Z=26.
2σ
3σ
Notes: 来源：G:\keyan\科研任务\211212_硅微条模拟\220301_Channel response vs External Capacitor in HERD SCD\PNG_MIPs_Z1_Z26\*

## Slide 19: Combining Proton(Z=1) and Iron(Z=26)
Detector | Coupling cap. [pF] | SNR of Z=1 | Total non-saturated signal amplitudes of Z=26 [fC]
IHEP-25 | 20 | 2.6 | 468
IHEP-60 | 50 | 3.3 | 444
FOOT-320 | 35 | 2.6 | 380
AMS-Up | 35 | 3.1 | 426
Notes: 来源：G:\keyan\科研任务\211212_硅微条模拟\220301_Channel response vs External Capacitor in HERD SCD\PNG_MIPs_Z1_Z26\ana_Z1_vs_Z26.csv
G:\keyan\科研任务\211212_硅微条模拟\220301_Channel response vs External Capacitor in HERD SCD\PNG_channel_vs_energy\ IHEP-60_IP0_50pF.png & IHEP-60_IP0.5_50pF.png
G:\keyan\科研任务\211212_硅微条模拟\220301_Channel response vs External Capacitor in HERD SCD\PNG_channel_vs_energy\ AMS-Up_IP0_35pF.png & AMS-Up_IP0.5_35pF.png
Noise level: 0.41 fC
Total charges of normal incident proton: 3.67 fC
Total charges of 30deg incident iron: 4270 fC

## Slide 20: Combining Proton(Z=1) and Iron(Z=26)
Detector | Coupling cap. [pF] | SNR of Z=1 | Total non-saturated signal amplitudes of Z=26 [fC]
IHEP-60 | 50 | 3.3 | 444
IHEP-60，Readout strip
IHEP-60，Float strip
Z=1
Z=26
Z=1
Z=26
Notes: 来源：G:\keyan\科研任务\211212_硅微条模拟\220301_Channel response vs External Capacitor in HERD SCD\PNG_MIPs_Z1_Z26\ana_Z1_vs_Z26.csv
G:\keyan\科研任务\211212_硅微条模拟\220301_Channel response vs External Capacitor in HERD SCD\PNG_channel_vs_energy\ IHEP-60_IP0_50pF.png & IHEP-60_IP0.5_50pF.png
G:\keyan\科研任务\211212_硅微条模拟\220301_Channel response vs External Capacitor in HERD SCD\PNG_channel_vs_energy\ AMS-Up_IP0_35pF.png & AMS-Up_IP0.5_35pF.png
Noise level: 0.41 fC
Total charges of normal incident proton: 3.67 fC
Total charges of 30deg incident iron: 4270 fC

## Slide 21: Combining Proton(Z=1) and Iron(Z=26)
Detector | Coupling cap. [pF] | SNR of Z=1 | Total non-saturated signal amplitudes of Z=26 [fC]
AMS-Up | 35 | 3.1 | 426
AMS-Upgrade，Readout strip
AMS-Upgrade，Float strip
Z=1
Z=26
Z=1
Z=26
Notes: 来源：G:\keyan\科研任务\211212_硅微条模拟\220301_Channel response vs External Capacitor in HERD SCD\PNG_MIPs_Z1_Z26\ana_Z1_vs_Z26.csv
G:\keyan\科研任务\211212_硅微条模拟\220301_Channel response vs External Capacitor in HERD SCD\PNG_channel_vs_energy\ IHEP-60_IP0_50pF.png & IHEP-60_IP0.5_50pF.png
G:\keyan\科研任务\211212_硅微条模拟\220301_Channel response vs External Capacitor in HERD SCD\PNG_channel_vs_energy\ AMS-Up_IP0_35pF.png & AMS-Up_IP0.5_35pF.png
Noise level: 0.41 fC
Total charges of normal incident proton: 3.67 fC
Total charges of 30deg incident iron: 4270 fC

## Slide 22: Conclusion
SPICE simulation of CCE with readout & float strip incidence.
Verified by AMS-02 results.
Two extremes:
  Smallest signal: 0 degree proton (Z=1) hitting float strip
  Largest signal: 30 degree iron (Z=26) hitting readout strip
The coupling capacitance affects:
  The SNR when proton (Z=1) hitting float strip
  The total non-saturated amplitude when iron (Z=26) hitting readout strip
The best sensors are:
  IHEP-60 with 50 pF coupling cap., SNR=3.3 for Z=1
  AMS-Upgrade with 35 pF coupling cap. , SNR=3.1 for Z=1