## Slide 1: News from IHEP
Rui Qiao; Wenxi Peng; Ke Gong

## Slide 2: Outline
Install precision
Plan for test beam
Brief introduction to the SCD structure

## Slide 3: News(1): Install precision
HERD is collecting the requirement about install precision.
Base on the DAMPE (A. Tykhonov et al., NIMA 2018), the tracker is re-alignment in orbit every two weeks.
Six free correction parameters for each sensor:
The hit position is correct via:

## Slide 4: New(2): Test beam plan from IHEP&PMO SCD
Contribution | Ladder | Sensor | Purpose
IHEP | Short *2 | MICRON(25 & 60 um) *1 | Charge Measurement
PMO | Long *2 | DAMPE *7 | Assembling Qualification

## Slide 5: Incident angle requirement
From simulation, 95% cumulative events corresponds to 0~50deg in X-Z or Y-Z plane.
HERD want to expand SCD dynamic range to Z=28.
HERD suggests SCD detector to incline 50deg (along strip direction) during test beam for the extreme performance.
TOP
SCD
Side
SCD

## Slide 6: Incident angle requirement
A student is study Allpix2 silicon pixel simulation tools. The result differ from the AMS02 simulation algorithm in large incident angle(perpendicular to strip direction).
45 deg
60 deg

## Slide 7: Incident angle requirement
Objective | Incident angle | Purpose
Primary | 50 deg along strip direction | Dynamic range Charge sharing
Secondary | 50 deg perpendicular to strip direction | Verify simulation
320um * tan(50) = 380um

## Slide 8: Incident position requirement
IHEP SCD, pitch 80um
Width 25um
Width 60um
Ext. Cap.
Want to study the performance of different width & external capacitor.
25um
60um
25um
60um
Beam1
Beam2
Rely on mobile platform to change incident position

## Slide 9: Test beam trigger
HERD provide two trigger type as the last test beam:
  TTL (Traditional)
  DI2C (Flight model)
SCD contribution | Prefer trigger type
IHEP | TTL
PMO | TTL
Perugia | ??

## Slide 10: Man power
Due to Omicron variant, stronger restriction for Chinese Academy of Science (including IHEP & PMO) to send employees and students abroad.
Can Perugia team help:
  Install & uninstall IHEP & PMO SCD and DAQ
IHEP & PMO team can help remote control & logging

## Slide 11: New(3): Brief introduction to the SCD structure
Top SCD
4 sides SCD
Support
&
Fanout
cover
SCD & PSD

## Slide 12: General structure
Support
&
Fanout
Cover
honeycomb & 4 layers SCD
*2
honeycomb & PSD

## Slide 13: Preliminary size of side SCD
Module | Width (m) | Height (m)
SCD | 1.55 | 0.91
Sensor | 0.71*2= 1.42 | 0.86
TFH | 0.05 | 
Center Support | 0.03 | 

## Slide 14: Preliminary size of Top SCD
Module | Width (m) | Height (m)
SCD | 1.7 | 1.7
Sensor | 0.786*2= 1.572 | 0.786*2= 1.572
TFH | 0.05 | 
Center Support | 0.03 |