## Slide 1: The reason of charge equalization in TCAD simulation of AMS-02
Rui Qiao; Wenxi Peng; Ke Gong

## Slide 2: Background
When TCAD simulating AMS02 with various coupling capacitance, we found the cumulative charge tend to slowly equalize. With smaller coupling capacitance, the charge equalization is stronger.
Simulation of AMS02 with 1uF coupling capacitance
Simulation of AMS02 with 50pF coupling capacitance

## Slide 3: Charge equalization
There are only interstrip capacitances connecting the two neighboring readout channels.
Capacitance is conductive for fast signal, but non-conductive for slow signal. So the slow charge equalization is hard to understand.
Bulk capacitance
Coupling capacitance
Interstrip capacitance
Equivalent circuit of AMS-02
Readout channels

## Slide 4: TCAD simulation with simple structure
TCAD charge injection into two-strips detector
Parameter | TCAD | AMS02
Strip occupancy | 50% | 50.9%
Strip Gap [um] | 10->100 | 13.5
Coupling Cap. [pF] | 100->1000 1E6 | 700
Simulation with only two strips.

## Slide 5: TCAD simulation with different strip gap
The 10um strip gap behave different from others
Charge equalization is only observed with 10um strip gap.
SEU Strip
Neighboring Strip
SEU Strip
Neighboring Strip
Cumulative Charge(Y) vs Time(X)
1uF coupling capacitance
Cumulative Charge(Y) vs Time(X)
100pF coupling capacitance
Strip
Gap
10um

## Slide 6: TCAD simulation with different coupling cap
With 20um~100um strip gap (excluding 10um strip gap), no charge equalization is observed with all coupling capacitance.
Cumulative Charge(Y) vs Time(X)
20um strip gap
Cumulative Charge(Y) vs Time(X)
100um strip gap
SEU Strip
Neighboring Strip
SEU Strip
Neighboring Strip

## Slide 7: Conclusion
No charge equalization is expected via the equivalent circuit of AMS-02.
No charge equalization is observed in TCAD simulation with
  Strip gap: 20~100 um
  Coupling capacitance: 100pF~1uF
Charge equalization is only observed in TCAD simulation with strip gap 10um. TCAD is hard to use correctly.