## Slide 1: WA6 Report APPLE-X Undulator for the AQUA line at EuPRAXIA@SPARC_LAB
Alberto Petralia, ENEA FSN, C. R. Frascati
on behalf of the WP6 collaboration team
EuPRAXIA@SPARC_LAB TDR Review Committee, Monday 6 June 2022 – Frascati

## Slide 2: Apple-X Undulator structure
y
z
0
Lu/2
-Lu/2
λu
z=0
z=λu/4
z=λu/2
z=3/4 λu
Ingoing field
Outgoing field
x
y
Longitudinal view
Halbach array
Transverse view
G1
G2
G3
G4
y
z
x
φ hole 5.5 mm
φ ext pipe 5 mm
Gap 1.5 mm
Transverse plane
view
pipe support 1 mm
Remanent field Br = 1.35 T
Undulator period λu = 18 mm
4 blocks / period, NdFeB
Min. gap = 1.5 mm
# of periods N = 110 (Lu=2m)
Simulation with RADIA
Change of polarization by longitudinal shift (Δz) of G2 and G4

## Slide 3: Why an Apple-X for AQUA?
Apple type undulator: Variable polarization, Linear/Circular
Apple-X geometry allows K>1 with a 5 mm round vacuum pipe
Emax = 1 GeV
  λ = 4 nm
Krms ≈ 1
λu = 18 mm
Requirements on radiation and constraints on the beam parameters give:
Minimum gap 1.5 mm (not less for mechanical issues) to have K>1

## Slide 4: Wavelength Tunability
Ky
Kx
Circular Pol.
0.7 < Kx,Ky < 1.2
Same range of tunability for LP and CP, intrinsically due to the Apple-X symmetry
Parameters optimized for operation at 4 nm
Ky
0.9 < Ky < 1.7
Linear Pol.
@ E = 1 GeV
3.5 nm < λ < 5.8 nm
Ky
Kx
Krms
K vs phase
Δz/λu

## Slide 5: Transverse Field profile and homogeneity
By @ z=0
y
@ x=0
x
By @ z=0
@ y=0
Linear Pol.
Circular Pol.
x
By @ z=0
Bx @ z=/4
@ y=0
By @ z=0
Bx @ z=/4
y
@ x=0
@ 0.2 mm - dBy/dy < 0.05%, dBy/dx < 0.3%, dBx/x < 0.03%, dBx/dy < 0.3%
@ 0.4 mm - dBy/dy < 0.2%, dBy/dx <1.18%, dBx/x < 0.15%, dBx/dy < 1.18%
By
Bx

## Slide 6: End magnets design and field integrals
Standard block size lz = /4
Symmetric
Zero-displacement orbit
Z=0
¼ ½ ¾
¾ ½ ¼
within typical values (Ix,y <0.5 G m, IIx,y <0.5 G m2)
ending magnets distance/width optimized for LP operation
I1 (G m)
I2 (G m2)
Δz/λu
Δz/λu
Variation of Field Integrals with phase (Δz/λu) at minimum gap
Iy
Ix

## Slide 7: Trajectory
For a 2 m long undulator (Nper=110)
LP (H)
Exit position and angle must be close to 0 for an electron moving on axis
Optimized for the LP operation
> 0 value in CP due to the magnetic properties of NdFeB
Can be managed by correctors and/or correction coils
CP
hor
vert

## Slide 8
LP
off: 0.5 mm
Focusing properties
Looking at the Trajectory:
LP - Focusing in X, def. In Y
CP - Focusing in both planes with equal strength
Focusing map can be evaluated numerically (Kick maps = Kick angle vs entrance position)
Linear variation of Kick angles with the off-axis displacement for entrance offset < 0.8 mm
hor
vert
CP
off: 0.5 mm
off: 0.8 mm
off: 1 mm
off: 0.8 mm
off: 1 mm

## Slide 9: Magnetic Forces on girders
G1
G2
G3
G4
G3
G4
Max Fx = ± 920 kg Max Fy = ± 1200 kg Max Fz = ± 160 kg
x
y
z
@ minimum gap = 1.5 mm
Can be managed by conventional motors
G1
G2

## Slide 10: Conclusion and remarks
Chosen geometry: Apple-X
Settled parameters, optimized for operation @ 4 nm – 1 GeV
Krms constant for any setting of polarization, same tunability in LP and CP
Transverse fields in CP show a full symmetry between X and Y coordinates
Field integrals values within typical limits with conventional ends design
Focusing properties solved numerically (Kick maps)
X,Y acceptable region of operation < 0.2 mm (to be improved)
Estimation of forces acting on girders, no compensating magnets required
Next steps
Design tolerances study
Mechanical design (based on the SABINA Apple-X)
Correction coils design
Phase shifters