## Slide 1: Machine Development scenarios and operational considerations
D. Mirarchi, P. Hermes, S. Redaelli, M. Solfaroli Camillocci, J. Wenninger
Acknowledgments: C. Antuono, Q. J. Demassieux
2nd Workshop on electromagnetic dipole moments of unstable particles

## Slide 2: Introduction
The LHC: biggest and most powerful particle accelerator ever built
What does it mean?
And in HL-LHC stored energy increased to ~ 700 MJ
Very sensitive machine, several constrains for operations with high intensity beams!
Highly efficient collimation system needed for a safe beam disposal at any time!
15-50mJ/cm3
Ladybug at 10 km/h
Quench limit
LHC design 360 MJ
Airbus A320 at ~100 km/h
Stored energy

## Slide 3: Outline
Setting the scene
Handling movable objects in the LHC
Operating with beams
Conclusions

## Slide 4: Outline
Setting the scene
Handling movable objects in the LHC
Operating with beams
Conclusions

## Slide 5: Schematic layout
Secondary halo deflected by a bent crystal (Target Collimator Crystal Splitting) at larger aperture than TCP
Interaction products channelled by a second bent crystal (Target Collimator Crystal Precession)
Dedicated absorber to intercept deflected halo that did not interact with target
Deflected halo impacts on a target
TCCS
TCCP
More details in design principles in EPJC 80, 929 (2020)
Latest development in layout for proof of priciple studied in Pascal’s talk

## Slide 6: Operational scenarios at 6.8 TeV
Machine Development
Nominal operations
Machine Protection
Aim
Beams
Operations
Dedicated beam time for
proof of principle
Setup beams
(up to 3 x 1011 p)
Possible to mask
some interlocks
Flexibility
for expert handling
Physics production
Full machine
(>3 x 1014 p)
All protections active
Fully automated
handling

## Slide 7: Aim of the project
Perform a proof of principle, being ready for nominal operations
To be done during
Machine Development
Devices must be compatible
with high-intensity beams
Goniometer design to be compatible with high-intensity proton beams
What can be re-used from present experience with handling crystals and other movable objects in LHC?
Knowhow
HW control architecture
What needs to be reviewed?

## Slide 8: Basic needs to operate into the LHC
Movable devices into the LHC primary vacuum:
Extreme safety, reliability, control of their status and positions are a paramount
Beam based setup required (very important for crystals)
Do not jeopardize machine performance:
Aperture restriction
Impedance
Electron cloud
Vacuum
Avoid to introduce an aperture bottleneck
Avoid local heating due to impedance,
do not induce beam instability
No issues for beam instability expected,
material with low secondary electron yield to avoid local heating
Bakeout to avoid outgassing,
vacuum acceptance test to be compatible with LHC UHV of 10-9 mbar

## Slide 9: Present goniometer to handle crystals in the LHC
Developed for feasibility studies, upgraded along the years while gaining operational experience
Main features:
Four goniometers are installed in the LHC for crystal collimation purposes:
Stepper motor with 5 mm resolution for linear stage (same actuator as for standard collimators)
Piezo actuator with <1mrad resolution for angular stage
Replacement pipe to ensure electrical conductivity and hide the crystal during nominal operations with protons
Crystal

## Slide 10: Goniometer needs for nominal operations with p
Linear stage:
  Present stepper motors can be used for both TCCS and TCCP
Angular stage:
  Same accuracy as present goniometer for both TCCS and TCCP (may be relaxed for TCCP)
Replacement pipe:
  To be removed, feasibility studies ongoing for the development of a design compliant with impedance requirements
More details in Quentin’s talk
C. Antuono

## Slide 11: Outline
Setting the scene
Handling movable objects in the LHC
Operating with beams
Conclusions

## Slide 12: Controls in a nutshell
CCC (CERN Control Centre)
FESA
(Front-End Software Architecture)
FEC
(Front-End Card)
FPGA
Device

## Slide 13: Low level control & Machine protection
All movable object in LHC have several layers of control and protection:
Environmental Survey System (ESS)
  Reads all environmental parameters, e.g. temperatures
  A beam dump is triggered if above threshold
Motor Drive Control (MDC)
  Receives the commands
  Verifies the consistency of the order
  Performs the movement
Position Readout & Survey (PRS)
  Read actual position via LVDT (Linear Variable Differential Transformer)
  Checks that the actual position is within a well defined tolerance with 100 Hz rate
  A beam dump is triggered if outside tolerances

## Slide 14: Actual handling from the CCC
Manual handling via dedicated GUI
Machine Development
Settings stored in
LHC Software
Architecture (LSA)
database
Fully automated handling via sequencer
Nominal operations
Critical settings (like limits) protected by digital signature!

## Slide 15: HW commissioning
Full set of checks to confirm that interlocks
trigger beam dump request correctly
Complete performance validation carried out between machine closure and first beam injection
Machine Protection validation
Repeated cycles to simulate operational use and check faults/stability/reproducibility
Stress test

## Slide 16: Outline
Setting the scene
Handling movable objects in the LHC
Operating with beams
Conclusions

## Slide 17: How do I get allocated beam time?
Prepare a detailed MD procedure and step to be followed to prepare and recover the machine, to be prepared with the LHC Operation team
Very sensitive, expensive, and unique machine: many requests and each choice must be well justified
Submit a Machine Development (MD) request
Get approved based on physics motivations and feasibility (LHC Studies Working Group, LSWG)
Get in touch with involved team from which support is required:
Do you need to change machine configuration? LHC Beam Operation Committee (LBOC)
Do you need to move collimators? Collimation Working Group (CWG)
Do you need to change optics? Optics Measurements and Correction (OMC)
Do you risk to make beams unstable? Instability Working Group (IWG)
Are your studies considered potentially dangerous? Machine Protection Panel (MPP)
Prepare a detailed MD note with main highlights and key results achieved

## Slide 18: What and how can we learn?
Each test must be carefully planned:
a not optimal manipulation at top energy can lead to several hours lost, deep knowledge of the LHC necessary
Main observable: hadronic showers developed when beam interacts with obstacles
Beam loss artificially increased introducing transverse white noise
The LHC is a very stable machine!
Proof of principle focused on probing basics crystal features in a circular accelerator
Step 0: beam based alignment of all devices
Optimal channeling orientation and quality of crystalline lattice
Multi-turn channeling efficiency and geometrical crystal bending
A limited number of measurements can be performed in each fill!
Intensity limited to a maximum of 3 x 1011 p,
i.e. 30 bunches of 1 x 1010 p
Sustained and uniform losses for long time needed (up to 20-30min): gentle excitation of 3 bunches required

## Slide 19: Angular scan
Bent crystal
Deflected halo
Massive Absorber
➛ ➛ Beam ➛ ➛
Monitoring of losses at the crystal location as a function of its angle
Main outcomes:
  Optimal channeling orientation as a function of transverse crystal position (minimum of losses)
  Crystalline lattice quality (depth of well due to reduction of nuclear interaction rate)
  Qualitative evaluation of geometrical bending (well extension)
AM
AM
VR
CH
R. Rossi
First channeling
at 6.5 TeV!

## Slide 20: Absorber scan
Monitoring of losses at absorber as a function of its position, while crystal in channeling
Main outcomes:
  Multi-turn channeling efficiency as a function of transverse crystal position (error function plateau)
  Geometrical crystal bending (displacement of channeled halo)
➛ ➛ Beam ➛ ➛
Bent crystal
Deflected halo
Massive Absorber
M. D’Andrea
First efficiencies at 6.8 TeV!

## Slide 21: Looking further - learning from past
TCCS
Deflected halo
Massive Absorber
➛ ➛ Beam ➛ ➛
TCCP
Pixel
detector
Static conditions
TCCP angular scan
It will be like being on SPS extraction line…
…but with beam up 6.8 TeV!
Proof of principle done in SPS
Data from “NIM A 1015 (2021) 165747”
Key requirement: beam based alignment for precise knowledge of relative position to circulating beam

## Slide 22: Wish list
Can we stop LHC ramp at intermediate energies?
  Technically possible, non trivial preparation
  Synergies with other experiments may be found
Main outcomes:
  Measure single-pass TCCP channeling efficiency
  Validation of simulation tools
  Improved prediction of Lc yield in nominal operations
PRD 103, 072003

## Slide 23: Outline
Setting the scene
Handling movable objects in the LHC
Operating with beams
Conclusions

## Slide 24: Conclusions
Very interesting and ambitious project
Knowledge acquired in the past decade of operations in SPS and LHC crucial to steer feasibility studies
Massive “hidden” work necessary to get approved to install movable objects in the LHC, and to make them working properly
Rich program for proof of principle
Required expertise to make it happen acquired along the years
Further ideas on how to reach milestones for physics operations

## Slide 25: Outline
BACKUP

## Slide 26: Using scraper
Possible to measure:
multi-turn single channeling efficiency
multi-turn double channeling efficiency
Single-pass channeling efficiency of TCCP
NIM A 1015 (2021) 165747