## Slide 1
Giorgio Riccobene INFN-LNS
Towards acoustic
UHE neutrino detection
in the Mediterranean Sea

## Slide 2: Large Area Detectors for HE neutrinos
Optical Detection
(ICECUBE-KM3NeT)
Medium: Seawater, Polar Ice
 (throughgoing and contained)
e, (contained cascades)
Carrier: Cherenkov Light (UV-visible)
Attenuation length: 100 m
Sensor: PMTs
Instrumented Volume: 1 km3
Radio Detection
(RICE, ARIANNA, ARA)
Medium: Salt domes, Polar Ice
 (cascades)
Carrier: Cherenkov Radio
Attenuation length: 1 km
Sensors: Antennas
Instrumented Volume: >1 km3


Medium: Seawater, Polar Ice, Salt Domes
 (cascades)
Carrier: Sound waves (tens kHz)
Attenuation length:  10 km
Hydro-phones
Instrumented Volume: >100 km3
Acoustic Detection
(Prototypes)
em cascade
e
em cascade

hadron
cascade
1 TeV 100 PeV 1000 ZeV

## Slide 3: Acoustic detectors expected sensitivity
1100 hydros in 1 km3
Vertical arrays of hydrophones
1500 km3, 200 hydros per km3
5 years
threshold 5 mPa
A “complementary” km3-scale detector ?
10 years, threshold 5 mPa
5 years, 15 mPa, 95% CL
1 year, threshold 35 mPa
Acoustics
.. with cuts
- No cuts
Largely spaced detectors for UHE neutrino detection
Standard approach
Possible KM3 complementarity
See Rolf Nahnhauer’s talk tomorrow

## Slide 4: R&D on acoustic detection in ANTARES: AMADEUS
AMADEUS comprises 36 hydrophones on two lines of ANTARES
A test bench to study the feasibility of a large acoustic UHE neutrino detector
Study of acoustic environment and backgrounds
Methods to reconstruct direction

## Slide 5: R&D on acoustic detection in ANTARES: AMADEUS
Setup of Acoustic Storey with Hydrophones
Titanium cylinder with electronics
3 custom designed Acoustic ADC boards 16bit @ 250kHz
~10cm
Hydrophone: Piezo sensor with pre-amplifier and band pass filter in PU coating
Typical sensitivity: -145 dB re 1V/Pa
0o
90o
-90o
-60o
120o
Reconstruted acoustic pulses directions
Ferry routes

## Slide 6: NEMO-ODE: Ocean noise Detection Experiment
Thetrahedral antenna (1m size):
4 Reson TC4042 hydrophones (special production for 2500 m depth).
Low cost professional audio electronics (96 kHz, 24 bit sampling, )
Hydrophones synchronised and phased.
On-line monitoring and recording on shore. Recording 5’ every hour
Data taking from Jan. 2005 to Nov. 2006 (when NEMO Phase 1 was deployed).
Sea Noise measurement and modelling (presently under study)
Bioacoustics: study of sperm whales population in the East Med Sea
First experiment to perform long-term measurement and monitoring of the acoustic background @ 2000 m depth
CIBRA

## Slide 7: NEMO-ODE: acoustic noise spectrum in deep-sea
Average acoustic noise 2005-2006
Sea State 2
Sea State 0
The average noise in the [20:43] kHz band is
5.4 ± 2.2stat ± 0.3syst mPa
The average SPD is close to SS2, with increase at low frequency probably due to diffuse anthropogenic noise.
Peaks are due to pingers and shipping instrumentations continuosly present in the area.
Study of acoustic background level and its variation as a function of time (due to weather, seismic, biological and anthopogenic sources).
G. Riccobene et al., NIM-A 604 (2009), S149

## Slide 8: Acoustic positioning for KM3NeT: an opportinity for acoustics detection
Use acoustic positioning systems
The detector positioning system is a mandatory subsystem for the detector providing:
Guide during the deployment of the telescope structures and infrastructures
Optical module position during the telescope operation for muon track reconstruction
  Requirements:
  relative positioning accuracy: <20 cm (less than PMT diametre)
  absolute positioning accuracy: <1 m to optimize pointing resolution
  no interference with the optical detectors
  easy installation
  data acquisition/transmission system compliant with KM3NeT electronics
Key elements
Auto-calibrating Long Baseline of acoustic transceivers anchored in known and fixed positions.
Array of acoustic sensors (hydrophones) moving with the Detection Unit mechanical structure
Auxiliary devices: compasses, CTD , sound celerimeters, current metres
Data analysis system on-shore
Hydrophone position calculation
TDoA (Time Difference of Arrival)
TEmit(LBL) – TReceive(Hydrophone)
Geometrical Triangulation
LBL
transceivers
Detection Unit
Hydrophone

## Slide 9: Acoustic detectors on the NEMO phase 2 tower
2 PMTs
1 hydrophone
Installation and operation of a NEMO tower in Capo Passero
8 floors: 32 Optical Modules. Bar length 8 m.
Deployment 2011
18 hydrophones for acoustic positioning (NEMO phase II)
and multidisciplinary science (SMO – FIRB MIUR)
  New technology:
  New high pressure-calibrated hydrophones
  (in collaboration with SMID and NATO)
  New front-end electronics
  Syncronization with the detector Master clock
  Underwater GPS time stamp
  2 Opto-Acoustic modules (ECAP)
  2 Free Flooded Ring hydrophones (UPV-CPPM)
  All data to shore
  Expected overall resolution for positioning few cm
  Multidisciplinary science (SMO)
  Tests for neutrino acoustic detection (SMO)
40 m

## Slide 10: Novel deep sea calibrated hydrophones
SMID hydrophones and preamps (+ 38 dB gain)
Sensitivity and pressure calibration measured and certified by NATO – URC (La Spezia)
Radiation lobe
30 kHz
50 kHz
Hydrophone + preamplifier moulded in deep sea cable 7.5 m length
Hydrophone sensitivity calibrated at NATO - URC (40 hydrophones)
Measured differences ≤ ±2 dB
Relative Hydrophone sensitivity
variation with hydrostatic
pressure at 20 kHz
300 Bar
400 Bar
Measured variations ≤ ±1 dB

## Slide 11: Acoustic data chain onboard NEMO phase II
ADC
192 kHz
24 bits
Storey Control Module
Adds GPS Time
Sends Acou-data to shore
On-Shore
Storey Control Module
Data Parsing
Optical data
Acoustic positioning
and bio-acoustics
Hydros +
preamps
OMs
optical
fiber link
Point to point storey connection , “All data to shore” , underwater GPS synchronisation
Ethernet
GPS
GPS clock transmission
Data parsing/distribution
Main storage
Analysis
INFN-LNS
INFN Shore Laboratory
Sensor data acquistion
GPS time stamping
Data transmission
- fixed latency
- known optical walk
Deep Sea Detetcor
GPS receiver
Capo Passero
Trigger
Storage
Acoustic data
F. Ameli et al, NIM A doi:10.1016/j.nima.2010.04.130

## Slide 12: Test bench performances
1 µs 1.5 mm in water
Measured system Latency = 166.1 µs
10 kHz < f < 80 kHz
Preliminary
 < 100 ns
Measured electronics noise spectrum
Assuming transceiver pulse:
f= 32 kHz A=180 dB re 1 µPa @ 1m
See F. Simeone’s talk
friday

## Slide 13: Towards the synchronised acoustic Long Base-Line
SCM
on-shore
SCM off-shore
Optical link
Signal
Emission
Board
Acou
Board
preamp
preamp
Trigger
Time of trigger known
(accuracy < ns )
Signal to
transmitters
FFR
SCM on-shore
Transmits GPS time
Sends user trigger
Sends user commands and settings
SCM off-shore
Inserts time in acoustics data
Interfaces commands and trigger to SEB
Signal Emission Board
RS-232 connection from shore allows to:
Set amplitude to emit
Set frequency to emit
Set repetition rate
Digitized
Data
Slow
Control
Board
RS232
Transceivers: Sensor X30
TVR (transmission) 133 dB re uPa/V @ 1m
RVR (reception) -193 dB re V/uPa @1 m
Frequency range 20 kHz – 40 kHz
Beam pattern Radial: Omni
Axial: Toroidal (60°)
Operating Depth unlimited
UPV (Spain)
CPPM (France)

## Slide 14
Chart: Frequency [kHz]
| 18.0 | 20.0 | 22.0 | 24.0 | 26.0 | 28.0 | 30.0 | 32.0 | 34.0 | 36.0 | 38.0 | 40.0 | 42.0
A=1 | 160.0149 | 161.0515 | 162.9897 | 166.4534 | 168.923 | 168.6557 | 168.8348 | 170.5212 | 170.1484 | 169.267 | 169.1823 | 169.2036 | 168.3331
A=0.5 | 155.4547 | 157.0555 | 158.0307 | 161.7801 | 161.1594 | 160.4909 | 163.6582 | 164.2037 | 164.2789 | 163.8176 | 164.3534 | 164.3534 | 164.7169
A=0.28 | 155.0309 | 157.1411 | 158.1072 | 160.1363 | 161.5781 | 162.1705 | 163.0761 | 162.9897 | 163.4958 | 163.2464 | 162.5442 | 163.3304 | 162.2655
Tests of the acoustic transceivers and electronics
The sound emission board
Preliminary
Test of sound emission:
FFR +Sound emission board
Transceiver pressure test at IFREMER Brest

## Slide 15: Joint tests: transceivers and hydrophones
Water tank tests at university of Valencia (Gandia):
Hydrophones SMID, Transceiver FFR
Signal emitted by the Sound emission board: 30 µs (1 cycle) | f= 32 kHz |A  10 Vp
trigger time
e.m. pulse
on H1 and on H2 at
166.1 +7.5 = 173.6 µs
acoustic pulse on H1
(about 15 cm)
acoustic pulse on H2
(about 30 cm)
Preliminary

## Slide 16: Opto Acoustic modules for NEMO phase II and KM3NeT
Adopt design of Acoustic Modules (AMs), used successfully in AMADEUS as part of ANTARES
Design allows for integration of acoustic sensors into pressure housing of photo sensors to form Opto-Acoustical Modules (OAMs)
Piezo sensor + preamplifier
30mm
21mm
Aluminum tube:
Piezo + preamplifier
Mechanical container
shielding
ECAP Piezo

## Slide 17: Opto Acoustic modules for NEMO phase II
Acceptance: ± 70°
OAM layout for the tower
Piezo inside OAM
Noise floor spectrum
hydrophone
Test with empty glass sphere

## Slide 18: The Capo Passero Infrastructure
Shore Laboratory in Capo Passero harbour
Suitable for KM3NeT and EMSO
Shore laboratory
Power supplier 10 kV - 50 kW
Optical fibre link to LNS (end 2011)
Submarine cable:
100 km - 20 fibres, DC-sea return
DC/DC Converter 10 kV-375 V 10 kW
3 ROV e.o. output connectors
The Capo Passero Site lies on a flat and wide plateau
CP Site
Will host: ANTARES mini-line, NEMO Phase II - SMO, KM3NeT Prototype

## Slide 19: Design of acoustic sensors and electronics for KM3NeT
Multi PMT option adopted for KM3NeT: DOM (Digital Optical Module)
DOM:Multi PMT
Central Logic Board
Acoustic Mezzanine
Piezo inside the DOM
Hydrophone outside
the DOM

## Slide 20: KM3NeT and EMSO

## Slide 21: Acoustic detectors at the INFN-LNS Catania Infrastructure
LNS Test Site Laboratory
at the port of Catania
LNS-INFN Catania
Internet Radio Link
Test Site South
5 km
20 km
Test Site North
5 km
NEMO JB
Two observatories with sensors for bioacoustics, ocean monitoring, geohazards re ready for deployment
4 hydrophones
CTD
Seismometer
Magnetometers
ADCP
pressure gauge
4 hydrophones
GPS
time- stamp

## Slide 22: NEMO-ODE hydrophones the sperm-whales !
Very good news from ODE:
Almost daily detection of
sperm-whales
The major environmental agencies declared that sperm-whales were declining in the area
Estimated population of sperm-whales (units of 1000) from 1700 to 2000
N. Nosengo, G. Pavan and G. Riccobene, Nature 462 (2009), 560
Dolphins and sperm-whales’ sounds detected almost daily.
Optimal SNR in deep sea. Optimal sampling frequency and sensitivity.

## Slide 23: Sperm-whales’ tracking
Sperm-whale click
Wave direction reconstruction through TDoA on 4 hydrophones  source tracking
Limited size of the ODE detector permits to measure wave source direction in plane wave approximation.
Surface reflection permits determination of source position.

## Slide 24: Improved algorithms for tracking sperm-whales
Correct speed  10 km/h
Dive profile
F. Bénard, H. Glotin and P. Giraudet
UMR CNRS LSIS – Univ. du Sud Toulon Var
Depth (m)
Time (s)
F. Bénard et al., J. Appl, Aco. 71 (2010), 994
F. Bénard, H.Glotin and P. Giraudet, Appl. Acoust. 71 (2010), 994

## Slide 25: Improved algorithms for tracking sperm-whales
Depth (m)
15th august 2005 15:00, two sperm whales are diving together at -1000 m depth
Demo available at http://glotin.univ-tln.fr
F. Bénard, H.Glotin and P. Giraudet
UMR CNRS LSIS – Univ. du Sud Toulon Var

## Slide 26: Sperm-whales’ click analysis: size of the animals
P2-P1 (ms)
Total Length (m)
Head = 3.41 ± 0.05 m  Total length = 9.72÷10.50 m
Young male or female
About 50 animals identified
IPI = head(m) * cs / 2
Measurement of Inter-Pulse-Interval permits to determine of the size of the sperm whale
youngs
females
males
P1
P2

## Slide 27: Sperm-whales’ typical sounds and population
“regular clicks” (3 sperm whales)
coda (1 sperm whale)
Hunting, exploration, communication
communication
“3+1” Mediterranean dialect ? (54%)
“2+1” Atlantic ? (43%)
Most of the detected sperm-whales transit the area of the Gulf of Catania towards or from the Messina Strait.
Seasonal presence
Sperm-whales’ groups dimensions
G. Pavan et al., Proc. IE meeting on IT-based detection of bioacoustical patterns (2008), 7
CIBRA

## Slide 28: Noise spectrum correlation with ships and biological sources
Independent CIBRA analysis:
Number of dolphins detected during day and night.
Night is the hunting time for dolphins
They emit both echolocalization clicks (>20 kHz) and whistles.
In the spectral region between 20 and 40 kHz we observe a day-night effect with upto 50% variations.
In this region dolphins give a strong contribution to noise
kHz
dB
00/06
19/23
07/12
13/18
Dolphin detection rate
Preliminary
September 2005
Catania-Naples
ferry

## Slide 29: Geo-hazard: towards tsunami early warning systems
- Monitoring of volcanic and seismic activity in Sicily
- Development of Tsunami early warning systems
SN1 Connection
3-axis broadband seismometer
Low frequency hydrophone
3 axis accelerometer and gyro
Absolute pressure gauge
Differential pressure gauge
Scalar and vectoria magnetometer
Single point 3-axis current meters
Acoustic doppler current profiler
Conductivity, temperature and depth meter
4 large bandwidth hydrophones

## Slide 30: Acoustic waves: towards tsunami early warning systems
Peloponnesus (Greece, Feb. 14, 2008)
Sumatra (March 28, 2005)
Papua New Guinea (Nov. 7, 2006)
MW=6.6
MW=6.9
MW=6.2
MW=8.6
Multiparameteric observatory for early detection of tsunamigenic events:
- Seismic waves
- Magnetic field change
- Low f sound waves
Tsunamy early warning

## Slide 31: Conlcusions
Mediterranean groups have run experimental test towards acoustic neutrino detection
Technological R&D is in advanced state. Deep sea tests will run soon.
Efforts are converging in the framework of KM3NeT: acoustic positioning, neutrino detection tests, Earth and Sea science
Dedicated Acoustic JRA have been submitted within the HEAP-MM request to EU
(thanks to L. Thompson and K. Graf for coordination!)
Strong interaction with EMSO and other multidisciplinary science groups