## Slide 1: RD51 Test Beam Setup
Slots for DUTs
MCP for time reference (σt≈5ps)
Picosec sketch
Standard configuration:
3mm MgF2 radiator
12nm CsI photocathode
200um drift gap
128um thick mesh
100um amplification stage
GasNe/C2H6/CF4 (80/10/10)

## Slide 2: Preliminary results RD51 PicosecMM
We participated in the RD51 test beam in May/June 2022
10x10
Single-pad
New gap and mesh configurations
Thin-gap
Thin-mesh
Resistive MM
B4C photocathode
Baseline detector
RMS=23ps
RMS=21ps
RMS=22ps
RMS=18ps
RMS=24ps
RMS=41ps

## Slide 3: Status R&D PicosecMM
Pavia single-pad detector:
Micromegas from RD51
Still waiting for radiators (shipping before the end of July)
CsI deposition @ CERN in one/two days from arrival
Start of calibration in August @ GDD lab
Participate in RD51 October test beam as parasites
Pavia multi-pad detector:
Still waiting for radiators (shipping before the end of July)
Micromegas order placed @ Rui’s lab
  Should be ready before the end of September
Housing and readout board to be produced after the arrival of the components
Start of calibration expected in October/November