## Slide 1
Soren Prestemon
US Magnet Development Program
Lawrence Berkeley National Laboratory
US MDP instrumentation and diagnostics needs

## Slide 2: Outline
The Magnet Development Program vision and goals, & priorities of the current Roadmaps
Driving questions of the program
The roles of magnet diagnostics
HTS vs LTS magnets – some critical distinctions
Perspective on diagnostics needs of the MDP
Summary

## Slide 3: Recap of our MDP vision and goals
Maintain and strengthen US Leadership in high-field accelerator magnet technology for future colliders
Focus on the four primary goals identified in the the original MDP Plan
  Explore the performance limits of Nb3Sn accelerator magnets, with a focus on minimizing the required operating margin and significantly reducing or eliminating training
  Develop and demonstrate an HTS accelerator magnet with a self-field of 5T or greater, compatible with operation in a hybrid HTS/LTS magnet for fields beyond 16T
  Investigate fundamental aspects of magnet design and technology that can lead to substantial performance improvements and magnet cost reduction
  Pursue Nb3Sn and HTS conductor R&D with clear targets to increase performance and reduce the cost of accelerator magnets
Further develop and integrate the teams across the partner laboratories and Universities for maximum value and effectiveness to the program
Identify and nurture cross-cutting / synergistic activities with other programs to more rapidly advance progress towards our goals

## Slide 4: Program roadmap – 2020 Detailed Plan
Strategic priorities for the current plan:
  Probing stress management structures
  Hybrid HTS/LTS designs
  Understanding and impacting the disturbance-spectrum
  Advancing both LTS and HTS conductors, optimized for HEP applications
=> Need to focus towards key hybrid magnets

## Slide 5: Some driving questions of the program
Driving questions related to the ultimate performance limits of high-field accelerator magnets
  What is the nature of accelerator magnet training? Can we reduce or eliminate it?
  What are the drivers and required operation margin for Nb3Sn and HTS accelerator magnets?
  What are the mechanical limits and possible stress management approaches for Nb3Sn and 20 T LTS/HTS magnets?
  What are the limitations on means to safely protect Nb3Sn and HTS magnets?
Driving question related to conductor development for high-field accelerator magnets
  What are the near and long-term goals for Nb3Sn and HTS conductor development? What performance parameters in Nb3Sn and HTS conductors are most critical for high field accelerator magnets?

## Slide 6: The roles of magnet diagnostics
Diagnostics are our “eyes and ears” into magnet behavior and performance
We predict magnet behavior and performance via advanced modeling
  Solid agreement between models and diagnostics is an indication of understanding
Diagnostics can serve multiple purposes
  E.g. support quench detection while also providing data for system integrity monitoring
  Provide insight into complex EM phenomena, e.g. current redistribution, vortex dynamics
  Identify mechanical responses, e.g. strain, interface behavior
Data capture and analysis requirements can span orders of magnitude
  E.g. in sensitivity and in temporal bandwidth

## Slide 7: In LTS, we need insight for control and for design feedback
Diagnostics for control & event analysis:
  Reliable diagnosis of quench for protection – voltage-based systems work!
    Always interested in “cleaner” signals, and localization
  Quench antennas are in constant demand – non-invasive, ”local”, broadband
Diagnostics for design:
  What are the energy sources in the disturbance spectrum?
  What design modifications can best influence performance?
Can diagnostics be identified to monitor system integrity over time?
    Fatigue, radiation effects, etc.

## Slide 8: HTS vs LTS superconductors & magnets – some key distinctions
HTS materials outperform LTS at higher field, but under-perform at low field
=> hybrid magnets are most efficient

## Slide 9: Recap of motivation for magnet protection design
Traditional superconducting magnet design ensures magnet can survive quenches
  Motivation:
    spontaneous quenches => lack of reliable precursor, not controllable
    Training => potential for improved performance after quenching
  Design:
    Detect quench, trigger protection response
    Response typically includes some mix of extraction via dump, heaters to enhance QP, etc.
      Use the low heat capacity of the superconductor to our advantage

## Slide 10: HTS superconducting magnets behave differently
Higher MQE implies not (?) susceptible to spontaneous quenches => no “random” behavior
So far no indication that HTS magnets exhibit training => no performance enhancement
Questions for diagnostics:
  Are there quench precursors that can be seen with sufficient time to extract energy (fully or partially) and reliably avoid runaway quenches?
  What is the impact on detection & response of HTS magnets in presence of LTS “outsert”?
T. Shen et al., PHYS. REV. ACCEL. BEAMS 25, 122401 (2022)

## Slide 11: REBCO in particular exhibits flux flow regime
LTS transitions rapidly – typically determined by ”n-value”
REBCO has sizeable regime of “flux-flow” – resistive regime
Thermally activated region incapable of supporting transport current
Wilson, lecture notes
q
r
metallic
q
r
Oxide HTS
flux flow
Wai-Kwong Kwok et al 2016 Rep. Prog. Phys. 79 116501
Penetration of vortices into a superconductor: real-time magneto-optical movie. Each vortex carries one quantum of magnetic flux and is seen as a bright dot. After cooling in a low magnetic field, the field is ramped and vortices slowly enter the superconductor from the edge (located at the top). At larger fields the surface barrier is broken and many vortices penetrate very fast. Movie window: 25x35 microns, sample: NbSe2 crystal, Lab: University of Oslo. More details: http://www.fys.uio.no/super/results/sv

## Slide 12: Transition behavior is complex in HTS cables
Anisotropy & Irreversibility-field impact modeling/understanding of EM response for REBCO
Conductor homogeneity is an issue (particularly for REBCO)
Current sharing is a function of many parameters
X. Wang et al., SUST 35 (2022) 125011
Can current sharing allow Ic inhomogeneity-tolerance?
Can it enable use of short(er) tapes?
  Answer seems to be mixed…

## Slide 13: Perspective on diagnostics needs of MDP
Primary considerations for HEP are:
  Magnet protection in the broad sense
  Understanding performance limitations
  Identifying degradation mechanisms, boundaries
Characteristics we would like from diagnostics:
  Capable of spatially and temporally locating critical events
  Providing sufficient details to identify and characterize the event source
  Automated, “resolved” data capture and storage to enable further data mining
  Diagnostics should be reliable, redundant, preferably non-invasive, and utilize independent physics mechanisms

## Slide 14: Some ideas on where I think/hope things are headed
High bandwidth diagnostics coupled to in-situ FPGA data analysis
Multiple “physics-independent” diagnostics that are analyzed and cross-corelated
AI/ML utilized to weed out irrelevant data and to identify critical events/behavior
Almost all data acquisition, analysis, and decision making occurring ”below the header”
  Only digital data sent “out”, preferably via redundant fiberoptics (non-conductive)
Stored diagnostics data is monitored/analyzed routinely for system integrity checks
  Modeling is coupled to diagnostics => digital twin that corelates cause and effect
Cryo-power electronics (MOSFETS, IGBTs, etc) are developed to actively control/route power => become integral to magnet protection

## Slide 15: Summary
Instrumentation and Diagnostics are core elements that provide the “science” of magnets
We count on diagnostics for…
  insight into performance,
  feedback on design, and
  for safe operation
Diagnostics experts must interact closed with modeling experts, magnet designers, and magnet operators – communication is vital in both directions!