## Slide 1
2nd Instrumentation and Diagnostics for Superconducting Magnets Workshop
Marcos Turqueti
2023
Advances in Cryo-Electronics

## Slide 2
Collaboration

## Slide 3
Why?
Reduced noise: Analog signals are susceptible to noise and interference from various sources, such as electromagnetic interference (EMI) and radio frequency interference (RFI). Digitizing signals close to the sensor reduces the distance the signal has to travel before being converted to a digital signal, enhancing the SNR;
Improved accuracy: Digitizing signals close to the sensor can improve accuracy by reducing signal attenuation, distortion, and other losses that can occur when signals are transmitted over long distances;
Lower power consumption: Digitizing signals close to the sensor can reduce the power consumption of the overall system. This is because analog signals require more power to transmit over longer distances, while digital signals can be transmitted with less power;
Eliminating high voltage on signal lines outside the cryostat;
Simplifying interfaces. For a fully immersed DAQ a single optical fiber can come from the cryostat instead of hundreds of lines for a fully instrumented system.

## Slide 4
FD2-VD Photon Detector Cold Electronics Workshop
At very high E-fields the electron (hole) does not remain in the same band during transport. For example, an electron can scatter with an electron which is in the valence band an knock it into the conduction band
In a semiconductor electrons can become “hot” at any temperature, by attaining energy E>kT . Some hot electrons exceed the energy required to create an electron-hole pair, resulting in impact ionization.
A very small fraction of hot electrons exceeds the energy required to create an interface state (e.g., an acceptor-like trap), in the Si-SiO2 interface, for electrons (~4.6eV for holes). This alters the transistor characteristics.
Problems with Cold Electronics
Temperature dependence of majority carrier concentration in n-doped silicon. The phosphorus concentration is 10¹⁵ cm⁻³
Freeze-out reduces the carrier concentration at the conducting band with decreasing temperature. Freeze-out, however, depends on the dopant type and semiconductor type.

## Slide 5
Commercial off-the-shelf cryogenic components (4k-77k)
  ADCs, Amplifiers, Diodes, FPGAs, Laser Diodes, Optical Isolators , Voltage Regulators, Transistors and Passives
Field Programmable Gate Array (FPGA) on Cryogenic Environments
Cryogenic Magnetic Sensors
Optical Power Converter
Plastic Fiber Optic Communications
GFET for Cryogenic Applications
Custom Cryogenic Application Specific Integrated Circuit
Ongoing Activities
ATAP, Nuclear Sciences and Engineering

## Slide 6
Head Interface
Computer
Laser P. Supply
Optical
Power Conversion
Typical Readout Chain
FPGA
Power Fiber
Comm Fiber
Voltage Taps
Strain Gauges
Quench Antenna
Other
ISOADC
ADC
ADC
ADC
DC Power
OR

## Slide 7
Head Interface
Computer
Laser P. Supply
Optical
Power Conversion
Typical Readout Chain
FPGA
+
ISODIGITIZER
Power Fiber
Comm Fiber
Voltage Taps
Strain Gauges
Quench Antenna
Other

## Slide 9
Field Programmable Gate-Array
500 I/Os
Circa 2016
fADC

## Slide 10
3 mm
Integrated Sensors
Power + Serial Digital Line

## Slide 11
Pre-amp
qAMP(THS4131)
Signal Amplifier
JFET
MX11 cooled LN i=8mA
Cables
FE-qAMP (1.1m) – 105pF (per line)
qAMP-DAQ (11m) – 1nF (per line)

## Slide 12
Optical Power

## Slide 13
13
POF Receiver
LN - Blue TX, Yellow RX (1MHz)
POF Under Test
POF Receiver – When cold requires the receiver voltage bias to be increased. Generally the transmitter needs to work on top of a higher light intensity. Clock speeds up to 100MHz are achievable with POF.
Optical Communications
Plastic Optical Fiber

## Slide 14
Electrical properties: Graphene has a very low resistivity at room temperature, as well as intrinsic mobility over 100 times that of silicon and ideal coupling between charge carriers in an atomic layer.
  Superior Noise Performance can be achieved
  Lower Power Dissipation
  Fast devices
High thermal conductivity: Graphene is an isotropic conductor that dissipates heat in all directions and has better thermal conductivity than other materials.
Good optical properties: Graphene is extremely thin and has very high conductivity, when combined with the right substrate it is an attractive material for building highly efficient magnetic detectors.
Cryogenic operation: Graphene is not a semiconductor and therefore is not subjected to carrier-freeze out. GFETs improve its noise performance when operating cold.
Excellent Radiation Hardness
W=L=50 μm
Graphene Field Effect Transistor (GFET)

## Slide 15
Demonstrate the spinning current noise cancellation technique with GFET.
Lucas Brouwer LNBrouwer@lbl.gov / Marcos Turqueti Mturqueti@lbl.gov
GFET Hall Effect Probe

## Slide 16
GFET Amplifier