## Slide 1: SPARC_LAB synchronization system status/upgrade
Luca Piersanti, Marco Bellaveglia, Alessandro Gallo, Simone Tocci

## Slide 2: Synchronization system general architecture
FLAME Area
SPARC Bunker
BLD. 7:
TEX + THz users
CONTROL ROOM
Modulator Hall
K1
K2
K3
SYNCH HUB
FLAME
LASER
PC
LASER
LINAC
FEL UNDULATOR
THz UNDULATOR

## Slide 3: Synchronization system general architecture
PC laser
Klystron 1
Klystron 2
Klystron 3
RMO
Locking
electronics
KLY phase loop 1
KLY phase loop 2
5712 MHz
2856 MHz
FLAME laser
Locking electronics
Laser systems
RF systems
Synchronization Diagnostics
2142 MHz

## Slide 4: Reference Master Oscillator (RMO)
RMO currently in use @SPARC_LAB is from RALAB and has coherent outputs at three different frequencies:
  2856 MHz (RF S-band): ~60 fs RMS jitter (10 Hz - 10 MHz from f0)
  5712 MHz (RF C-band): ~60 fs RMS jitter
  2142 MHz (3/4 RF S-band, for diagnostics interference-free purpose): ~60 fs RMS jitter
We are planning to switch to different manufacturer

## Slide 5: RF reference distribution
Coaxial cables built to minimize the elongation VS temperature @ 24 °C (using a suitable dielectric material)
For demanding applications (e.g. longer paths, lower attenuation) an active stabilized link is required (see upgrade slides)
Coaxial cables Commscope Andrew
For a 3/8" cable (FSJ2-50):
cable length
carrier frequency
in MHz
propagation velocity
(relative to c)

## Slide 6: PC laser locking system
Galvo motor inside MIRA oscillator bypassed
Native noisy locking electronics bypassed
Native BW limited PD bypassed
New photo detector, phase detector and loop error amplifier designed and optimized
Stepper motor:
coarse positioning
low freq. drift compensation
Piezo motor:
fine positioning,
up to 5-10 kHz BW
12.6 ns
Piezo driver
Phase detector and error amp
RMO
Signal
Mode-locked laser oscillator cavity
Photo-detection
and filtering
Stepper driver
Control system
software

## Slide 7: PC-laser locking recent upgrades and open points
New fast PD in-loop installed (Hamamatsu G4176-03, 30 ps rise time)
New fast PD for out-of-loop diagnostics installed
Optimization of the amplifier chain (low noise amp.)
Measured jitter relative to the reference is ~20 fs RMS
7
In-loop PD
Out-of-loop PD

## Slide 8: PC-laser locking high resolution measurement

## Slide 9: RF sources locking: intra-pulse phase loop (Klystron loop)
Phase noise source is the klystron high voltage switch (thyratron)
Very short time ≈ 3μs available to reach steady state wideband loop transfer function (≈1 MHz) required.
PLL on:
Dt < 70 fsRMS
PLL off:
Dt ≈ 500 fsRMS

## Slide 10: Intra-pulse feedback performance and open points
Intra-pulse feedback high resolution measurements show a residual jitter ̴50 fs RMS between klystron output and RF reference
A number of optimization are still in progress:
  Substitution of a damged DC (distortion in the RF signal -> error ampl.)
  Upgrade of the fast phase shifters (high BW) and error amplifier (fast OP-AMP)
  Investigation on a «feed forward» circuit to pre-compensate the modulator HV jitter

## Slide 11: Future upgrades for LLRF and synchronization systems
During 2023 a major upgrade of the RF and synchronization systems is foreseen at SPARC:
  3 new digital LLRF system
  New RMO
  New RF distribution electronics
  Re-cabling of several RF devices with phase stable cables
  Refurbishment of the Synchronization hatch (ongoing)
  Intra-pulse feedback around the C-band klystron (supplied by a solid-state modulator) is under design to test the limit of such technology
  Commissioning of a commercial optical synchronization system (MENLO) to serve PC-laser, FLAME (with fiber link active stabilization). In the future 2 more clients are foreseen: betatron source and THz users
  OMO and one stabilized fiber link already commissioned at LNF (currently the link is being re-commissioned after a fault)
  2 cross-correlators used as phase detectors (PC-laser and FLAME) to be commissioned
  Design and realization of a dedicated error amplifier to close the loop around the 800 nm oscillators (PC-laser and FLAME)
  Spare parts purchasing