## Slide 1
Sapienza University of Rome
PhD Course on «Accelerator Physics»
Low Emittance Muon Accelerator (LEMMA)
Study of the features of a multiple targets system for the LEMMA project.
September 06, 2022
Supervisors:
Prof. Gianluca CAVOTO
Dr. Francesco COLLAMATI
Student:
Fausto CASABURO

## Slide 2
Outline of the presentation
Introduction:
Muon Colliders.
The LEMMA project.
LEMMA Multi-target studies:
Investigation of a multi-target system building.
Thermal model.
Planning of thermal studies at MAMI accelerator.
e+e-→µ+µ- cross-section:
Measurement at CERN.
Relevance of the thesis:
If a multi-target system could resiste the heating it will be a huge step for future accelerators.
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
Cross-section
Conclusion

## Slide 3
Muon Colliders
Why a muon collider?
Muons are elementary particles.
mμ ≈ 207me.
Negligible synchrotron radiation and beamstrahlung → Extend lepton accelerators to multi-TeV scale.
Challenges of a muon collider:
Low muon lifetime (~ 2.2µs at rest).
Need of low emittance to reach high luminosity (~1034cm-2s-1).
Comparison between a muon collider and an hadron one. (From D. Lucchesi et. al. «Muon Collider to expand frontiers of particle physics»).
Comparable Feynman e.w. amplitudes
*10 enhancement due to additionaly strong interactions
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 4
Proton driven Muon Collider
Classical scheme (proton driven):
Few GeV protons on target.
Muons produced as tertiary particles (pμ~100MeV).
Advantages:
Cross-section (~1mb at most) → High muon rate (1013-1014µ/s).
Disadvantages:
High emittance → Cooling system.
Proton driven muon collider scheme (From M. Bauce talk at APS 2021).
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 5
Low EMittance Muon Accelerator (LEMMA)
The LEMMA project:
Exploit e+e-→µ+µ- (√s~0.212).
Positron beam.
Low Z fixed target (Be, C).
Goal 1011 μ±/s.
Muon production in e+ e- annihilation (From M. Bauce talk at APS 2021).
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 6
Muon production in LEMMA scheme
Process at √s~0.212GeV:
Cross section increases with √s.
Opening angle and energy spread increase too → Evaluate emittance deterioration (45GeV positron beam currently under study).
Cross section (left), scattering angle (center) and energy spread (right) of muons produced in electron-positron annihilation (From M. Bauce talk at Giornate sull’European Strategy 2020, and M. Antonelli et al. «Novel proposal for a low emittance muon beam using positron beam on target»).
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion
45GeV beam
45GeV beam

## Slide 7
LEMMA advantages and disadvatages
Advantages:
High Lorentz boost (γ~214) → laboratory lifetime ~500μs.
Low emittance → No cooling.
Disadvantages:
Small cross-section (~1µb at most) → High intensity positron beam.
LEMMA concept (From M. Bauce talk at APS 2021).
NIM A Reviewer: “A major advantage of this proposal is the lack of cooling of the muons…. the idea presented in this paper may truly revolutionise the design of muon colliders … “ ( From R. Raimondi talk at La Thuile 2018).
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 8
Target options for LEMMA
Goal:
Continuos muons production preserving muons and beam quality.
Heavy & thin:
Low emittance.
High beam loss → low muon efficiency.
Very light & thik:
Higher muon efficiency.
Muon emittance increase.
Not too heavy & thin:
Optimization of muon efficiency and emittance → Be, C (ρ- ~O(1024e-/cm3)).
Muon production (From M. Bauce talk at Giornate sull’European Strategy 2020).
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 9
The multi-target proposal
Target best thickness (muon optimization):
0.3X0, but it would melt.
Reduce the deposited energy splitting the target.
Challanges:
Maximise muon number.
Minimise emittance and thermomechanical stress.
Multi-target concept (From arXiv 1905.04747).
Muon production as a function of X0 (From arXiv 1905.04747).
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 10
GEANT4 simulation of the multi-target
Starting point (from single target studies):
45GeV Gaussian positron beam (σ=300µm, 3*1011 e+/bunch).
3mm Be slices (~0.85%X0).
1mm C slices (~0.52%X0).
First step:
2 slices.
Relative distance d=2cm.
Pictorial view of the multi-target.
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 11
Goal of the GEANT4 studies on the multi-target
Goal:
Deposited energy.
Beam intensity and energy loss.
Beam emittance increasing.
Muon production.
Muon emittance.
Parametric studies:
Beam features.
Multi-target features.
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 12
Deposited energy density in the multi-target
Target discretization in (R,z):
Peak Energy Deposited Density (PEDD) σ=300µm, 3*1011e+/bunch :
Be: 22J/cm3 (threshold 230J/cm3).
C: 27J/cm3 (threshold 210J/cm3).
Thresholds from https://dx.doi.org/10.1007/s10765-021-02913-x
Deposited energy density by 3*1011 primary positrons- Be 3 mm (single slice thickness) .
PEDD
First target
Second target
Sketch of the positron Gaussian beam and target discretization in (R,z) cylindrical shells.
Gaussian
core
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 13
Parametric study:
Beam spot size [150µm;1000µm].
Results (3*1011e+/bunch):
PEDD decreasing as 1/σ2.
Be [2.1 J/cm3- 88J/cm3] (PEDD).
C [2.6 J/cm3- 110J/cm3] (PEDD).
PEDD by 3*1011 primary positrons- Be 3 mm
(slice thickness) target as a function of spot size.
500 µm
First target
Second target
1000 µm
150 µm
300 µm
Deposited energy density in Be 3 mm (slice thickness) target for several spot sizes.
Deposited energy density as function of spot-size
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 14
Theory:
Mean energy crossing the target:e
Muon production threshold 43.69GeV.
Parametric study:
Be slices [1.5mm-6mm] (45GeV e+).e
C slices [0.5mm-2mm] (45GeV e+).
Results:
dre+43.69GeV/dx ~0.010 mm-1 (Be).
dre+43.69GeV/dx ~0.018 mm-1 (C).
d<E>/dx ~0.12 GeV/mm (Be).
d<E>/dx ~0.21 GeV/mm (C).
Be 12mm
Be 6mm
Be 3mm
C 2mm
C 1mm
C 4mm
Beam losses
Surviving positrons with energy over muon pair production threshold for several turns.
Intensity loss of surviving positrons with energy over the muon production threshold in a Be multi-targets as a function of total thickness.
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 15
Beam losses as a function of beam energy
Theory:
Mean energy crossing the target:e
Muon production threshold 43.69GeV.
Parametric study:
Beam energy [44GeV;48GeV] (Be 6mm, C 2mm total thickness).
Results:
Be: dre+43.69GeV/dx from ~ 0.007mm-1 (48GeV) to ~ 0.02 mm-1 (44GeV).
C: dre+43.69GeV/dx from ~ 0.01mm-1 (48GeV) to ~ 0.03 mm-1 (44GeV).
Surviving positrons with energy over muon pair production outgoing a 6 mm Be and 2 mm C multi-target as a function of the beam energy.
Beryllium
Carbon
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 16
Beam emittance increase due to scattering angle
Scattering angle contribution to emittance (εRMS):
Exiting angle:
Coulumbian scattering → Emittance increasing.
εRMS given by:
being
Parametric study:
Be slices [1.5mm-6mm] (45GeV e+).
C slices [0.5mm-2mm] (45GeV e+).
Results:
εRMS increases with the thickness (but few nm*rad).
x-x’ correlation of primary positrons exiting a 6 mm total thickness Be meniscus multi-target.
εRMS results of primary positrons outgoing a multi-target.
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Thermal
model
Test at MAMI
TB 2018
Conclusion

## Slide 17
Positron regeneration proposal
Goal:
Possibility to produce e+ via γ→e+e-.
Source for LEMMA.
Positron regeneration simulation:
Magnet (2T).
Tungsten regenerator (r=1mm, l=2cm).
Pictorial view of positron regeneration.
Positron regeneration scheme. (From arXiv 1905.05747).
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 18
Positron regeneration in the multi-target scheme
Parametric study:
Be slices [1.5mm-6mm] (45GeV e+).e
C slices [0.5mm-2mm] (45GeV e+).
Acceptance conditions arXive 1905.05757):
r<0.5cm (z-axis)
Angle [-0.5rad;0.5rad].
Energy [5MeV;20MeV].
Positron regeneration results:
Regenerated positrons increases with the thickness of the target.
Their number is higher than the loss ones.
Normalized number of photons produced in the multi-target and hitting the regenerator (nγreg), regenerated positrons (ne+reg) and regenerated positrons passing the acceptance conditions (ne+regcut).
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 19
Deposited energy density in the regenerator
Parametric study:
Be slices [1.5mm-6mm] (45GeV e+).e
C slices [0.5mm-2mm] (45GeV e+).
Results (3*1011e+/bunch):
Dependency on the radius and on the beam axis.
PEDD [120 J/cm3- 350J/cm3] (Be 6mm total thickness).
PEDD [70 J/cm3- 230J/cm3] (C 2mm total thickness).
PEDDs lower than threshold (675J/cm3).
12 mm
6 mm
3 mm
Deposited energy density in the regenerator by photons produced by a single bunch of 3*1011 positrons in a 6mm total thickness Be multi-target..
Deposited energy density in the regenerator by photons produced by a single bunch of 3*1011 positrons in a Be multi-target..
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 20
Theory
Muon production:
Parametric study:
Be slices [1.5mm-6mm] (45GeV e+).e
C slices [0.5mm-2mm] (45GeV e+).
Results (n+=1):
Efficiency ~10-7 µ±/e+(Be 6mm,C 2mm).
Be: dµ/dX0 ~1.6*10-5 X0-1.
C: dµ/dX0 ~1.1*10-5 X0-1.
Muon production in the multi-target
3mm
6mm
12mm
18.6 GeV
26.2 GeV
22GeV
Dependency on the thickness of the number of muons produced in Be cylindrical multi-target.
Energy spectrum of muons produced in a Be cylindrical multi-target.
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 21
Theory
Muon production:
Parametric study:
Be slices [1.5mm-6mm] (45GeV e+).e
C slices [0.5mm-2mm] (45GeV e+).
Multi-turn results:
Beam energy loss→ Saturation after few tens of turns (no decay considered).
Muon production in a multi-turn scheme
Muon production in a Be and C multi-target for several runs.
Be 12mm
C 1mm
C 2mm
C 4mm
Be 12mm
Be 6mm
Be 3mm
C 2mm
C 1mm
C 4mm
Mean energy of the beam after hitting the multi-target for several turns.
Be 6mm
Be 3mm
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 22
Muon production as a function of beam energy
Theory
Muon production:
Parametric study:
Beam energy [44GeV;48GeV] (Be 6mm, C 2mm total thickness).
Results (n+=1):
Similar scattering angle in Be,C.
Be: dµ/dX0 from ~ 0.9*10-5 X0-1 (44GeV) to ~ 2.7 *10-5 X0-1 (48GeV).
C: dµ/dX0 from ~ 0.6*10-5 X0-1 (44GeV) to ~ 1.8 *10-5 X0-1 (48GeV).
Beryllium
Carbon
Muons number (left) and scattering angle (right) in a 6mm total thickness Be and 2mm total thickness C multi-target as a function of the beam energy.
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion
Beryllium
Carbon

## Slide 23
x-x’ correlation of muons produced in a 6mm total thickness Be multi-target.
.
First target
Second target
Mean RMS angle and its contribution to emittance multi-target.
Scattering angle contribution to emittance (εRMS):
Exiting angle:
Coulumbian scattering → Emittance increasing.
εRMS given by:
being
Parametric study:
Be slices [1.5mm-6mm] (45GeV e+).e
C slices [0.5mm-2mm] (45GeV e+).
Results:
εRMS increases with the thickness (but few nm*rad).
Muons from first slice → larger contribution to εRMS.
Scattering angle contribution to emittance εRMS
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 24
Dependency of εRMS on relative distance in a 6 mm total thickness Be and 2 mm C multi-target.
Beryllium
Carbon
Mean RMS angle contribution to emittance (εRMS):
Exiting angle:
Coulumbian scattering → Emittance increasing.
εRMS given by:
being
Parametric study:
Relative distance [0.5cm-4cm] (45GeV e+, Be6mm, C2mm).e
Results:
Larger drift for larger relative distance → εRMS increases.
εRMS as a function of relative distance
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 25
Beryllium
Carbon
Mean RMS angle contribution to emittance (εRMS):
Exiting angle:
Coulumbian scattering → Emittance increasing.
εRMS given by:
being
Parametric study:
Number of slices [2-5] (45GeV e+).
Results:
Same total slice thickness→ larger εRMS using more slices (due to vacuum space).
Example 2*6mm Be εRMS~4.6nm*rad, while 4*3mm Be εRMS~8.9nm*rad,
Dependency of εRMS on the number of targets.
Sizes of each slice 3mm Be and 1mm C.
εRMS as a function of number of targets
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 26
Beryllium
Carbon
Dependency on beam energy of εRMS (right) on the beam energy in a 6 mm total thickness Be and 2 mm total thickness C target.
Mean RMS angle contribution to emittance (εRMS):
Exting angle:
Coulumbian scattering → Emittance increasing.
εRMS given by:
being
Parametric study:
Beam energy [44GeV-48GeV].e
Results:
dεRMS/dE ~2.5nm*rad/(GeV) (Be 6mm).
dεRMS/dE ~2.2nm*rad/(GeV) (C 2m).
εRMS as a function of beam energy
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 27
Small thickness target:
Geometric emittance:
EXMP-scheme:
Muon production in photon-electron interaction.
Normalized emittance:
bening
EXMP-based formula for LEMMAscheme:
Normalized emittance:
Theoretical formulas of muon emittance
EXMP scheme (From C. Curatolo and L. Serafini «Electrons and X-rays to Muon Pairs (EXMP)).
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 28
3mm
6mm
12mm
Angular spectrum of muons produced in a Be ìmulti-target, for several total thicknesses.
Theory:
For small target thicknesses:
EXMP-based developed formula:
The emittance (ε) is:
being
Parametric study:
Spot size [150 µm;1000 µm] (45GeV e+).
Results:
ε increases with the spot size.
Rough values but Upper Limit (UL) on beam emittance from EXMP formula.
MC
Theoretical
EXMP-based
Emittance of muons as a function of spot size
Dependency of the emittance on the spot size in a 6 mm total thickness Be multi-target.
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 29
First target
Second target
Deposited energy density in additional materials
Parametric study:
Liquid H 36 mm~0.40%X0 (45GeV e+).e
Liquid He 39 mm ~0.62%X0 (45GeV e+).e
Li 9 mm~0.58%X0 (45GeV e+).e
Deposited energy results:
d<E>/dx ~0.023 MeV/mm (H).
d<E>/dx ~0.024 MeV/mm (He).
d<E>/dx ~0.080 MeV/mm (Li).
d<E>/dx ~0.28 MeV/mm (Be).
d<E>/dx ~0.32 MeV/mm (C).
Peak Energy Deposited Density (PEDD) σ=300µm, 3*1011 e+/bunch :
~2.0 J/cm3 (H).
~ 1.8 J/cm3 (He)
~ 6.4 J/cm3 (Li)
PEDDs lower than Be, C.
First target
Second target
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion
PEDD by 3*1011 primary positrons (σ=300μm) for several materials.
Deposited energy for unit of thickness for several materials.

## Slide 30
Muon production in additional materials
Theory:
Muon production:
Parametric study:
Liquid H, 36 mm (45GeV e+).e
Liquid He, 39 mm (45GeV e+).e
Li, 9 mm (45GeV e+).e
Results (n+=1):
H: dµ/dX0 ~ 3.8*10-5 X0-1
He: dµ/dX0 ~ 2.8*10-5 X0-1
Li: dµ/dX0 ~ 2.1*10-5 X0-1
H: dµ/dx ~ 0.43*10-8 X0-1
He: dµ/dx ~ 0.38*10-8 X0-1
Li: dµ/dx ~ 1.4*10-8 X0-1
Muon production for unit of thickness of several materials.
He 78mm
Li 9mm
H 72mm
Be 6mm
C 2mm
Muon production as a function of the turn for several materials.
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 31
Mean RMS angle contribution to emittance (εRMS):
Exting angle:
Coulumbian scattering → Emittance increasing.
εRMS given by:
being
Parametric study:
Liquid hydrogen, 36 mm (45GeV e+).e
Liquid helium, 39 mm (45GeV e+).e
Liquid lithium, 9 mm (45GeV e+).e
εRMS of muons results:
Higher εRMS than using 6mm Be and 2mm C total thickness multi-target.
Muons εRMS increase in additional materials
Mean RMS angle contribution to emittance of muons for additional materials.
x-x’ correlation of of muons produced in a 72mm total thickness H multi-target.
.
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 32
Proposed shapes of the multi-target
Goal:
Minimise heat exchanges and thermomechanical stresses.
Proposed shapes:
Cylindrical.
Meniscus.
Hourglass.
Linear-hourglass.
Considerations:
The shape does not affect deposited energy and kinematics, but to be consider for thermomechanical stress studies (view factors).
Proposed geometries
Cylindrical
Meniscus
Hourglass
Linear-hourglass
Considered geometrical shapes.
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 33
Thermal model
Features:
Collaboration with SBAI Department.
Based on the deposited energy got by multi-target simulation.
Single target (up to now).
Goal:
Thermal evolution in the target.
Reference values:
45GeV positron beam (σ=300µm, 3*1011 e+/bunch).
3*1014 e+/s → O (107µ±/s).
3mm Be and 1mm C targe.
Published Article:
‘’Theoretical Modeling for the Thermal Stability of Solid Targets in Positron-Driven Muon Collider” (International Journal of Thermo Physics).
Considered beam.
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 34
Thermal model Fourier’s equation based
Thermal evolution in the target:
Fourier’s equation:
2D space (R,z),
k, cp and D=k/(ρcp) recalculated at each Δt→Long computational time.
Thermal evolution in the target (45GeV, σ=300µm, 3*1011 e+/bunch, R=5cm), for a single train:
Beryllium ΔT=451K (L=3mm).
Carbon ΔT=782K. (L=1mm).
Temperature rise at center due to single bunch. Be target (R=5cm, L=3mm ).
Bunch
No diffusion
Diffusion
Temperature rise at center due to
a single train. Be target (R=5cm, L=3mm ).
Train
No Train
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 35
Thermal model IR-based
Approximate-fast method:
Based on emitted energy via Infra-Red (IR) radiation:
being Pcw=Ed/trep
Results:
Thermal stability in long time scale.
Future perspective:
Experimental tests needed.
Application to multi-targets.
Temperature rise at long time scale. Be (left) and C(right) target. 45GeV, σ=300μm, 3*1011e+/bunch.
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 36
Planning of thermal studies @MAMI
Goal:
Thermomechanical properties of the target.
Test the thermal model.
MAinz MIcrotron (MAMI) Accelerator:
Mainz (Germany).
Electron Beam.
E~180MeV-1600MeV.
ΔE/E~2*10-5
Max ~50µA.
~7000h/year running.
MAMI accelerator.
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 37
Thermal studies @MAMI setup
Setup:
800MeV e-.
Single C target (thickness [0.5mm;1.3mm]).
Vacuum chamber.
Thermal camera to measure the heating.
Scheme of experimental test at MAMI.
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 38
GEANT4-based planning of thermal studies @MAMI
Theory:
Responsivity damage of IR
GEANT-4 simulation goal:
Radiation flux on the thermal camera to provide its safety.
GEANT4 simulation:
Steel vacum chamber 1mm thickness with 3 mylar windows
5cmx5cmx5mm scintillator. (reference value).
Estimation of radiation reaching the scintillator and deposited energy in it.
Vacuum chamber and scintillator
Scintillator
Chamber
Target
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 39
Radiation estimation @MAMI
Parametric study:
Target thickness [0.5mm-1.3mm] (800 MeV e-).e
Results:
Particle flux and deposited energy increase with the thickness of the target.
Example if ~1.3*105 e-/bunch (ILC test, S. Rieaman talk at AWLC 2017) → ~1.3particles/bunch and ~0.6MeV/bunch (s=1.3mm).
Mean values of deposited energy in scintillator.
Total
Particle flux hitting the scintillator.
ph0tons
electrons
total
positrons
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 40
Particle flux hitting the scintillator as function of wall thickness of the shield Al2O3. Target thickness 1.3mm.
Radiation estimation @MAMI
Reason:.
Thermal camera protection using an IR shield.
Materials:
Sapphire (Al2O3).
Quartz (SiO2 ).
Zinc sulfide clertran (ZnS).
Parametric studies:
Shield material (800MeV e-, C 1.3mm).
Shield thickness [1mm-4.mm] (800MeV e-, C 1.3mm).e
Results:
Particle flux and deposited energy reduced by the shield.
Best results using Al2O3.
Particle flux and deposited energy covering the scintillator with an IR shield. Target thickness 1.3mm. Shield thickness 1mm.
electrons
positrons
ph0tons
total
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 41
LEMMA Test Beam 2018 @CERN
Test beam (TB) goal:
Muon production in e+e-→µ+µ-.
Calibration runs:
18GeV-26 GeV electron and muon beams.
Data taking runs:
45 GeV positrons on target (Be, C).
Measurements:
Muon emittance.
Muon cross-section normalized to the Bhabha one.
Test Beam facility at CERN.
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 42
Experimental setup of the Test Beam 2018
Instruments for analysis:
Trackers.
Scintillators.
Lead Glass (LG).
HORSA absorber.
Analysed data:
22GeV electron and muon beams (calibration).
45GeV positron beam on C targets (2 and 6 cm).
Experimental setup.
Scintillator
Tracker 37
Lead Glass block
HORSA absorber
Scintillator
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 43
Cross-section measurement at Test Beam 2018
Parametric study:
C 2 cm ~10%X0 (45GeV e+).e
C 6 cm ~31%X0 (45GeV e+).e
Results (22GeV):
Nµ/Ne ratio in agrees with MC simulations.
But low statistichs.
Future perspective:
New test beam to increase statistichs.
Published article:
’Muon detection in electron – positron annihilation for muon collider studies’’ (Nuclear Instrument and Methods A).
Experimental ratio of produced 22GeV muons over electrons. 45GeV e+ on C target.
MC ratio of produced 22GeV muons over electrons. 45GeV e+ on C target.
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 44
Conclusions
Conclusions:
The LEMMA project overcames the cooling problem.
A single thick target would melt.
A multi-target could reduce the deposited energy.
Trade-off between muon production and deposited energy.
Be has lower deposited energy for unit of thickness, higher muon production for unit of X0, lower εRMS for unit of thickness and lower number of needed slices than C.
~1018e+/s needed to get 1011μ±/s (1.3*105W in 3mm Be and 5.1*104W 1mm C slices).
“Fatti non foste a viver come bruti, ma per seguir virtute e canoscenza.”
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 45
Future perspective
Future perspectives:
Implement in the simulation more functions (example magnets).
Apply the thermal model to more slice with differtent shapes.
Validate the thermal model by experimental tests (MAMI and other planned tests).
Weigh kinematic results with thermomecanical stress ones.
“La quale se non v’è dispiaciuta affatto, vogliate bene a chi l’ha scritta, e anche un pochino a chi l’ha raccomodata. Ma se in vece fossimo riusciti ad annoiarvi, credete che non s’è fatto apposta.”
Introduction
Muon Colliders
LEMMA
Multi-target
Deposited energy
Positrons
Positrons regeneration
Muons
Additional materials
Shapes
Thermal model
Test at MAMI
TB 2018
Conclusion

## Slide 47
BACKUP

## Slide 48
LEMMA proposed scheme
LEMMA scheme:
Injector.
Multi-target.
Muon accumulator.
Classical source.
γ-source.
Positron ring.
Extraction.
Energy compressor LINAC.
One of LEMMA scheme (From M. Bauce talk at APS 2021).
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 49
View factor
View factor:
Each slice of the multi-target is subjected to:
being
The radiation heat transfer also depends on shapes and orientations →view factor:
View factor of the heat transfer between two surfaces. (From M. Vio et al. “Corsi di fisica tecnica”).
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 50
Deposited energy in the multi-target
Parametric study:
Be slices [1.5mm-6mm] (45GeV e+).e
C slices [0.5mm-2mm] (45GeV e+).
Deposited energy results:
Increasing with the thickness.
d<E>/dx ~0.28 MeV/mm (Be).
d<E>/dx ~0.32 MeV/mm (C).
Energy spectrum- Be 3 mm (single slice thickness) – I target.
Dependency of <Edep> on the slice thickness– Be I target.
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 51
Beam loss as a function of number of targets
Theory:
Mean energy crossing the target:e
Muon production threshold 43.69GeV.
Parametric study:
Number of slices [2;5] (45GeV e+).
Results:
dre+43.69GeV/dx ~0.010 mm-1 (Be).
dre+43.69GeV/dx ~0.018 mm-1 (C).
d<E>/dx ~0.12 GeV/mm (Be).
d<E>/dx ~0.21 GeV/mm (C).
Beryllium
Carbon
Beryllium
Carbon
Mean energy of the beam (left) and number of positrons with energy over muon pair production exiting the multi-target as a function of the beam energy. The thicknesses of each slice are 3mm for Be and 1mm for C.
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 52
Beam loss as a function of beam energy
Theory:
Mean energy crossing the target:e
Muon production threshold 43.69GeV.
Parametric study:
Beam energy [44GeV;48GeV].
Results:
Be: dre+43.69GeV/dx from ~ 0.007mm-1 (48GeV) to ~ 0.02 mm-1 (44GeV).
C: dre+43.69GeV/dx from ~ 0.01mm-1 (48GeV) to ~ 0.03 mm-1 (44GeV).
Mean energy of the beam (left) and normalized number of positrons with energy over muon pair production outgoing a 6 mm Be and 2 mm C multi-target (right) as a function of the beam energy.
Beryllium
Carbon
Beryllium
Carbon
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 53
Photons production
Features:
Bremsstrahlung, e+e- annihilation → photon production.
Radiated energy:
Positron source.
Parametric study:
Be slices [1.5mm-6mm] (45GeV e+).e
C slices [0.5mm-2mm] (45GeV e+).
Results:
dE/dx~2.0*10-11J/mm (Be).
dE/dx~3.4*10-11J/mm (C).
Dependency of photon energy on the thickness of a Be multi-target.
Energy spectrum of radiated energy by photons produced in a 6mm Be total thickness multi-target.
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 54
Deposited energy in the regenerator
Parametric study:
Be slices [1.5mm-6mm] (45GeV e+).e
C slices [0.5mm-2mm] (45GeV e+).
Results:
d<E>/dx~9.1MeV/mm (Be).
d<E>/dx~17MeV/mm (C).
Higher deposited energy than in the multi-target, but easilier to replace.
Dependency of deposited energy in the regenerator on the total thickness of a Be multi-target.
Deposited energy in the regenerator by photons produced in a 6 mm total thickness Be multi-target.
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 55
Electrons and positrons production
Features:
Main background for muon production.
Mainly produced by Bhabha scattering.
Positrons could be recirculated in the beam.
Parametric study:
Be slices [1.5mm-6mm] (45GeV e+).e
C slices [0.5mm-2mm] (45GeV e+).
Results:
Low energy (mean energy few MeV);
Number and mean energy increase with the thickness.
Energy spectrum of secondary electrons/positrons produced in a 6mm total thickness Be multi-target.
Normalized number ne± and mean energy <E> of produced electrons/positrons in the multi-target.
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 56
Muon production as a function of number of slices
Theory:
Muon production:
Parametric study:
Number of slices [2;5] (45GeV e+).
Results:
Number increases with the number of slice.
Efficiency ~10-7- 10-6 µ±/e
Be: dµ/dX0 ~1.6*10-5 X0-1.
C: dµ/dX0 ~1.1*10-5 X0-1.
Beam energy loss→ Saturation.
Dependency on number of targets of produced muons in Be multi-target. Size of each slice 3mm.
2 slices
3 slices
4 slices
5 slices
Muon production in a Be multi-target for several runs. Size of each slice 3mm.
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 57
Beryllium
Carbon
Dependency on beam energy of RMS/E (left) and εRMS (right) on the beam energy in a 6 mm total thickness Be and 2 mm total thickness C target.
Beryllium
Carbon
Mean RMS angle contribution to emittance (εRMS):
Exting angle:
Coulumbian scattering → Emittance increasing.
εRMS given by:
being
Parametric study:
Beam energy [44GeV-48GeV].e
Results:
εRMS increases with the beam energy.
dεRMS/dE ~2.5nm*rad/(GeV) (Be 6mm).
dεRMS/dE ~2.2nm*rad/(GeV) (C 2m).
εRMS as a function of beam energy
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 58
He 78mm
Li 9mm
H 72mm
Be 6mm
Beam loss in additional material
Theory:
Mean energy crossing the target:e
Parametric study:
Liquid H, 36 mm (45GeV e+).e
Liquid He, 39 mm (45GeV e+).e
Li, 9 mm (45GeV e+).e
Kinematics of positrons results:
dre+43.69GeV/dx ~0.43*10-3 mm-1 (H).
dre+43.69GeV/dx ~0.52*10-3 mm-1 (He).
dre+43.69GeV/dx ~2.5*10-3 mm-1 (Le).
d<E>/dx ~0.5*10-2 GeV/mm (Be).
d<E>/dx ~0.6*10-2 GeV/mm (Be).
d<E>/dx ~2.9*10-2 GeV/mm (Be).
Ratio of surviving positrons with energy over muon pair production threshold for several turns.
Mean energy of positrons for several turns.
C 2mm
Li 9mm
H 72mm
C 2mm
He 78mm
He 78mm
Be 6mm
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 59
Mean RMS angle contribution to emittance (εRMS):
Exting angle:
Coulumbian scattering → Emittance increasing.
εRMS given by:
being
Parametric study:
Liquid H, 36 mm (45GeV e+).e
Liquid He, 39 mm (45GeV e+).e
Li, 9 mm (45GeV e+).e
εRMS of positrons results:
εRMS of positrons compareble/lower than using 6mm Be and 2mm C total thickness multi-target.
Mean RMS angle contribution to emittance of positrons for additional materials.
Beam εRMS increase in additional materials
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 60
Chrinstensens safety factor test
Results:
Christensens failure criterion not satisfied using a 300 μm spot size.
1000 μm spot size needed.
Christense safety factor evolution in a 3mm Be and 1mm C target using a spot size σ=300µm (left) and σ=1000µm (right).
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 61
Theoretical modeling for the thermal stability of solid targets ina a positron driven muon collider
More information:
Cesarini G. et al. ‘’Theoretical Modeling for the Thermal Stability of Solid Targets in Positron-Driven Muon Collider” , International Journal of Thermophysics, ISSN 0195-928X, Vol 42, Number 163, 2021, http://dx.doi.org/10.1007/s10765-021-02913-x
Published article on IOTP.
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 62
Proposed parameters for thermal studies @MAMI
Beam:
800MeV e-.
Spot size 10µm.
Angular spread 1µrad.
Energy spread 13keV.
Target:
Single C target.
Radius [3cm;5cm].
Thickness [0.5mm;1.3mm].
Scheme of experimental test at MAMI.
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 63
Deposited energy @MAMI
Parametric study:
Thickness [0.5mm-1.3mm] (800MeV e-).e
Deposited energy results:
Increasing with the thickness.
d<E>/dx ~0.32 MeV/mm (same of LEMMA).
Dependency of mean deposited energy <E> on the thickness. The radius is 4cm.
Energy spectrum- C 0.9 mm.
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 64
Deposited energy density @MAMI
Parametric study:
Thickness [0.5mm-1.3mm] (800MeV e-).e
Deposited energy density results:
Dependency on the radius position.
Peak Energy Deposited Density (PEDD) σ=10µm, 3*1013 e+/bunch :
2.3*106J/cm3.
PEDD higher than threshold (210J/cm3 ).
Thresholds from https://dx.doi.org/10.1007/s10765-021-02913-x
Deposited energy density by 3*1013 primary positrons- 1.3 mm total thickness target.
Deposited energy density by 3*1013 primary positrons- C 0.9 m.
PEDD
Gaussian
core
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 65
Deposited energy density @MAMI as a function of spot size
Parametric study:
Beam spot size [10μm-2000 μm].e
Results (3*1013 e+/bunch):
PEDD decreasing as 1/σ2.
PEDD from 4.8*102 J/cm3 (2000μm) to 2.3*106J/cm3 (10μm).
PEDDs still larger than threshold (210J/cm3 ).
Lower number of e-/bunch is needed.
Considerations:
It doesn’t affect the goodness of presented results (just rescale the deposited energy density).
Dependency of energy density on position on the radius by 3*1013 electrons in a 1.3 thickness target.
Dependency of PEDD of 3*1013 electrons in a 1.3mm thickness target.
10 µm
100 µm
200 µm
50 µm
300 µm
400 µm
500 µm
400 µm
1000 µm
2000 µm
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 66
Radiation estimation @MAMI as a function of surface
Parametric study:e
Scintillator surface [9cm2;121cm2] (1.3mm C).
Results:
Particle flux and deposited energy in the scintillator increase with the surface area.
Mean values of deposited energy in scintillator as a function of surface area. Thickness 1.3mm.
positrons
phtons
electrons
Particle flux hitting the scintillator as a function of the surface area.
total
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 67
Additional planned thermal stress studies
Planning ahead:
Apply the thermal model multi-targets of different shapes.
Measurement of target thermo-elastic properties in a wide temperature range.
Mearument of thermal diffusivity and IR emissivity via photo-thermal radiometry and IR thermography.
Detection of demage and thermo-mechanical stress when the target is subjected to intense LASER radiation.
Thermomechanical stress test with LASER scheme.
Example of targets produced at LNL. From S. Corradetti talk at Muon Collider Meeting 2021.
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 68
Features :
1-inch thick fused silica layers.
Three PMT to detect the Cherenkov light produced in each of the fused silica layers
Sequence of alternating active and passive layers along z to filter muons against electrons;
Among the pairs of fused silica layers tungsten shields;
HORSA absorber
HORSA absorber during the test beam.
HORSA absorber layout.
HORizontal Smart Absorber (HORSA)
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 69
Tracker – LG correlation:
22 GeV electrons and muons.
Maximum energy deposition in LG for [6 cm; 9cm] on the tracker.
LG calibration:
22 GeV electrons.
µ=3447ADC, σ=174ADC → 1GeV=(156.7±7.9)ADC.
Tracker- central LG correlation.
Deposited energy in central LG by 22GeV electrons.
muons
electrons
3447 ADC
Calorimeter calibration of Test Beam 2018
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 70
Muon identification by data of Test Beam 2018
22GeV muon identification:
22GeV muon beam.
Deposited energy in central LG <1GeV.
Signal region EHORSA <2000 ADC.
Deposited energy in central LG by 22 GeV muons.
Signal region – 22 GeV muons.
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018

## Slide 71
Muon detection in electron positron annihilation for muon collider studies
More details:
Amapane N. et al. ‘’Muon detection in electron – positron annihilation for muon collider studies’’ – Nuclear Instruments & Methods in Physics Research A, Elsevier, ISSN 0168-9002, Vol. 1024, Pages 166129, 2021, https://doi.org/10.1016/j.nima.2021.166129
Published article on NIM A.
LEMMA scheme
View factor
Deposited energy
Positrons
Photons
Positron regeneration
Elecontrons and positrons
Muons
Additional materials
Thermal model
Test at MAMI
Thermal studies
TB 2018