## Slide 1: Space gravitational wave antenna DECIGO and B-DECIGO
Seiji Kawamura (Nagoya University), DECIGO working group
GWADW
May 24, 2023, @ Elba, Italy

## Slide 2: DECIGO Deci-hertz Interferometer Gravitational Wave Observatory
Thruster
FP cavity
Finesse: 10
Drag-free spacecraft
Mirror
R: 0.5 m
M: 100 kg
Laser
P: 10 W
: 0.515 m
1,000 km
Sun
Earth
Pre-conceptual design
Orbit
  Seto, Kawamura, Nakamura, PRL, 2001
  Kawamura, et al., PTEP, 2021
frequency band: 0.1 Hz - 10 Hz
bridges the gap between LISA and ground-based detectors (GBD)
follow-up for LISA and predictor for GBD

## Slide 3: Target sensitivity and aimed science
Frequency [Hz]
Correlation
(3 years)
Strain [Hz-1/2]
10-3 10-2 10-1 1 10 102 103
10-19
10-20
10-21
10-22
10-23
10-24
10-25
10-26
BH-BH
Coalescence
NS-NS (z=1)
1 cluster
BH-NS
(10 M z=1)
PBH related
(1000 M z=10)
5 years
3 months
Detect primordial gravitational waves (PGW)
Prediction of NS-NS coalescences
Measure acceleration of expansion of Universe
Reveal formation of intermediate-mass BH
Detect Primordial-BH related GWs
Improve accuracy of general relativity
PGW (GW~2×10-15)

## Slide 4: Update of PGW
Frequency [Hz]
Correlation
(3 years)
Strain [Hz-1/2]
10-3 10-2 10-1 1 10 102 103
10-19
10-20
10-21
10-22
10-23
10-24
10-25
10-26
1 cluster
PGW (GW~1×10-16)
PGW (GW~2×10-15)
The upper limit of PGW has been reduced by the Planck observations, etc.
The target sensitivity of DECIGO should be improved to enhance the possibility of detection of PGW.

## Slide 5: Optimization with quantum noise
Iwaguchi, et al., Galaxies, 2021
Ishikawa, et al., Galaxies, 2021
The following parameters are optimized for the best SNR for a given mirror radius
        Cavity length
        Reflectivity of mirror
        Laser power (up to 100 W)
Considering only quantum noise
Constant mirror mass is assumed
GW~1×10-16
Cut-off frequency for double white dwarf (DWD) noise: 0.1 Hz

## Slide 6: Optimization with thermal noise and DWD noise
Values/type for each model: 23 in total
Design parameters
For a given radius,
optimize the other parameters
Parameter | Range
Mirror radius | 0～1 m
reflectivity | 0～1
Laser power | 0～100 W
Arm length | No limit
Parameter | Value
DWD cut-off frequency | 0.07 Hz / 0.1 Hz
Pressure inside spacecraft | Pa / Pa
Mirror model | Constant mass (100 kg) / Constant thickness (0.5 m, 100 kg)
Parameter | Value
DWD cut-off frequency | 0.07 Hz / 0.1 Hz
Pressure inside spacecraft | 
Mirror model | Constant mass (100 kg) / Constant thickness (0.5 m, 100 kg)

## Slide 7: Results
Cut-off frequency: 0.1Hz Cut-off frequency: 0.07Hz
Constant thickness
Constant mass
10-8 Pa
10-8 Pa
10-9 Pa
10-9 Pa
Kawasaki, et al., Galaxies, 2022

## Slide 8: Relationship between GW@0.1Hz and SNR
The current upper limit
Predicted by Starobinski model
Considering quantum noise and thermal noise
Vacuum：10-9 Pa
DWD cut-off frequency: 0.07 Hz
Mirror: Constant thickness
GW

## Slide 9: Quantum locking with optical spring
  Yamada, et al., PLA, 2020
  Yamada, et al., PLA, 2021
  Ishikawa, et al., PRD, 2023
Sub Cavity
Main Cavity
1,000 km
~1 m
~1 m
1/11
Sub Cavity
Detuned
Detuned
  Posters in this workshop:
  Ishikawa, Shimizu, Umemura, Tsuji

## Slide 10: Sensitivity
PGW (GW1×10-16)
Radius of mirror: 1 m
Arm length: 5,000 km
Radius of mirror: 0.5 m
Arm length: 1,000 km
Considering only quantum noise
DWD cud-off frequency: 0.1 Hz
Mass of mirror: 100 kg
Laser power: 100 W
PGW (GW1×10-16)

## Slide 11: Roadmap
 |  |  |  |  |  |  |  |  |  |  |  |  | 2034 |  |  |  |  |  |  |  | 
Mission |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Objectives | Test of key technologies |  |  |  |  |  |  |  |  | Detection of GW w/ minimum spec. Test FP cavity between S/C |  |  |  |  |  | Full GW astronomy |  |  |  |  | 
Scope | 1 S/C 1 arm |  |  |  |  |  |  |  |  | 3 S/C 3 interferometers 1 cluster |  |  |  |  |  | 3 S/C 3 interferometers 4 clusters |  |  |  |  | 
DICIGO Pathfinder
B-DECIGO
DECIGO
R&D
Fabrication
R&D
Fabrication
R&D
Fabrication
SWIM
Now updating the roadmap
Target

## Slide 12: B-DECIGO Deci-hertz Interferometer Gravitational Wave Observatory
Thruster
Drag-free spacecraft
Mirror
R: 0.15 m
M: 30 kg
Laser
P: 1 W
: 0.515 m
100 km
Conceptual design
Orbit: TBD
# of clusters: 1
  Nakamura, et al., PTEP, 2016
FP cavity
Finesse: 100
Prediction of timing and location of NS-NS (BH) coalescence
Revelation of origin of ~30 M BBH
Much better parameter estimation of binaries
Removal of foreground for DECIGO
Verification of technologies for DECIGO

## Slide 13: Progress on technologies for B-DECIGO
Dual-pass FP cavity Low-noise thruster
High-power stabilized laser
  Posters in this workshop: Ono

## Slide 14: Related mission: SILVIA
SILVIA
  Space Interferometer Laboratory Voyaging towards Innovative Applications
  Candidate for small satellite mission at ISAS/JAXA in collaboration with DECIGO and infrared interferometer team
  Objectives: Demonstration of the formation flying technology and drag-free technology
Recent progress
  Feb. 2020: SILVIA mission proposed to ISAS
  Aug. 2020: Approved to proceed to “Idea implementation process”
  Dec. 2022: Approved to proceed to “Mission definition phase”
  Now: Study for mission definition underway

## Slide 15: Summary
DECIGO will accomplish a variety of science, including direct detection of PGW, for which we are updating DECIGO design.
B-DECIGO will verify technologies for DECIGO as well as accomplish a variety of science, including frequent prediction of NS-NS.
Image of
B-DECIGO
©NEC