## Slide 1: Advanced LIGO Detector Commissioning Observing Run 4
Elenna Capote
LSC Fellow, LIGO Hanford Observatory
Gravitational-Wave Advanced Detector Workshop
May 2023

## Slide 2: O4 Commissioning Goals
Double O3 circulating power (~400 kW in arms)
Reduce technical noises
Achieve 4.5 dB of frequency -dependent squeezing
  Addressed in later talk
Achieve 160+ Mpc of BNS inspiral range
L1 O3 (130 Mpc)
Optimistic O4 projection (190 Mpc)
Double laser power
More squeezing
Reduce technical noise (2x)
Reduced radiation pressure & technical noise
Credit: P. Fritschel, G2300213

## Slide 3: Pre-O4 Status

## Slide 4: Pre-Stabilized Laser
2W NPRO seed laser, 2 neoVAN-4S-HP amplification stages
Serves 110W to vacuum
J. Driggers
M. Nakano
LHO
LLO

## Slide 5: Test Mass Replacements
ITM replaced at LHO, ETMs replaced at LLO
Eliminates point absorbers limiting high power operation, reduces beam jitter coupling
Enabled new violin and acoustic mode damper installation
B. Weaver
M. Nakano
ITMY installation, LHO
Hartmann Wavefront Sensors, LLO
ETMX
ETMY

## Slide 6: Output Port Upgrades
Low noise DARM
Old Dark Noise
New Dark Noise
Frequency [Hz]
10
100
1000
Thermal radius of curvature actuator on Output Mirror 2
Allows improvement of IFO to OMC mode matching
New electronics for Output Mode Cleaner photodetectors
  New transimpedance amplifier
  New whitening filter
  lower noise, higher range ADC
  Improved electrical isolation
New low loss faraday isolator (both sites)
New lower loss OMC (LLO)

## Slide 7: Scatter Mitigation
Removal of window between HAM5 and HAM6 at output port
Damping the high-Q suspended baffles to reduce their velocity
Before/After Arm Cavity Baffle Damping, LLO
RED: Pre-O4, septum window present
BLUE: after removal of window
Frequency [Hz]
DARM (LHO)
S. Soni, LLO
10
100

## Slide 8: High Power Operation
 | LHO | LLO
Input Power (W) | 76 | 63.6
Power Recycling Gain | 45.6 | 37.8
Arm Power (kW) | 430 | 325
New challenge: IFO thermalization
Sideband gain, cavity detuning, noise couplings, arm power evolve for over 6 hours of initial lock stretch
V. Frolov
Effective Arm Power (MW)
Time [sec]
3600
7200
10800
14400
PRCL optical gain [au]

## Slide 9: High Power/Mode Matching Challenge: Parametric Instabilities
Source: Wikipedia, Gaussian beam
(Not covered by acoustic mode damping)
COMSOL simulation of 80 kHz PI
High power operation limited by arm cavity HOM interaction with acoustic modes
A. Brooks
D. Brown

## Slide 10: Online Noise Subtraction
Apply NonSENS algorithm online for noise subtraction
Can subtract:
calibration line sidebands
length and angular sensing and controls noise
jitter noise
frequency noise
Calibration lines subtracted separately
Pictured: subtraction of calibration lines, jitter noise, length sensing and control

## Slide 11: Limiting Noises: LLO
Current challenges:
(assumed) Excess coating Brownian noise
Unknown noise, 10-30 Hz
Improvements:
Angular controls noise
Quantum noise
Length sensing and control (MICH+SRCL)

## Slide 12: Limiting Noises: LHO
Improvements:
Angular controls noise
Laser frequency noise (1-5 kHz)
Quantum noise
Challenges:
Beam jitter noise (100-1000 Hz)
Laser frequency noise (20-40 Hz)
Length sensing and controls noise
Unknown noise, 20-100 Hz

## Slide 13: Thank you! Questions?

## Slide 14: Extra Slides

## Slide 15: Projections