## Slide 1: CN Test Beam Preparation
Rui Qiao; Ke Gong, on behalf of IHEP
JiaJu Wei, on behalf of PMO

## Slide 2: Full connection test
2 IHEP SCD & 2 PMO SCD on the common base
Base
IHEP SCD
PMO SCD1
PMO SCD2
IHEP PSD (not shown)

## Slide 3: Full connection test
220V
Swiss ->CN
Adaptor
10m power cable
5m power strip. 8 sockets
SCD1
SCD2
SCD1
SCD2
DAQ1
DAQ2
NoteBook1
NoteBook2
IHEP
PMO
DAQ1
DAQ2
PC & Mon 1
PC & Mon 2
DC
DC

## Slide 4: Full connection test
IHEP SCD pedestal(top) and noise level (bottom)
The noise level is 2~3 ADC counts after common noise subtraction
PMO SCD noise level distribution. The noise level is 3~3.5 ADC counts after common noise subtraction

## Slide 5: DAQ Test
IHEP DAQ1
IHEP DAQ2
PMO DAQ1
PMO DAQ2
Backup Trigger Board
Backup Host PC
IHEP PC1
IHEP PC2
PMO PC1
PMO PC2
DI2C
The CN SCD follow the DI2C & Sync Start/Stop protocol.
After properly connection and setting IP, the DAQ will automatically start/stop. NO manual control is in need.
Sync Start/Stop

## Slide 6: Transportation
detector | component | ID | Region
IHEP SCD | Detector *2 | A01 | 3
 | DC& Power cord *1 | A02 | 2
 | DAQ *2 | A03 | 1
 | PC *2 | A04 | 1
 | Network cable *4 | A05 | 1
PMO SCD | Detector *2 | B01 | 4
 | bracket *2 | B02 | 3
 | DC& Power cord *1 | B03 | 2
 | DAQ *2 | B04 | 4
 | PC *2 | B05 | 4
 | monitor *2 | B06 | 1
 | Network cable *4 | B07 | 1
PSD | Detector | C01 | 4
 | Support | C02 | 3
 | DC&Power cord *3 | C03 | 2
 | Pre-Amplifier | C04 | 4
 | DT | C05 | 4
 | ADC | C06 | 4
 | Cables | C07 | 4
 | Router | C08 | 4
 | PC&USB Converter | C09 | 4
 | Mobile Platform | C10 | 4
 | backup NDL SiPM board | C11 | 3
 | SPARE Calbles | C12 | 4
other | Base | D01 | 3
 | Top cover | D02 | 3
 | 220V Power supply cable*2 | D03 | 4
 | tool、gasket *2 | D04 | 3
1
2
3
4
The package has already been send to Geneva at Nov. 2nd by plane.

## Slide 7: Documentation
We have been writing the ‘Installation Manual’ . The Chinese version is finished, and we are doing the translation.
The CN SCD can automatically start/stop during experiment. So No ‘Operation Manual’ is in need.
The ‘Uninstallation Manual’ will be prepared.

## Slide 8: Solution to illuminate all 10 regions of IHEP SCD
The beam spot of high-Z ion is small.
The beam spot should illuminate all 10 regions with various setups.
However, no mobile platform is prepared.
60um
25um
5*20channels
0ohm
0ohm
5*20channels
68pf
47pf
20pf
100pf
3.6 cm

## Slide 9: Solution to illuminate all 10 regions of IHEP SCD
100 pF
68 pF
47 pF
20 pF
0 ohm
100 pF
68 pF
47 pF
20 pF
0 ohm
IHEP SCD1
60um width
IHEP SCD1
25um width
100 pF
68 pF
47 pF
20 pF
0 ohm
100 pF
68 pF
47 pF
20 pF
0 ohm
IHEP SCD2
60um width
IHEP SCD2
25um width
3.6mm
Ion beam
Common Base

## Slide 10: Solution to illuminate all 10 regions of IHEP SCD
Ion beam
100 pF
68 pF
47 pF
20 pF
0 ohm
100 pF
68 pF
47 pF
20 pF
0 ohm
IHEP SCD1
60um width
IHEP SCD1
25um width
100 pF
68 pF
47 pF
20 pF
0 ohm
100 pF
68 pF
47 pF
20 pF
0 ohm
IHEP SCD2
60um width
IHEP SCD2
25um width
3.6mm
Common Base
7.2 mm
plate
7.2 mm
plate
7.2 mm aluminum plate*4

## Slide 11: Solution to illuminate all 10 regions of IHEP SCD
Ion beam
100 pF
68 pF
47 pF
20 pF
0 ohm
100 pF
68 pF
47 pF
20 pF
0 ohm
IHEP SCD1
60um width
IHEP SCD1
25um width
100 pF
68 pF
47 pF
20 pF
0 ohm
100 pF
68 pF
47 pF
20 pF
0 ohm
IHEP SCD2
60um width
IHEP SCD2
25um width
3.6mm
Common Base
7.2 mm
plate
7.2 mm
plate
3.6 mm aluminum plate*4
3.6 mm
3.6 mm

## Slide 12: Conclusion
A full connection test of IHEP & PMO SCD has been performed. The noise level is low.
An automatic DAQ system has been test. After proper setup, NO manual control is in need.
The package has been seen to Geneva at Nov. 2nd by plane.
‘Installation Manual’ is being prepared.
Proposal to illuminate all 10 regions by inserting 2 types of plates.