## Slide 1
Simone Atzori
INGV researcher
THE KEY ROLE OF RADAR IMAGES IN THE UNDERSTANDING OF EARTHQUAKES

## Slide 2: A bit of history
1978 Launch of the first SAR satellite (SEASAT)
198* Pioneer experiments on radar interferometry (InSAR)
1992 Launch of ERS-1 (ESA) satellite
1992 M 7.3 Landers earthquake
1993 First interferogram of an earthquake
1995 Launch of ERS-2 (ESA) satellite
2002 Launch of Envisat (ESA)
2007 Launch of the first COSMO-SkyMed (ASI) satellite
2012 End of my contract

## Slide 3: Presentation outline
Synthetic Aperture Radar images: image characteristics, advantages and limitations;
InSAR processing: from SAR raw data to the maps of displacement
Seismic source: from the displacement map to the seismic source
Examples: L’Aquila and New Zealand EQ

## Slide 4: Synthetic Aperture Radar images
SAR antenna is an active sensor: a set of microwave pulses is sent toward the Earth and their backscattered echoes are recorded by the same antenna.
A lateral transmission is used to avoid the return of overlapping echoes

## Slide 5: SAR image characteristics
Imaging is day/night and all-weather
High spatial resolution are achieved with the synthetic aperture
Intensity and phase of the backscattered signal are recorded
The pixel position is based on the satellite/earth round-trip travel time
Side looking results in images with distorted geometry (slant range)
Mt. Etna
foreshortening
layover and shadow
Flight direction

## Slide 6: Focused SAR image (amplitude)
range
azimuth
Flight direction
ENVISAT image (27/04/2008)
C-band (l = 5.6 cm)
Abruzzi (Italy) region
Mountains “lay down” toward the SAR antenna. Geometric distortions must be compensated to pass from the range/azimuth geometry (slant range) to the ground-corrected and geocoded reference system.

## Slide 7: Focused SAR image (phase)
In a single image the phase is “wrapped” and completely uncorrelated between adjacent pixels. Apparently the phase content is not meaningful.
range
azimuth
Flight direction

## Slide 8: The radar phase
Centers of signal scattering in a single ground cell
All the scattering centers contribute to the composition of the phase backscattered to the antenna
Phase content of a single SAR image
Re
Im
j

## Slide 9: Ground displacement
S1 satellite at time t1
S2 satellite at time t2
Satellites are supposed to acquire images from the same position
If scattering centers in a pixel are stable, the phase difference is only due to the change in the antenna/pixel distance, the line-of-sight direction
two images are acquired at times t1 and t2, encompassing a ground deformation.
If the phase content of a single image is of no practical use, the comparison between the phase change across two images acquired at different times can be representative of the surface topography and/or the ground displacement:

## Slide 10: From theory to real world
Scattering centers in a ground cell are not so stable (e.g. tree leaves)
Satellite never passes twice exactly in the same position
Radar signal can change velocity trough the atmosphere
Phase difference can be uncorrelated with the displacement (loss of coherence)
Phase difference contains a contribution from the topography and the Earth curvature
Phase difference is due to a propagation delay and not a real displacement
condition
consequence

## Slide 11: InSAR processing
Image focusing
Image coregistration
Phase difference
Removal of fringes due to earth curvature and topograpy
Filtering (interferogram enhancement)
Phase unwrapping
Phase to displacement conversion
Geocoding

## Slide 12: Interferogram generation
27/04/2008 before an EQ
12/04/2009
after EQ
Raw interferogram
Phase difference

## Slide 13: Differential interferogram
Real ground deformation
Atmospheric artifacts
“flat earth”
topography
Differential interferogram
raw interferogram

## Slide 14: Phase Unwrapping
unwrapping algorithm
wrapped interferogram
unwrapped interferogram

## Slide 15: Ground resolution and accuracy
wavelenght (l) 5.6 cm
antenna height (H) 870 km
look angle (q) 23°
bandwidth (B) 15.6 MHz
light speed 300·106 m/s
antenna length (Lant) 10 m
Ground resolution
assuming…
when…
then…
(accuracy)

## Slide 16: InSAR application field
Land subsidence (water pumping, oil spill, etc.)
Urban areas monitoring
Landslide monitoring
Ice sheet motion
Volcanic deformation
Earthquake induced deformation

## Slide 17: The seismic source model
Source parameters
position
L length
W width
d depth
s strike angle
d dip angle
s dislocation
r rake angle
From Okada (1985), BSSA
(and others…)

## Slide 18: InSAR data modeling
Observed data
Inversion algorithm
(linear, non-linear)
Geophysical model
Source model
Cost Function minimization
Forward modeling
Geophysical model
Predicted data

## Slide 19: The L’Aquila earthquake
X-band interf.
C-band interf.
data
model

## Slide 20: The New Zealand sequence
September 4, 2010, Darfield earthquake: Mw 7.0
February 21, 2011, first Christchurch earthquake: Mw 6.1
June 13, 2011, second Christchurch earthquake: Mw 6.0

## Slide 21: InSAR maps of the Darfield EQ
ALOS-Palsar
L-band: 23.6 cm
PRE: August 13
POST: September 28
Look Angle: 38.9°
Spatial Baseline: 357 m
Temp. Baseline: 30 d
Orbit: Ascending
ENVISAT
C-band: 5.6 cm
PRE: September 1
POST: October 6
Look Angle: 23.3°
Spatial Baseline: 300 m
Temp. Baseline: 35 d
Orbit: Ascending

## Slide 22: A complex fault system
3D view from south-east
3D view from north-west

## Slide 23: Thanks!