## Slide 1: Muon cooling at J-PARC
S. Kamioka
KEK, IPNS
Muon4Future

## Slide 2: Table of contents
Introduction
Key technologies and expected performance
Current status of muon cooling experiments
Future prospect

## Slide 3: Table of contents
Introduction
Key technologies and expected performance
Current status of muon cooling experiments
Future prospect

## Slide 4: Ultra-slow muon (USM)
μ+ cooling is important technique for future experiments using μ+
  Muon precision measurement, muon acceleration and colliders…
Development of ultra-slow muon source: muon cooling at J-PARC
Laser ionization of thermal muonium
  Surface μ → Mu target→ Emission of thermal Mu → Laser ionization of vacuum emitted Mu → USM → Extracted by E-field
Muonium target
Immersion lens
Surface Muon
E: 3.4 MeV
P = 27 MeV/c
Δp/p = 0.05
Pulsed UV laser
Laser ionization (Mu→μ + e)
μ+
Ultra-slow muon (USM)
E = 30 meV, p = 2.3 keV/c, Δp/p = 0.4
(thermal)Mu

## Slide 5: Specification of USM
Normalized RMS emittance : ~ 0.5 π mm mrad.
  Surface muon: ~ 1000 π mm mrad.
  Determined by Mu spatial distribution and its energy
Energy: 30meV
  Determined by temperature of the target. px,y ~ 3keV/c.
Polarization: 50%
  Due to fast spin exchange interaction of muonium (4GHz)
Efficiency: up to 10-3 / μ
  Depends on the laser energy and muonium target.
Timing profile: short pulse. FWHM ~ 2 ns
  Determined by laser pulse. USM is short pulse in usual.
Only positive muon can be cooled

## Slide 6: Proposed experiments featuring USM
USM = short pulse & low energy muon source
Many experiments featuring USM are proposed (some of them: ongoing).
  Muon g-2/EDM experiment
  Mu 1S-2S spectroscopy experiment shares the same technique
  muSR
  Transmission muon microscope
  μTristan
Transmission Muon Microscope
Muon g-2/EDM experiments
J-PARC MLF U-line (USM facility)

## Slide 7: Overview of current USM experiment at J-PARC
Several experiments featuring USM are underway at different beamlines.
U-line: Study of USM→muSR & muon microscope.
S-line: muonium 1S-2S spectroscopy experiment + RFQ acceleration of USM
H-line: H2 area is under construction and will be used for g-2 experiment and muon transmission microscope

## Slide 8: Table of contents
Introduction
Key technologies and expected performance
Current status of muon cooling experiments
Future prospect

## Slide 9: High efficiency muonium target
A laser ablated aerogel target
  Aerogel: Long term stability and room temperature
  Holes at the surface to increase the effective emission area.
  10 times better emission efficiency compared to a conventional aerogel.
Modeling of the target using random walk inside a target.
  Temperature is evaluated to be 320K from the measured emission profile.
Another target: Hot tungsten (2000K)
This target is also used at MLF.
Today, I focus on the aerogel target.

## Slide 10: Resonant multi-photon ionization
Ionization of muonium directly from its ground state is very difficult.
  No intense 13.6eV light source exists.
Mu is once excited to its higher energy state, then it is ionized.
  Mu excitation w/ VUV or DUV pulse and ionization using UV pulse.
  Feasible as excitation is much efficient + longer wavelength.
Two development: 1S→2P→unbound & 1S→2S→Unbound.
1S state
Unbound
91nm
Very difficult
1S state
Unbound
2P state
122nm
355nm
1S state
Unbound
2S state
244nm
244 nm
Plan. A
Most efficient
Plan. B
+ Useful for
spectroscopy

## Slide 11: Resonant multi-photon ionization
Ionization of muonium directly from its ground state is very difficult.
  No intense 13.6eV light source exists.
Mu is once excited to its higher energy state, then it is ionized.
  Mu excitation w/ VUV or DUV pulse and ionization using UV pulse.
  Feasible as excitation is much efficient + longer wavelength.
Two development: 1S→2P→unbound & 1S→2S→Unbound.
1S state
Unbound
91nm
Very difficult
1S state
Unbound
2P state
122nm
355nm
1S state
Unbound
2S state
244nm
244 nm
Plan. A
Most efficient
Plan. B
+ Useful for
spectroscopy
The most efficient process, but technically difficult
Technically easier wavelength, but high energy is required

## Slide 12: Solid state VUV light source
Key technology for 1S->2P->Unbound scheme is a high energy, 25Hz, long time stable VUV light source
  Large Mu emission region→ (relatively) high energy is required.
  Goal: 122nm, 100μJ, 2ns, 80GHz linewidth, 25Hz rep
All solid-state laser for 122-nm light source at J-PARC
  Solid state laser → long lifetime and better stability.
5μJ at the muonium target is under operation at MLF U-line.
Y. Oishi et al, 2023 J. Phys.: Conf. Ser. 2462 012026

## Slide 13: Expected performance at MLF H-line
Simulation assuming J-PARC MLF H-line. (efficiency depends on a beamline)
  Surface μ→stopping inside target→muonium diffusion→laser ionization
Expected USM flux : ~105 Hz with 100μJ @122-nm+300mJ @355-nm.
  Efficiency: ~ 1×10-3 / surface μ
Laser
Y-Z
X-Y
Surface
μ
Mesh electrode (surface of aerogel at z=0)
Laser
Velocity distributions
Expected USM spatial distribution
30meV
Timing profile
2ns

## Slide 14: Table of contents
Introduction
Key technologies and expected performance
Current status of muon cooling experiments
Future prospect

## Slide 15: Demonstration of muon cooling
Recently, experimental demonstrations and evaluations of USM w/ aerogel target are being performed at J-PARC MLF.
Extracting the USM with a SOA lens, then USM is detected by a MCP after magnetic and electrical bend.
Target
Laser
Surface μ
Mesh electrodes
Electrostatic
lens
MCP
B and E bend for particle selection
Schematic view of the experimental setup
Up to 30keV

## Slide 16: Demonstration @ MLF U-line
1S-2P-unbound scheme. Performed last year at MLF U-line.
Aerogel target + Laser (~2.5μJ @122-nm and ~7mJ @355-nm.)
  USM rate after extraction is 330Hz. The best record so far.
Laser frequency scan→ observing narrower resonance width than that of Mu emitted from a hot target (2000K)
Report in the Muon Advisory Committee 2022
Convolution of doppler effect and linewidth of 122nm pulse

## Slide 17: Demonstration @ MLF S-line
Collaborating with Muonium 1S-2S spectroscopy experiment, evaluation of the emittance of USM is ongoing (from March 2023).
  A 244-nm pulsed laser is developed by Okayama univ.
Using MCP and CCD camera as a beam profile monitor, q-scan measurement is underway to estimate the initial phase space of USM.
  RFQ acceleration test in this FY.
MCP for counting event rate & Beam profile monitor to measure USM beam size after extraction
World 1st acceleration of USM
will be performed in this FY
RFQ @ MLF

## Slide 18: Recent laser upgrade activities: 1S-2P-unbound scheme
Difficulty is the amplification of 1062.78nm for generation of 122nm.
  Nd:YGAG/Nd: YSAG for 1062.78nm has worse crystal quality.
  Brute-force amplification using longer/larger crystals results in worse quality.
Another important R&D is the degradation of optics
  VUV/DUV is harmful for optics and crystal.
R&D of new amp. for ×2 energy.
R&D to increase the lifetime of optics (Recently, focusing on residual gases)
Improvement of design for H2 area
  For better laser efficiency by design

## Slide 19: Recent laser upgrade activities: For 1S-2S-unbound scheme
High energy 244-nm pulse laser is under development at KEK Tsukuba.
  To see the possible best performance of 1S-2S-unbound scheme.
  Easier handling/evaluation than 122-nm → Useful for USM R&D
  It can also generate intense 355-nm pulse→ for 1S-2P scheme.
1064nm
SHG
532 nm
732 nm
244 nm
THG
Ti:Sapphire crystal
810 nm or 885nm LD
Nd:YAG crystal
(Solid state)
Nd:YAG laser
AMP
Ti:S laser
AMP
355 nm
(for 1S-2P)
Two applications

## Slide 20: Current status of the laser at Tsukuba
Development at 5Hz is underway to focus on study of laser efficiency.
  Solid-state Nd:YAG laser can generate <1.8J at 1064nm (goal: 2J)
  High energy 244nm generation test in this summer + high energy 355nm generation in this FY.
  Switched to 25Hz after that.
Nd:YAG laser system
Ti:S laser system

## Slide 21: Table of contents
Introduction
Key technologies and expected performance
Current status of muon cooling experiments
Future prospect

## Slide 22: Milestones of USM source development
FY 2023
FY 2024
FY 2025
FY 2026
Towards >105 Hz in FY 2026 at MLF H2 area
  Laser upgrade, new beam area and acceleration test. (4MeV)
First USM acceleration using an RFQ
Construction of a new laser room
USM flux 1kHz @ MLF U-line (2023-2024)
H2 area is ready
Lasers for short term R&D is installed at H2.
USM generation test at H2 area
Start the development of a new laser for 100μJ @ 122-nm.
USM flux: 10kHz at MLF U-line
4.3 MeV acceleration of USM using IH
100μJ@122-nm and 300mJ@355-nm for long-term use are ready.
Designed USM flux @ H2-area

## Slide 23: For future
Proposals to achieve more USM flux or better spin polarization.
  Just increasing the laser energy more and more is not efficient at some point.
Exciting ideas as candidates for the future improvement.
C. Zhang et al, NIM. A, 1042 (2022) 167443
Proposal of multi-layered Mu target
T. Nakajima. Journal of the Optical Society of America B 2012, 29(9): 2420-2424
Proposal of optical pumping of Mu
Larger Mu emission region
→ Ideally five times more USM flux with five times more laser.
→ 2.5 time more USM with the same laser energy
Color: # of pulse (one, two, three)
Circularly polarized laser→ re-polarization of spin

## Slide 24: Summary
Muon cooling with a high efficiency muonium target and high energy pulsed lasers are being developed at J-PARC.
Ultra-slow muon (USM)
Demonstration of ultra-slow muon generation with a laser ablated aerogel target and lasers are ongoing.
Development of more intense laser towards 105 Hz are ongoing in parallel.
  Two schemes in parallel for efficient development.
New ideas for more intense or polarized USM have been proposed. Interesting future plans.

## Slide 25: Acknowledgments
J-PARC g-2/EDM muon source group
  T. Mibe, J.H. Brewer, K. Ishida, S. Kamel, G.M. Marshall, A. Olin, K. Suzuki
MLF U-line
  S. Kanda, N. Teshima
Laser development
  Y. Oishi, M. Yoshida
Mu 1S-2S spectroscopy group from Okayama univ.
  S. Uetake, Y. Imai, S. Yamamoto and others.