## Slide 1
Upgrade of the
ALICE Inner Tracking System
Vito Manzari – INFN Bari
(vito.manzari@cern.ch)

## Slide 2
Outline of current detector
Upgrade: Physics motivations & Design goals
Upgrade options & Preliminary studies
Ongoing R&D
Timeline
Conclusions
Outline

## Slide 3
Detector:
Size: 16 x 26 meters
Weight: 10,000 tons
Central Barrel
2 p tracking & PID
Dh ≈ ± 1
ALICE detector layout

## Slide 4
Dedicated heavy ion experiment at LHC
Study of study behavior of strongly interacting matter under extreme conditions of compression and heat in heavy-ion collisions, mostly by means of Pb-Pb collisions 5.5 TeV CM-energy (NN)
Proton-proton collision program
  Reference data for heavy-ion program
  Genuine physics (momentum cut-off < 100 MeV/c, excellent PID)
Barrel Tracking
Pseudo-rapidity coverage |η| < 0.9
Robust tracking for heavy ion environment
  up to 150 points along the tracks
Wide transverse momentum range (100 MeV/c – 100 GeV/c)
  Low material budget (13% X0 for ITS+TPC)
  Large lever arm provides good tracking resolution at high pt
PID over a wide momentum range
Combined PID based on several techniques: dE/dx, TOF, transition and Cherenkov radiation
Rate capabilities
Interaction rates: Pb-Pb < 8kHz, p-p < 200 kHz (~30 events in the TPC)
Multiplicities: central Pb-Pb events ~2000, Pb-Pb MB ~ 600
The ALICE experiment

## Slide 5
The ITS (Inner tracking System) consists of 6 concentric barrels of silicon detectors based on 3 different technologies
  2 layers of silicon pixel (SPD)
  2 layers of silicon drift (SDD)
  2 layers of silicon strips (SSD)
“Current” Inner Tracking System

## Slide 6
Layer | Det. | Radius (cm) | Length (cm) | Surface (m2) | Chan. | Spatial precision (mm) |  | Cell (μm2) | Max occupancy central PbPb (%) | Power dissipation (W) | 
 |  |  |  |  |  | rf | z |  |  | barrel | end-cap
1 | SPD | 3.9 | 28.2 | 0.21 | 9.8M | 12 | 100 | 50x425 | 2.1 | 1.35k | 30
2 |  | 7.6 | 28.2 |  |  |  |  |  | 0.6 |  | 
3 | SDD | 15.0 | 44.4 | 1.31 | 133K | 35 | 25 | 202x294 | 2.5 | 1.06k | 1.75k
4 |  | 23.9 | 59.4 |  |  |  |  |  | 1.0 |  | 
5 | SSD | 38.0 | 86.2 | 5.0 | 2.6M | 20 | 830 | 95x40000 | 4.0 | 850 | 1.15k
6 |  | 43.0 | 97.8 |  |  |  |  |  | 3.3 |  | 
  The ALICE ITS in numbers
Radial coverage defined by beam-pipe (inwards) and requirements for track matching with TPC (outwards)
Inner layers: high multiplicity environment (~100 tracks/cm2)  2 layers of pixel detectors
“Current” Inner Tracking System

## Slide 7
The ITS tasks in ALICE:
  Secondary vertex reconstruction (c, b decays) with high resolution
    Good track impact parameter resolution
    < 60 µm (rφ) for pt > 1 GeV/c in Pb-Pb
  Improve primary vertex reconstruction, momentum and angle resolution of tracks from outer detectors
  Tracking and PID of low pt particles, also in stand-alone
  Prompt L0 trigger capability (FAST OR) with a latency <800 ns (SPD)
The ITS is the main tool for studying yields and spectra of particles containing heavy quarks
ITS role in ALICE

## Slide 8
Pb-Pb event

## Slide 9
5 readout chips/sensor
  0.25µm CMOS
  13.68 mm x 15.58 mm
  thinned to 150 µm
SPD sensor and pixel chip
p-in-n silicon sensor
  72.72 mm x 13.92 mm
  200 µm thin
40960 bump bonds
  ~25µm diameter
  Stand-off:
  ~12 µm (Pb-Sn)

## Slide 10
SPD module integration
~1200 wire-bonds

## Slide 11
1 sensor
1 sensor
10 readout chips
physical size = 200 mm x 15 mm x 2 mm
material budget = 1.1% X0 -> no copper
~10 million channels in 1200 pixel chips
120 detector modules – half staves (40 on inner and 80 on outer layer)
10 sectors
SPD module

## Slide 12
200 µm thick carbon fiber support
Δz= 28.3 cm, r= 3.9 cm & 7.6 cm
SPD half-barrel

## Slide 13
The SPD was installed in ALICE in Jun‘07
Beam pipe
Outer layer
Inner layer
Minimum clearance to beam pipe 5 mm
SPD integration

## Slide 14
“Global”
  Seeds in outer part of TPC @lowest track density
  Inward tracking from the outer to the inner TPC wall
  Matching the outer SSD layer and tracking in the ITS
  Outward tracking from ITS to outer detectors  PID ok
  Inward refitting to ITS  Track parameters OK
“ITS stand-alone”
  Recovers not-used hits in the ITS layers
  Aim: track and identify particles missed by TPC due to pt cut-off, dead zones between sectors, decays
    pt resolution <≈ 6% for a pion in pt range 200-800 MeV/c
    pt acceptance extended down to 80-100 MeV/c (for )
pt resolution
TPC-ITS prolongation efficiency
Tracking strategy and Performance

## Slide 15
The transverse impact parameter in the bending plane d0(rφ) is the reference variable to look for secondary tracks from strange, charm and beauty decay vertices
Impact parameter resolution is crucial to reconstruct secondary vertices : below 75 µm for pt > 1 GeV/c
Good agreement data-MC (~10%)
The material budget mainly affect the performance at low pt (multiple scattering)
The point resolution of each layers drives the asymptotic performance
ITS standalone enables the tracking for very low momentum particles (80-100 MeV/c pions)
Pb-Pb
“Current” ITS performance: impact parameter
Notes: in the bending plane: d0(rφ)

## Slide 16
dE/dx measurement
  Analogue read-out of charge deposited in 4 ITS layers (SDD & SSD)
  Charge samples corrected for the path length
  Truncated mean method applied to account for the long tails in the Landau distribution
PID performance
  PID combined with stand-alone tracking allows to identify charged particles below 100 MeV/c
  p-K separation up to 1 GeV/c
  K- separation up to 450 MeV/c
  A resolution of about 10-15% is achieved
p-p
p-p
Pb-Pb
“Current” ITS performance - PID

## Slide 17
Extend ALICE capability to study heavy quarks as probes of the QGP in heavy-ion collisions
  Main Physics Topics
    Energy loss
      charm and beauty RAA vs pT down to low pT
    Thermalization of heavy quarks: charmed and beauty baryons
      baryon to meson ratio, flow
    Quarkonia
  Mapping to ALICE
    Heavy flavour at midrapidity with hadronic (and semi-electronic)
    decays  ITS barrel upgrade
    Heavy flavour and resonances with muons in the forward direction  endcap on the MUON side
ITS Upgrade – Physics Motivations

## Slide 18
Increase vertex resolution by a factor of ~3
  Identification of secondary vertices from decaying charm and beauty
  Increase statistical accuracy of channels already measured by ALICE: e.g. displaced D0, J/Ψ
  Measurement of new channel:
    e.g. charmed baryon Λc
    or even more exotic channels: Λb
Higher standalone tracking efficiency
  Extended trigger capabilities
  Selection of event topologies with displaced vertices at Level 2 (~100 μs)
    impact parameter of displaced tracks
    distance from prim. to sec. vertices
    pointing angle
    selection cuts: kinematics, PID? (being studied)
Improve standalone pT resolution
  Charm and beauty with ITS standalone (or +TRD) tracking and TOF PID (??)
ITS Upgrade – Design goals

## Slide 19
Get closer to the IP
  Radius of innermost PIXEL layer is defined by central beam pipe radius
    Present beam pipe: ROUT = 29.8 mm, ΔR = 0.8 mm
    
    New Reduced beam pipe: ROUT = 19 mm, ΔR = 0.5 mm
Reduce material budget (especially innermost layers)
    reduce mass of silicon, electrical bus (power and signals), cooling, mechanics
    Present ITS pixel layers: X/X0 ~1.14% per layer
  
    Target value for new ITS: X/X0 ~0.3 – 0.5% per layer
Reduce pixel size
  Reduce size of interconnect bumps, monolithic PIXELS
    currently 50mm x 450mm
How to improve the impact parameter resolution

## Slide 20
Higher standalone tracking efficiency
  Higher granularity
    increase number of layers in the outer (seeding) and inner region (occupancy)
    increase granularity of central and outer layers
Extended trigger capabilities
  High standalone tracking efficiency
  Low readout time < 50μs for Pb-Pb, ~μs for p-p (current ITS ~1ms in both cases)
Increase momentum resolution
  increase track length
  increase spatial resolution
  reduce material budget
How to improve tracking, triggering and pT resolution

## Slide 21
Up to 7 silicon layers (r = 2.2 ÷ 45 cm) to cover from IP to TPC
4 innermost layers made of pixels, outer 3 layers either pixels or double sided strips
Hit density ~ 100 tracks/cm2 in HI collisions
Possibility of topological trigger – central Pb-Pb readout time < 50 µs
Add high resolution pixel layer closer to IP (r=2.2 cm)
Pixel size ~ 20-30 µm (rφ), σ(rφ) ~ 4 ÷ 6 µm
Material budget 0.3 ÷ 0.5% X0 per layer
Power consumption 250-300 mW/cm2
Radiation tolerant design (innermost layer) compatible with 2 Mrad / 2 x1013 neq over 10 years (safety factor ~2 included)
Requirements for the ITS upgrade

## Slide 22
Two design options are being studied
  “New SPDs”: replace SPD with new SPD consisting of 3 layers
   improve pointing resolution
  “All New”: replace entire ITS with a combination of Pixel/Strips  topological trigger
ITS Upgrade scenarios
Upgrade
Current

## Slide 23
Improvement of the
impact parameter resolution

## Slide 24
Improvement of the
standalone tracking efficiency

## Slide 25
Extending ITS tracking
to ~50cm 
ITS standalone
ITS standalone
outermost layer at 43 cm
outermost layer at 50 cm
Improvement of the
standalone pT resolution

## Slide 26
Preliminary
(cuts to be optimized)
An example of physics performance – D0

## Slide 27
Λc pKπ as a benchmark case in p-p
Comparison between current and new ITS in the same pT bin (pT > 3GeV/c)
Very preliminary
An example of physics performance – Λc

## Slide 28
Very preliminary
No signal in data with the current ITS in any pT bin
An example of physics performance – Λc
Λc pKπ as a benchmark case in Pb-Pb

## Slide 29
In one current SPD layer
  Carbon fiber support: 200 μm
  Cooling tube (Phynox): 40 μm wall thickness
  Grounding foil (Al-Kapton): 75 μm
  Pixel chip (Silicon): 150 μm  0.16%
  Bump bonds (Pb-Sn): diameter ~15-20 μm
  Silicon sensor: 200 μm  0.22%
  Pixel bus (Al+Kapton): 280 μm  0.48%
  SMD components
  Glue (Eccobond 45) and thermal grease
Two main contributors: silicon and interconnect structure (bus)
Material budget of each current SPD layer

## Slide 30
How can the material budget be reduced?
  Reduce silicon chip thickness
  Reduce silicon sensor thickness
  Thin monolithic structures
  Reduce bus contribution (reduce power)
  Reduce edge regions on sensor
  Review also other components (but average contribution 0.1-0.2%)
What can be a reasonable target
  Hybrid pixels: ~0.5% X0
    silicon: 0.16% X0 (at present 0.38%)
    bus: 0.24% X0 (at present 0.48%)
    others: ?? (at present 0.24%)
  Monolithic pixels: 0.37% X0 (e.g. STAR)
How material budget can be reduced

## Slide 31
Hybrid pixels
  State-of-the art in LHC experiments
  2 components: CMOS chip and high-resistivity sensor connected via bump bonds
Monolithic pixels
  Made significant progress, soon to be installed in STAR
  1 component, sensing layer included in the CMOS chip
Figure Stanitzki, M. (2010). Nucl. Instr. and Meth. A doi:10.1016/j.nima.2010.11.166
Figure - Rossi, L., Fischer, P., Rohe, T. & Wermes, N. (2006). Berlin: Springer.
Pixel Technologies

## Slide 32
Limit on pixel size given by current flip chip bonding technology ~ 30 µm
Material budget target < 0.5 % X0 ( 100 µm sensor, 50 µm chip)
High S/N ratio, ~ 8000 e-h pairs/MIP
Edgeless sensors to reduce insensitive overlap regions
Power/Speed optimization possible (shaping time O(µs)) to reduce the power budget
Proven radiation hardness
R&D: thinning, low cost bump bonding, edgless detectors, lower
power FEE chip
Hybrid Pixels & Ongoing R&D

## Slide 33
State-of-the-art architecture (MIMOSA family) uses rolling-shutter readout
Pixel size ~20 µm possible
Material budget target < 0.3 % X0 (50 µm chip)
New developments:
  1. Evaluation of properties of a quadruple well 0.18 CMOS
    radiation tests structures
    study characteristics of process using the MIMOSA architecture as reference
    design of new circuit dedicated to ALICE (MISTRAL)
    investigation of in-pixel signal processing using the quadruple-well approach
  2. Novel high resistivity base material for depleted operation (LePix)
Monolithic Pixels & Ongoing R&D

## Slide 34
Development of new strip detectors for outer layers
  R&D: double sided, shorter strips, new readout electronics
Electrical bus for distribution of power and signals
  at present: multilayer (5 layers) for SPD and double sided for SDD and SSD
  R&D: new power distribution techniques, layout optimization, integration of cooling
Cooling system options
  air cooling
  liquid cooling with carbon foam structure
  liquid cooling with polyimide micro-channels structure
  evaporative cooling with silicon micro-channels structure
Other R&D activities

## Slide 35
The upgrade should target the 2017-18 (Phase I) shutdown
  The scope of the upgrade Phase I should be well tailored to what can be reasonably prepared and tested within the next six years and installed in 15 months, with safety margin, in order not to degrade the present detector
  Decisions on upgrade plans in terms of physics strategy, detector feasibility, funding availability, will be taken in 2012
end 2011: Preparation of a technical proposal
2011-2014: R&D for Phase I
2014-2016: Production and pre-commissioning for Phase I
2017-2018: Installation and commissioning for Phase I
It will possibly require a two-stage approach: Phase I in 2017 and Phase II
in 2020 and beyond)
ITS Upgrade Timeline

## Slide 36
The current Inner Tracking System performance is well in agreement with the design requirements and expectations
  The achieved impact parameter resolution allows to reconstruct the secondary vertices of charm decays
  Standalone capability allows to track and identify charged particles with momenta down to 100 MeV/c
An upgraded ITS will extend the ALICE physics capabilities:
  Spectacular increase of the statistical accuracy in the measurements of yields and spectra of charmed mesons and baryons already possible with the present detector
  A significant extension of the present physics programme with many new measurements that at present are not possible
Several options for the detector technology implementation are being investigated and developed
Conclusions

## Slide 37
Back-up slides

## Slide 38
Heavy-flavours at midrapidity - mesons and baryons

## Slide 39
Heavy-flavours at midrapidity - electrons

## Slide 40
p-p
p-p
p-p
< 100 MeV/c
< 100 MeV/c
p-p
“Current” ITS performance - impact parameter

## Slide 41
41
CURRENT
UPGRADE
B from displaced J/Ψ: current vs upgrade

## Slide 42
Vertex resolution estimation in Pb-Pb
Method to evaluate resolution on the vertex position
The track sample is randomly divided into two
A primary vertex is reconstructed for each of the sub-sample
The resolution is extracted from the  of the distribution of the residual between the two vertices
The resolution is extrapolated for most central (5%) Pb-Pb collisions
Vertex resolution in Pb-Pb collisions at √s = 2.76 TeV as a function of half of the tracklets multiplicity of the event
Vertex reconstruction
Notes: The asymptotic limit estimates the size of the luminous
region, seen for the vertices reconstructed with tracks
(filled markers).
The resolution is extrapolated
for most central (5%) Pb-Pb
collisions (orange box).

## Slide 43
1 additional SPD layer (Layer 0) at a few mm radial distance from beampipe
Study effect of variation of beampipe radius from 25 to 19mm
r = 25mm (CMS request) r = 22 mm (ATLAS request)
r = 19mm (ALICE request)
Radial distance of the innermost pixel layer

## Slide 44
1 additional SPD layer (Layer0) at a 22mm radius
Study effect of variation of Layer0 thickness from 1.0% to 0.3% X0
  Current SPD + Layer0 with 1.0% X0
  Current SPD + Layer0 with 0.8% X0 (150mm silicon: sensor + readout chip
  Current SPD + Layer0 with 0.6% X0 (150mm silicon and lighter multilayer bus)
  Current SPD + Layer0 with 0.4% X0 (Monolithic pixels a la STAR)
Effect of layer thickness

## Slide 45
1 additional SPD layer (Layer 0) at 22mm radius
Study effect spatial resolution: 12 μm (present design), 6 μm, 2 μm
Effect of spatial resolution

## Slide 46
ALICE Running Scenario
ALICE PPR Vol. 1, p. 1591

## Slide 47
Pb-Pb collisions
  max interaction rate: 5kHz
  minimum time distance between interactions: ~5μs (pile-up in TPC)
  event tagging in ITS: matching with external detectors ( bunch crossing not required)
  signal shaping: ~μs (determined by signal/noise optimization)
  event size (innermost layer): 1.2 kbit/cm2
    30 clusters/cm2 (MB events)
    <fired pixels> ~ 8/cluster for MAPS 20x20μm2
    18-bit cluster address + 21-bit cluster shape (no smart encoding) 40-bit / cluster
  data throughput: 6 Mbit /scm2
  readout time: <50μs
  required bandwidth: 24 Mbit /scm2
  a bandwidth of 250 Mbit /scm2 is adequate for a maximum interaction rate ~50kHz MB
Timing requirements

## Slide 48
Beauty via displaced electrons: strategy and results

## Slide 49
Beauty via displaced electrons: strategy and results
The impact of the ITS upgrade is two-fold:
  Reduced material budget decreases electrons from photon conversions, one of the main background sources  increase S/B
  Better impact parameter resolution improves the separation of displaced electrons (from B) and backgrounds from the primary vertex (e.g. Dalitz decays)

## Slide 50
Particle | Decay Channel | c (m) | Mass (GeV/c2)
D0 | K + (3.8%) | 123 | 1.8645
D+ | K + + (9.5%) | 312 | 1.8694
 | K+ K + (5.2%) + + - (1.2%) | 150 | 1.9683
 | p K + (5.0%) | 59.9 | 2.2865
50-150 m
Example - Direct Topological Identification of the Open Charm
Properties of Open Charm Hadrons
Goal:
determine DCA (distance of closest approach) of decay vertex (secondary vertex) relative to the primary vertex

## Slide 51
Λc daughter particles pT spectra