## Slide 1
CHANNELING in crystals:
INFN-Ferrara activities
L. Bandiera, A. Mazzolari
12/11/2022
Contacts: bandiera@fe.infn.it
mazzolari@fe.infn.it

## Slide 2: Crystal Channeling
electron
proton
crystalline plane
proton
Amorphous medium/
non oriented crystal
Oriented crystal

## Slide 3: Channeling in a bent crystal
Channeling of a charged particle beam in a bent crystal results in steering of its trajectory
Bent crystals can be used in particle accelerators as elements for collimation or extraction
E. Tsyganov, 1976

## Slide 4: Bent crystals to steer ultrarelativisitc particle beams
V.S.
Bent Si crystal – 4 mm long
8.3 Tesla supermagnet – 15 m long
Elective applications in crystal assisted
beam collimation and extraction
A 50 μrad at 6.5 TeV is equivalent to a 300 T dipole magnet bending!!!

## Slide 5: Crystal collimation at LHC
Losses on a single absorber, reduction of machine impedance, higher currents
A possible scheme for upgraded collimation at HL-LHC
  Reduction of losses in cold regions (i.e. protect magnets from quenching)
  Present collimation system already at its limit for ions:
  fragmentation of heavy-ion beams in secondary particles of small divergence and Z/A slightly different from the primary beam -> difficult to intercept by the collimation system and can produce significant heat-load in the superconducting magnets.
Since 2009, ten years of experimental investigation carried on by UA9 collaboration @SPS & @LHC together with the LHC Collimation group.
Notes: he collimation system, which is optimized to provide a good protection with proton beams, has shown a cleaning efficiency with heavy-ion beams which is worse by up to two orders of magnitude. The reason for this reduced cleaning efficiency is the fragmentation of heavy-ion beams into isotopes with a different mass to charge ratios because of the interaction with the collimator material.

## Slide 6: Crystal channeling with 6.5 TeV protons @LHC
First successful test with 6.5 TeV protons in Nov 2015!
Strip Si crystal (INFN)
Piezo-goniometer (CERN/EN-STI)
https://cds.cern.ch/journal/CERNBulletin/2015/49/News%20Articles/2105080?ln=en
http://home.infn.it/newsletter-eu/pdf/NEWSLETTER_INFN_17_italiano_pag3.pdf
In collaboration with LHC Collimation group
channeling
Beam trajectory in LHC
~50 μrad deflection
Studies still on-going at LHC (2+2 crystals installed): INFN-CERN contract for bent crystals supply!
beam loss monitor
W. Scandale et al., Phys.Lett. B758 (2016) 129-133
Notes: The horizontal projection of the trajectory of a halo particle deflected by the crystal due to channeling at the bend angle α = 65 μrad (solid line up to the first horizontal TCSG1 and then by dot-dashed line to show the trajectory propagation in the case without the collimators): (a) for the beam injection with 450 GeV/c, (b) for the maximum momentum of 6500 GeV/c. Dashed lines show the beam envelope for the crystal distance from the orbit. Vertical lines show the positions of the collimators TCSG and TCLA and the primary collimators TCP (they are not visible for the injection case because they were shifted far from the orbit for the measurements). The positions of BLM1 and BLM2 for measuring the losses in the crystal and in the first horizontal TCSG1 behind the crystal, respectively, are shown schematically.

## Slide 7: Measuring baryons MDM & EDM @LHC
N.Neri, https://indico.cern.ch/event/755856/contributions/3260539/attachments/1779601/2895655/Neri_PBCJan19.pdf
Large deflection (15 mrad) to enhance the precession effect
and to send particles within the LHCb acceptance
Sensitive to g-2 of the particle
Cofinanced by ERC CoG SELDOM (PI N. Neri, Milano)
“Parasitic fixed-target experiments” were proposed for LHC
(see SPSC-EOI-012 and Eur. Phys. J. C (2017) 77:181)
New experiment @IR3
Before a possible test @LHCb detector, a proof-of-principle demonstration in a different LHC point is required @Interaction Region 3 in LHC (IR3).
From: E. Spadaro Norella https://agenda.infn.it/event/31703/timetable/?print=1

## Slide 8: Enhancement of bremsstrahlung in aligned crystals
Single atom
String of atoms
e-
e-
HE
e-
Channeling Radiation (1976, Kumakhov)
Notes: Crystal-assisted collimation: a curved crystal deviates the halo directly to the primary absorber.
8

## Slide 9: Coherent Bremsstrahlung gamma-ray sources
Intense and monochromatic gamma source
MAMI – Germany
JLAB – USA
MAXLAB – Sweden
ELSA - Germany
Linearly polarized photons
usually exploited
for photonuclear researches
e- @ 8 GeV
JLAB example: underlying symmetry of the quark degrees of freedom in the nucleon, the nature of the parity exchange between the incident photon and the target nucleon.
Degree of linear photon polarization achievable @MAMI in different diamond orientation
Notes: Crystal-assisted collimation: a curved crystal deviates the halo directly to the primary absorber.
9

## Slide 10
Classical scheme: magnetic undulator in a free electron laser
keV X-rays
λu⁓ cm
Innovative scheme:
Crystalline undulator->
Hard X-rays and gamma rays
λu < mm
Korol, Solov'yov, Greiner, J.Phys.G, v.24, L45 (1998)
An operating CU could produce highly monochromatic X- and γ-ray beams
-
Crystalline undulator
as an intense X- and γ-ray source
APPLICATIONS: in basic sciences (from nuclear physics to solid state) and life, in technology and medicine. For example, they can be used for the disposal of radioactive waste or the production of radioisotopes for nuclear medicine by photo-transmutation.
TECHNO-CLS

## Slide 11: Hybrid crystal based positron source for future colliders
UNPOLARIZED POSITRON SOURCES
1. Conventional
R.Chehab/FCPPL-Clermont/2014
e-
e+
e-
γ
amorphous
2. e+ from channeling radiation
e-
γ
e+
e-
Tests performed at CERN (WA 103) and at KEK
crystal
Idea of R. Chehab, V. Strakhovenko and A. Variola, NIM B 266 (2008) 3868
3. Hybrid crystal based positron source
Option for FCCee
Ideal for linear colliders or LEMMA

## Slide 12: Hybrid source for FCCee
configuration | tgt. PEDD | e+ rate [e+/e-] | e+ beam size [mm] | e+ beam divergence [mrad] | e+ mean energy [MeV]
conventional, 17.6 mm W am | 0.038 | 13.7 | 0.67 | 25.915 | 48.7
hybrid, 2mm W cry + 1 m distance + 11.6 mm W am | 0.008 | 15.1 | 1.24 | 26.841 | 45.6
hybrid, 2mm W cry + 2 m distance + 11.6 mm W am | 0.004 | 14.9 | 1.55 | 29.208 | 46.1
hybrid, 2mm W cry + 0.6 m distance + 11.6 mm W am | 0.013 | 15.1 | 1.05 | 27.392 | 46.2
configuration |  | e+ rate [e+/e-] | e+ beam size [mm] | e+ beam divergence [mrad] | e+ mean energy [MeV]
conventional, 17.6 mm W am | 0.038 | 13.7 | 0.67 | 25.915 | 48.7
hybrid, 2mm W cry + 1 m distance + 11.6 mm W am | 0.008 | 15.1 | 1.24 | 26.841 | 45.6
hybrid, 2mm W cry + 2 m distance + 11.6 mm W am | 0.004 | 14.9 | 1.55 | 29.208 | 46.1
hybrid, 2mm W cry + 0.6 m distance + 11.6 mm W am | 0.013 | 15.1 | 1.05 | 27.392 | 46.2
Comparable e+ rate at the target exit, but much less PEDD in the converter target!
L. Bandiera et al., Eur. Phys. J. C (2022) 82:699
e+ source optimization with 6 GeV e- beam**
Crystal radiator
Test foreseen at PSI in 2025

## Slide 13: Crystals technology at INFN-Ferrara
Collimation & beam steering
Innovative radiation sources
Pair production studies
Innovative detectors
Innovative radiation sources
Beam steering
ERC-CoG CRYSBEAM (LHC beam extraction)
ERC-CoG SELDOM (Studies of MDM and EDM of charmed baryons)
MCA-IRSES CUTE (crystalline undulators)
MSCA-RISE PEARL (crystalline undulators) MSCA-RISE N-LIGHT (crystalline radiation sources)
EIC-PATHFINDER TECHNO-CLS (crystalline radiation sources)
Beam steering
Innovative radiation sources
Innovative radiation and positron sources
Innovative detectors
Beam extraction
Involved in Channeling experiments since 2000

## Slide 14: INFN-Ferrara infrastructure
Laboratory fully equipped for silicon micro and nanomachining
ISO4 certified clean room (130 m2)
High-resolution x-ray diffraction
Dicing and polishing equipment
White light and Fizeau inteferferometers

## Slide 15: INFN-Ferrara infrastructure
Laboratory fully equipped for silicon micro and nanomachining
Fotolitography
Equipment for silicon chemical etching
Nanoimprint

## Slide 16: Test facilities
e- @ subGeV
MAMI (Mainz, Germany)
e± @6 GeV
DESY (Hamburg, Germany)
p, e±, π± @ (1-400) GeV
CERN EA&NA
(Geneve, Switzerland)
e- @multi-GeV
SLAC (Stanford, USA)

## Slide 17: FERRARA TEAM
Laura Bandiera
Vincenzo Guidi
Andrea Mazzolari
Marco Romagnoni
Mattia Soldani
Alexei Sytov
Main external collaborations
CERN, DESY, MAMI, MBN Center, INP Minsk, IJCLab
Main italian collaborations
UniPD, UniRoma, UniInsubria, UniMilano
Legnaro labs, Frascati Labs

## Slide 18: Summary
INFN-Ferrara has unique infrastructures in the world for the production of crystals for the manipulation of particle beams.
Collaborations with laboratories and accelerators all over the world.
Crystals as innovative elements for the manipulation of particle beams, for the realization of intense radiation and particle sources and useful elements for fundamental physics research .
Contacts: bandiera@fe.infn.it
mazzolari@fe.infn.it