## Slide 1
E. V. Pagano1, C. Boiano2, G. Cardella3, A. Castoldi2,5, E. De Filippo3, E. Geraci3,4, B. Gnoffo3,4, C. Guazzoni2,5, G.
Lanzalone1,6, C. Maiolino1, N.S. Martorana3, F. Noto1, A. Pagano3, S. Pirrone3, G. Politi3,4, F. Risitano3,7, F. Rizzo1,4, P. Russotto1, G. Santagati3, M. Trimarchi2,4, and C. Zagami1,4
1INFN, Laboratori Nazionali del Sud, Catania, Italy
2INFN, Sezione di Milano, Milano, Italy.
3INFN, Sezione di Catania, Catania, Italy. 4Dipartimento di Fisica ed Astronomia, Università di Catania, Catania, Italy.
5Politecnico di Milano, Dip. Elettronica, Informazione e Bioingegneria, Milano, Italy
6Università di Enna ‘‘Kore’’, Enna, Italy.
7Dipartimento di Scienze MIFT, Università di Messina, Messina, Italy.
CHIRONE Coll.
NArCoS: a new correlator for neutrons and charged particles with high angular and energy resolution
(Neutron Array for Correlation Studies)

## Slide 2
Project’s motivations
The advent of the new facility for Radioactive Ion Beams (RIBs)
in particular for the n-rich ones
From: M. Lewitowicz EURISOL-DF 15-16 Nov 2017, Lisbon
“The RIBs are an important opportunity”
(C. Horovitz)
FRAISE@LNS
  WPCF 2023 – Catania (Italy) - 7 november 2023
E. V. Pagano. LNS-INFN
1

## Slide 3
IDEA
6.4 cm
6.4 cm
300 μm
32 strip front
32 strip back
Δstrip = 2 mm
Interstrip = 0.1 mm
T
DSSSD 32x32
300 μm
NArCoS
≈ 12 cm
CP
n
100/150 cm
50/75 cm
3x3x3cm3
SiPD
EJ276G
To realize a prototype of detector able to detect at the same time charged particles and neutrons with high energy and angular resolution for reaction studies and applications
Candidate: The plastic scintillator EJ276-Green Type (ex EJ299-33) (3x3x3cm3)
1 cluster: 4 consecutively cubes -> 3x3x12 cm3
Reading the light signal: SiPM and digitalization
Neutron detection efficiency ≈ 50% for the prototype (16 clusters)
Modular, reconfigurable (in mechanic and electronic)
Discrimination of n/γ from PSD (but also light charged particles)
Energy measurement from ToF (Δt≤0.5 ns with LToF≈1÷1.5m)
TOF measured using the RF of the CS or with an ancillary MCP (low intensity exotic beams)
  WPCF 2023 – Catania (Italy) - 7 november 2023
E. V. Pagano. LNS-INFN
2

## Slide 4
DSSSD 32x32
300 μm
NArCoS
≈ 12 cm
T
LNArCoS=150 cm
LDSSSD=75 cm
θ≈5°
Solid angle ≈ 7 msr (0.07%)
Angular resolution DSSSD ≈ 0.15°
Angular resolution NArCos ≈ 1.25°
<EFF>≈25%
For one cluster
L=150 cm; ΔT=0.5 ns
Time of flight
*
Expected performances
*the mechanical structure will have the possibility of an angular muvimentation
  WPCF 2023 – Catania (Italy) - 7 november 2023
E. V. Pagano. LNS-INFN
3

## Slide 5
DSSSD 32x32
300 μm
NArCoS
≈ 12 cm
T
LNArCoS=150 cm
LDSSSD=75 cm
θ≈5°
Solid angle ≈ 7 msr (0.07%)
Angular resolution DSSSD ≈ 0.15°
Angular resolution NArCos ≈ 1.25°
<EFF>≈25%
For one cluster
L=150 cm; ΔT=0.5 ns
Time of flight
*
*the mechanical structure will have the possibility of an angular movimentation
Expected performances
  WPCF 2023 – Catania (Italy) - 7 november 2023
E. V. Pagano. LNS-INFN
4

## Slide 6
i-Spector from CAEN (3x3 cm SiPM and electronics)
Detector Configurations:
  EJ-276G + PMT
  EJ-276 + i-Spector
  EJ-276G + i-Spector
Lab measurements with radioactive sources:
  Vacuum Chamber
  Pb shield
  Gamma sources: 133Ba, 137Cs, 60Co, 152Eu
  Alpha source: 241Am
  Digitizer from CAEN
Data analysis of heavy ion reactions:
  CHIMERA scattering chamber (LNS)
  Detector at 11˚ in lab frame
  Beam: 124Sn at 20 MeV/A (CHIFAR experiment)
  Targets: 64Zn and 64Ni
  GET digital electronics
Latest resuls: tests by using the SiPM (i-Spector CAEN)
The test was done during the master thesis work of A. Simancas in Catania (EVP tutor)
Example of signal and integration windows
E.V.Pagano, G. Politi, A. Simancas et al., submitted at NIM A
EJ276
EJ2766
  WPCF 2023 – Catania (Italy) - 7 november 2023
E. V. Pagano. LNS-INFN
5

## Slide 7
Gamma spectra
Chart: Energy Calibration
| 490.268700 | 1199.663075 | 2807.622700
E (keV) | 207 | 478 | 1041
EJ-276G + i-Spector
50%
Pagano E.V. et al., Nucl. Instr.. Methods A, 889 (2018) 83-88 )
  WPCF 2023 – Catania (Italy) - 7 november 2023
E. V. Pagano. LNS-INFN
6

## Slide 8
PSD studies using sources
Detector | FoM
i-Spector + EJ-276 | 0.98
i-Spector + EJ-276G | 1.47
PMT + EJ-276G | 1.03
EJ-276 + i-Spector
EJ-276G + i-Spector
Particle Identification Paramenter
Test with radioactive sources (low background). Sources 241Am + 137Cs. Setup: EJ276 + SiPM (I-spector). EJ276G + SiPM (I-spector)
Comparison between the two plastic versions: the “ordinary” and the “green shifted”
  WPCF 2023 – Catania (Italy) - 7 november 2023
E. V. Pagano. LNS-INFN
7

## Slide 9
PSD studies using beams
CHIFAR exp @LNS (spokesperson:EVP, E. De Filippo, P. Russotto)
PSD Method | FoM(γ, Z=1) | FoM(Z=1, Z=2) | FoM(γ, LCP)
Integration | 1.08 | 0.78 | -
Decay Time | 0.95 | 0.87 | 0.71
LCP = Light Charged Particles
Neutrons included in Z=1
EJ-276 + i-Spector
Test with beam (high background). Setup: EJ276 + PMT (1.6 kV) reaction 124Sn + 64Zn @ 20 AMeV
More information about the “Decay time” identification technique:
E. V. Pagano et al. NIM A 905 (2018) 47-52
  WPCF 2023 – Catania (Italy) - 7 november 2023
E. V. Pagano. LNS-INFN
8

## Slide 10
What about the neutron detection efficiency?
GEANT 4 simulation in order to estimate the neutron detection efficiency
Mean value for one detection cluster (3x3x12 cm3) ≅ 25%
Mean value for one detection cell (3x3x3 cm3) ≅ 9%
Chart: Neutron Energy (MeV)
| 5.000000 | 10.000000 | 15.000000 | 20.000000 | 25.000000 | 30.000000 | 35.000000 | 40.000000 | 45.000000 | 50.000000
Threshold: 0 MeV | 0.73885 | 0.64887 | 0.63202 | 0.61637 | 0.58801 | 0.55677 | 0.52164 | 0.48584 | 0.4566 | 0.43198
Threshold: 0,5 MeV | 0.61694 | 0.52443 | 0.49243 | 0.46943 | 0.43505 | 0.4035 | 0.37923 | 0.344 | 0.32274 | 0.303
Threshold: 1,5 MeV | 0.45549 | 0.43661 | 0.39352 | 0.3785 | 0.33972 | 0.31454 | 0.28583 | 0.26613 | 0.23653 | 0.22364
Threshold: 4 MeV | 0.21851 | 0.30611 | 0.24987 | 0.23292 | 0.27953 | 0.27154 | 0.25158 | 0.23958 | 0.20489 | 0.19209
Mean value for a 36-cell array (9x9x12 cm3) ≅ 33%
Scheme of Simulation Geometry: 36 (3 x 3 x 4) cell array
Libraries: QGSP_BIC_HP
  WPCF 2023 – Catania (Italy) - 7 november 2023
E. V. Pagano. LNS-INFN
9

## Slide 11
Two configurations will be tested in order to study the crosstalk problem
The central cel at 5° in the Lab Frame
Preparation of the CROSSTEST exp at LNL (23-30 Nov 2023)
Efficiency calculation (GEANT4)
Crosstalk problem study (GEANT4)
3x3 Matrix
3x3 Matrix
%
%
Simulation studies
See G. Santagati talk for details
3 clusters
3 clusters
%
%
Neutron beam from the reaction: p + 7Li —> n + 7Be @5.5 MeV (proton energy of the CN accelerator)
  WPCF 2023 – Catania (Italy) - 7 november 2023
E. V. Pagano. LNS-INFN
10

## Slide 12
Preparation of the CROSSTEST exp at LNL (23-30 Nov 2023)
Prototype Electronics
Prototypal readout electronic and mechanic for the CROSSTEST exp at LNL (23-30 Nov 2023)
in coll. with INFN-MI (C. Boiano)
AmBe source: PSD test
Each elementary cell of EJ276G (3x3x3 cm3) is equipped with a matrix of 25 SiPM (6x6 mm2) of 30 𝜇m of thickness (≈ 40k microcells). The SiPM matrix is coupled with the plastic having theirs PAC and bias/temperature compensation circuit
400 ns
Fast respons < 4 ns
500 MHz sampling
Electronic Board for housing the 9 elementary cells with its electronic readout boards, with the out of the signals, test ingress, temperature monitoring and bias ingress
Pulser signal test
  WPCF 2023 – Catania (Italy) - 7 november 2023
E. V. Pagano. LNS-INFN
11

## Slide 13
Purposes of the project
Nuclear fundamental physics
Some applications
Energy of interest: 5≤ E ≤100 AMeV (having particular attention to the Fermi regime)
Intensity interferometry (HBT effect)
n-n, n-p, n-LCP, n-IMF, n-TLF, n-PLF
Studies related to the nuclear symmetry energy (EOS) and its dependence to the nuclear density
Neutron stars (nuclear astrophysics)
Reaction mechanism
Reaction times
Clustering
Validation of nuclear dynamics model (BUU,QMD)
Measurements of the neutron signal in the n-rich RIBs (SPES, SPIRAL2, FRIB, FAIR)
Radioprotection
Measurement of neutron flux (single measurement, cross section)
Validation of MC based code (GEANT4, MCNPX)
Homeland security
  WPCF 2023 – Catania (Italy) - 7 november 2023
E. V. Pagano. LNS-INFN
12

## Slide 14
Correlation functions
Intensity interferometry (HBT effect)
Space-time characterization of the emitting source
N. Colonna et al., PRL 75, 23 (1995) 4190-4193
R. Ghetti et al., PRL 87, 10 (2001)
neutron-neutron
proton-proton
0.0
0.5
1.0
1.5
1
2
3
4
1
3
5
7
q (MeV/c)
1+R(q)
proton-neutron
52Ca+48Ca E/A=80MeV
Central collision
Lie-Wen Chen et al., PRL (2003); PRC(2005)
Purposes of the project: a few example for the fundamental nuclear physic
  WPCF 2023 – Catania (Italy) - 7 november 2023
E. V. Pagano. LNS-INFN
13

## Slide 15
In proton therapy, in particular in the pediatric one (but not only), the “damage” caused from the neutron to the healthy cells is one of the principal causes of the so called “ secondary radio-induced tumors” in particular if there are used degraders or collimators (passive technique)[1].
Anti-cancer therapy:
Risk of secondary radio-induced cancers
[1] Hall, E. J (2006) Intensity-modulated radiation therapy, protons, and the risk of second cancers.
Int J Radiat Oncol Biol Phys 65: 1-7.
Measurement of cross sections (d2σ/dθdE) have a huge interest for the validations of Monte Carlo code like GEANT4 in particular for neutrons in the Fermi energy regime
Validation of Monte Carlo codes
Purposes of the project: a few example applications
Neutron Camera
Possible device for homeland security and health safety to be installed in airports, ports, etc...
  WPCF 2023 – Catania (Italy) - 7 november 2023
E. V. Pagano. LNS-INFN
14

## Slide 16
The results obtained with the EJ276 scintillator coupled to a SiPM are encouraging. It seems possible to build a versatile and modular detector for neutrons and light charged particles with high angular and energy resolution, readout by using silicon photomultiplier and signal digitalization. The studies of the neutron detection efficiency and of the crosstalk problem and their influence on the experimental results are going on using the GEANT4 software, moreover these studies will be extended by means of a real experiment, the CROSSTEST at the LNL, within the end of the 2023.
The prototypal electronics readout is ready to be tested with sources and also in the CROSSTEST experiment
New studies on the timing properties of the EJ-276 green version and on its PSD capability coupled with the new electronic have to be done in the next future.
The study of the mechanical configuration of the NArCoS prototype is ongoing.
An extension of the study for the efficiency and for the crosstalk problem for the prototype in its final configuration has to be done by means of GEANT4 and also with new experiments to be performed in Catania at LNS and in Legnaro at LNL
Conclusions and perspectives
  WPCF 2023 – Catania (Italy) - 7 november 2023
E. V. Pagano. LNS-INFN
15

## Slide 17
For more info see :
1) Pagano E.V. et al., N.S., Nucl. Instrum. Methods A, 889 (2018) 83-88
2) Pagano E.V. et al., N.S., Nucl. Instrum. Methods A, 905 (2018) 47-52
3) Pagano E.V. et al., IL NUOVO CIMENTO 41 C (2018) 181
4) Pagano E.V. et al., JPS Conf. Proc. 32, 010096 (2020)
5) Pagano E.V. et al., IL NUOVO CIMENTO 43 C (2020) 12
6) Pagano E.V. et al., J. Phys.: Conf. Ser. 1643 (2020) 012037
7) Pagano E.V. et al., IL NUOVO CIMENTO 45 C (2022) 64
8) Pagano E.V. et al., Front. Phys. 10:1051058
9) Pagano E.V. et al., LNS Report (2022)
10) Pagano E.V., G. Politi, A. Simancas et al., NIM A submitted (PSD comparisons between EJ276G+SiPM and EJ276+SiPM)
11) Pagano E.V., G. Santagati et al., NIM in prep. (simulations on efficiency and crosstalk )
Thanks for the attention
  WPCF 2023 – Catania (Italy) - 7 november 2023
E. V. Pagano. LNS-INFN
16