## Slide 1: Programma di sviluppo per il design di cavità SC per la sezione alta energia: contributo INFN
D. Sertore
INFN Milano – LASA
for the SRF group

## Slide 2: Introduction
Fast acceleration is key for muon survival rate
Needs large RF voltage in short length
  High-gradient RF system
Huge total RF voltage per turn in circular accelerator
Few turns, one m+ and one m- bunch simultaneously
This presentation is freely taken from «SRF Systems for Rapid Cycling Synchotron» presented at 2022 Muon Collider Annual Meeting

## Slide 3: Introduction
hybrid RCS 5 TeV
norm. cond. RCS
hybrid RCS 1.5 TeV
hybrid RCS
Both in the same tunnel
Rapid cycling synchrotrons (RCS) chain, counter-rotating m+/m- bunches
Conventional RCS and 2…3 hybrid RCS: normal and supercon. magnets
63 GeV  0.31 TeV
0.31 TeV  0.75 TeV
0.75 TeV  1.5 TeV
(1.5 TeV  5 TeV)

## Slide 4: Distributed RF system along the circumference
Limit energy gain per RF station
  Avoid large energy difference between counter-rotating m+/m- beams
    During first turn in RCS1 energy gain is about 20% of beam energy!
  Transverse optics can limit the impact of beam energy differences
  Not the most stringent constraint
Ein
Ein+eVRFsin(fS)
Ein
Ein+eVRFsin(fS)

## Slide 5: Why distributed RF system? How many stations?
Multiple longitudinal kicks per turn to smoothen synchrotron motion again
  Stable synchrotron oscillations and phase focusing for QS << nRF ∙ 1/p
  Tracking simulations to determine longitudinal emittance growth (with BLonD code)
  Favourable range of nRF ≈ 30
  Tune QS as large as 1.5
F. Batsch
Long. emittance growth versus nRF in RCS1

## Slide 6: Rapid Cycling Synchrotron (RCS) parameters
Principle of hybrid RCS (RCS2, 3 and 4):
  Fast ramping of normal conducting magnets from negative to positive field: -1.8 T  + 1.8 T
  Fixed-field super-conducting magnets in addition (max. 10 T)
Beam orbit moves during acceleration  frev and fRF sweep
Assume max. 10 cm orbit length change for RCS2
A. Chancé

## Slide 7: RF frequency sweep (example of RCS2)
RF frequency sweep need in ~1 ms, from injection to extraction
Df/f = Dl/(2pR) ≈ 1.7 ∙ 10-6  Df ≈ 2.2 kHz
  Control RF frequency during ‘beam pulse’
  In addition to compensation of Lorentz force detuning
Reported tuning ranges for ILC-style cavities
  W. Cichalewski et al., ICALEPCS2015: Df ≈ 1.2 kHz
  Y. Pischalnikov, ILCX2021-ILC: Df ≈ 3 kHz
Faster: Turn-by-turn transient beam-loading correction
  FerroElectric Fast Reactive Tuners (FE-FRT)
Piezo
Typical path length change during
acceleration
A. Chancé

## Slide 8: Why super-conducting?
Large RF voltage during long pulses
Energy efficient acceleration technology
High accelerating gradient per RF structure length: 30 MV/m
Standing wave operation for counter-rotating bunches
RF voltage and acceleration time

## Slide 9: RCS RF system choices
Frequency | Accelerator | Remark
352 MHz | LEP | Moderate gradient
400 MHz | LHC, FCC | Moderate gradient
800 MHz | ERL, (FCC) | Alternative option also for mRCS
1.3 GHz | TESLA, ILC, FELs (XFEL) | Wide-spread technology with decades of experience
1.5 GHz | JLab-CEBAF | 
Common frequencies for superconducting RF
Starting assumption

## Slide 10: Pulsed of operation, duty cycle
Repetition rate of RCS chain: 5 Hz (as ILC)
Minimum beam pulse length for RF system?
Pulse length ~1.6 ms same order as for ILC (beam pulse length 0.7 ms)
 | RCS1 | RCS2 | RCS3 | (RCS4)
Ejection energy, Eej [TeV] | 0.31 | 0.75 | 1.5 | (5.0)
Circumference, 2pR [km] | 5.99 | 5.99 | 10.7 | (35)
Acceleration time, beam pulse length, tacc [ms] | 0.34 | 1.1 | 2.4 | (6.4)
Beam pulse

## Slide 11: First beam loading considerations
Only one high-intensity bunch (of each type) accelerated in RCS
Average beam current more than three times (2) above ILC
Very strong transient beam loading
 | ILC | RCS1 (and RCS2)
Number of bunches, nb | 1312 | 1 each m+ and m-
Bunch spacing, tbs | 554 ns | Trev = 20 ms
Bunch intensity, Nb | 2 ∙ 1010 p/b | 2.5 (2.3) ∙ 1012 p/b
Average beam current, Ib | 5.8 mA | 2  ~20 mA

## Slide 12: External loading and feedback requirements
Steady-state detuning to minimize reflected power (reactive beam loading compensation)
  DfRF/fRF ≈ 5 ∙ 10-7  DfRF ≈ 2  0.32 kHz
Optimal external quality factor
  Optimal external quality factor Qext,opt ≈ 1…2 ∙ 106 (within 1…10 ∙ 106 of tunable fundamental power coupler for ILC)
Assuming constructive interference of counter-rotating m+ and m--bunches
Beam-loading of counter-rotating beams subject to further studies

## Slide 13: Transient power and feedback considerations
With 2  20 mA beam current, power to beam ~2  430 kW
Beam induced voltage at fRF about 2 x 1.7 MV during bunch passage (builds up)
Conventional direct feedback (e.g., loop delay, td ≈ 700 ns in LHC) too slow
  Correction would be applied after bunch
Need 1-turn delay feedback with m+/m- separation
Muon RCS advantage: only one bunch per beam and few turns
Explore cycle-by-cycle adaptive compensation
m+
m-
P. Baudrenghien, T. Mastoridis, PRAB 20, 011004 (2017)
Example: LHC RF feedback system

## Slide 14: Summary
Challenging 1.3 GHz RF system for mRCS
Main ‘non-conventional’ assumptions
  Modular, distributed RF system: ~30 RF stations (700 9-cell cavities, RCS1) ideally equidistant  infrastructure
  Longer pulses than ILC: 2.4 ms (6.4 ms) beam pulse for RCS3(4)
  More power, larger beam current
  Cavity tuning to compensate orbit length sweep during acceleration (~few kHz)  in addition to measures against Lorentz force detuning and mechanical resonances

## Slide 15: WP6 task 6.1 Status
“… aims to provide a preliminary design concept for the SRF cavities for acceleration in the Rapid Cycling Synchrotrons (RCS) of the HEC of the muon collider …”
Two meetings up to now
  From 2023, monthly meeting
First discussion on parameters presented at October Meeting (reported in this presentation)
All partners (CEA, INFN, Uni. Rostock*) share all thematic. Within this:
  CEA
    Fundamental power coupler (FPC)
    Beam Loading
  INFN
    High Order Mode
    Frequency sweep
  Uni. Rostock
    SRF Cavity study, especially frequency choice.
* WP task leader

## Slide 16: Summary of RF requirements
Parameter | Value | Remark
Frequency, fRF | 1.3 GHz | 
Tuning range (piezo), Df | 2.2 kHz | Sweep for acceleration, hybrid RCS2/3/4
Gradient, VRF/l | 30 MV/m | 
Beam pulse length, tacc | 0.34/1.1/ 2.4/6.4 ms | RCS1/2/3/4
Beam current, IDC | 2  20 mA | 
Power to the beam (max., RCS1) | 2  250 MW | ~2  430 kW/cavity

## Slide 17: General parameters
 | RCS1314 GeV | RCS2750 GeV | RCS31.5 TeV
Circumference, 2pR [m] | 5990 | 5590 | 10700
Energy factor, Eej/Einj | 5.0 | 2.4 | 2.0
Repetition rate, frep [Hz] | 5 (asym.) | 5 (asym.) | 5 (asym.)
Number of bunches | 1m+, 1m- | 1m+, 1m- | 1m+, 1m-
Bunch population | 2.5x1012 | 2.3x1012 | 2.2x1012
Survival rate per ring | 90% | 90% | 90%
Acceleration time [ms] | 0.34 | 1.04 | 2.37
Number of turns | 17 | 55 | 66
Energy gain per turn, DE [GeV] | 14.8 | 7.9 | 11.4
Acc. gradient for survival [MV/m] | 2.4 | 1.3 | 1.1
Acc. field in RF cavity [MV/m] | 30 | 30 | 30
Max. RF voltage for fs=45° [GV] | 20.9 | 11.2 | 16.1

## Slide 18: Thank you !