## Slide 1: Status of Flash Therapy in Pisa
Maria Giuseppina Bisogni
Universita’ e INFN sezione di Pisa
INFN4LS meeting, Presidenza INFN, Roma, 10/11/2022

## Slide 2
FLASH RADIOTHERAPY
Radiation-therapy technology able to deliver at ultra-high dose rate ( ≥40 Gy/sec) a total dose in 100-200 msec
allow to treat tumors without inducing drastic toxicities on the surrounding normal tissues
Notes: When we irradiate tissues with very high dose rate and the total dose is given in milliseconds we observe a particular effect named Flash effect. Basically The flash effect is a biological phenomenon that consist in a remarkable sparing of normal tissues while the effect on tumors is maintained the same. So we can reach a very strong differential effect between the tumor cells and the healty cells achieving a significant increase in the therapeutic index of radiotherapy.
We can thus achieve a significant increase in the therapeutic index of radiotherapy
The Flash effect is a biological observation wich can be done when we irradiate tissues with very high dose rate and the dose is given in milliseconds and consist in a remarkable sparing of normal tissues while the effect on tumors is maintained the same. So we can reach a very strong differential effect between the tumor cells and the healty cells.
We can thus achieve a significant increase in the therapeutic index of radiotherapy
When we irradiate tissues with very high dose rate and the total dose is given in milliseconds we observe a particular effect named Flash effect. Basically The flash effect is a biological phenomenon that consist consist in a remarkable sparing of normal tissues while the effect on tumors is maintained the same. So we can reach a very strong differential effect between the tumor cells and the healty cells.
We can thus achieve a significant increase in the therapeutic index of radiotherapy

## Slide 3
FLASH radiation therapy
Limitation of ’’Conventional’’ RT
radiation-induced toxicities
Flash-RT would allow:
To treat radioresistant tumor increasing total dose without the associated surrounding tissue toxicity of CONV-RT
To treat diffuse/Non localized tumors where CONV-RT can not deliver tumoricidal doses
To treat tumors where radiotherapy already offers good local control but without the side effects typical of CONV-RT
possibility of widening the therapeutic "window"
possibility of increasing the therapeutic doses
Notes: Infact despite these advances several tumors are still incurable for example radioresistant tumors because the doses that we need to delivery to achieve tumor control often overlaps with those that cause complication. After all the main limitation of conv-RT still remain radiation-induced toxicities and in practice conv-RT can not cure all the patients we would like to cure.
In this scenario a great opportunity to increase the therapeutic index of radiotherapy is represented by flash-radiotherapy this thecnology infact seems to increase the differential effects of radiations between normal tissue and tumor very strongly.
because the main limit of conv-RT still remains the radiation induces toxicities. As you can see in the picture the therapeutic index of radiotherapy that is the relationship between the probability of tumour control (TCP) and the risk of normal tissue complications (NTCP) in several oncological conditions is very narrow because the doses necessary to achieve tumour control usually overlap with those that can cause complications so basically today conv-RT can not cure all the patients we would like to cure.
In this scenario flashradiotherapy has emerged as a treatment technique with the great potential of increase the differential effect of radiotherapy between normal tissue and tumor. compared to conventional radiotherapy increasing the therapeutic index. Flash radiation therapy will allow us to treat…..
The Flash effect is a biological observation wich can be done when we irradiate tissues with very high dose rate and the dose is given in milliseconds and consist in a remarkable sparing of normal tissues while the effect on tumors is maintained the same. So we can reach a very strong differential effect between the tumor cells and the healty cells.
We can thus achieve a significant increase in the therapeutic index of radiotherapy
The dose delivered to the tumor is, hence, limited by the toxicity to nearby healthy tissue; this can mean that a tumor cannot be completely killed, and the efficacy of radiotherapy will be decreased. Thus, preventing or mitigating radiation-induced healthy tissue injury has always been a topic of particular interest in radiotherapy research.
The goal of radiotherapy is to deliver as much dose to the tumour whilst sparing normal tissue. Every dose of radiation delivered to a patient, with the aim of cure of a tumour, is limited by the possibility of serious damage to normal tissues. The balance between the probability of tumour control (TCP) and the risk of normal tissue complications (NTCP) is a measure of the therapeutic ratio of the treatment.
For some tumours, such as carcinoma of the prostate, there is evidence of a dose– response curve with dose escalation leading to increased tumour control rates. As shown in Fig. 1, there is also a dose–response curve for normal tissues and dose escalation may lead to increased normal tissue damage.
Normal tissue damage cannot be completely avoided because the doses necessary to achieve tumour control usually overlap with those that can cause complications.
The therapeutic index of radiotherapy has been progressively increasing thanks to the technological progress of the last 20 years
Flash It could be used in the clinic to allow for an increase of total dose in the treatment of tumours resistant to radiation that are currently associated with worse patient outcomes, as a higher dose could be used without the associated surrounding tissue toxicity of CONV-RT. It could also be used in situations where radiotherapy offers good tumour control but is associated with tissue toxicity as the same dose could be administered but with less toxicity than that of CONV-RT.

## Slide 4
Questioni aperte fondamentali per un ampio utilizzo
clinico della Flash e sua ottimizzazione
Teoriche
Quantitative
Capire i meccanismi radiobiologici alla base dell’effetto
Tecnologiche
Dipendenza dose, dose-rate, dose-per-pulse e instantaneous dose-per-pulse
Dipendenza da LET
Campi adiacenti
Frazionamento
Realizzazione LINAC elettroni VHEE (100-250 MeV)

## Slide 5
Per capire i problemi teorici e le dipendenze quantitative cosa serve?
Esperimenti Radiobiologici quantitativi
LINAC dedicato
Dosimetria
Multidisciplinarieta'

## Slide 6
Centro multidisciplinare per lo sviluppo e l’implementazione della Flash radiotherapy (CPFR)
Inaugurazione 28/6/2022
Notes: We are working to aquire:
-most robust data about the radiobiological
mechanisms underlying the effect
-knowledges of the quantitative
relationships between the flash effect
and the parameters of the beam
(dose-rate, dose-per-pulse, LET…)
and the characteristics of the
irradiated tissue (type, volume…)

## Slide 7
SIT ELECTRONFLASH 4000
Electrons 9 MeV
Triode gun
1 cm ∅ smallest applicator

## Slide 8
CPFR Research Program
Main Goals
Quantitative Radiobiological Experiments
in vitro/organoids/ex-vivo/in vivo
Theoretical/computational
radiobiological modelling
Understand the mechanism underlying the Flash effect
Quantitatively assess the relationship between beam parameters and Flash effect
BASIC RESEARCH GOALS
To optimize the clinical
implementation of the Flash RT with
low energy electrons.
To acquire propedeutic data for the
future development and clinical
implementation of VHEE flash RT
Notes: We are going to carry out quantitative radiobiological experiments using in vitro, organoid, ex vivo and in vivo models combined with a multi-scale and multi-methodological computer simulation and modeling approach. To obtein a complete, yet detailed comprehension of the mechanisms of the UHDR differential effects and to asses the relationship between beam parameters and flash effect
8

## Slide 9
CLINICAL GOALS
for Flash low-energy electron beams
CPFR Research Program
Main Goals
Pre-clinical in vivo studies
Development of a clinical dosimetric
protocol
Development of a patient
positioning and centering system
Development of a specific TPS
(Treatment Planning System)
SKIN TUMORS
UVEAL MELANOMA
CLINICAL TRIALS
Notes: Finally, a clinical protocol will be defined for the treatment of dermatological tumors through the optimization of Irradiation parameters, the definition of the most appropriate clinical settings and the criteria for patient selection.
9

## Slide 10
Collaborations
Marie Curie Institute (Parigi)-2020
Iridium Network (Anversa)-2021
CPRF (Pisa)-2022
ELECTRONFLASH
radiobiological experiments
dermatological treatments (3y)
LIAC FLASH
IORT FLASH (5y)
VHEE FLASH
treatment of deep tumors (?)
The network between these Centers is paramount for exchanging ideas, standardizing procedures and acquiring more data
Notes: to answer these questions also in Pisa we created a multidisciplinary center dedicated to the flash radiotherapy thanks first of all to the knowledge of Doctor Martino who has been involved for many years in IORT and electron beams and the support of Fondazione Pisa, University of Pisa and AOUP and soon we will have an electron linac for the research that will be placed inside the radiotherapy unit of AOUP
We are working to aquire:
-most robust data about the radiobiological
mechanisms underlying the effect
-knowledges of the quantitative
relationships between the flash effect
and the parameters of the beam
(dose-rate, dose-per-pulse, LET…)
and the characteristics of the
irradiated tissue (type, volume…)

## Slide 11
Research Toward VHEE Clinical Device
Pencil beam delivery mode
Multiple-field arrangement
to conform the dose
It is crucial to investigate quantitative dependencies of the flash effect from :
Irradiated volume
Adjacent fields
Fractionaction
Challenges
Optimize the delivery method
Optimize the clinical use
Collaboration with Sapienza Università di Roma and
INFN
Notes: For the timescale involved in flash effect this is equivalent to the fractionation of the dose.
to optimize depth-dose distribution with electrons of energy greater than 100 MeV
The development of Flash VHEE devices is paramount for exploiting the Flash effect on a wider range of deeply seated tumors. Quantitative experiments and theoretical modelling of the dependencies of the Flash effect are needed to optimize the delivery method and the clinical use of the Very-High-Electron-Energy (VHEE) Flash Therapy.
As we can see on the right, for VHEE it is necessary to investigate quantitative dependencies of the flash effect from total irradiated volume, irradiation modality and total dose delivered. This is because to optimize depth-dose distribution with electrons of energy greater than 100 MeV pencil beam delivery is necessary, since it can mitigate electron lateral spread. This means that the dose is delivered with many small adjacent fields, therefore/thus the volume effect and the adjacent field effect becomes fundamental for evaluating the Flash effect. Also, multiple-field arrangement is necessary to conform the dose . Due to the timescales involved, this is equivalent to fractionating the dose, thus evaluating at which point the flash effect is maintaned and if there is a dose-threshold value for which the flash effect kicks in is of great importance. Another parameter to study is the instantaneous dose per pulse, as shown on the left. This can be of great advantage for laser driven VHEE modalities since the pulse lenght is intrinsically much smaller, resulting in much larger IDPP values.
For the timescale involved in flash effect this is equivalent to the fractionation of the dose
Prima cosa: perché la tecnologia laser-driven?la tecnologia laser-driven è molto indietro attualmente rispetto a quella standard a radiofrequenza (RF) perché si basa su processi fisici intrensecamente meno controllabili e riproducibili, sia in termini di fluenza che di spettro energetico. Il motivo per cui vi è interesse nel loro sviluppo derivano dal fatto che il processo di accelerazione delle particelle avviene in uno spazio molto piccolo, ovviando così alle difficoltà di accelerare in RF elettroni ad alta energia (VHEE) su lunghezze compatibili con i Linac medicali (entro 3 metri).
La caratteristica peculiare di questo tipo di tecnologia è quella di avere impulsi molto più brevi dei microsecondi dei linac a RF, quindi hanno un instantaneous dose-per-pulse (e solo quello) molto maggiore; questo significa che un eventuale incremento dell’effetto Flash con l’IDPP sarebbe una giustificazione anche clinico-radiobiologica (oltre a quella pratica relativa alle dimensioni e all’ingombro) al loro sviluppo.
Quindi te puoi riassumere dicendo:
Per la VHEE in generale – studio delle dipendenze quantitative illustrate a destra
Specificamente per la VHEE tramite tecnologia laser-driven – IDPP perché gli impilsi sono ridotti e di conseguenza è molto maggiore l’IDPP
Passiamo alla colonna di destra, VHEE in generale:
Per ottimizzare la distribuzione di dose in profondità con elettroni con E>100 MeV è necessaria un erogazione mediante pencil beam (singolo fascetto che “spazzola” il volume interessato. Questo per minimizzare lo spread laterale degli elettroni); questo significa erogare la dose mediante una serie di piccoli campi adiacenti. Diventa quindi fondamentale valutare per l’effetto Flash, sia l’effetto volume che quello dei campi adiacenti
oltre all’utilizzo della modalità pencil beam, sempre per conformare in modo accettabile la dose in profondità, è necessario utilizzare tecniche multicampo; per i tempi in gioco riguardanti l’effetto Flash questo equivale a frazionare la dose. E il mantenimento dell’effetto flash frazionando la dose equivale a valutare la dipendenza di quest’ultimo dalla dose (capire se c’è e quanto è un valore soglia e la dipendenza a partire da quel valore)
11

## Slide 12
Caratterizzazione fascio
PDD con flashDiamond
Profilo al BU uniforme per diversi cm
DPP circa 23 Gy/p
Chart: PDD FLASH Diamond
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40 | 45 | 50 | 43 | 30
 | 0.95522 | 0.97015 | 0.97015 | 0.98507 | 0.97015 | 0.97015 | 0.98507 | 0.98507 | 0.98507 | 1 | 1 | 1 | 1 | 0.9697 | 0.95455 | 0.95455 | 0.93939 | 0.92424 | 0.90909 | 0.87879 | 0.84848 | 0.81818 | 0.80303 | 0.72727 | 0.66667 | 0.59091 | 0.5303 | 0.43939 | 0.36364 | 0.28788 | 0.22727 | 0.16667 | 0.045455 | 0.0090909 | 0.078182 | 0.51515

## Slide 14
Esperimenti in vitro e in vivo
Esperimenti svolti in vivo e in vitro in condizioni CONV e FLASH
Riproducibilità del set-up garantita dal cannone a triodo

## Slide 15: Scintillator Dosimeters
Pulse time structure and linearity: the area of the signal of the monitoring system.
The linearity was verified in the whole dose range, the maximum available dose rate was tested (23 Gy/pulse) and different pulse widths were used.
M.G. Bisogni, M. Morrocchi,
E. Ciarrocchi et al.

## Slide 16: Experiment with Electron FLASH Linac accelerator @ CPFR
Experimental conditions
E = 9 MeV
Pulse duration: 0.1-4 us
Dose per pulse: from 0.1-5 Gy
Istantaneous dose rates up to MGy/s
10x10, 5x5, 1x1 mm2 10 um thick SiC
Alanine dosimeters at the build-up
30,40,100 mm Applicator
RC circuit connected to the detector to slow down
the current acquisition in the electrometer
Measurements
SiC response as a function of the BIAS voltage at the maximum dose per pulse and dose rate (5 Gy/pulse)
SiC response as a function of the dose per pulse to verify linearity in single pulse
Comparison with alanine detectors
R
C
5x5 mm2 10x10 mm 2 1x1 mm 2
2 cm air
SiC detectors for beam monitoring and dosimetry for FLASH
Courtesy of F. Romano,
G. Milluzzo

## Slide 17
Alanine pellets (diameter ~4.8 mm, height ~3.0 mm, and mass ~68 mg) are simple amino acid sample provided by Gamma Service (Germany).
Bruker Elexys E580 EPR spectrometer
Stack of alanine pellets for PDD
E = 9 MeV
Pulse duration: 4 us
Istantaneous dose rates up to MGy/s
Comparison with MC simulations
Monte Carlo
EPR
Depth [mm]
Courtesy of F. Romano, G. Milluzzo,
M. Marrale
Alanine detectors for UHDR beam absolute dosimetry
  Dose per pulse [Gy]

## Slide 18
Beam monitoring
Torino (INFN & Università degli Studi)
Silicon sensor
Number of strips: 11
Strip area: 2.2 mm2
Active thickness: 45
Total thickness: 615
LeCroy Digital oscilloscope
(WAVERUNNER 640Zi)
10 GS/s sampling rate
Beam test @ CPFR
4-5/10/2022
30 and 40 mm applicator
One strip readout through the oscilloscope
Courtesy of A. Vignati

## Slide 19
Courtesy of M. Marafini

## Slide 20
Ecosistema Innovazione «Tuscany Health Ecosystem» THE (HUB UNIFI- partners UNIPI and INFN) 110 spoke1: Advanced radiotherapies and diagnostics in oncology (spoke leader CNR; partner affiliati UNIFI, UNIPI, INFN)
Partenariato esteso Medicina di Precisione (PE6) Diagnostica e terapie innovative nella medicina di precisione (HEAL ITALY – PE6)
«Health Extended ALliance for Innovative Therapies, Advanced Lab-research, and Integrated Approaches of Precision Medicine»
SPOKE 5) Next-Gen Therapeutics
SPOKE 6) Healthy Toolbox
MISE/IPCEI Salute (superata fase 1)
EU UHD Pulse 2 (INFN, UNIPI)

## Slide 21
Organizzata da AIFM in collaborazione anche con INFN
~200 partecipanti
18 invited talks
Round table

## Slide 22
Acknowledgments
F. Paiar
S. Ursino
S. Capaccioli
F. Di Martino
M. Costa
E. Ciarrocchi, D. Del Sarto, S. Linsalata, A. Kraan, M. Montefiori, M. Morrocchi, J. Pensavalle, A. Retico, V. Rosso
M. Marafini, Centro Fermi and INFN Roma1
F. Romano, INFN Catania
A. Vignati, INFN and UNI Torino

## Slide 23: Thank you

## Slide 24: Back up

## Slide 25
BASIC RESEARCH GOALS
CPFR Research Program
Main Goals
SKIN
2D biological array for radiobiological
experiments
Skin tumours: Flash-RT tumour response/
initial clinical application of low energy EF
Healthy skin: fundamental organ at risk for
the VHEE
BRAIN
Promising results from preclinical data
(neurocognitive sparing flash effect)
Poor prognosis of primary tumors and
metastases (unmet needs)
Specific expertise in “in vivo” quantitative-
functional analysis
SPINAL CORD
Cornerstone of primary organs at risk in
clinical practice
Yet to be investigated
(most available data focused on brain, lung
and bowel)
CLINICAL GOALS
for Flash low-energy electron beams
Notes: Our next step will be to reach these two main goals one related to basic research and the secondo to the clinic application of Low ernergy EF to treat superficial tumors we planned to achieve these two main goals one related to basic research and the other to the clinical implementation of our electron flash device for the treatment of superficial tumors.
We are going to focus our attention on these organ/tissues.
…. the spinal cord is the main organ limiting the administration of high doses on tumors arising in the head and neck and thorax and finally because it is Yet to be investigated
25

## Slide 26: Structure of the dosimeter
Plastic scintillator - Kuraray SCSF-78J, 10 mm length and 1 mm diameter
Clear optical fiber - Thorlabs, 1 mm diameter and 25 m long
Optical coupling - Cyanoacrylate glue in Peek tube
3
PMMA
block
irradiated region
Courtesy of E. Ciarrocchi

## Slide 27
Keithley 6517A
SiC
Voltage
Signal
G. Milluzzo et al., in prep. for Med. Phys.
Pulse duration=4 us
Unpublished data
(F. Romano, G. Milluzzo)
SiC response as a function of the dose-per-pulse
Results
First test ever performed with SiC with UHDR beams for FLASH radiotherapy successfully caried out
Optimal linearity od the two investigated SiC detectors up to several Gy/p ( correspondent to instantaneous dose rate of several MGy/s)
Promising results for an implementation of these detectors in the protocols
Design and realization of 2D high spatial resolution configuration in progress

## Slide 28: Courtesy of F. Romano, G. Milluzzo
  Silicon carbide instead of Si or C
  Scalable device fabrication
  Diamond-like properties
Diamond
20um 2um 0.2um
SiC with bulk
5x5 mm2 1x1 cm2
Freestanding membranes
Test with proton micro-beam with IBIC technique
Characterization with UHDR electron beams @CPFR
collaboration
SiC detectors for beam monitoring and dosimetry for FLASH