## Slide 1: LUXE/GBP plans at CLEAR for December 2022
M. Bruschi (INFN Bologna)

## Slide 2: Next test beam at CLEAR
Goal: test of a full readout chain
  192 Strip detector + FERS card (64 channels)
CAEN electronics used for the first time
  First day(s) we have to check that everything is working properly
    Quick feedback needed on the detector’s response and quality of the data
Last few days for the actual measurements
Beam conditions
  1 BC per train, max 10 pC/BC
  Beam width as small as possible (~ 1mm in both directions)
    Beam must be contained in 3.2x20 mm2
  in this conditions: Dose ~ 1.6 Gy/sec  130 kGy/day
  Signal amplitude (at FERS input)
    LUXE: ~ 5 pC peak at the first station with CCE ~ 10%
    CLEAR TB: ~ 15 pC (CCE~2%, sx=sy~1 mm)
  Foresee scans in X and Y directions
Experimental setup
  1 thin YAG screen upstream
    Need to know:
      if minimum charge needed to get the profile measurement with the scintillator is compatible with the DUT
      Acquisition frequency
  DUT
    2 layers of strips

## Slide 3
Sapphire
detector
Total height 12.5 mm
Socket - Samtec SS4-50-3.00-L-D-K-TR
Header- ST4-50-1.00-L-D-P-TR
Transition Board
In view of the test beam Dec. 2022:
Use of common flat cables and adapters to connect the detector(s) to FERS
Sapphire
detector
Transition PCB
Mated height: 4.00 mm
34-pin Male 2.54mm pitch header
RS 674-1296
Sensor PCB
Sensor PCB #1
Sensor PCB #2
34-pin Male 2.54mm pitch header
RS 674-1296
J1
J2
32 strips
+2 GND
2x17 contacts, female socket for crimping
3 meters common flat-cable 34 wires
FERS J1
FERS J2
J3
J4
J6
J8
34-pin Male 2.54mm pitch headers
RS 674-1296
SAMTEC HSEC8-170-01-S-DV-A-K-TR
32 odd strips from Sensor #1-J1 to FERS J1 Ch.0..31
J1= odd strips
J2= even strips
32 even strips from Sensor #1-J2 to FERS J1 Ch.32..63
J5
J7
16 odd strips from Sensor #2-J1 to FERS J2 Ch.0..15
16 even strips from Sensor #2-J2 to FERS J2 Ch.16..31
16 odd strips from Sensor #2-J1 to FERS J2 Ch.32..47
16 even strips from Sensor #2-J2 to FERS J2 Ch.48..63
FERS Carrier Board