## Slide 1: Validation of the simplified Model
AMS-02 Upgrade

## Slide 2: Agenda
Model
Materials
Contacts
Joints
Constraints
Eigenfrequencies

## Slide 3: Model Problems
Interference between Connectors / Plates inside octoframe

## Slide 4: Mass of simplified Model
Property | Value
Total Mass | 76.962 kg
Volume | 0.12563
Property | Value
Total Mass | 76.962 kg
Volume | 

## Slide 5: Center of Mass of simplified Model

## Slide 6: Distance Vertix - COM
Vertix: Upper Edge of Upper mechanical Structure
Global Coordinate System
Vertix
COM
Position of COM depending on the Vertix Coordinate System: (-0.3631 m I -8.8813 m I – 0.0727 m)

## Slide 7: Materials
Object | Material | Material in ANSYS |  |  | 
 |  | Reference | Density [kg/m3] | Compressive Modulus [MPa] | Shear Modulus [MPa]
Feet, Radiator, Radiator Fixation, Vibration Bracket | Aluminum | Aluminum Alloy | 2770 | 69 080 | 26 692
Vibration bracket Interior | PEEK | PEEK (40% carbon fiber) | 1445 | 203 000 | 124 290
Honeycombs | Carbon Fiber | *Honeycomb | 36* | 890* | 380*
Sensors | Anisotropic Silicon | Silicon Anisotropic | 2330 | - | -
LEF, LBB | PCB – FR4 | PCB laminate, Epoxy/ Glass fiber, FR-4 | 1990 | 11 264 | 10 827
Octoframe, Octo frame Fixation | M46/EX-1515 | Epoxy Carbon UD (395 Gpa) Prepreg | 1566.4* | - | -
Mechanical structure, Skins | M55J/EX-1515 | Epoxy Carbon UD (395 Gpa) Prepreg | ? | - | -
* Ansys reference material is corrected with these given values

## Slide 8: ANSYS Material: Epoxy Carbon UD (395 Gpa) Prepreg

## Slide 9: Material Calculation for M46J/EX-1515 and M55/EX-1515
Meeting Outcome: No Correction of the Young Modulus to the Flexular Modulus needed since the object to be examined is out of sandwich structure and not a lamina of composite materials.
Instruction: Correct Young Modulus, Density Poisson ratio and the remaining values and the rest of the data remains in Ansys standard.
Question: I'm a little confused right now about the correct assignment of axes in terms of the model, or how relevant that is.
M46 M55

## Slide 10: Corrected ANSYS Material to M46J/EX-1515

## Slide 11: Corrected ANSYS Material to M55J/EX-1515

## Slide 12: ANSYS Material: Honeycomb

## Slide 13: Corrected ANSYS Material to Honeycomb

## Slide 14: Contacts
Full bonded contacts on small parts and QLCS
  QLCS Layers
  Fixation Plates, Octoframe, Feet
Bonded Imprinted surfaces on big parts
  Upper and Lower Mechanical Structure
How is the 70 mm Honeycomb fixed? As first I assumed it is bonded from each side

## Slide 15: Joints
RBE2 Elements modelling the screws in the Vibration brackets, Feet, Mechanical Structures and Fixations for the Radiator and Octoframe
1 free DOF in z (fixed through contacts)

## Slide 16: Constraints
Fixed Bottomside of the Feet to approximate stiff plate below it

## Slide 17: Distributed Masses

## Slide 18: Mesh
Coarse Mesh but the Eigenfrequencies do not change a lot while refinement (around 10 Hz, and already they are pretty low)
It may be possible to refine the mesh of the QLCS a little more , but only to a limited extent. When I tried to apply 5 mm, the solver already could not solve it due to missing memory. The smallest mesh here is at 15 mm.

## Slide 19: Eigenfrequencies

## Slide 20: Mode Shape 1: 47 Hz

## Slide 21: Mode Shape 2: 51 Hz

## Slide 22: Mode Shape 3: 52 Hz

## Slide 23: Mode Shape 4: 52 Hz

## Slide 24: Mode Shape 5: 68 Hz

## Slide 25: Mode Shape 6: 100 Hz

## Slide 26: Mode Shape 7: 105 Hz

## Slide 27: Mode Shape 8: 110 Hz

## Slide 28: Mode Shape 9: 110 Hz

## Slide 29: Mode Shape 10: 113 Hz