## Slide 1
P. Antonioli
INFN-Bologna
Status EIC_NET initiative and EIC project
The Italian Contribution to the Electron Ion Collider

## Slide 2
Why this talk?
We are in Italy ;-)
We will have Giornate Nazionali since this afternoon (an introduction)
If you are not from Italy (or you are not working currently with INFN) is however good thinking about "your future": how your country community is contributing/will contribute to the EIC?
We want to grow a new "EIC generation"  know your "space"
How I can/want to contribute?
CAVEAT: some information here are "old" on purpose: last updates on R&D during "Giornate Nazionali"
CAVEAT: I take advantage of nice ePIC presentation made by Silvia Dalla Torre on Tuesday

## Slide 3: A long story is becoming reality
2015 NP LRP
“We recommend a high-energy high-luminosity polarized EIC as the highest priority for new facility construction following the completion of FRIB.”
https://www.bnl.gov/eic/
2012 White paper
The Electron-Ion Collider: the next QCD frontier
2018 National Academy Science report
“The committee finds that the science that can be addressed by an EIC is compelling, fundamental and timely.”

## Slide 4
A long story is becoming reality
https://www.bnl.gov/eic/
Dec 2019/Jan 2020
CD-0 ("mission need") status achieved
BNL site selection
Jun 2021
Following CDR presented, CD-1 passed

## Slide 5: A little bit of (Italian) history
Italian groups first interested to EIC physics are from HERA diaspora (HERMES in particular), from COMPASS (DIS @ CERN SPS program), from JLab ("hadron physics") and from a strong theoretically community (Pavia, Perugia, Cagliari, ...)
Some Italian groups participated to early R&D efforts for EIC (funding from DoE) and EIC User Group acted as the first "engine" to coalesce groups...
Marco is now EICUG chair

## Slide 6: 2016 Nuclear Physics INFN community meeting
2016
https://agenda.infn.it/event/10586/contributions/3969/attachments/2968/3258/Rossi_INFN2016.pptx
One of the first presentations to the largest INFN community
Check the slides!
Patrizia is Associate Director at JLab

## Slide 7: A little bit of (Italian) history (II)
https://agenda.infn.it/event/12368/?ovw=True
2017
Silvia is now ePIC deputy spokesperson
Marco is now dRICH sub-system leader
(Note: Google is unable to find a photo of Marco, apparently)

## Slide 8: EICUG meeting in Italy...
2017
“INFN consider EIC an important opportunity for the hadronic physics community and encourage partnerships and collaborations with the other Institutions involved in the project’’
E. Nappi,
then INFN vicepresident
Groups coalesced in a formal proposal of an INFN initiative to explore EIC opportunities in May 2018
EIC_NET initiative approved by INFN Nuclear Physics committee in September 2018
EIC_NET started operations beginning of January 2019

## Slide 9: and INFN "EIC_NET" initiative
Groups coalesced in a formal proposal of an INFN initiative to explore EIC opportunities in May 2018,
EIC_NET initiative approved by INFN Nuclear Physics committee in September 2018
EIC_NET started operations beginning of January 2019
https://indico.ectstar.eu/event/29/timetable/?view=standard

## Slide 10: EIC_NET status: a growing community
A growing community with different background: COMPASS, JLAB/CLAS12, ALICE, ATLAS, CMS, STAR, DARK SIDE, ...
TS
FE
PD
BO
TO
GE
RM1 RM2
PV
BA
SA
CS
LNS/CT

## Slide 11
https://agenda.infn.it/category/1561/

## Slide 12: from this year first RRB meeting (April 2023)
RRB = Resource Review Board 
meeting of funding agencies representatives of different countries

## Slide 13: Not only the detector: the accelerator
Many developments in critical R&D for accelerator design
https://indico.bnl.gov/event/15342/contributions/64650/attachments/42380/70993/2022-07-26-EICUG-Satogata-AcceleratorDesign.pdf
T. Satogata@EICUG meeting – July2022
design consolidation of different components needed
no show stoppers
R&D needed in different areas but not critical
HSR Vacuum upgrade needed due to higher current and shorter bunch length:
  resistive-wall impedance
  e-cloud buildup
  Solution identify in copper-clad (to reduce resistivity) and aC (amorphous Carbon) thin film to reduce secondary electron yield

## Slide 14: EIC accelerator: international contributions (& INFN)
T. Satogata@EICUG meeting
"INFN acceleratori" involvement!

## Slide 15: Some more details
SEY Characterization of coated surfaces at LNF
Development of a system ("turn-on key") for SEY measurements to be performed on site at BNL

## Slide 16: Not only the detector: the magnet ?

## Slide 17: Not only the detector: the magnet ?

## Slide 18: Potential involvement of an Italian excellence: ASG semiconductors

## Slide 19: What are doing INFN groups?
TS BA LNS SA + Duke + NISER
dRICH
radiators
aerogel
pressurized Argon vs C2F6
optics
mechanics
photosensors
SiPM
LAPPD
SiTracker
Simulation & computing
Physics (SIDIS, Exclusive tagging, diffractive, hadron spectroscopy and hadronization, ...)
MAPS 65 nm technology
streaming readout
El. cal. @JLAB + TRIDAS
Toward detector definition and optimization, simulation capacity will be key: a big working space for all our groups
ALCOR
FE TS LNF (RM1)
FE BA
FE LNS + BNL/JLab
GE TS
TO
GE RM2
BA TS PD
PV CS TO
BO FE
CS-SA-CT
TS CT CS BA
DAQ for dRICH

## Slide 20: dRICH R&D: the idea and the main prototype
hadron identification crucial for SIDIS
radiators: Aerogel (n=1.02)/ Gas (n=1.008)
3 m2 area, 3x3 mm2 pixel
SiPM (LAPPD) option for photosensors
2021 test beam
Building dRICH Collaboration
one of the 2023 tasks
dRICH “prototype” to study performance

## Slide 21: dRICH prototype 2021 @ test beams
MAPMT detector box
Tracking with GEM
Preliminary results on sq resolution with aerogel and gas
aerogel
gas

## Slide 22: dRICH 2022 test beam campaign
direct comparison between MAPMT and SiPM readout
Finalize resolution studies (in better controlled beam conditions)
FE
Test @SPS and PS

## Slide 23: Bringing irradiated sensors on a dRICH (prototype)
CERN PS T10 October 2022
irradiated/annealed sensors
ALCOR streaming readout
time tagger with scintillators
timing
cooling keeps sensors at T= -30 oC
Cherenkov photons visible!
29 November 2022
P. Antonioli - CPAD 2022 Workshop

## Slide 24: Irradiated sensors on test beam/dRICH prototype
see also Daniel, Luisa and Nicola's posters

## Slide 25: dRICH: the next steps (happening in 2023)
Assess Aerogel producers (Aerogel Factory – Japan and Aspen USA, no longer Budker availability [Russia!])
Equip dRICH prototype with SiPM plane (eRD102 milestone)
Explore the pressurized-Argon option (as gas replacement, high GPW: 11100!)
Explore mirror options (preferred: carbon fiber CMA-USA)
Synergy with ALICE3/RICH
FE BA
Annalisa's poster!

## Slide 26: Pressurized-Ar vessel
Original idea discussed by S. Dalla Torre at first YR meeting (March 2020) https://indico.bnl.gov/event/7449/contributions/35912/attachments/27095/41303/DallaTorre_RICH_high-p_March2020_Temple.pdf
Increase Ar pressure to increase number of photons
Identified material (DuPont® Nomex® 410) in carbon –fiber + honeycomb
First prototype to evaluate FME: to be delivered now
A sector protoype?
FE / LNS + BNL/Jlab

## Slide 27: SiPM: radiation tolerance studies and FEE
Readout via ALCOR (candidate ASIC for SiPM readout)
ALCOR v2:
Just delivered to us
Will be used in 2023
BO FE CS SA CT
TO

## Slide 28: Setup for SiPM characterization
DCR
I-V
Pseudo-efficiency (with LED): integrated coincdence/triggers as proxy
Next steps (will be reported tomorrow)
Laser measurement
Local Cooling (SiPM readout box)
BO FE CS SA CT
see Luisa's poster
on readout box

## Slide 29: Some results on irradiation campaigns
Irradiation at Centro di Protonterapia @ Trento
2021 campaign: irradiation at different levels + 1 annealing cycle
2022 repeated (small) irradiation and annealing cycles
Next steps:
Complete 2022 campaign (Nov/Dec)
Investigating effects with neutron source at LNL
Use data to model annealing cycles in the experiment (pre-TDR!)
Timing analysis with laser
“dRICH cooled tile” possibly going to -40 C (or -50 C) [LHCb synergy]
Next steps:
Investigating ALCOR capabilities in gated mode
Preparing for ALCOR v3
Test methodology for in-situ annealing
Bring on board “Southern Italy cluster” CS-CT-SA

## Slide 30: Run with FBK?
Agree with FBK a devoted run (under convenzione INFN-FBK) to explore:
Improvements on DCR standard rate [“optimization”]
Development of monolithic mini-tiles (2x2 or 4x4) to optimize geometrical acceptance
Light concentration (microlensing or nanophotonics approaches)
A successful run with FBK might be “win-win” operation for TDR/CD-3
Note recently released results from FBK, A. Gola @RICH2022

## Slide 31: LAPPD / HRPPD
S. Dalla Torre, Meeting with INFN referees
SiPM and LAPPD validation would make PID@EIC “safe”
LAPPD are “large size” MCPs at moderate cost
Large gain and low noise, uses ALD to increase lifetime
INCOM  spin-off of Argonne + Chicago Univ.
Strips readout, prototypes available with capacitive coupling (pixelated version)
LAPPD R&D kept “open” for dRICH (plan B if SiPM is not validated). Strategic for INFN to achieve know-how on this sensor.
Large interest in the community. First LAPPD workshop on 21 March 2022 by INFN TS, BNL and ANL https://indico.bnl.gov/event/15059/
GE TS

## Slide 32
2021 results in US
Setup lab in TS, joint effort with GE (readout) in 2022!

## Slide 33: Starting activities in 2022 and next steps
Time resolution measurements at test beam
Space resolution measurement in the lab (existing laser, needed motor stage)
Test variation of gain/efficiency in magnetic field  test planned in US and in Italy
Next steps

## Slide 34
see Deb's poster!

## Slide 35: Silicon tracker (vertexing)
In both initial detector proposals (ATHENA and ECCE) "ITS3" MAPS ALICE technology selected
ATHENA
ECCE

## Slide 36: Silicon tracker (vertexing)
INFN EIC groups working on EIC Silicon vertex:
are active members in ITS3/ALICE: access to 65 nm technology
R&D activities within ITS3 / ALICE so far
+ work in EPIC tracking WG  “stitched sensors” scheme for EIC (see next slide)
BA PD TS

## Slide 37: Silicon tracker (vertexing)
Different options under discussion:
Synergy with ALICE can be really a win-win operation for INFN vis a vis EIC project.
INFN consider synergistic investment on 65 nm technology for ALICE and ePIC

## Slide 38: Simulation (dRICH)
Simulation work for dRICH mainly from TS (a post-doc)
+ Duke University
Convened dRICH software group at EPIC level (the only one PID detector) with INFN-DUKE-NISER-(BNL)
Miniworkshop sharing experience among RICH detectors on reconstruction algorithms
TS

## Slide 39: Simulation (tracking)
BA developed fast simulation tool that is well suited to give feedback on different configuration
Already adapted from ATHENA to ECCE  EPIC
Versatile tool for simulation
LNS SA joining BA TS on simulation efforts
BA

## Slide 40: Physics (last but not least!)
Activity in CS (S. Fazio) on exclusive processes (critical for GPD studies) generators
Example: DCVS on deuterium gives access to neutron structure measurement
Other interests:
TO: diffractive
dRICH  SiDIS
Vertexing  HF
PV CS TO

## Slide 41: A map end of 2022
TS BA LNS SA + Duke + NISER
dRICH
radiators
aerogel
pressurized Argon vs C2F6
optics
mechanics
photosensors
SiPM
LAPPD
SiTracker
Simulation & computing
Physics (SIDIS, Exclusive tagging, diffractive, hadron spectroscopy and hadronization, ...)
MAPS 65 nm technology
streaming readout
El. cal. @JLAB + TRIDAS
Toward detector definition and optimization, simulation capacity will be key: a big working space for all our groups
ALCOR
FE TS LNF (RM1)
FE BA
TS LNS + BNL/JLab
GE TS
TO
GE RM2
BA TS PD
PV CS TO
BO FE
CS-SA-CT
TS CT CS BA
DAQ for dRICH

## Slide 42: some update (not all)
TS BA LNS SA + Duke + NISER
dRICH
radiators
aerogel
pressurized Argon vs C2F6
optics
mechanics
photosensors
SiPM
LAPPD
SiTracker
Simulation & computing
Physics (SIDIS, Exclusive tagging, diffractive, hadron spectroscopy and hadronization, ...)
MAPS 65 nm technology
mRWELL
Toward detector definition and optimization, simulation capacity will be key: a big working space for all our groups
ALCOR
FE TS LNF (RM1)
FE BA
FE LNS + BNL/JLab
GE TS
TO
GE RM2
BA TS PD PV
PV CS TO
BO FE
CS-SA-CT
TS CT CS BA
DAQ for dRICH
exploring this possibility!
BO ( + RM2/GE)

## Slide 43
aerogel proximity focusing pfRICH
imaging EMCal

## Slide 44
Status EIC_NET initiative and EIC project
The Italian Contribution to the Electron Ion Collider
My == Your!
?

## Slide 45
Detector
Physics