## Slide 1: Francesco Stellato University of Rome Tor Vergata & INFN on behalf of the WA8 collaboration team
WA8
Scientific Case
@
November 30th, 2022

## Slide 2
WA 8 - Users
Project Summary
Build up the scientific case and gather a users community for a
plasma-based sase FEL lasing in the water window (4 nm)
& for a seeded FEL lasing @ 50-180 nm
1- Experimental techniques
2- Technical requirements (beamline  dedicated presentation)
experimental end-station (to be defined)
3- Correlated services (external lasers, data acquisition, storage)

## Slide 3
WA 8 – Photon Sources
Project Status
Parameter | Value
Wavelength | 4 nm
Photons/pulse | 10 10 - 10 11
Pulse duration | < 50 fs
Focal spot | 6 µm
Parameter | Value
Wavelength | 50-180 nm
Photons/pulse | 10 13 - 10 14
Pulse duration | 20/200 fs
Focal spot | 6 µm
AQUA - ARIA
Betatron
Lasers, THz, …

## Slide 4
SAC General comments:
The presentation at the meeting includes several exciting prospects in terms of scientific ideas.
The main beamline AQUA aims to reach the water window (∼4 nm) with a flux of in the order to 1011 photons/pulse. This gives an excellent opportunity for experimental programs from imaging to various spectroscopy techniques in the water window. The second beamline, ARIA, aims for the VUV-wavelength range (50 to 180 nm).
Both electron and photon beamlines will be set-up side-by-side, space in the hall seems to be available.
We’re pursuing the experimental plan in the water window and moving from a conceptual design towards a technical design.
We’re pushing the experimental plan in the VUV range better defining the possible application in this energy range.
General Comments

## Slide 5
SAC: As for AQUA, it is not clear what the radiation bandwidth is, as it is not clear how photons will be delivered to the sample (e.g., after a monochromator?). The scientific case of AQUA includes coherent diffractive imaging (CDI), X-ray spectroscopy, Raman spectroscopy, and molecular fragmentation.
AQUA
Radiation bandwidth will be <0.5% (RMS) @ the C K-edge (AQUA)
High temporal resolution / High spectral resolution (one of the two)
Open discussion with WA6 and WP4 about beam monochromatization
– Not appropriate at low charge (photon flux is already low),
can be implemented in the high charge case (300 pC)
  Useful in X-ray Spectroscopy; alternative for linear processes,
  ghost spectroscopy can be used with a long e-bunch
  Single-shot diagnostics without mono is sufficient for other techniques and allows to have a higher photon flux on the sample
  Decision: no monochromator for phase 0, but space for a monochromator foreseen in the beamline layout for the operation with a pure linac-acceleration
AQUA

## Slide 6
XAS schemes -
Simpler than XES, but requires care in terms of
incident photon wavelength
SASE + monochromator
Seeded
Seeded + monochromator
SASE w/o monochromator
 Ghost spectroscopy, stochastic spectroscopy
Chergui, M., & Zewail, A. H. (2009). Electron and X‐Ray Methods of Ultrafast Structural Dynamics: Advances and Applications. ChemPhysChem, 10(1), 28-43.
Kayser, Yves, et al. "Core-level nonlinear spectroscopy triggered by stochastic X-ray pulses." Nature communications 10.1 (2019): 1-10.
SAC: It is not clear whether X-ray spectroscopy includes both absorption and emission or only one of these.
AQUA - X-Ray Spectroscopy
X-ray Emission Spectroscopy
Many possibilities, more complex experimental setups (not for phase 0)
Ultrafast soft X-ray emission spectroscopy of surface adsorbates using an X-ray free electron laser
X-ray Emission Spectroscopy at X-ray Free Electron Lasers: Limits to Observation of the Classical Spectroscopic Response for Electronic Structure Analysis
Energy-dispersive X-ray emission spectroscopy using an X-ray free-electron laser in a shot-by-shot mode

## Slide 7
SAC: Molecular fragmentation is an interesting topic, but it was not clear how it would be carried out. Are these photo-emission spectroscopy experiments (they seem more relevant for ARIA)?
Kastirke, Gregor, et al. "Photoelectron diffraction imaging of a molecular breakup using an x-ray free-electron laser." Physical Review X 10.2 (2020): 021052.
E. Kukk 2021, «Formative period in the x-ray-induced photodissociation of organic molecules» Phys. Rev. Res. 3, 013221
AQUA + ARIA - Molecular Fragmentation
Molecular fragmentation can be carried out in different schemes.
FEL pump – FEL probe (single FEL pulse or split-and-delay)
Optical Laser pump – FEL probe
FEL pump – IR probe
Photo-emission spectroscopy (PES) + mass spectrometry experiments are
well-suited for the ARIA energy range, but interesting measurements can also
be performed at AQUA exploiting inner shell absorption
(S2p, B1s, C1s, and hopefully N1s at some stage) for chemical sensitivity.

## Slide 8
SAC: No liquid phase experiments are mentioned, but the presentation of test experiments at Elettra appears at the end of the presentation. This is an important development.
Coherent diffraction imaging measurements, but also XAS measurements, at AQUA will typically be performed using liquid jets.
Thin and/or flat jets will be needed to minimize photon absorption in the soft X-rays
This allows keeping biological samples fully hydrated and therefore close to physiological conditions
AQUA + ARIA -Sample Delivery techniques

## Slide 9
Energy region between Oxygen and Carbon K-edge
2.34 nm – 4.4 nm (530 eV -280 eV)
Water is almost transparent to radiation in this range
while nitrogen and carbon are absorbing (and scattering)
The water-window is a sweet spot for coherent imaging of biological samples living in their native state
, but offers great possibilities also for soft X-ray spectroscopy (metal L-edge) in liquid
3 nm 2 nm
AQUA - Coherent Imaging Experiments
in the Water Window
Simulation of
a E.coli pattern
Electron density reconstruction 1 µm

## Slide 10
Nanomaterials, especially those significantly scattering in the EuPRAXIA@SPARCLAB energy range
Technology development: photovoltaic, H storage
Biomedical applications: functionalized, bio-compatible materials
High time-resolution pump-probe studies
Nanotubes
Nanoparticles
Soot (engines emissions)
Volcanic ashes
Huang et al. Nanoscale (2018)
Starodub et al. Nature comm (2012)
Takahasi et al. NanoLetters (2013)
AQUA - Coherent Imaging Experiments
Materials

## Slide 11
Liquid line
Gas line
Liquid jet
A gas stream is used to focus a liquid jet down to 10 μm diameter
Gas line
Gas bottle
Sample reservoir
Pros
Hydration
Thin water column Pump-probe “ready”
Cons
High sample consumption
Operation instabilities
Sample Delivery – Liquid Jets @ AQUA

## Slide 12
Sample Delivery – Liquid Jets
Test of different 3D printed nozzles
(different inner fiber diameter, different operating pressures)
for
Fiber Diffraction+Coherent Imaging
on protein fibrils @ EuXFEL SPB/SFX beamline
TEM Liquid jet injection Diffraction pattern

## Slide 13
A drop-on-demand system can be used to generate 20-40 μm diameter droplets
An electrospray source can generate small droplets and an associated Differential Mobility Analyzer can size-select particles
Sample Delivery – Miscellanea

## Slide 14
First experimental run at Elettra, CiPo beamline
C K-edge absorption of Glycine
[1 M] in water
Prototype set-up tested @ Elettra in collaboration with FERMI-EIS beamline
M. Coreno, R. Mincigrucci, G. Bonano, et al. work in progress!
Sample Delivery – Liquid sheets
Notes: Small “blue” shift of 0.25 eV of the C K-1 -> Π* transition wth reference to gas phase spectrum
Blue shift is characteristic of hydrogen bonding with solvent

## Slide 15
A liquid jet is sprayed into a system of aerodynamic lenses, which produces a stream of small droplets with a thin solvent layer surrounding the sample. If a volatile buffer is used, the droplets dry quickly and the samples are surrounded by only a few layers of solvent.
Pros
Hydration Low background
Cons
Low sample density  low hitrate
Sample Aerosols – Liquid Jets @ ARIA

## Slide 16
Sample deposited on thin Si3N4 membranes
10 μm
Raster scans of crystals in silicon nitride wafers
Coquelle et al., Acta Cryst D 2015
Pros
Low sample consumption
Hydrated «masks»
Shelby IUCrJ 2019
Cons
Relatively slow
Membrane background
Sample Delivery – Fixed Targets
Ideal for a low repetition-rate machine

## Slide 17
SAC: The ARIA FEL would fill an important gap as there are hardly any vacuum ultraviolet (VUV) FEL at present (except in Dalian, China), which operates at a single energy of 24 eV. The major advantage over HHG sources is photon flux, though here again, it is not clear how the beam will be delivered to the sample.
Beam delivery on samples:
no monochromator (seeded FEL, bandwidth t.b.d.), but of course focusing optics.
Details to be defined in the following months
Sample delivery:
Aerosol injector, fixed targets
ARIA

## Slide 18: AQUA - Techniques @ 4 nm
Coherent imaging
X-ray (Absorption & Emission)
spectroscopy
Raman spectroscopy
Photoemission Spectroscopy
Photoelectron Circular Dichroism
Photo-fragmentation of molecules
Time of Flight Spectroscopy
ARIA - Techniques @ 50-180 nm
4 nm
50-180 nm
AQUA vs ARIA
SAC: More or less the same scientific topics. WHAT DOES THAT MEAN? In none of the two cases was the option of chirality studies mentioned. These lend themselves to both photon (absorption) and electron (photoemission) spectroscopy.
Liquid Phase  Gas Phase

## Slide 19
Chirality
Chiral molecules are non-superimposable to their mirror images.
Enantiomers, optical isomers, have essentially the same physical and chemical properties and can only be distinguished via their interaction with a chiral object, such as circularly polarized light or another chiral molecule
Chiral reactivity is governed by nuclear rearrangements occurring on picosecond to femtosecond timescales.
Circular polarized x-ray pulse
High flux beam
Short pulses
High repetition rate
UV/x-ray pump (linear polarization)
Circularly polarized X-ray light sources can probe the ultrafast chiral electronic and nuclear dynamics through spatially localized resonant core transitions.
The mechanism of the photochemical asymmetric reactions in “soft materials”, such as aminoacid films
Chirality in resonant plasmonic-biomolecular systems: The method: Circular Dichroism (CD)
Chiral plasmonic nanostructures
Chirality in Complex organic compounds: bio-organic molecules
- Ilchen, Markus, et al. (2021): Communications Chemistry 4.
- Giri, Sucharita, Jean Christophe Tremblay, and Gopal Dixit. (2021): PRA 104.
-. Rouxel, Jérémy R., Markus Kowalewski, and Shaul Mukamel. (2017): Structural Dynamics 4.
- Baykusheva, Denitsa, et al. (2019): Proceedings of the National Academy of Sciences 116..
Notes: t is, for instance, responsible for odor perception, taste, and the effect of most pharmaceutical drugs on any living organism. In fact, the molecular building blocks of all known biological matter possess a chiral, i.e., a handed, structure

## Slide 20
Time-resolved chiral X-Ray photoelectron spectroscopy & Photoelectron circular dichroism (PECD)
* D. Faccialà et al., (2022) http://arxiv.org/abs/2202.13704
The source of the asymmetries :initial orbital or by the chirality of the surrounding effective potential.
broken mirror symmetry
15 fs
10 Hz
75 fs
Pump-off
Pump-on
Electronical dynamics of chiral molecules * : AQUA

## Slide 21
Valence shell photoelectron circular dichroism *
Chirality in Complex organic compounds (bio-organic molecules) : ARIA
PECD
Photoelectron spectrum
*Nahon, L., Garcia, G. A., & Powis, I. (2015). J. Electron Spectrosc. Relat. Phenom.,204, 322-334
Takahashi, Jun-ichi, et al. (2009) International Journal of Molecular Sciences 10.7 3044-3064..
Relaxation Dynamics in Photoexcited Chiral Molecules : TR-PECD
The photoelectron images

## Slide 22
X-Ray Raman Spectroscopy
UV-vis Raman spectroscopy: monochromatic UV beam excites valence electrons into the conduction band and measures energy losses (Stokes) or energy gains (anti-Stokes), Raman scattering, related to vibrational and rotational states of the system of interest.
X-ray Raman scattering (XRS) X-ray can be applied to excite core electrons into the conduction band higher order transitions (quadrupole) are allowed. (low-cross section)
Study case: Materials in extreme conditions (high pressure) (TR-XRS)
Stimulated (electronic) Raman scattering
A pump–probe Raman experiment on a protein; To study electronic charge transfer in rhenium modified azurin, a benchmark system for photoinduced fast electron transfer in proteins
Zhang, Yu, et al., (2014): The journal of physical chemistry letters 5.21 3656-3661.

## Slide 23
Stimulated (electronic) X-ray Raman scattering
by a single SASE pulse, the overall bandwidth is large enough to reach valence excited states. (@EuXFEL) (b) Two-color SASE or enhanced-brightness SASE: (two pulses with frequencies at the pump and Stokes frequency).
Covariance mapping and Ghost imaging for data analysis
* Weninger, Clemens, et al. (2013)"Stimulated electronic x-ray Raman scattering." PRL 111.23 : 233902.
Cavaletto, Stefano M., Daniel Keefer, and Shaul Mukamel. (2021): Physical Review X 11.1 011029.
Kimberg, Victor, et al. . (2016): Faraday Discussions 194 305-324.
Kimberg, Victor, and Nina Rohringer. . (2016): Structural Dynamics 3.3 034101.
9.5 mm
T=40 fs
I=1017 W/cm2
Right (a) Level diagram for resonant stimulated electronic X-ray Raman scattering in neon. (b) Three single-shot spectra. (c) Normalized single-shot X-ray Raman spectra in neon as a function of central XFEL photon energy.
Atomic gases Neon @LCLS*
Molecules CO (two-color) @XFEL
Transition metals @SACLA
Proof of principle experiments :
Notes: The XFEL pulses are focused into a gas cell of 9.5 mm length filled with neon to spot
sizes of 2 m using a Kirkpatrick-Baez (KB) focusing optics.
A grating spectrometer of 1 eV energy resolution is fielded
downstream. (b) Typical raw spectrum
Pumping with a SASE XFEL, therefore, results in stable line position and line profile when tuned above the K edge, and emission of variable line shape and stochastic line shifts when pumping below the K edge, which results in resonant Raman scattering

## Slide 24
Experimental activities of the EuPRAXIA@SPARC_LAB project
Development and characterization of novel optics to manipulate and characterize coherent radiation
Microchannel plates (MCPs)
Team Marcello Coreno, Sultan Dabagov, Monica De Simone, Alessandro D’Elia, Katarzyna D. Kocurek, Augusto Marcelli, Mikhail Mazuritskiy, Awad Mohamed, Javid Rezvani, Fabio Zuccaro, …
Experimental proposals at Elettra: No. 20170171, No. 20175238 and No.20215699
Eph= 92 eV
Slit: 100*100 um
Pinhole=100 um
Single MCP
d=8 cm
d=12 cm
d=4 cm
d=1 cm
Eph= 92 eV
Slit: 300*300 um
Pinhole=30 um
Two flat MCPs

## Slide 25
Progress and plans
A new proposal [#20225369] was submitted to the CiPo beamline @ELETTRA “Focusing properties of single and double flat MCP-devices and coherence characteristics of transmitted X-ray radiation”
Data analysis of the experiments Proposal #20215699 in progress [2 planned manuscripts]
(a)
(c)
(b)
A second robot with 6 degree of freedom for rotational and translations movements has been ordered (expected delivery December 2022).
The experimental chamber will be upgraded to host the second robot. An upgrade of the software to allow moving in a coordinated way the two robot is planned in 2023.
We aim to evaluate the transversal coherence of soft X-ray SR and FEL sources with devices based on MCP optics.
New suppliers of MCP optics have been identified.

## Slide 26
Tailoring of the AQUA scientific case based on updated beam parameters & definition of required beamline components
Extension of the ARIA scientific case
Experiments on sample delivery systems and fiber diffraction @ EuXFEL
and acquisition of sample delivery instruments (syringe pumps)
4. Acquisition of mechanical components for X-ray optics
  & sample manipulation
WA 8 – Summary: Main Updates

## Slide 27
Second users’ meeting organization (Temptative date: late 2023)
Gathering the national and international future users community
  Conference presentations
  Invited talks at international universities
WA 8 – Summary: Main Updates

## Slide 28
WA 8 – Summary: Things to do
Finalization (for the time being) of the scientific case
Technical description of the experimental endstation(s)
  Detectors
  Sample manipulation
Correlated services definition
External lasers
Data acquisition
Data Storage
Sample preparation laboratories
4. Coordination with the second EuPRAXIA site & with EuAPS