## Slide 1: Lattice Update
P. Raimondi,
INFN-LNF
Elba May - 29, 2011

## Slide 2: Summary
Present Arc design
Present FF design
Parasitic crossing and injection
Two tunnels (Ler ½ Her) studies
Arc solutions for SR Undulator insertion:
- Concentrated
- Distributed
To do list

## Slide 3: SuperB Arcs
LER
HER
HER and LER arcs have conceptually the same lattice. LER arc dipoles are shorter (bend radius about 3 times smaller) than in the HER in order to match the ring emittances at the asymmetric beam energies.
mx = 3p, my = p
Cell in HER
mx = 1.5p, my = 0.5p
Cell in HER

## Slide 4: Layout of HER arcs
V12 Old
V12 mod
Short ring

## Slide 5: LER FF optics
IP
Y-sext
X-sext
V12
Match & SR
Crab

## Slide 6: Spin Rotation
IP
HER
HER
LER
LER
S.r. solenoids (90° spin)
S.r. dipoles (270° spin)
90° spin rotation about x axis
  90° about z followed by 90° about y
“flat” geometry => no vertical emittance growth
Solenoid scales with energy => LER more economical
Solenoids are split & decoupling optics added.

## Slide 7: “Parasitic” crossing
Doglegs have been removed and the secondary crossing (“parasitic) is made by lengthening the first 3p cell in HER by about 25 meters
This makes the two beam lines cross with and angle of about 165mrad (was about 150 with the dogleg) and there should be no interference between the two beam lines (some readjustment still needed for LER  in progress)
This longer HER cell is suitable for the injection
Lot of space remaining for utilities (RF, feedbacks, wigglers,...)

## Slide 8: Injection Cell and Injection Bump

## Slide 9: Ler half Her size
Rationale for half size Ler is to gain flexibility in optimizing the two rings independently.
Summary of the present studies:
- Her becomes 8% shorter and 10% less emittance
- Ler has 3nm emittance and very hard to decrease it because we need more and shorter arc cells and the quads and sextupoles get too strong
Given this and all other complications that arise (second crossing, etc…), such possibility seems unlikely to develop in a suitable one.

## Slide 10: Ler Half size Her

## Slide 11: Insertions for SR Undulators
We are considering Her Insertions, but it seems that Ler might as well have the same optic and layout
At the moment we have developed two possible solutions:
- 2 sections with 5 insertions in a row in the middle of the arcs. 10 lines total
6 insertions in the mux=0.75 cell distributed along the Arcs. 12 lines total

## Slide 12: 5 Consecutive cells

## Slide 13: 5 Consecutive cells

## Slide 14: 6 Distributed Insertions
Alternating sequence of:
Cell1 mux = 1.5, muy=0.5
Cell2 mux = 1.215, muy=0.688
Undulator insertions: length = 3.5m betax/y = 3.2m
Optic flexible to change beta’s and mu’s

## Slide 15: 6 Distributed Insertions
Chromatic functions

## Slide 16: 6 Distributed Insertions
Arcs Dynamic Aperture:
90 sigmas in X
50 sigmas in Y
dE/E > 2%
X-tracking with
dE/E=1%

## Slide 17: Concentrated vs Distributed
Distributed solution seems better:
- Better D.A.
- More flexibility in the optic (for each line)
- More space for Light-Lines
- Indipendent shielding among lines

## Slide 18: Arc with SL insertions summary
A solution with 12 SL insertions exists with better performances w.r.t. latest design (that has no insertions)
- emittance 10% smaller
- SR power 10% smaller
- momentum compaction 10% larger
- ARC Transverse D.A. 20 larger
- ARC energy acceptance more than doubled

## Slide 19: To Do list
Need to have a team in Frascati to work out the layout, define and optimize the solutions. Such group should have all the expertises on hand (SL ones, magnets etc.)
Define the tasks for the W.B.S.

## Slide 20: To Do list
In order to define the layout and the lattice there is a very long list of items:
- Iterate the layout and lattice optimization with site constraints
- Work out the injection lines.
- Make the FF H/L L/R like for the V12 (add/subtract 30mrad to the FF L/R)
- Work out the vertical separation: hopefully find the solution for the two arcs vertically displaced by about 0.5m. This will double the avalaibility for SR lines.
- Insert the Injection cells in the proper places
- Need to go to lunch…