## Slide 1: IHEP BeamTest 2022
Rui Qiao; Ke Gong; Wenxi Peng; RuiJie Wang; Bing Lu

## Slide 2: The detectors
IHEP SCD 1&2
PMO SCD 1
PMO SCD 2
PSD
Five detectors on a common base:
  Two IHEP SCDs
  Two PMO SCDs
  One IHEP PSD
Notes: G:\keyan\科研任务\221114_HERD束流测试\图片\来自BT2022微信群\微信图片_20221205131004.jpg

## Slide 3: The IHEP SCDs
The IHEP SCDs have width of 3.6cm, dividing into 10 sections.
As the ion beam spot is small, it was adjust to hit between section 6th & 7th .
SCD2
60um
SCD2
25um
SCD1
60um
SCD1
25um
ch0
ch199
ch199
ch0
The beam spot was shaped by the hollow VETO. The beam spot is ~4mm below the laser.
Notes: G:\keyan\科研任务\221114_HERD束流测试\文档\20221122_束流击中情况及调整.pptx

## Slide 4: The beam spot and the height adjustment
Stage1:
Initial height
Stage2:
3.6mm higher
Stage3:
VETO OFF
Stage4:
23mm higher
Notes: G:\keyan\科研任务\221114_HERD束流测试\png\IHEP_SCD2\cluster\

## Slide 5: The long term detector status
We monitor the change of pedestal and net rms.
The change of pedestal(Y) of 200 channels as a function of date(X). SCD2 has pedestal change of +/- 10 ADC
The change of net rms(Y) of 200 channels as a function of date(X). SCD2 is perfect, while SCD1 has two more noisy channels

## Slide 6: Data analysis framework
Section Selection
ETA correction
Raw Data Conversion
Pedestal analysis and subtraction
CN analysis and subtraction
Cluster Finding
Charge reconstruction
Charge sharing
Raw data processing
High-level data processing

## Slide 7: Preliminary charge response
The additional 20 pF decrease the signal, or say expand the dynamic range. The SN of low-Z does not significantly decrease.
Charge spectrum of IHEP-25um with 0 Ω. The linear range is Z=1~6.
Charge spectrum of IHEP-60um with 20 pF. The linear range is Z=1~9.
Notes: G:\keyan\科研任务\221114_HERD束流测试\python_code\debug\快速电荷重建\step6_构造最终修正系数\*

## Slide 8: Multiplicity
The cluster multiplicity(Y) as a function of the sqrt of the maximum cluster amplitude(X). Heavy ion has larger multiplicity.
The amplitude(Y) of the 256 channels(X) in 10 heavy ions events.
Notes: G:\keyan\HERD项目文档\周进展\资料\20221130_束流实验分析结果\*

## Slide 9: Preliminary charge sharing
Additional 20 pF cap.
0 Ω
Sqrt Seed ADC (Y)
Vs
Sqrt Cluster ADC (X)
Sqrt Seed ADC (Y)
Vs
Sqrt Cluster ADC (X)
Sqrt Neighbor ADC (Y)
Vs
Sqrt Cluster ADC (X)
Sqrt Neighbor ADC (Y)
Vs
Sqrt Cluster ADC (X)
Notes: G:\keyan\科研任务\221114_HERD束流测试\python_code\debug\Seed通道_vs_Sum_读出条\*
G:\keyan\科研任务\221114_HERD束流测试\python_code\debug\临近通道_vs_Sum_读出条\*

## Slide 10: Conclusion
The SCD performance is reviewed:
  The pedestal shift max. +/- 10 ADC.
  The noisly level is stable.
  Ion peak clearly identified. Linear response of Z=1~6 using 0 Ω, and Z=1~9 using 20 pF.
  Differenent charge sharing performance on various setup.
  High multiplicity for heavy ion.

## Slide 11: Future plan
ID | Mission | Person in charge
1 | Charge reconstruction (in lineary range) | WeiShuai Zhang
2 | Charge sharing | RuoSi Lu
3 | Heavy ion response | Rui Qiao
4 | Common Noise | TBD