## Slide 1
C. Grimani M. Fabi
F. Sabbatini & M. Villani
University of Urbino Carlo Bo and INFN Florence
HASPIDE GENERAL MEETING
Florence February 2-3, 2023
WG5 in collaboration with WG1
Space Weather and dosimetry in space

## Slide 2: WG5 Fi-Ub: scientific objectives
a-Si:H instrument configuration optimization for space
Solar flare detection: photon and electron detection in the keV-MeV range
Solar energetic proton (SEP) event monitoring (from MeV through at least 400 MeV)
Gamma-ray bursts detection from galactic magnetar
Preparation of the ASI proposal (HASPIDE Coll. + S. Perri UniCal + Industries)

## Slide 3
Solar flare and energetic particle event monitoring
Magnetar flaring
Hard X rays and soft gamma rays associated with GRBs (we mainly focus here on magnetar flaring since many of them are galactic) allow for increasing the ionization of ionosphere thus disturbing VLF in the range 3-30 kHz – ozone layer depletion

## Slide 5
Solar activity intensity (11-year cycle) GSMF Polarity effects (22-year cycle; since 2013 + polarity)
106 tons/s p,e- 200-800 km/s
6 part/cm3 near Earth 0.3-5 keV
Solar activity
Singh & Bhargawa Astrophys. Space Sci. (2019) 364:12
LPF
LISA

## Slide 7
SEP continuous, multi-spacecraft observations allow us to study the role of particle interplanetary scattering and transport effects (PSP, SolO, BepiColombo, STEREO, ACE)
Critical energy differential flux measurements from tens of MeV up to not less than 400 MeV for protons are proposed for reliable measurement parameterization above this energy and for flux normalization with Space Station observations: goal medium-intense events (>107 protons cm-2 > 30 MeV)
SEP and inner S/C dose monitoring allowed by a:Si-H detectors. These detectors with different arrangements can be also considered for soft (1.55-12.42 keV) X-ray and solar electron detection
Neutron production in the atmosphere (SEP contribution vs Forbush decreases and proton precipitation in the atmosphere - mandatory SEP flux correct estimates above 500 MeV)
a:Si-H detectors are characterized by high dynamic range, radiation resistance, adjustable geometrical shape, low weight and power consumption
Possible use in space of amorphous silicon hydrogenated
detectors: the scientific case

## Slide 8: Halo CME and SEP event on October 29, 2021: a case study
Papaioannu et al., A&A, 660, L5, 9pp, 2021
Flare X1
Soft X-rays
Radio bursts:
III, II, IV
EUV

## Slide 9: Photon and electron fluxes from star flaring
Electron fluxes from solar flares
Electron fluxes of IP and galactic origin
Fenimore, Klebesadel and Laros, ApJ, 460, 964, 1996
SGR 0525-66/GRB 790305b
Sun
5x1044 erg
1.9×1045 ergs s-1
CG et al., CQG, 2009

## Slide 10: SEP event on October 29, 2021 observations
Papaioannu et al., A&A, 660, L5, 9pp, 2021

## Slide 11
Papaioannu et al., A&A, 660, L5, 9pp, 2021
onset
Peak space
Peak GLE (red curve)

## Slide 12: Optimization of a a:Si-H detector for long-duration intense solar energetic particle event monitoring
a:Si-H active material and tungsten as passive material
CSDA proton range in tungsten (Z=74)
Tungsten density: 19.25 g/cm3
Geometrical factor max for 400 MeV protons 0.6 cm2 sr
for about 1 kg detector
Energia | CSDA range | Range | Massa
300 MeV | 99.33 g/cm^2 | 5.16 cm | 2.5x2.5 → 620 g 2.0x2.0 → 397 g 1.5x1.5 → 223 g
350 MeV | 127.1 g/cm^2 | 6.60 cm | 2.5x2.5 → 795 g 2.0x2.0 → 508 g 1.5x1.5 → 286 g
400 MeV | 156.8 g/cm^2 | 8.15 cm | 2.5x2.5 → 979 g 2.0x2.0 → 627 g 1.5x1.5 → 353 g
SEP event October 28, 2021 GLE 73
Blue dots: data gathered in space up to 100 MeV with Solar Orbiter. Orange squares: Neutron Monitor data.
The blue curve is the best fit with data up to 100 MeV.
The red curve is the best fit with data up to 400 MeV-> SEP monitoring in space, far from Earth should be monitored up to minimum energies of 400 MeV. Only near-Earth detectors cover this energy range.

## Slide 13: SEP critical observation energy interval
CG+, J. Ph. Conf. Ser. , 31, 045018, 2014
 | Solar minimum | Solar maximum | Onset | Peak/Decay
GCR | 19% | 6% |  | 
SEP 13/12/2006 |  |  | 90% | 98% (peak)
SEP 14/12/2006 |  |  | 99% | 100% (decay)
SEP 23/2/1956 |  |  | 25% | 99.5% (peak)
SEPs > 70 MeV e < 0.4 GeV
Proton percentage below 400 MeV

## Slide 14: Intense SEP event occurrence
The yearly SEP-event occurrence in the fluence range 106-1011 protons/cm2
above 30 MeV can be estimated according to the Nymmik [ICRC proc. 1999a,b]
model on the basis of the number of the yearly predicted sunspot number:
NSEPs [NSSmin, NSSavg, NSSmax]=0.0694 NSS[min, avg, max]
Nymmik has found that the SEP event fluence () distribution shows a power-law
trend with an exponential cut-off
dNSEPs=C  e-  x d
where x=4x109
where C can be determined on the basis of the total number of expected SEP events

## Slide 15: SEP predictions during the selar cycle 26
YEAR | Sunspot Number | # SEP events
2035 | 68 | 5
2036 | 76 | 5
2037 | 77 | 5
2038 | 74 | 5
2039 | 63 | 4
2040 | 42 | 3
2041 | 32 | 2
2042 | 21 | 1
2043 | 11 | 1
2044 | 5 | <1
Nymmik R A et al 1999a Proc. 26th Int. Cosmic Ray Conf. (Salt Lake City) vol 6 pp 268–71
Nymmik R A et al 1999b Proc. 26th Int. Cosmic Ray Conf. (Salt Lake City) vol 6 pp 280–3
Singh & Bhargawa Astrophys. Space Sci. (2019) 364:12
65% of the
events belong to
the fluence range
106 -107 protons cm-2
For instance
November 13, 2006
and May 7, 1978

## Slide 16: SEP event November 29, 2020
Mason et al., A&A 656, L12 (2021)
Kollhoff et al., A&A 656, A20 (2021)
F. Sabbatini – SolO HET data

## Slide 17: WG5 activity: highlights
WG5: general aims and scientific cases (C. Grimani)
Fluka Monte Carlo – Simulation geometries (M. Fabi)
SEP fluxes at low and high energies and simulations for particle detection
(M. Villani)

## Slide 18
Manuscript submitted to Experimental Astronomy
just appeared on arXiv