## Slide 1: Cool Copper Collider
Emilio Nanni
HG 2023
10/18/2023

## Slide 2: Acknowledgements
HG 2023
Community Events
More Details Here (Follow, Endorse, Collaborate):
https://web.slac.stanford.edu/c3/
https://sites.google.com/view/ec4c3
Fermilab, SLAC, LANL & Snowmass Session in Seattle
Cornell Aug. 31st-Sept. 1st
https://indico.classe.cornell.edu/event/2283/overview
ACCEPTED PRX Energy
Next Workshop In Feb. ‘24 - Announcement Coming Soon

## Slide 3: What’s Next for the Energy Frontier?
HG 2023
The Energy Frontier 2021 Snowmass Report
Physics goals beyond HL-LHC:
1. Establish Yukawa couplings to light flavor ⟹ precision & lumi
2. Search for invisible/exotic decays and new Higgs ⟹ precision & lumi
3. Establish self-coupling ⟹ > 500 GeV e+e- operations

## Slide 4: Linear vs. Circular
HG 2023
Linear e+e- colliders: ILC, C3, CLIC
Reach higher energies (~TeV), and can use polarized beams
Relatively low radiation
Collisions in bunch trains
Circular e+e- colliders: FCC-ee, CEPC
Highest luminosity collider at Z/WW/ZH
limited by synchrotron radiation above 350 – 400 GeV
Beam continues to circulate after collision

## Slide 5: Various Proposals
HG 2023
ILC
250/500 GeV
250/550 GeV
… > TeV
CEPC
240 GeV
CLIC 380/1000/3000 GeV
FCC-ee
240/365 GeV

## Slide 6: A novel route to a linear e+e- collider

## Slide 7: Breakthrough in the Performance of RF Accelerators
HG 2023
RF power coupled to each cell – no on-axis coupling
Full system design requires modern virtual prototyping
Electric field magnitude produced when RF manifold feeds alternating cells equally
Optimization of cell for efficiency (shunt impedance)
Control peak surface electric and magnetic fields
Key to high gradient operation
Tantawi, Sami, et al. PRAB 23.9 (2020): 092001.

## Slide 8: Cryo-Copper: Enabling Efficient High-Gradient Operation
HG 2023
Cryogenic temperature elevates performance in gradient
Material strength is key factor
Impact of high fields for a high brightness injector may eliminate need for one damping ring
Operation at 77 K with liquid nitrogen is simple and practical
Large-scale production, large heat capacity, simple handling
Small impact on electrical efficiency
Cahill, A. D., et al. PRAB 21.10 (2018): 102002.
Cryogenic temperature elevates performance in gradient
Increased material strength is key factor
Increase electrical conductivity reduces pulsed heating in the material

## Slide 9: C3 Cool Copper Collider
Snowmass
C3 is based on a new rf technology
Dramatically improving efficiency and breakdown rate
Distributed power to each cavity from a common RF manifold
Operation at cryogenic temperatures (LN2 ~80-K)
Robust operations at high gradient: 120 MeV/m
Scalable to multi-TeV operation
High Gradient Operation at 150 MV/m
Cryogenic Operation at X-band
C3 Prototype One Meter Structure
High power Test at Radiabeam
Nasr, et al., PRAB 24.9 (2021): 093201.

## Slide 10: Accelerator Complex
Snowmass
8 km footprint for 250/550 GeV CoM ⟹ 70/120 MeV/m
Large portions of accelerator complex compatible between LC technologies
Beam delivery / IP modified from ILC (1.5 km for 550 GeV CoM), compatible w/ ILC-like detector
Damping rings and injectors to be optimized with CLIC as baseline
C3 Parameters
C3 - 8 km Footprint for 250/550 GeV (to scale)
C3 Main Linac Cryomodule
9 m (600 MeV/ 1 GeV)

## Slide 11: Technical Timeline for 250/550 GeV CoM
HG 2023
Technically limited timeline developed through the Snowmass process
Energy upgrade in parallel to operation with installation of additional RF power sources
P5 Report Dec. 23
Nex European Strategy Report??
Notes: Run plan to match ILC at 250, we remain open to input -> Higher energy faster, push harder for luminosity

## Slide 12: Ongoing Technological Development
HG 2023
Modern Manufacturing
Prototype One Meter Structure
Preliminary Alignment and Positioning
High Accelerating Gradients
Cryogenic Operation
Integrated Damping with NiChrome Coating
LCWS 2023 - Twelve C3 presentation with technical updates from detector background simulations to alignment studies

## Slide 13: Alignment and Vibrations
System level optimization essential for achieving performance
HG 2023
RF Structure Optimization
Main Linac Beam Dynamics
Vibration Measurements and Analysis
Two-Phase Fluid Simulations
Precision Short and Long Range Alignment
3.55 mm iris radius
2.0=Emax/Eacc
1.23=Hcoup/Hwall
White (C3), Schulte (CLIC)
Alignment Parameters | Units | Value
Raft Components | μm | 5
Short Range (~10m) | μm | 30
Long Range (>200m) | μm | 1000
Structure Vert. Vibration | μm | 9
Quad Vert. Vibration | nm | 15
BPM Resolution | μm | 0.1
BPM-Quad Alignment | μm | 2
Electric Field
Magnetic Field
M. Shumail, Z. Li
K. Shoele
H. Van Der Graaf
Z. George, V. Borzenets, A. Dhar, D. Palmer
100 nm resolution
Approved effort to test cold
https://arxiv.org/pdf/2307.07981.pdf

## Slide 14: Beam Dynamics and Luminosity Studies
Studies ongoing towards ensuring target luminosity
HG 2023
Damped / Damped-Detuned Spectrum
Wei-Hou Tan, Zenghai Li
See C3 talks at ECFA Workshop on e+e- Higgs/EW/Top Factories
https://agenda.infn.it/event/34841/
Ntounis, Gray, Vernieri
H. Xu et al., LANL
Emittance Preservation with HOM Suppression
Compatible with ILC-like Detector
Opportunities to Collaborate: DR, Bunch Compressor, BDS, …

## Slide 15: Outlook

## Slide 16: The Complete C3 Demonstrator
HG 2023
Demonstrate fully engineered cryomodule
~50 m scale facility
3 GeV energy reach
Answer technical questions needed for CDR

## Slide 17: Power Consumption and Sustainability
250 GeV CoM - Luminosity - 1.3x1034
Parameter | Units | Value
Reliquification Plant Cost | M$/MW | 18
Single Beam Power (125 GeV linac) | MW | 2
Total Beam Power | MW | 4
Total RF Power | MW | 18
Heat Load at Cryogenic Temperature | MW | 9
Electrical Power for RF | MW | 40
Cryoplant Electrical Power | MW | 60
Accelerator Complex Power | MW | ~50
Site Power | MW | ~150
Surface-Site Mockup
Precision-Weighted Carbon Footprint
Compact footprint <8 km for both underground and surface sites
  Underground – less constraints on energy upgrade
  Surface – lower cost and faster to first physics
Sustainability - construction + operations CO2 emissions per % sensitivity on couplings
  Polarization and high energy to improve sensitivity
  Construction CO2 emissions → minimize excavation and concrete
  Operations → limit power, decarbonization of the grid and dedicated renewable sources
Accepted PRX Energy, https://arxiv.org/abs/2307.04084
Notes: Sustainability lcws talk and paper

## Slide 18: Synergies with Future Colliders
RF Accelerator Technology Essential for All Near-Term Collider Concepts
C3 Demo is positioned to contribute synergistically or directly to all near-term collider concepts
CLIC - components, damping, fabrication techniques
ILC - options for electron driven positron source based C3 technology
Muon Collider - high gradient cryogenic copper cavities in cooling channel, alternative linac for acceleration after cooling
AAC - C3 Demo utilized for staging, C3 facility multi-TeV energy upgrade reutilizing tunnel, 𝛾𝛾 colliders
FCC-ee - common electron and positron injector linac from 6 to 20 GeV
  reduce length 3.5X OR reduce rf power 3.5X
HG 2023
90% seeds < 8 um-rad with lattice errors
Planned test at Argonne
Tracking with Lucretia includes longitudinal and transverse wakes, chromatic effects etc
Error study is 100 seeds, 100 μm element offsets, 300 μrad element rolls (rms)
  No corrections applied
Vibrant International Community for Future Colliders is Essential

## Slide 19: Conclusions
HG 2023
C3 provides a rapid route to precision Higgs physics with a compact 8 km footprint
  Higgs physics run by 2040
  US-hosted facility possible
C3 time structure is compatible with ILC-like detector design and optimizations ongoing
C3 upgrade to 550 GeV with only added rf sources
  Higgs self-coupling and expanded physics reach
C3 is scalable to multi-TeV
C3 Demo advances technology beyond CDR level
  5 year program, followed by completion of TDR and industrialization
  Three stages with quantitative metrics and milestones for decision points
  Direct and synergistic contributions to near-term collider concepts
More Details Here (Follow, Endorse, Collaborate):
https://web.slac.stanford.edu/c3/

## Slide 20: Questions?

## Slide 21: Additional Material

## Slide 22: Table of Parameters
HG 2023

## Slide 23: Full Parameters
HG 2023

## Slide 24: C3 Demonstration R&D Plan
HG 2023
C3 demonstration R&D needed to advance technology beyond CDR level
Minimum requirement for Demonstration R&D Plan:
Demonstrate operation of fully engineered and operational cryomodule
  Simultaneous operations of min. 3 cryomodules
Demonstrate operation during cryogenic flow equivalent to main linac at full liquid/gas flow rate
Operation with a multi-bunch photo injector - high charges bunches to induce wakes, tunable delay witness bunch to measure wakes
Demonstrate full operational gradient 120 MeV/m (and higher > 155 MeV/m) w/ single bunch
  Must understand margins for 120 - targeting power for (155 + margin) 170 MeV/m
  18X 50 MW C-band sources - off the shelf units
Fully damped-detuned accelerating structure
Work with industry to develop C-band source unit optimized for installation with main linac
This demonstration directly benefits development of compact FELs, beam dynamics, high brightness guns, etc.
The other elements needed for a linear collider - the sources, damping rings, and beam delivery system – more advanced from the ILC and CLIC – need C3 specific design
Our current baseline uses these directly; will look for further cost-optimizations for of C3

## Slide 25: Upgrade Options
Snowmass
Cryogenics Scale to multi-TeV
Parameter | Units | Baseline | High-Lumi
Energy CoM | GeV | 250 | 250
Gradient | MeV/m | 70 | 70
Beam Current | A | 0.2 | 1.6
Beam Power | MW | 2 | 16
Luminosity | x1034 | 1.3 | 10.4
Beam Loading |  | 45% | 87%
RF Power | MW/m | 30 | 125
Site Power | MW | ~150 | ~180
Caution: Requires serious investigation of beam dynamics - great topic for C3 Demonstration R&D
Luminosity
Energy
arXiv:1807.10195 (2018)
HTS Pulse Compressor
REBCO Coatings
Le Sage, CERN Collaborators
Qo ~ 400k
Beam power can be increased for additional luminosity
C3 has a relatively low current for 250 GeV CoM (0.19 A) - Could we push to match CLIC at 1.66 A? (8.5X increase?)
Pulse length and rep. rate are also options
Scalability studied to 3 TeV
Requires rf pulse compression for reasonable site power
Higher gradient option (155 MeV/m) in consideration

## Slide 26: Further Cavity Optimization Possible
HG 2023
Dipole
with symmetrization 100X reduction
V1-simple-stub
(not ideal cancellation)
V2-symm-stub
(good cancellation)
Single side coupling iris induces dipole and quad fields
Coupling hole symmetrization and racetrack shape incorporated to minimize dipole and quad fields
Dipole
Quad
Quad
w/o symmetrization
✅
dipole, quad calculated at 50MV/m
Zenghai Li

## Slide 27: RF Source R&D Over the Timescale of the Next P5
HG 2023
RF source cost is the key driver for gradient and cost
Significant savings when items procured at scale of LC
Need to focus R&D on reducing source cost to drive economic argument for high gradient
Understand the Impact on Advanced Collider Concept Enabled by the Goals Defined in the DOE GARD RF Decadal Roadmap
https://science.energy.gov/~/media/hep/pdf/Reports/DOE_HEP_GARD_RF_Research_Roadmap_Report.pdf
Relative Cost
Gradient/Cost Scaling vs. RF Source Cost for Main Linac

## Slide 28: RF Power Requirements
HG 2023
70 MeV/m 250 ns Flattop (extendible to 700 ns)
~1 microsecond rf pulse, ~30 MW/m
Conservative 2.3X enhancement from cryo
No pulse compression
Ramp power to reduce reflected power
Flip phase at output to reduce thermals
One 65 MW klystron every two meters -> Matches CLIC-k rf module power
Gradient
Thermals
RF Power

## Slide 29: Gaussian Detuning Provides Required 1st Band Dipole Suppression for Subsequent Bunch, Damping Also Needed
HG 2023
Dipole mode wakefields immediate concern for bunch train
4𝜎 Gaussian detuning of 80 cells for dipole mode (1st band) at 𝑓𝑐=9.5 GHz, w/ ∆𝑓/𝑓𝑐=5.6%
First subsequent bunch s = 1m, full train ~75 m in length
Damping needed to suppress re-coherence

## Slide 30: Distributed Coupling Structures Provide Natural Path to Implement Detuning and Damping of Higher Order Modes
HG 2023
Individual cell feeds necessitate adoption of split-block assembly
Perturbation due to joint does not couple to accelerating mode
Exploring gaps in quadrature to damp higher order mode
Detuned Cavity Designs
Quadrant Structure

## Slide 31: Implementation of Slot Damping
ILC Update
Need to extend to 40 GHz / Optimize coupling / Modes below 104 V/pC/mm/m
NiCr coated damping slots in development
Tapered Slot
Kick Factor
Vacuum Space Model
Kick Factor * Q
Two Cell Prototype
H. Xu, NCRF W 17th May 13:30
NiCr Tested at 80K

## Slide 32: Implementation of Slot Damping
HG 2023
Need to extend to 40 GHz / Optimize coupling / Modes below 104 V/pC/mm/m
NiCr coated damping slots in development
Tapered Slot
Kick Factor
Vacuum Space Model
Kick Factor * Q
Damping Slot Prototype

## Slide 33: RF Power Requirements and Cryogenics
ILC Update
70 MeV/m 250 ns Flattop (extendible to 700 ns)
~1 microsecond rf pulse, ~30 MW/m
2.3X enhancement from cryo
No pulse compression
Ramp power to reduce reflected power
Flip phase at output to reduce thermals
<2.5 kW/m of structure for C3-250/550
15% cooling efficiency with LN
Gradient
Thermals
RF Power
M. Breidenbach, CF W 17th May 14:15

## Slide 34: Beam Format and Detector Design Requirements
HG 2023
ILC timing structure: Fraction of a percent duty cycle
Power pulsing possible, significantly reduce heat load
  Factor of 50-100 power saving for FE analog power
Tracking detectors don’t need active cooling
  Significantly reduction for the material budget
Triggerless readout is the baseline
C3 time structure is compatible with ILC-like detector overall design and ongoing optimizations
1 ms long bunch trains at 5 Hz
2820 bunches per train
308ns spacing
ILC timing structure
C3 timing structure

## Slide 35: Why 550 GeV?
HG 2023
We propose 250 GeV with a relatively inexpensive upgrade to 550 GeV
An orthogonal dataset at 550 GeV to cross-check a deviation from the SM predictions observed at 250 GeV
From 500 to 550 GeV a factor 2 improvement to the top-Yukawa coupling
O(20%) precision on the Higgs self-coupling would allow to exclude/demonstrate at 5𝜎 models of electroweak baryogenesis

## Slide 36: One note on polarization
HG 2023
There are extensive comparisons between the FCC-ee plan and the C3/ILC runs that show they are rather compatible to study the Higgs Boson
When analyzing Higgs couplings with SMEFT, 2 ab-1 of polarized running is essentially equivalent to 5 ab-1 of unpolarized running.
  Electron polarization is essential for this. But, there is almost no difference in the expectation with and without positron polarization.
  Positron polarization allows more cross-checks of systematic errors. We may wish to add it later.
  Positron polarization brings a large advantage in multi-TeV running, where the most important cross sections are from e-Le+R
arXiv:1708.08912
arXiv:1801.02840

## Slide 37: Physics: Higgs Production at e+e-
HG 2023
ZH is dominant at 250 GeV
Above 500 GeV
Hvv dominates
ttH opens up
HH production accessible with ZHH
Delivers a rich physics program
The Energy Frontier 2021 Snowmass Report
Notes: ZH -> width, couplings of the Higgs to b/c, and invisible/exotic decays (no trigger!)

## Slide 38: Sustainability
HG 2023
Sustainability - construction + operations CO2 emissions per % sensitivity on couplings
  Polarization and high energy to improve sensitivity
  Construction CO2 emissions → minimize excavation and concrete
  Operations → limit power, decarbonization of the grid and

## Slide 39: Global Contributions
C3 Technical Timeline Only Possible with the Exceptional Progress of ILC and CLIC
Benefit from injector complex and beam delivery concepts
Continue to benefit from technological improvement by ILC and CLIC
HG 2023
Vibrant International Community for Future Colliders is Essential
High Efficiency RF Sources (CLIC)
I. Sarchev, CERN
Electron Driven Positron Source
Nanobeams for IP (ATF)
https://www-atf.kek.jp/atf/
Courtesy of Y. Enomoto