## Slide 1: Short-pulse RF research at the AWA facility
JOHN POWER
On behalf of the AWA facility at Argonne National Laboratory
Oct 17, 2023
https://www.anl.gov/awa

## Slide 2: Next-Generation Accelerator technology at the AWA
BASIC RESEARCH
….. on 3 THEMES (next slide)
DEVELOPING APPLICATIONS
….. NEAR-TERM & MID-TERM as stepping-stones towards a LONG-TERM e+/e- LC.
enabling GV/m STRUCTURE WAKEFIELD acceleration to produce bright GeV-class electron beams at the Argonne Wakefield accelerator

## Slide 3: AWA Research themes
Timeless research themes
Beam Production
APPLICATION
Beam Manipulation
Beam manipulation and control.
Beam Diagnostics.
e.g. Double Emittance Exchange
Advanced Acceleration
Structure Wakefield Acceleration
        Two beam acceleration
        Collinear wakefield acceleration
Plasma Wakefield Acceleration
e.g. SWFA
High-brightness sources
High-charge sources
Novel cathodes
e.g. RF Photoinjector
THEME 3
THEME 1
THEME 2
10 TeV Linear Collider
  10 GeV Compact XFEL
10 MeV UED
not exhaustive

## Slide 4: e-beam Driven Structure Wakefield Acceleration (SFWA)
Collinear Wakefield Acceleration
DB
MB
PWFA-like
A. Zholents, et al, NIMA 829, 190-193 (2016)​
A. Zholents, et al, Proceedings of IPAC2018​
main beam
drive beam
Klystron-like
CLIC CDR​: https://project-clic-cdr.web.cern.ch/CDR_Volume1.pdf​
W. Gai, C. Jing, J.G. Power, JPP 78, 339-345 (2012)​
drive beam
main beam
Power Extraction and Transfer Structure (PETS)
Accelerator
Two Beam Acceleration

## Slide 5: The Argonne Wakefield Accelerator (AWA) Facility
Beam Test Facility to enable novel acceleration
Drive RF Photoinjector (65 MeV)
  single bunch: 100nC
  bunch train: 600 nC
Argonne Cathode Test Stand (2-4 MeV)
Cathode research and diagnostics
Physics of high-gradient breakdown
Witness RF photoinjector (15 MeV)
Provides two-beam capability
Bright beams for low-energy experiments
Experimental Switchyard
Highly reconfigurable
6D phase space manipulation
Laser
100 mJ (IR), 10 mJ (UV),
300 fs – 6 ps (UV)
temporal shaping
https://www.anl.gov/awa

## Slide 6
The long and
winding road
to
High-Gradient
Kilpatrick
(1970s)
Juwen Wang
(1980s)
??
??

## Slide 7: Limits to high gradient operation
RF Breakdown  main problem
Field emission/dark current (unwanted beam loading and ionizing radiation can blind beam diagnostics, etc.)
Excessive conditioning time
Structure (most studied):
X-band, NCRF, 100<pulse length<1000 ns, OFE Copper BDR = 1e−6 m-1
RF Breakdown guidelines
Esurf < 250 MV/m,
Pulse heating: DT < 50 0C,
Power: abs(Sc) < 5 MW/mm2
Stored Energy: U < 1 J
Simakov, Dolgashev, Tantawi, “Advances in high gradient normal conducting accelerator structures, NIMA, Volume 907, 2018, https://doi.org/10.1016/j.nima.2018.02.085

## Slide 8: 3 promising paths to higher gradients
Material: Hard bi-metallic alloy (SLAC: Cu:Ag 0.8% Ag)
Temperature: cryogenic temp (SLAC/UCLA/LANL: cold copper)
1
2
3
Short RF pulse
(ANL/Tsinghua/PSI)
Notes: Not exhaustive list …

## Slide 9: The Short Pulse RF Advantage
3
3e−7/m, 100 MV/m, 200ns
Scaling Law
H. H. Braun, et al., “High-power testing of 30 GHz accelerating Structures at CTF II”, CLIC Note 475
W. Wuensch, et al., “A demonstration of high-gradient acceleration”, PAC’03
Short pulse < 100 nsec
PSI: 90 nsec TW gun
Tsinghua: Short ~50 nsec
AWA/Euclid/NIU: Ultrashort ~10 nsec
New physics? Empirical scaling law, underlying mechanism may change
Challenges: Challenges to operate in the short-pulse regime: broadband couplers, efficiency, stability, etc.
A. Grudiev, S. Calatroni, and W. Wuensch
Phys. Rev. ST Accel. Beams 12,102001 (2009)
S. Doebert et al.,PAC’05
https://accelconf.web.cern.ch/p05/PAPERS/ROAC004.PDF
klystron
TBA
1 ms
0.1 ms
long pulse regime
CLIC 2003

## Slide 10
TBA: RF power generation: PETS
drive beam
main beam
Power Extraction and Transfer Structure (PETS)
Accelerator
Two Beam Acceleration

## Slide 11: short pulse rf generation
TBA drive beam PETS
…
ZONE1
ZONE3a
…
magnets & diagnostics
Drive bunch train
-5 GW beam power
-100A, 6 nsec
1.3 GHz Drive gun (Cs2Te photocathode)
  High charge bunch train (up to 600 nC)
  Final beam energy: ~65 MeV
……..
(Drive RF photoinjector)
(PETS)
Short RF pulse
(2 Hz)
  disk-loaded waveguide: 400 MW
  Metamaterial: 565 MW
Dielectric PETS: 80 MW
11.7 GHz
26 GHz
Notes: X-band test has become a general capability of AWA (work underway for 26 GHz to THz)

## Slide 12: PETS results at AWA
Dielectric X-band PETS (200 MW)
DOI: 10.1103/PhysRevAccelBeams.23.011301
2000 2005 2010 2015 2020 2025
1000 MW
900 MW
800 MW
700 MW
600 MW
500 MW
400 MW
300 MW
200 MW
100 MW
0 MW
C-band
dielectric
(2000)
C-band
dielectric
(2008)
X-band dielectric (2018)
X-band metallic (2018)
X-band metallic (2020)
X-band MTM (2019)
X-band MTM (2021)
AWA energy upgrade
15 MeV  65 MeV
K-band dielectric (2010)
J. Picard et al., PRAB 25, 051301 (2022)
MTM X-band PETS (565 MW)
  Highest peak power as 565 MW from a train of eight bunches with a total charge of 355 nC
Metallic X-band PETS (400 MW)
J. Shao et. al., https://accelconf.web.cern.ch/ipac2019/papers/MOPRB069.pdf

## Slide 13
TBA: high-gradient structures: accelerator
drive beam
main beam
Power Extraction and Transfer Structure (PETS)
Accelerator
Two Beam Acceleration

## Slide 14: High gradient structure test stand
Beam on YAG1
…
…
ZONE1
(Drive RF photoinjector)
ZONE3a
(PETS)
Example:
X-band gun beamline
high gradient test stand

## Slide 15: HIGH GRADIENT ACCELERATING STRUCTURES
Dielectric Loaded Accelerator (DLA)
2000 2005 2010 2015 2020 2025
400 MV/m
350 MV/m
300 MV/m
250 MV/m
200 MV/m
150 MV/m
100 MV/m
50 MV/m
0 MV/m
C-band TBA
DLA (2000)
K-band TBA DLA (2018)
X-band metallic (2018)
X-band metallic (2021)
AWA energy upgrade
15 MeV  65 MeV
X-band TBA DDA (2022)
X-band PC Gun (2021)
W-band CWA metallic (2015)
C-band TBA
DLA (2008)
C-band CWA
PBG (2009)
X-band MTM (2023)
Single-cell Dielectric
Disk Accelerator (DDA)
3-cell Disk Loaded Waveguide
1.5 cell X-band Photocathode Gun
Single-cell Disk Loaded Waveguide
Metamaterial Accelerator

## Slide 16
16
100 MV/m Dielectric Disk Accelerator
See poster: Sarah Weatherly
High-power test results (Summer 2023)
AWA drive gun arcing limited run to 293 nC
PETS = 222 MW
Gradient ~78 MV/m (no arcing, no multipactor)
Drive Gun working now, will continue testing in November
Next step: Multicell DDA
Special attention to triple junction design
Clamped structure, like single cell.
RF design and fabrication are completed

## Slide 17: Initial rf conditioning of Xgun*
quick ramp-up
dark current loading
conditioning & dark current reduction
Xgun conditioning
test stand
RF
Xgun
Faraday cup & YAG
*W.H.Tan et. al., Phys. Rev. Accel. Beams 25, 083402, August 2022 (2022)
Gun performance
  387 MV/m on the photocathode
  BDR ~4e-6 (estimated)
  Ultra low dark current (<1pC per RF pulse)**
First beam
**J. Shao et. al., 10.1103/PhysRevLett.115.264802
Notes: Shao’s PRL ref from 2015 that shows field emission depends on stored energy.

## Slide 18
SHORT-PULSE REGIME
X-band RF test stand (500 MW, 2 Hz)
  RF power generation
    565 MW metamaterial PETS
    400 MW metallic PETS
    200 MW dielectric PETS
  High-gradient structures
    300 MV/m X-band TW accelerating metallic accelerator
    400 MV/m X-band photocathode gun
    100 MV/m X-band TW dielectric disk accelerator
    100 MV/m X-band transverse deflector
      Discovery of BIAR regime (see HG2022 Jiahang Shao)
Next Steps
  Test Xgun V1 to higher gradients … once Xgun V2 is working
  Generate higher-charge drive dunch trains
  Demonstrators
    100 MeV high-brightness Xgun photoinjector beamline
    500 MeV demonstrator
  Upgrade AWA drive beam energy from 65 MeV to ~130 MeV
summary

## Slide 19
Big Thanks to our team!
Gongxiaohui Chen (AWA) Scott Doran (AWA) Alex Ody (AWA) Wanming Liu (AWA) John Power (AWA) Charles Whiteford (AWA) Eric Wisniewski (AWA) Gwanghui Ha (was at AWA, now at NIU) Jiahang Shao (was at AWA, now at IASF) Maomao Peng (was at AWA) | Chunguang Jing (Euclid Techlabs / AWA) Ernie Knight (Euclid Techlabs) Sergey Kuzikov (Euclid Techlabs) Ben Freemire (Euclid Techlabs) Sergey Antipov (Euclid Techlabs, now at PALM Scientific) Xueying Lu (NIU / AWA) Philippe Piot (NIU / AWA) Emily Frame (NIU) Wei Hou Tan (NIU, now at SLAC) Sarah Weatherly (IIT)
We also thank funding agencies: DoE HEP and SBIR programs and ANL LDRD.

## Slide 21
extras

## Slide 22: Short-pulse high-power test at AWA
BD type I
BD type II
- Distorted main pulse
- Disappeared after conditioning
- Likely to be caused by multipacting
Main pulse
Secondary pulse
H. Xu et al., PRAB 22, 021002 (2019)
- Blocked secondary pulse and normal main pulse
- Probability decreases after conditioning
- Likely to be caused by RF breakdown
Main pulse
Secondary pulse

## Slide 23: Results discussion (I)
Comparison of short and long pulse results
Fit to BDRE30
Accelerating gradient of the normal cell and the input matching cell reaches 270 MV/m and 310 MV/m
Surface field of the input matching cell reaches 500 MV/m
Gradient improved at least twofold using short pulse (limited conditioning period, only secondary pulse taken into consideration)
BDR vs. pulse length doesn’t follow the empirical scaling law in short-pulse regime
New physics of RF breakdown in short-pulse regime

## Slide 24
Breakdown Insensitive Acceleration Regime (BIAR)
RF causes BD and plasma generation
RF pulse
0 ns
Plasma expansion to block RF transmission
after ~10 ns
ANL: ϕ10-20 μm
Tsinghua: ϕ30-100 μm
Transmitted RF pulse and accelerated beam not influenced by RF breakdown
Reduced structure damage due to limited energy available for breakdown avalanche
Results discussion (II)

## Slide 25: Xgun: 1.5 cell RF photocathode gun
RF Design
RF
beam
COAXIAL RF-INPUT COUPLER
1.5-CELL
XGUN
IRIS DISK
Overcoupled -mode @11.7 GHz
RF
S. Kuzikov et al., (IPAC21)
An X-band Ultra-high Gradient Photoinjector
https://accelconf.web.cern.ch/ipac2021/papers/wepab163.pdf
S11 simulation (CST)
S11 measurement (N.A.)
Cathode is the Cu backwall
Parameter | Value
Frequency | 11.7 GHz
Mode | p
t_fill | 5.4 nsec
RF pulse length | 9ns (3 ns rise, 3 ns flat, 3 ns, fall)
Power | 250
Cathode Field | 470
25/36

## Slide 26: Xgun beamline
drive bunch train
PETS
power splitter
Xgun
Xgun beam
imaging
solenoid
ICT
spectrometer
dipole
YAG &
Pepper pot
quad
BPM
laser injects from
the 1st viewport
main solenoid
(w/ iron plate)
YAG
(energy meas.)
RF
RF
rf load
current configuration
spectrometer
quad
[1] M. Peng, et al., (IPAC 19)
Generation of high power short rf pulses using an X-band metallic power extractor driven by high charge multi-bunch train. https://accelconf.web.cern.ch/ipac2019/papers/MOPRB069.pdf
[2] J. Shao, et al., (IPAC 21)
High-power test of a highly over-coupled X-band rf Gun driven by short rf pulses
https://accelconf.web.cern.ch/ipac2021/papers/thpab331.pdf

## Slide 27: Metamaterial accelerator
Efficient structure design to explore gradient limitation
  190 MV/m peak gradient from 115 MW input RF
  11.7 GHz structure optimized for 6 ns FWHM RF pulses extracted from the drive beam
  Breakdown Insensitive Accelerating Regime (BIAR)

## Slide 28: The Argonne Wakefield Accelerator
The AWA Bunker
Witness
Drive
AWA Vacuum and Experimental Zones
ACT
EXPERIMENTAL AREA
Zones 2-5 are experimental areas
Zones 2, 4, and 5 have ~ 1 m experimental area
Zones 3A & 3B are fully re-configurable
5 Zones
28/36

## Slide 29: XFEL in biar?
TBA---9GeV Compact FEL in BIAR regime
Fast filled accelerator
Yuliang Jiang, et al, PRAB 24, 112002 (2021)
Advantages:
Short pulses
Drive beam can generate RF at multiple frequencies
Automatically sync’ed
Challenges:
Still in research phase
Kickers
Waveguides

## Slide 30: WHY AAC? … Why SWFA?
AAC technology is versatile
Long-term
  1-10 TeV e+e- linear collider
  Higg’s Factory
Mid-term
  XFEL light sources
  Inverse Compton sources
Near-term
  Compact accelerators for societal applications or Stewardship (E.g. Industrial, Security, Medical applications.)
AAC Roadmap: PWFA, LWFA, SWFA
30
SWFA
  Positron acceleration
  Takes advantage of much existing technology from today’s accelerators
  Recent progress (few MV/m  300 MV/m at X-band, exploring GV/m …)
IP
e-
e+
3TeV
1
10
1
10
SWFA 3 TeV linear collider
SWFA XFEL