## Slide 1: X17 @ n_TOF
Riccardo mucciola

## Slide 2: X17 ATOMKI results
A significant anomaly has been recently in the emission of electron-positron pairs in the 7Li(p,e+e-)8Be and 3H(p,e+e-)4He reactions:
Krasznahorkay, A.J.; et al.:
"Observation of Anomalous Internal Pair Creation in 8Be: A Possible Indication of a Light, Neutral Boson".
Physical Review Letters. 116 (42501): 042501 (2016).
Krasznahorkay, A.J.; et al.:
"A new anomaly observed in 4He supports the existence of the hypothetical X17 particle".
Physical Review C 104, 044003 (2021).
This anomaly has been interpreted as the signature of a BOSON (hereafter X17) not foreseen in the standard model of particle physics.
X17 boson could be a mediator of a fifth force, characterized by a strong coupling suppression of protons compared to neutrons.
This evidence/scenario is presently not confirmed or excluded by other experiments or groups.

## Slide 3: X17 @ n_TOF
Basic idea: new study of excited 4He exploiting the conjugated reactions:
3H(p,e+e-)4He
3He(n,e+e-)4He
OBJECTIVES:
Probing X17 existence
X17 Mass, quantic numbers, coupling, life-time, ..
Proto-phobic nature of the fifth force.
Data Vs Theoretical nuclear physics

## Slide 4: Theoretical calculations
Theoretical calculations for kinematical signature for different X17 boson (scalar, pseudo-scalar, vector, axial).,
Calculation for different center-of-mass energies.
M. Viviani et al.: PRC 105, 014001 (2022)

## Slide 5: Theoretical calculations
M. Viviani et al.: PRC 105, 014001 (2022)
Theoretical calculations of expected counts at different lepton plane angles,
Calculation for different natures of the X17 boson (scalar, pseudo-scalar, vector, axial).
Wide energy range (protons and neutron beams) to explore all resonances with different Jπ
Large detector acceptance for statistics and kinematics

## Slide 6: Facilities
n_ToF @ CERN: pulsed neutron beam in a wide energy range (thermal<En<100 MeV).
Time of flight to establish the single neutron energy (10-108 eV)
LUNA-MV @ LNGS: high intensity proton beam and low background
Terminal Voltage ~ 0.2 – 3.5 MV
I max ~ 100 μA of protons
Underground operation
3He(n,X17)4He
Measurements:
2022-24 (CERN LoI approved)
3H(p,X17)4He
Measurements:
2023-25 (LoI in preparation)

## Slide 7: uRwell detector
uTPC with drift gap and uRwell
Active area of 38x46 cm2
Ar/CF4/CO2 (60:20:20) gas mixture
3D track reconstruction
Under construction at CERN

## Slide 8: Demonstrator
Demonstrator funded by INFN
Two uRwell detectors and two scintillator cubes
Capsule holding 3He gas
Test at EAR2 @ n_TOF in 2023

## Slide 9: uRwell Simulations
GARFIELD simulations to study detector performances
Electric field and electrons drift velocities simulated
The track reconstruction in a magnetic field is being studied

## Slide 10: Garfield tracks
Tracks of different energies (2-18 MeV)
Magnetic field of 500 G
No visible curvature in the perpendicular plane

## Slide 11: Energy reconstruction
Assume interaction vertex at the origin
Fit circumference arc using straight track and vertex
Tangent (red line) used for angle determination (see later)
PRELIMINARY

## Slide 12: Energy reconstruction
PRELIMINARY

## Slide 13: Emission Angle Reconstruction
Theta reconstructed using linear fit of the track
Phi reconstructed using tangent to circumference at emission vertex
PRELIMINARY

## Slide 14: Angles Recontruction
PRELIMINARY

## Slide 15: Conclusions
New detection setup for X17 based on uRwell to reach high angular acceptance,
Search of X17 mainly via 3He(n, e+e-)4He reaction,
Simulations to study the feasibility of measurements with magnetic field are ongoing.
Demonstrator will be tested at EAR2 @ n_TOF at the end of 2023,
Possible measurements with protons beam at other facilities (e.g., LUNA),
Physics program will start in 2024->2025.

## Slide 16
The X17 Team
E. Cisbani (ISS ROMA)
N. Colonna (INFN BARI)
G. De Angelis (ISS ROMA)
M. D'incecco (LNGS)
G. Gervino (UNITO)
C. Gustavino (INFN ROMA)
C. Massimi (UNIBO)
P. Mastinu (INFN LNL)
B. A. Mohammadzadhe (INFN ROMA)
A. Mengoni (ENEA BO)
R. Mucciola (UNITO)
C. Petrone (IFIN-HH)
F. Santavenere (ISS ROMA)
M. Viviani (INFN PISA)
And others...
Thank you
for your attention!

## Slide 17: Backup

## Slide 18: Geant4 setup
Simulations performed with Geant4 to study high number of events:
2/4 uRwell detectors,
20 cm from beam,
Magnetic field of max 500 G parallel to beam direction.

## Slide 19: Simulations
SIMULATION:
SETUP with all used materials
Realistic n_TOF beam
IPC/X17 events rate (normalized to ATOMKI data)
OUTPUT:
Acceptance/efficiency/MS
Signal/Noise
Detector performance
e+e- ID and 4-momenta
X17 invariant mass