## Slide 1
Quantum noise in Gravitational Wave Detectors
Jean-Pierre Zendri`
INFN Sezione di Padova
On behalf of the Virgo collaboration
Workshop on
Quantum Technologies for Fundamental Physics
Erice, 1-6 September 2023

## Slide 2
Motivation
Typical strain power spectral density

## Slide 3
Michelson Interferometers: GW signal
Laser
PD
BS
M1
M2
/
/
Symmetric Detector configuration
  BS 50:50
  Same arm length
The injected laser beam does not reach the photodetector “PD”
A gravitational wave generates a difference “x” in the arms length leading to a signal “” in the quadrature orthogonal to that of the injection laser.
x/2
x/2

## Slide 4
Michelson Interferometers: Quantum Noise
/
/
BS
M1
Laser
PD
/
/
The input laser amplitude () and phase () fluctuations are constrained by QM :
For a symmetric interferometer and assuming equal mass mirros do not generate any signal in the dark port
The quantum fluctuations () of the vacuum field entering in the detection port do not cancel out and generate the quantum noise detected on PD
C.M. Caves, Phys. Rev. D 23, 1693 (1981)

## Slide 5
Back action
Shot noise
Michelson Interferometers: Standard Quantum Limit
BS
Laser
PD
/
/
Quantum noise generators
Optomechanical coupling κ
Signal
Shot noise
Back action noise
Strain sensitivity assuming a coherent vacuum state
At minimum () Standard quantum limit

## Slide 6
Squeezed states:
  squeezing factor
  Squeezing angle
Michelson interferometer with squeezing
Coherent State
3.5 dB
Quantum noise can be manipulated with squeezed light
  ,
  The SQL can be surpassed in a limited frequency region if
Squeezed State
Phase Squeezing
Ampl. Squeezing
3.5 dB
3.5 dB
enerates shot noise (high frequency)
enerates radiation pressure noise (low frequency)

## Slide 7
Michelson Interferometers: Ponderomotive squeezing
Input field
Output field
Coherent state: the variance the same for both the orthogonal quadratures regardless of the choice of
Output field: due to the radiation pressure contribution () the variance of the two quadratures are different and are dependent
The output field is a frequency dependent squeezed field in which the signal quadrature () is in general not aligned to that of the minimal noise ()
Signal
Quadrature

## Slide 8
FDS source
Frequency dependent squeezing (FDS)
The injected squeezing ellipse angle is rotate as a function of the frequency to compensate from the rotation resulting from the optomechanical coupling with the interferometer.
The minimum of the output noise is always aligned with the signal quadrature. Quantum noise is suppressed by a factor over the all the whole detection band.

## Slide 9
Frequency Dependent Squeezing with Filter Cavities
-
-
Phase Squeezing
Amplitude Squeezing
Frequency dependent squeezing
Frequency dependent squeezing is generated by exploiting the dispersion in the reflection of a frequency independent squeezing source from adetuned optical cavity
For the “resonant sideband extraction” configuration (LIGO,Virgo) the optimal rotation is obtained with a single cavity with FWHM and detuning
For the next observation run for Virgo
Phys. Rev. D 65, 022002 (2001)
Phys. Rev. D 90, 062006 (2014)

## Slide 10
Real GW detectors
Arm cavity
Arm cavity
PR mirror
SR mirror
Resonant sideband extraction scheme (LIGO and Virgo) the optomechanical coupling factor ( instead of ) in the detector bandwidth
For the detuned configuration the mechanical susceptibility (and therefore ) is affected by the optical spring
Dual Recycled configuration

## Slide 11
Squeezing degradation: quantum decoherence from lossses
IN
OUT
Losses:
  Loss mechanism
  Absorption, clipping and scattering
  Misalignment and geometrical mode mismatch
  Polarization error
  Photodetector quantum efficiency
  High order mode
  Beam Splitter model
  Frequency dependent
Phys. Rev. D 104, 062006 (2021)
  The total amount of losses tipically range between 20% and 40%
  In general not fully explained with the loss budget.
Phys. Rev. D 104, 062006 (2021)

## Slide 12
  The mismatch cause a beam splitter like mixing between LG00 and HOM
  The two mode experience different phase evolution during propagation
  Another mismatch mix back the modes leading to an additional effective loss contribution which can also be negative (coherent cancellation)
The role of the High Order Modes (HOM)
  The scattered light couple to the high order modes resulting in a loss in the fundamental mode.
  Particularly efficient mechanism if the resonance frequency of the HOM falls close to that of the fundamental mode.
  Mirror roughness Map
  RTL versus mirror RoC
  LG00
  HOM
  SQZ
  OMC
  ITF
  Gouy Phase
  Coher
  Wavefront deformation
  Mode Mismatch

## Slide 13
Squeezing degradation: dephasing
Generated by a phase jitter between the LO (ITF carrier) and the squeezed field which manifests with a squeezing angular ijtter.
The low frequency contribution (mainly deriving from seismic and acoustic noise) is suppressed with the coherent control loop to less than few mrad-rms.
At high frequencies contribution comes mainly from control sidebands unbalancing or interacting with the interferometer contrast defect
Phys. Rev. Lett. 125, 131101 (2020)
Typical values of the optical losses and angular jitter in GW detectors
Produced 10 dB
3 dB
4 dB
5 dB
6 dB
7 dB
8 dB

## Slide 14
The Virgo Gravitational wave detector
Virgo collaboration
  18 countires
  132 Institutes
  700 members
Virgo site
European Gravitational Observatory (EGO
Cascina, Italy
Quantum noise reduction in Virgo
Observation Run O3 (Apr. 2019-Mar. 2020)
  Power recycled configuration
  Frequency Dependent Squeezing
Observation Run O4
  Dual recycled configuration
  Frequency dependent Squeezing
Virgo detector:
  Long arm (3km) cavities
  Located in Cascina (Italy)

## Slide 15
The Observation run O3
Power recycling configuration
Frequency independent squeezing injection

## Slide 16
The AEI vacuum squeezed source
M.Mehmet and H.Vahlbruch, CQG 36, 015014 (2019)
Squeezed states generated with parametric down conversion in crystals
Double resonant linear OPA cavity
Low residual phase noise (3.5 mrad RMS)
Up to 12 dB of squeezing measured in the audio band
The AEI squeezer in Cascina
~1meter

## Slide 17
The Observation run O3: results
No SQZ injection
Amplitude SQZ injection
Phase SQZ injection
Up to 3 dB of shot noise reduction
5-8 % BNS horizon enhancement
Long term stability
Phys. Rev. Lett. 123, 231108 (2019)
First evidence of squeezed light enhanced quantum radiation pressure noise on a 42 Kg test mass
Phys. Rev. Lett. 125, 131101 (2020)
(for LIGO Nature 583, 43 (2020)
Optical losses 43%, Phase noise 60 mrad
(for LIGO Phys. Rev. Lett. 123, 231107 (2019))

## Slide 18
Filter Cavity Length Optimization for Virgo
Cavity length-dependent squeezing degradation sources
FC round trip losses (yellow):
  Optical losses
  Mixes the two quadratures thereby corrupte squeezing with anti-squeezing
Phase noise (pink): produced by the residual cavity length fluctuations which generate detuning variations
Cavity length-independent degradation sources
Mode mismatch between the squeezed beam and the FC
All other sources (injection and detection losses) assumed to be frequency independent
Target parameters
Linewidth | 25 Hz
FC Round trip losses | 40 ppm
Residual FC length noise | 1 pm
Mode mismatch | 2%
The optimal FC length is about 300 meters corresponding to finesse of 10000

## Slide 19
Virgo FDS source
Filter Cavity
North Arm
BS
SR
NI
Det

## Slide 20
Virgo FDS source
North Arm
BS
SR
NI
Det
Filter Cavity Mirrors
IM vacuum tank
IM suspension system
Last suspension stage
Mirrors: Diameter 150 mm, Thickness 90 mm, Roughness <0.58 nm RMS

## Slide 21
Virgo FDS source
North Arm
BS
SR
NI
Det
Suspended Quantum Bench 1
Suspended Quantum Bench 2

## Slide 22
Virgo FDS source
North Arm
BS
SR
NI
Det
External Quantum Bench 1
Plus SQZ board

## Slide 23
Virgo Filter Cavity exprimental layout and controls
Filter Cavity control with Green

## Slide 24
Virgo Filter Cavity exprimental layout and controls
Diagnostic Configuration

## Slide 25
Virgo Filter Cavity exprimental layout and controls
Science configuration

## Slide 26
Virgo FDS source: results
 | Target | Achieved
Lock accuracy [Hz rms] | 1 | 1
Round Trip losses [ppm] | 60 ppm | 50-90
Mode mismatch | 2% | 1.5%
Round trip optical Losses |  | 10%
Phase noise |  | 40 mrad
Expected quantum noise suppression in Virgo @ 40 W (simplified model)
Phys. Rev. Lett. 131, 041403 (2023)
Squeezing degree measured at homodyne angle
ITF losses 16% (independently estimated)
DET losses 6% (estimated)

## Slide 27
EPR-FDS squeezing
Pump:
Signal:
Idler:
Advantage:
No needs of filter cavity
Drawback:
3dB loss of squeezing
Not trivial implementation of low noise homodyne detection

## Slide 28
EPR squeezing: experimental demonstrators
FDS experimentally demonstrated on table top experiments (with no radiation pressure effect)
Nature Photonics 14, 240 (2020)
Nature Photonics 14, 223 (2020)
EPR demosntrator with a suspendet interfe rometer with two 350 mm long arm cavities being developed in Cascina (Virgo site). The quantum radiation pressure noise contribution is expected to be observable.
Mirror mass: 300 gr.

## Slide 29
Dechoerence mitigation:Internal squeezing
1)Low readout losses dominant: parametric deamplification
Proof of concept
2)Low internal losses dominant: parametric amplification
arXiv:2303.09983
Applicable for GW detectors?
Several technological problems to deal with
To be combined with quantum back-action evading techniques
SQZ
Cohe
gain
Loss
Signal
Max 6 dB
>6 dB
Same SNR as input

## Slide 30
Speed meters
Zero Area Sagnac interferometer
Photodetector
Input
laser
: propagation time
The generalized momentum “p” is a quantum non demolution observable (not affected by back action)
The momentum of the test mass is a quasi quantum non demolution observable
Two basic schemes
  Michelson interferometer plus external “sloshing” cavity
  Speed meter
https://link.springer.com/article/10.1007/s41114-019-0018-y
Large scale proof of principle still lacking
New configurations compatible with the michelson interferometer configuration are are being considered

## Slide 31
Summary
The operation of the GW detectors beyond the Standard Quantum Limit has been demonstrated using Frequency Dependent Squeezing.
In the medium term improvements are expected by working on minimizing the sources of squeezing degradation.
On longer timescales alternative schemes could be considered (speed meters, internal squeezing, EPR..).

## Slide 32
Quantum noise in Gravitational Wave Detectors
THANKS
for the attention

## Slide 33
Back-up SLIDES

## Slide 34
Coherent Control Loop
1. The phase difference between the pump and the Control field is imprinted in the beat note (error signal) and is stabilized.
2. The phase between the Control field and the LO is extracted from thei beat signal and is stabilized.

## Slide 35
O3 Loss budget
Injection Losses (5-13)%
  Faraday
  Optics
  Alignment
  Mode matching to Output mode cleaner
Detection Losses (13-24)%
  In vacuum Faraday
  OMC losses
  Mode matching ITF Output Mode cleaner
  Quantum efficiency of PDs
  Dark noise
Interferometer Losses (5-11)%
  Optics
  Arm cavities losses
  alignment
Squeezer Losses (2.5-3.5) %
  OPA escape efficeincy
  Alignment

## Slide 36
Stray light issue
Stray ligth Path
Injection Path
Stray light
The back reflected light that recpmbine with the ITF can spoil the detector sensitivity. Required less than10-20 W of recombined power
Main contribution from OPO refelection
Example (O3)

## Slide 37
Stray light issue
Stray ligth Path
Injection Path
Stray light
The back reflected light that recpmbine with the ITF can spoil the detector sensitivity. Required less than10-20 W of recombined power
Main contribution from OPO refelection
Example (O3)

## Slide 38
FDS: Thermal detuning
A different thermo-optical response of the green and IR coatings generated a time dependent cavity detuning driven by thermal drifts
For the Virgo FC mirrors about 110 Hz/K
It is required to stabilize the mirror temperature within 10-20 mK